## Slide 1: Alignment of the ALICE MUON Spectrometer
Photogrammetry
&
Alignment with tracks

## Slide 2: Plan
ALICE forward MUON spectrometer
  geometry
  expected initial misalignments
Day 0 misalignment - Survey and photogrammetry
  brief approach description
  current results
Alignment with particles
  brief approach description
  current alignment performances
Further developments

## Slide 3: Geometry and expected misalignments
MUON tracking detectors:
5 stations
  2 quadrant type
  3 slat type
10 chambers (2 chambers / station)
156 detection elements
  2x4; 2x4; 2x18; 2x26; 2x26
  provide
    x (1 mm) - non bending plane
    y (0.1 mm) - bending plane
Tracking Chambers
Stations 1,2,3,4 and 5
Slats type
Quadrants type
MUON tracking detectors:
Expected initial precision:
  chambers x,y,z ~ 1 mm
  detection elements x,y,z ~ 500 m
Geometrical Monitoring System:
  chambers x,y,z ~ 20 m

## Slide 4: Photogrammetry and Survey
Survey and Photogrammetry should provide Day 0 misalignment file
  Survey: half-chamber with respect to ALICE
  Photogrammetry: slat or quadrant with respect to chamber
Useful for:
  Check of coded geometry in AliRoot
  GMS
  Alignment with tracks
Currently available:
  Photogrammetry - chamber 8I
  Survey+Photogrammetry - chambers 1, 2, 3, 4 & 5
Used targets

## Slide 5: Approach for all Detection Elements
Sticker targets:
  Unknown local position
  If enough (>3) fit a plane
    Provide  and  rotation
2. Button targets:
  Known local position
  Fit local to global transformation (using known  and )
    provide x,y,z translation and ,  and  rotation

## Slide 6: Current results – Ch1 (quadrants)
Lines: misalignments of (half-)chambers with respect to Alice
Circles: misalignments of detection elements with respect to chamber

## Slide 7: Current results – Ch5 (slats)
Support panel is bended
All results within mechanical specifications
Lines: misalignments of (half-)chambers with respect to Alice
Circles: misalignments of detection elements with respect to chamber

## Slide 8: Latest developments / updates
Survey to alignment code
  New MUONSurvey classes committed to SVN
  Input data from survey/photogrammetry report stored in the ALICE Survey Data Depot
  Use AliSurveyObj and AliSurveyPoint to read data
  Produce misalignment data using AliAlignObj and stores it in (local) OCDB
  Macro available for each of the already surveyed chambers
  Write class/macro for the full detector

## Slide 9: Alignment approach
Common approach:
Use theo. geometry to reconstruct tracks
Calculate residuals (track-cluster)
Shift by residual average (n tracks)
Iterate until convergence
Problems:
Convergence is not guaranteed
Residuals are biased
Alignment parameters will then be biased
Correlations not taken into account
Optimum approach:
  Use theoretical geometry to reconstruct tracks
  For each track calculate residual at each detector
    Fj(t1,t2,… ;d1,d2,…) = Tj - Cj
  Minimize 2 =  (Tj-Cj)2/j2
Limitations for simultaneous minimization (matrix inversion):
  Huge number of parameters!
Special structure of alignment problem
  1 set of global parameters (detector misalignments)
  several sets of independent local parameters (track parameters)
allows exact solution using matrix inversion by partitioning
Correlations taken into account
Real life, unknown position
Theoretical position
Real track
Reconstructed (biaised) track

## Slide 10: Alignment with tracks : Millepede
What you need to do:
Define your “alignment parameters”
  Global parameters
Define your “track model” (B=0)
  Local parameters
Define your “measurement”
  Must be sensitive to the parameters
Write a linear expression of your 2 to minimize:
Per detection element:
B=0, straight track (4 parameters)
X (~1.0 mm) and Y (~0.1 mm) position of hit
MUON
Developed by V. Blobel: http://www.desy.de/~blobel/wwwmille.html
AliMillepede, modified from a c++ translation by S. Viret (LHCb) of original fortran package:
http://alisoft.cern.ch/viewvc/trunk/STEER/AliMillepede.cxx?root=AliRoot&view=log
AliMUONAlignment, MUON specific alignment code using AliMillepede:
http://alisoft.cern.ch/viewvc/trunk/MUON/AliMUONAlignment.cxx?root=AliRoot&view=log

## Slide 11: Current Results B=0, N track dependence
Input misalignments:
Uniform
|X,Y|<300 m
||< 500 rad
100k - 150k is a reasonable number
Need more realistic events
Alignment precision:
RMSX = 20 m
RMSY = 10 m
RMS = 20 rad
All stations are included
Constrains are essential

## Slide 12: Realistic / Pessimistic B=0
Input misalignments:
Gaussian
X,Y=500 m
= 900 rad
Generated 320k “pp muon” events -> 46k used out of 210k tracks
Encouraging!
Further test needed (constraints)
Higher statistics
Alignment precision:
RMSX = 58 m
RMSY = 44 m
RMS = 79 rad
v4-07-00
AliGenMuonCocktailpp event:
At least 1 muon
No soft pt cut

## Slide 13: Latest developments / updates
Alignment evaluation and validation
  Study the alignment performance using the track residuals
(Half-)Chamber degrees of freedom
  Possibility to generate (half)chamber misalignments included to AliMUONGeometryMisAligner
  Extend alignment code to include (half-)chamber degrees of freedom
    Math for derivatives calculation
    Implementation into AliMUONAlignment
    Test with expected (half-)chambers misalignments
Remaining translation and 2 rotations degrees of freedom
  Possibility to generate misalignments along z and around x and y
  Extend alignment code to include them
    Math for derivatives calculation
    Implementation into AliMUONAlignment
    Test with expected misalignments
    Test physics impact

## Slide 14: MUON Calibration: Alignment requirements
Size of raw data (muon stream) to be copied on disk: 25 G
Access to OCDB:
  During raw data reconstruction to all relevant entries: MUON,
  ITS(SPD), FMD, ...
  During alignment phase to MUON/Align
Need of AliRoot reconstruction: Yes
Needed CPU:
  Reconstruction of raw data up to ESDs level:
  12 CPU days *2 (minimum number of reconstruction passes)
  Reading ESDs and running alignment code : ~10h (include various test for optimization
Output size
  ESDs from reconstruction :
  8.5 G *2 (at least 1 extra pass to validate alignment)
  Alignment output for monitoring/validation : 3 G

## Slide 15: MUON Calibration: Alignment strategy
The alignment task is crucial to be ready for the official reconstruction production
In any case it is imperative (for a small subset of data, e.g. B=0) to
  have fast access to raw data
  be able to run (various) reconstructions over same set of data
Tools:
  Alice Grid ( ~5000 machines & several Pbytes)
  Cern Analysis Facility
  Shall we foresee other Analysis Facilities?
Strategy about the tool we plan to use
  If CAF is the right tool, the access to raw data, OCDB and AliRoot installation will be necessary
  At least 2 reconstruction passes on the same data should be run, the second one to test and validate the found alignment parameters. For the first ever alignment we will expect 3 passes to be needed as we may start from very far away
All the above work is to be repeated for each B=0 run

## Slide 16: Summary & ToDo
Alignment to do list
  AliMillepede development
    AliMillepede class optimization (fully use symmetric properties of matrix)
  AliMUONAlignment development
    Complete and test extension to other degrees of freedom
    Test alignment performances with more realistic events
    Re-start B-on case study
      Define a valid linear track approximation
      Select high transverse momentum tracks
    Complete study of alignment performance (including physics)
      Initial misalignment
      Number of tracks
  Read survey (photogrammetry files)
    Process data as it becomes available
    Most of the chambers will be resurveyed at the end of the shutdown