## Slide 1: HTS present activities at SACM - projects
Areas: accelerators magnets (dipoles), high-field magnets (solenoids),
EuCARD: 5 T HTS insert; block design and fabrication,
EuCARD2: 5 T HTS dipole; cos theta design and fabrication,
NOUGAT: 10 T HTS insert solenoid (in 20 T resistive background field)
PhD: Contribution to the design and tests of YBCO high-Tc superconducting inserts: screening currents and protection, (Guillaume Dilasser)
EuCARD2 cos theta design
3D CAD coil end spacers
Comparison with analytical formulas taken from E. Zeldov, Magnetization and transport currents in thin superconducting films

## Slide 2: HTS activities at SACM - topics
ReBCO conductor,
Winding and fabrication:
  Stacked tapes and Roebel conductors,
  Dipoles: block design and cos theta design,
  Solenoids: pancakes and double pancakes.
Experiments:
  Tests of YBCO coils (EuCARD insert, EuCARD2 cos theta, pancakes, small solenoids)
  Screening currents: measurements of remanent magnetic field and creep in small YBCO coils,
  Vortex shaking: screening current damp in YBCO coils,
  Coils with metallic insulation: stability and quench protection in YBCO MI pancakes,
Simulations:
  3D Quench propagation in HTS coils (CAST3M),
  2D and 3D screening currents developments (MATLAB, CAST3M),
  Metallic-insulation simulations (MATLAB)
NOUGAT
Non-insulated pancake
Tests @ 77 K