## Slide 1: Micro Pattern Gaseous Detectors and potential applications beyond fundamental Physics
Filippo Resnati1,2
on behalf of CERN EP-DT-DD Gaseous Detector Development team
1CERN, 2ESS
ICHEP - Chicago - 6th August 2016

## Slide 2: Outline
Brief overview of Micro-Pattern Gaseous Detectors
Four examples of their application beyond fundamental Physics
Intuitive, simple and versatile readout for MPGDs suitable for applications beyond HEP
Filippo Resnati - ICHEP - Chicago - 6th August 2016

## Slide 3: Micro-Pattern Gaseous Detectors
Structures to provide suitable electric fields in gas to amplify the otherwise small amount of ionisation charge produced by the interacting particles
Filippo Resnati - ICHEP - Chicago - 6th August 2016

## Slide 4: MPGDs: a rich family
micro electrodes
hole-like
mesh-like
extended electrodes
MicroPin
MicroDot
MicroPic
MHSP
MicroGroove
MicroWell
Micro-bulk MM
RPWell
Micro-RWell
GEM
TH-GEM
LEM
GEMpix
MicroGap
MicroWire
MSGC
MicroMeGas
CAT
InGrid
GridPix
Filippo Resnati - ICHEP - Chicago - 6th August 2016

## Slide 5: Micromegas
+
-
-
Anode can be made resistive to reduce the discharge effects
cathode
segmented anode
pilar
120 um
metal mesh
Filippo Resnati - ICHEP - Chicago - 6th August 2016

## Slide 6: GEMs
-
-
-
-
-
-
-
-
-
-
-
+
-
-
-
-
-
-
-
-
-
-
-
-
-
-
Small gain of each stage reduces the discharge probability
50 um
70 um
cathode
segmented anode
cathode2
anode2
140 um
Filippo Resnati - ICHEP - Chicago - 6th August 2016

## Slide 7: Two remarkable examples
GEM for upgrade
of the forward
CMS muon system
120 cm
50 cm
MM for ATLAS upgrade of the NSM
2 m
1 m

## Slide 8: Beyond fundamental Physics
MPGDs found (and still finds) applications beyond fundamental Physics mainly (but not only) due to their imaging capabilities and the advantageous size over price ratio
Filippo Resnati - ICHEP - Chicago - 6th August 2016

## Slide 9: Some examples
C-RAD GEMINI: developments to obtain a radiation-hard detector based on GEMs for imaging and dosimetry during γ-ray treatments
Static XRF: GEM detector used for X-ray fluorescence of artworks in order to unveil underlying paintings over large surfaces
Multigen 2D: portable and battery-driven muon telescope based on Micromegas used for cosmic muon tomography
NMX at ESS: development of a GEM based neutron detector with gadolinium converter for NMX instrument at ESS
Filippo Resnati - ICHEP - Chicago - 6th August 2016

## Slide 10: C-RAD GEMINI
A strong trend has recently developed for using Electronic Portal Imaging Device (EPID) for online verification of the actually delivered dose distribution (Portal Dosimetry), an application for which none of the standard EPID detectors was designed nor optimised.
Detectors will be exposed to a very intense γ radiation.
Goals of the development: - superior radiation hardness - dose rate independence - dose linearity - zero ghosting
Filippo Resnati - ICHEP - Chicago - 6th August 2016

## Slide 11: C-RAD GEMINI
gamma
from 6 MV linac
GEM
pixelated readout
dedicated
electronics
patient
+
converter
electron
-
+
-
GEMs ensures high flux capability, linear response and radiation tolerance
C-RAD: Swedish company developing and commercialising the detector
Filippo Resnati - ICHEP - Chicago - 6th August 2016

## Slide 12: C-RAD GEMINI
Pelvic phantom
QA object (resolution and contrast measure)
40 cm
6 MV linac, 1.5 MeV average gamma energy, 3 MU dose
Filippo Resnati - ICHEP - Chicago - 6th August 2016

## Slide 13: X-ray fluorescence
X-ray fluorescence can be used to unveil underlying paintings. Large surface can be achieved by scanning with extraordinary energy and position resolution.
Three main concerns: - dangerous to move precious masterpieces - dangerous to have moving parts near the masterpieces - long time to scan
Filippo Resnati - ICHEP - Chicago - 6th August 2016

## Slide 14: X-ray fluorescence
A. Zielińska, 2013 JINST 8 P10011
- Position and energy sensitive method
- No position scan required
- The system can be brought to the museum
XRF imaging system for fast mapping of pigment distributions in cultural heritage paintings
Filippo Resnati - ICHEP - Chicago - 6th August 2016

## Slide 15: X-ray fluorescence
A. Zielińska, 2013 JINST 8 P10011
Filippo Resnati - ICHEP - Chicago - 6th August 2016

## Slide 16: MM Multigen 2D
Autonomous detector operation outside the laboratory: power consumption is a main issue.
Reduce the number of electronic channels with genetic multiplexing 1024 strips -> 61 channels
S. Bouteille et al., MPGD2015 contribution https://indico.cern.ch/event/451078/contributions/1113856/attachments/1171977/1692457/RD51_SBouteille.pdf
Battery and solar panel only
Muon telescope
Filippo Resnati - ICHEP - Chicago - 6th August 2016

## Slide 17: MM Multigen 2D
Muon flux intensity 4 weeks exposure
S. Bouteille et al., MPGD2015 contribution https://indico.cern.ch/event/451078/contributions/1113856/attachments/1171977/1692457/RD51_SBouteille.pdf
Muon tomography of a water tower
Dynamic study of the water content
Filippo Resnati - ICHEP - Chicago - 6th August 2016

## Slide 18: MM Multigen 2D
S. Procureur et al., 2016 RD51 Collaboration Meeting https://indico.cern.ch/event/532518/contributions/2195610/attachments/1286182/1913223/2016-06-07_-_RD51.pdf
Muon tomography of the Cheops Pyramid is ongoing
Filippo Resnati - ICHEP - Chicago - 6th August 2016

## Slide 19: NMX at ESS
Detector requirements:
- 3x 60x60 cm2 movable
- 20-100 cm operation distance
- time resolved (tens of us)
- <500 um X&Y spatial resolution
- <100 kHz/mm2 local flux
- ~20% efficient
- γ rejection not critical
Time binned diffraction pattern (simulation) from a 5 mm crystal
of perdeuterated rubredoxin at 20 cm from the detector (45o)
Neutron Macromolecular Crystallography instrument at ESS
Filippo Resnati - ICHEP - Chicago - 6th August 2016

## Slide 20: B-GEM & uTPC concept
Intrinsic resolution
standard ~1 mm
uTPC < 200 um
Straight track of alfa from 10B conversion
D. Pfeiffer et al., JINST 10 (2015) P04004
Filippo Resnati - ICHEP - Chicago - 6th August 2016

## Slide 21: Gd-GEM & uTPC concept
Intrinsic resolution
standard > 2 mm
uTPC < 400 um
Curly track of electron from Gd conversion
Larger absorption cross section of gadolinium enables the development of more efficient (O(15%)) detectors.
XGd + n -> X+1Gd+ + e-
Reconstruction of the curly tracks of the electron is more challenging, but the start of the track is well recognisable.
D. Pfeiffer et al., JINST 11 (2016), P05011
Filippo Resnati - ICHEP - Chicago - 6th August 2016

## Slide 22: Other type of amplification
Almost unavoidably light is produced during charge avalanche.
Depending on the gas mixture, the scintillation can be copious and at the right wavelength.
Not many gas mixtures scintillate in the visible window, for which most of the light sensors are optimised.
CF4 is one of them and noble gases with CF4 admixtures are effective scintillators.
Light yield comparison - common scintillator as NaI(Tl): ~40 ph/keV - GEMs in Ar/CF4 (80/20) at a gain of 105: ~106 ph/keV
Filippo Resnati - ICHEP - Chicago - 6th August 2016

## Slide 23: Optical readout
Record the light emitted during the Townsend avalanche with a camera using the detector as a scintillating plate
Advantages: - Simplicity, like taking a picture - Robustness, as a device off-the-shelf - Versatility, several uses and environments
Filippo Resnati - ICHEP - Chicago - 6th August 2016

## Slide 24: Only the techniques are new
Parallel mesh chamber filled with Ar/CH4/TEA 80%/8%/2%
seen through an image intensifier and a camera
G. Charpak et al., NIM A258 (1987) 177
Muons and delta rays
Filippo Resnati - ICHEP - Chicago - 6th August 2016

## Slide 25: The setup
10 cm
M = sensor size / image size
M ~ 0.1 -> Ω ~ 5x10-4
This implies:
large sensor, low noise, fast lens and a lot of light
10 mm
2 mm
2 mm
2 mm
Ar/CF4 80/20
plexiglass
+3 dioptre lens
25 mm f/0.95 lens
CCD camera
+
-
-
Filippo Resnati - ICHEP - Chicago - 6th August 2016

## Slide 26: X-ray images
Raw data: fast (<1 s) acquisition and no processing time
Charge acquisition (26/10/1998)
~7 cm
Light acquisition
X-ray tube with W target at 20 kV - 40 kV at few mA
Filippo Resnati - ICHEP - Chicago - 6th August 2016

## Slide 27: Fluoroscopy
50 ms exposure
10 Hz acquisition
Filippo Resnati - ICHEP - Chicago - 6th August 2016

## Slide 28: CT and 3D imaging
Image -> Sinograms -> Filtered Back Projection -> 3D image
Filippo Resnati - ICHEP - Chicago - 6th August 2016

## Slide 29: Single events
α from 220Rn & 216Po
X-rays from 55Fe
muon and δ-ray
shower from a charged pion
For hours in sealed mode at test beam
Filippo Resnati - ICHEP - Chicago - 6th August 2016

## Slide 30: Quantitative analysis
full energy
pileup
escape
55Fe source
24.7% FWHM
over 10x10 cm2
X-rays from 55Fe
Filippo Resnati - ICHEP - Chicago - 6th August 2016

## Slide 31: Fluorescence
Spatial- and energy-resolved
X-ray fluorescence of extended objects
O(20 min)
O(1 min)
17 cm
Filippo Resnati - ICHEP - Chicago - 6th August 2016

## Slide 32: Applications under investigation
Optical readout may be also used for:
- X-ray crystallography
- UV imaging
- neutron imaging
- gamma imaging
…
Filippo Resnati - ICHEP - Chicago - 6th August 2016

## Slide 33: Summary
Applications: medical imaging in high dose treatments, nanodosimetry, X-ray fluorescence, cosmic muon tomography, radon detectors.
Fundamental research other than HEP: neutron diffractometry, rare events searches (nuclear physics, dark matter, neutrino-less double beta, neutrino oscillation).
And possibly in the future: X-ray crystallography over large surfaces, homeland security, online beam monitor for hadron therapy, …
Filippo Resnati - ICHEP - Chicago - 6th August 2016