## Slide 1: LHC Accelerator Performance
Mike Lamont for the LHC team

## Slide 2: Exit Run 1(2010 – 2012)
Foundations well proven at 4 TeV
  Magnets, vacuum, cryogenics, RF, powering, instrumentation, collimation, beam dumps etc.
Huge amount of experience gained
  Operations, optics, collimation…
Healthy respect for machine protection
Main bend power converters: tracking error between sector 12 & 23 in ramp to 1.1 TeV

## Slide 3: 2013 - 2015
13-14
Aug 14-Apr 15
2015
April ‘13 to Sep. ‘14
Dipole training campaign
1st B E A M
5th April
3rd June
First Stable Beams
10th April Beam at 6.5 TeV
28th October Physics with record number of bunches
Peak luminosity 5 x 1033 cm-2s-1
Struggle
IONS

## Slide 4
2015: re-commissioning year, relaxed parameters, some issues…
UFOs
8 UFO dumps within 2 weeks (Sep 20 to Oct 5)
Conditioning observed
Radiation to electronics
Mitigation measures (shielding, relocation…)
Non-rad hard components used in LS1 upgrade
Exit 2015 with reasonable performance & hope for production in 2016
Electron cloud
Anticipated
Significant head load to cryogenics

## Slide 5: LHC 2016
Energy: 6.5 TeV
25 ns beam - nominal bunch population (~1.2e11)
Low emittance from injectors – variations possible
Squeeze harder in ATLAS and CMS
  beta* = 40 cm
  cf. 80 cm in 2015, 55 cm design
Choose a relatively bold set of operational parameters based on past experience

## Slide 6: Squeeze in ATLAS/CMS
Image courtesy John Jowett
βtriplet | Sigma triplet | β* | Sigma*
~4.5 km | 1.5 mm | 40 cm | 13 um
Lower beta* implies larger beams in the triplet magnets
Larger beams implies a larger crossing angle
Aperture concerns dictate caution – experience counts

## Slide 7
Overcome a few problems
WEASEL
PS MAIN POWER SUPPLY
SPS BEAM DUMP
Limited to 96 bunches per injection
2076 bunches per beam cf. 2750

## Slide 8: Peak luminosity
1034
Lower emittance from injectors
Reasonably quick ramp-up in number of bunches
  Limited by SPS beam dump to ~2100
  Electron cloud still very much with us but effects under control
LHCb and ALICE: levelled operation at ~3x1032 and ~2x1030 cm-2s-1 respectively

## Slide 9: Design luminosity reached
  Reduced beta* and lower transverse beam sizes from the injectors compensating the lower number of bunches

## Slide 10: Luminosity lifetime
Excellent luminosity lifetime – main component - proton loss to inelastic collisions in ATLAS, CMS and LHCb

## Slide 11: Then enjoy some remarkable availability
6 weeks
Heartbeat
Things that can go wrong

## Slide 12: Availability: 11th June – 23rd July
Stable Beams 67%

## Slide 13: Integrated luminosity
~20 fb-1 delivered to ATLAS & CMS
3 fb-1/very good week

## Slide 14: 2016 No one is more surprised than we are
Good peak luminosity, excellent luminosity lifetime
Stunning availability
  Sustained effort from hardware groups
Few premature dumps – long fills
  UFO rate down, radiation to electronics mitigated

## Slide 15: Stored energy per beam
Beam 1
2.2 mm gap
B1 collimators IP7

## Slide 16: Machine status - summary
Excellent and improved system performance
Good beam lifetime through the cycle
Operationally things well under control
Magnetically reproducible as ever
Optically good, corrected to excellent
Aperture is fine and compatible with the collimation hierarchy.
Magnets behaving well at 6.5 TeV

## Slide 17: Incoming 2016
~9 weeks of proton physics left…
Proton-lead run at √sNN of 5 and 8 TeV

## Slide 18: Run 2
Peak luminosity limited to ~1.7e34 by inner triplets
~40 fb-1/year in 2017 and 2018
Prepare for HL-LHC and post-LS2 LIU era
Prepare for 7 TeV operation
Extended Year End Technical Stop – 20 weeks CMS pixel upgrade; push 2 sectors towards 7 TeV

## Slide 19: Conclusions (1/2)
Excellent peak performance
  Design luminosity (squeeze, beams from injectors)
  Still margin for improvement in Run 2
Good integrated delivery
  Remarkable availability
  Electron cloud conditioning slowly
  Fortunate that UFOs have conditioned down

## Slide 20: Conclusions 2/2
Moved from commissioning to exploitation
LHC is enjoying the benefits of the decades long international design, construction, installation effort – foundations are good
Huge amount of experience & understanding gained and fed-forward
Progress represents a phenomenal ongoing effort by all the teams involved.

## Slide 21
Please don’t do this!

## Slide 22: Backup

## Slide 23: UFOs: Run 2 so far
2016
2015
arc UFOs (cell >11): rates similar to end of 2015
  did not lose conditioning over the Xmas stop

## Slide 24: Beam from injectors
Standard 25 ns scheme
PS circumference
BCMS (Batch Compression, Merging & Splitting)
Lower intensity, smaller bunches from PSB
Lower than nominal emittance taken a step further

## Slide 25: Dipole training 2/2
Campaign summary
All magnets have been trained to well over 7 TeV in SM18 before installation
Extensive re-training in situ was not expected
Training: frictional energy released during conductor motion