## Slide 1: RQS circuit Simulation results of Quench
Antonopoulou Evangelia
June 2011
Thanks to E. Ravaioli

## Slide 2: General Information – RQS circuit
Type | 600A
Imax | 600A
Converter | RPMBA
Magnet | MQS
# of m. | 4
EE | Yes

## Slide 3: Powering subsector A12 Circuit RQS.A12B2
Power Converter Attributes | 
Rcrowbar | 0.05Ω
Main parameters | 
R tot measured | 0.004010Ω
L tot | 0.124 H
Inductance per aperture | 0.031 H
Quench Protection System | 
Energy Extraction | DQEMC
Extraction Resistance | 700 mΩ
Parallel Protection Resistor per Magnet | 0.25 Ω

## Slide 5: Improved Schematic-RQS circuit (Main Circuit)
Power Converter
Crowbar
Magnets and Parallel Resistances
EE System
Resistance of the Busbar
Simulation of the Switches
Earthing point

## Slide 6: Latest Schematic-RQS circuit(1/2)
Thermal Model
Main Circuit

## Slide 7: Latest Schematic-RQS circuit(2/2)
Thermal Model
Electrical resistance
Thermal resistance
Thermal capacitance
Thermal resistance
of the insulation layer
Magnetic field
Inductance
Magnetic transfer function
Magnet 1
Magnet 2
Magnet 3
Magnet 4

## Slide 8: Crowbar
The system is based on a 50 mΩ Power Resistance series back-to-back thyristors being fired at a given output voltage, and then providing a safe path for magnet current

## Slide 9: Energy Extraction System
In all 600 A DC-current corrector circuits, the extraction facilities are inserted in series with the magnet chain. During normal operation the ex-traction breaker remains closed, herewith by-passing the dump resistor. In case of a fast power aboard or a quench of a magnet, the extraction breaker will be forced open, herewith switching the current to the dump -resistor. The extraction equipment is based on three individual, series-connected, high-speed, electro-mechanical AC circuit breakers

## Slide 10: Simulation of the Energy Extraction System

## Slide 11: The resistance of the switches in the EE system
Resistance of the switches:
Parabolic=2ms
exponential=11ms

## Slide 12: Snubber Capacitor
The electrical arc, between the breaker’s contacts, causes significant erosion of the contact surfaces. In the LHC 600 A EE systems the arcing time attains typically 7 ms at ultimate current leading to sufficient damage and required maintenance after just a few commutations. To minimize the arc influence and reduce the opening time, a capacitor bank is introduced across the breakers with the following characteristics:
- The capacitor voltage rating shall exceed the peak extraction voltage of 420 V.
- Internal inductance (Lesr < 80 nH) and resistance (Rs < 6 mΩ shall be low.
- Gives a capacitor value between 0.14 and 1.4 mF. Experiments have shown that the optimized capacitor value is 0.8mF.

## Slide 13: Simulation results of the influence of the snubber capacitor (1/3)
Without the snubber capacitor the arcing time attains 8ms

## Slide 14: Simulation results of the influence of the snubber capacitor (2/3)
With the snubber capacitor the opening time is reduced in 3ms

## Slide 15: Simulation results of the influence of the snubber capacitor (3/3)

## Slide 16: Simulation of the switches’ opening

## Slide 17
Data of PM_Browser

## Slide 19: Current in the RQS circuit comparison with PR_Browser data
Simulation: RQS.A34B2
PM_Browser event:
091115-060853.220_RPMBA.UJ33.RQS.A34B2

## Slide 20: Current in the Power Converter and the Crowbar
When the Power Converter is shutted down all the current pass by the crowbar until the discharge of the circuit.

## Slide 21: Voltage across the Crowbar

## Slide 22: Current in the circuit

## Slide 23: Current in the RQS circuit comparison with PR_Browser data
Simulation: RQS.A23B1
PM_Browser event:
091004-121213.580_RPMBA.UJ33.RQS.A23B1
Opening of the switch in the EE system
Shut down of the power converter

## Slide 24: Current of the magnets and their parallel resistance
After the shut down of the power converter, current pass by the parallel resistances of the magnets in order to protect them.
This current has the opposite direction of the current of the circuit.

## Slide 25: Voltage drop across the magnets

## Slide 26: Current in the EE system(1/2)

## Slide 27: Current in the EE system(2/2)

## Slide 28: Voltage in the Dump resistance
Simulation: RQS.A23B1
PM_Browser event:
091004-121213.580_RPMBA.UJ33.RQS.A23B1

## Slide 29: Electrical Resistance on the magnets

## Slide 30: Electrical Resistance on the magnets

## Slide 31: Temperature of the cable

## Slide 32: Thermal Power dissipated in the magnet due to quench

## Slide 33: Energy dissipated in the magnet due to quench

## Slide 34: Calculation of τ circuit with 2 magnets (RQS.A34B2)

## Slide 35: Calculation of τ circuit with 4 magnets (RQS.A34B2)

## Slide 36: Further steps in due course
Investigation of the missing resistance in order to be more accurate in the simulation of the quenches
Clarification of the misunderstanding test and comparison of the data of PM_Browser with my simulation

## Slide 37
Thank you for your attention
Merci beaucoup pour votre attantion
Ευχαριστώ για την προσοχή σας