Luminosity modeling for the LHC
F. Antoniou, G. Arduini, M. Hostettler, G. Iadarola, Y. Papaphilippou, S.Papadopoulou, G. Papotti, G. Trad
Acknowledgements:
Beam-Beam and Luminosity studies working group, J.E.Muller, M. Lamont, R . Tomas, B. Salvachua, M.Solfaroli
EVIAN meeting, 15-17 Dec 2015

---
Outline
Outline
- Introduction: Luminosity
- Luminosity model components
- Luminosity performance: RunI Vs RunII
- Luminosity model Vs RunII data
- Optimal Fill times for 2016
- Summary and Outlook

---
Introduction: Luminosity
Introduction: Luminosity
Model components :
Beam current decay with time
Beam size (or emittance) evolution with time

---
Luminosity decay
- During stable beams the interplay between different effects affects the bunch characteristics evolution:
  - Intra-beam scattering, Burn-off, Synchrotron Radiation, Beam-beam, noise, other unknown mechanisms, ...
- Many of the effects depend on the initial bunch brightness
- Big spread in the bunch by bunch behavior is observed
We need a model that takes the bunch-by-bunch variations into account
L [ mb^{-1} s^{-1} ]
N_b [10^{11} ppb]

---
Model components (1)
Emittance and bunch length evolution at Flat Top energy:
  - Intrabeam scattering (IBS):
    - Multiple Coulomb scattering effect leading to the redistribution of phase space and finally to emittance blow up in all three planes
    - → Analytical integrals
    - Iteration in time as the beam characteristics are evolving
  - Synchrotron Radiation (SR):
    - At high energies becomes important for proton beams as well, leading to emittance damping in all three planes
    - emittance damping time
- The emittance evolution due to IBS and SR has been fully parameterized
    - The parameterization is based on MADX computations using the IBS module
    - Their effect in any plane can be calculated through a function:
{dε_ι} over {dt}=f( En,N_{b0},ε_{x0}, e_{y0},σ_{l0})
{ε_ι} =ε_{i0} exp(-t/τ_i), τ_{i}:
[ε_{x}(t_{i}),ε_{y}(t_{i}),σ_{l}(t_{i})]=ComputeIBSEmitEvol(En, N_{b0},ε_{x}(t_{0}),ε_{y}(t_{0}),σ_{l}(t_{0}),timestep)

---
Model components (2)
Bunch intensity degradation
Luminosity burn-off: Luminosity decay due to the collisions themselves:
{N_{tot}(t)} = {N_{tot,0}} over {1+t/τ_{nuclear}}
{τ_{nuclear}} = {N_{tot,0}} over {L_0 σ_{tot} k}
: the initial beam intensity
: the initial Luminosity
: the total cross section
k the number of interaction points
N_{ tot,0}
L_{0}
σ_{tot}
It can be easily folded into the emittance evolution function in order to have a self consistent evolution

---
Other components
Luminosity model summary
The basic model includes the three main mechanisms of the transverse emittance, bunch length, bunch intensity and luminosity evolution due to IBS, SR and Burn-off
It can be easily applied and compared with the data for bunch by bunch and averaged quantities studies
  - On going effort to find correlations from the data from average and bunch by bunch behavior (brightness, long ranges, losses, blow-up,...)
Other sources need to be considered
  - Non-linearities of the machine
  - Noise effects
  - Scattering on residual gas
  - …

---
Luminosity performance: RunI Vs RunII
2015 configuration with low bunch intensity, low brightness and relaxed b* results in:
Low peak luminosity
Long luminosity lifetime
Integrated luminosity over a “typical” fill is very similar to what we used to get in 2012
Peak luminosity
Integrated luminosity (12h)
2012 (4 TeV)
50 ns, 1380 b.
1.7e11 ppb, 1.6 um (inj.)
b* = 60 cm
7200 (ub.s)-1
0.18 fb-1
2015 (6.5 TeV)
25 ns, 1825 b.
1.1e11 ppb, 2.5 um (inj.)
b* = 80 cm
4500 (ub.s)-1
0.17 fb-1
G. Iadarola
2012 (4 TeV, 50 ns) - Fill 3249
2015 (6.5 TeV 25 ns) – Fill 4485

---
Analyzing RunII data (1)
Analyzing RunII data
In Run II we have emittance measurements both at Flat Bottom and Flat Top
  - BSRT data for both beams and both planes
  - Convoluted emittance from luminosity from the experiments
  - Convoluted horizontal and vertical emittance from OP scans
- Comparison between the different methods not always in good agreement
  - Work in progress to understand the data
- The data were compared with the model predictions for all Fills that arrived at Stable Beams

---
Lumi model predictions Vs RunII data: Emittance @ SB
Luminosity model Vs RunII data: Emittance @ SB
- Fill 4538 is used as an example here
- Emittance evolution (averaged) during SB from BSRT, Lumi ATLAS and Lumi CMS
  - Different evolution
- Blow up observed, with respect to the model
- We need to understand the data and include other sources of emittance blow-up

---
Luminosity model Vs RunII data: Bunch current & bunch length @ SB
Smoother current decay and more bunch length damping is observed with respect to the model prediction

---
Luminosity model Vs RunII data: Bunch current & bunch length @ SB
- Smoother current decay and more bunch length damping is observed with respect to the model prediction
- Using the emittance evolution from the data (mean) → Very good prediction for the current and bunch length evolution
- Identify and add other sources of emittance evolution to the model is very important!
- The emittance blow up results in an integrated luminosity reduction of the order of 20%

---
Optimal Fill times for 2016
- 2016 proposed parameters:
  - *=40 cm in IP1/5
  - 410 rad (11 ) or 370 rad (10 ) in IR1 and 5
  - Similar bunch brightness and bunch length as in 2015 (1.2e11, 3μm, 1.3ns)
- Most probable turnaround time (based on 2015) of 6-8h (see M. Solfaroli)
- Using different emittance evolution scenarios (based on 2015 observations)
  - Long Fills are favorable
  - For 6h prep. Time: 18-20h
  - For 8h prep. Time: 22-24h
  - For 4h prep. Time: 13-15h
time [ h ]
t_{prep} [ h ]
L [ m^{-2} s^{-1} ]
Optimal t_{F} [ h ]

---
Summary and Outlook
Summary and Outlook
A model including IBS, SR and Burn-off at Flat Top (4TeV, 6.5TeV and 7TeV) and Flat Bottom energy is ready
  - Can be easily applied bunch-by-bunch
The model is based on analytical formulas which assume Gaussian distributions
  - This is not always the case for the LHC (especially in the longitudinal plane)
  - Work in progress to understand the effect of the beam distribution on the IBS evolution of the bunch characteristics (S. Papadopoulou)

---
Summary and Outlook
Observations from RunII data:
    - Differences have been observed on the emittance evolution from the different methods of measurement → Need to be understood
    - Using the emittance from the data, good prediction for the bunch length and bunch current evolution
    - Modeling the emittance evolution is a very important component of the model
- Based on the model and the observations, in 2016 long Fills should still be favorable
- Bunch-by-bunch analysis is in progress
  - Aims to identify correlations between the observed emittance blow-up and the bunch “lifestyle” (brightness, long-ranges, etc..)

---
THANK YOU FOR YOUR ATTENTION!