## Slide 1: Validation of Geant4 against the TARC benchmark: Testing neutron production, transportation and interaction
Alex Howard, ETH Zürich
TARC – experimental set-up and aims
Geant4 simulation
Comparing data with simulation
  Energy-time correlation
  Absolute Fluence
  Radial Distributions
Resurrection from 2008-today…
Summary and Conclusions

## Slide 2: Motivation for TARC Comparison
The production, interaction and transport of neutrons is important in a number of applications:
  Background radiation studies
  Radiation effects (single event upsets in electronics)‏
  Background and spill-over (LHC experiments)‏
Validation with TARC offers testing of Geant4 physics over a broad energy and process range
  Neutron production from ~GeV protons
  Secondary neutron production
  Thermalisation and capture
  Absolute fluence measurement
2008

## Slide 3: Geant4 Physics Modelling
The Geant4 BERTINI and BINARY cascade physics models were chosen for simulating hadron production
  Both of these include nuclear de-excitation models
The low energy neutron_hp package was used below 20 MeV for neutrons:
  Neutron interaction
  Transportation
  Elastic scattering
  Capture
Other “standard” Geant4 processes are included for elastic (hadrons), electromagnetic (all), stopping (hadrons)
Using physics lists QGSP_BERT_HP and QGSP_BIC_HP
2008

## Slide 4: The TARC Experiment
Neutron Driven Nuclear Transmutation by Adiabatic Resonance Crossing (Cern 96-97)‏
2.5 or 3.5 GeV/c proton beam.
334 tons of Pb in cylindrical 3.3m x 3.3m x 3m block.
The lead is 99.99% pure.
Beam enters through a 77.2mm diameter blind hole, 1.2m long.
12 sample holes are located inside the volume to measure capture cross-sections on some isotopes.
2008

## Slide 5: TARC – experimental set-up
2008

## Slide 6
Data taken 1996-1997, final publication 2002

## Slide 7: TARC – neutron validation and aims
Validates spallation neutron production from 2.5 and 3.5 GeV/c protons on pure lead
Validates energy-time relationship and thermalisation of neutrons
Absolute Neutron fluence spectrum from spallation production
Aims of experiment:
  neutron production by GeV protons hitting a large lead volume;
  neutron transport properties, on the distance scale relevant to industrial applications (reactor size);
  Measures capture cross-sections on a number of specific isotopes - efficiency of transmutation of 99Tc and 129I.
2008

## Slide 8: TARC simulation – single event 3.5 GeV/c proton on natural lead
TARC original simulation
FLUKA and custom transport
Geant4 – Bertini Cascade
neutron_hp
2008

## Slide 9: Neutron-energy time correlation
A first test of neutron transportation in Geant4 is to look at energy-time correlation
Due to the highly elastic nature of neutron scattering in lead and the high nuclear mass, there is a correlation between the neutron energy and its time of observation. This is particularly true at low energy, approximately independent of the initial neutron (and proton) energy
This has been verified experimentally and by TARC's own simulation (FLUKA + EA custom)‏
TARC measurements were carried out by measuring the time of capture on different resonant isotopes and by measuring the prompt signal in 3He gas counters
In Geant4 this relies heavily on the high precision neutron_hp model for neutrons < 20 MeV
2008

## Slide 10: Neutron Energy-Time Correlation
Geant4
Bertini + neutron_hp
Neutron energy and time are stored for the flux through a given radial shell
Reasonable agreement with expectation, although the low energy population is quite different between physics list (as expected)‏
Geant4
2008

## Slide 11: Neutron Energy-Time Correlation
Geant4
Bertini + neutron_hp
Neutron energy and time are stored for the flux through a given radial shell
Reasonable agreement with expectation, although the low energy population is quite different between physics list (as expected)‏
Geant4
TARC Paper
TARC simulation
2008

## Slide 12: Absolute Fluence Distribution @ 45.6cm
TARC data are measured at one position
Spectral fluence is determined from the energy-time correlation with cross-checks (lithium activation and 3He ionisation detectors)
TARC data are unbinned
E dF/dE
Simulated fluence is calculated by measuring the neutron track length through a spherical shell of radius 45.6cm
Measure counts in bin
  divide by bin width
  multiply by mean energy
2008

## Slide 13: Fluence Bertini cascade
2008

## Slide 14: Fluence Binary cascade
2008

## Slide 15: Fluence Binary cascade – Improved PreCompound
NEW PreCompound
Old model
2008
2008

## Slide 16: Ratio Plots of fluence G4/Data – Bertini
Ratio of 4shell : Data
Two-sets of data
Approximately 20-60% overestimated
Dominated by systematic errors of experiment
Shell approach better
Sub-structure – due to bertini?
Neutron Energy /eV
Geant4/Data
2008

## Slide 17: Ratio Plots of fluence G4/Data – Binary
Ratio of 4 Shell : Data
Approximately agrees (<20% under-estimated)‏
Dominated by systematic errors of experiment
Neutron Energy /eV
Geant4/Data
2008

## Slide 18: Ratio of fluence G4/Data – Improved PreCompound
Neutron Energy /eV
Geant4/Data
NEW PreCompound
Old model
2008
2008

## Slide 19: Radial Fluence Distributions
TARC measured the radial dependence of the neutron fluence in order to measure the slowing down within the lead volume with protons at 3.5GeV/c (slightly higher than fluence data)‏
In Geant4 a sequence of parallel shell volumes were created at different radii according to the experimental measurements (CPU efficient)‏
Fermi Age Theory predicts that the flux should be isotropic and TARC experimental data (+/- z-values) supports this over the energy range investigated
2008

## Slide 20: Radial Fluence Distribution - BERTINI
2008

## Slide 21: Radial Fluence Distribution - BINARY
Simulation in red
Data in Blue
Agreement very good
2008

## Slide 22: 2015…
Code is running
Some challenges with:
  Analysis
  MT
  Macros to compare data
NOW

## Slide 23: 1 event
NOW

## Slide 24: 1 event
NOW

## Slide 25: 1 event
NOW

## Slide 26: Energy vs. Timing plot - Bertini
NOW

## Slide 27: Energy vs. Timing plot - Binary
NOW

## Slide 28: Energy vs. Timing plot - QBBC
NOW

## Slide 29: Energy vs. Timing plot – QBBC No killer!
NOW

## Slide 30: Fluence – Bertini – 10k events
NOW
G4 in cyan and black (sorry)

## Slide 31: Fluence – Binary – 10k events
NOW
G4 in cyan and black

## Slide 32: Fluence – QBBC – 10k events
NOW
G4 in cyan and black

## Slide 33: Fluence – QBBC no killer – 10k events
NOW
G4 in cyan and black

## Slide 34: Ratio – Bertini – 10k events
NOW

## Slide 35: Ratio – Binary – 10k events
NOW

## Slide 36: Ratio – QBBC – 10k events
NOW

## Slide 37: Ratio – QBBC no killer – 10k events
NOW

## Slide 38: Memory Leaking…
Bertini running on my laptop:

## Slide 39: Memory Leaking…
Binary running on my laptop:

## Slide 40: Run times
Binary and BIC same at 2.5GeV/c
Bertini 30% slower at 3.5GeV/c
QBBC 15 times faster (killer)
And 7 times faster (no killer)

## Slide 41: Future Work
Radial distributions – ROOT issue (plotting is fun!)
Higher statistics – memory leaks?
Ref09 – memory leak is worse
  Can’t run more than 100 events on 40 threads (CSCS cluster)
Test other models/physics lists
Create a proper (code refactor) test/validation suite

## Slide 42: Thank you for your attention…