## Slide 1: Single Aperture Orbit Corrector: Progress on MCBXFB design WP3 Meeting
J. García, F. Toral (CIEMAT)
P. Fessia (CERN)
June, 2nd 2015

## Slide 2: Index
Requirements & specifications.
Summary last WP3 meeting (January 2015).
Magnetic design & field quality.
Detailed mechanical design & assembly tests.
Conclusions & Planning.

## Slide 3
Requirements & specifications

## Slide 4: MCBXFB orbit corrector requirements
Technical specifications | 
Magnet configuration | Combined dipole (Operation in X-Y square)
Minimum free aperture | 150 mm
Working temperature | 1.9 K
Working point | < 65%
Nominal current | < 2500 A
Iron geometry | MQXF iron holes
Field quality | < 10 units (1E-4)
Fringe field | < 40 mT (Out of the Cryostat)
Integrated field | 2.5 Tm
Physical length | < 1.505 m
Magnetic length | 1.2 m
Baseline field for each dipole | 2.1 T
Vertical dipole field
Horizontal
dipole field
Combined
dipole field
(Variable orientation)

## Slide 5: Strand & Rutherford Cable
Strand parameters | 
Cu:Sc | 1.75
Strand diameter | 0.48 mm
Metal section | 0.181 mm2
Nº of filaments | 2300
Filament diam. | 6.0 µm
I(5T,4.2K) | 200-210 A
Jc | 2800-3300 A/mm2
Cable parameters | 
No of strands | 18
Metal area | 3.257 mm2
Cable thickness | 0.845 mm
Cable width | 4.370 mm
Cable area | 3.692 mm2
Metal fraction | 0.882
Key-stone angle | 0.67 deg
Inner Thickness | 0.819 mm
Outer Thickness | 0.870 mm
Insulation: Fibre glass sleeve
Easier magnet assembly than using polyimide tape.
Need validation test of a suitable binder (double layer coil).
0.135 mm (real measurement)

## Slide 6
Summary last WP3 meeting (January 2015)

## Slide 7
Due to the sextupoles variation with the current, several iron geometries were tested in order to evaluate the problem and minimize this effect.
The difficulty comes because the field changes in two ways depending on the powering scenario: Orientation and intensity.
Finally, we had to choose between:
  High fringe field or…
  High variation of the multipoles with the current (when magnetic materials become saturated).
Taken this into account whole iron option was chosen despite the worse field quality. Currently under evaluation by the beam dynamics group.

## Slide 8: Since then…
A refined magnetic design has been calculated, including coil ends keeping the thickness of the collars.
A field quality study has been performed for the beam dynamics groups (WP2).
Mechanical detailed design has been performed at the collars, testing all stages of the assembly process.

## Slide 9
Magnetic design & field quality

## Slide 10: Cross section
Inner dipole (ID) & Outer dipole (OD) parameters | Units | ID | OD | 
Nominal field 100% (ID) | T | 2.11 | 2.23 * | 
Nominal Field (Modulus, 100% ID & 100% OD) | T | 3.07 |  | 
Nominal current | A | 1600 | 1470 | 
Coil peak field (Modulus, 100% ID & 100% OD) | T | 4.13 (ID) |  | 
Working point (Modulus, 100% ID & 100% OD) | % | 50.1 |  | 
Inductance/m | mH/m | 46.77 | 99.1 | 
Stored energy/m | KJ/m | 59.87 | 107 | 
Torque | Nm/m | 120000 |  | 
Aperture | mm | 156.2 | 230 | 
Iron yoke Inner Diam. | mm | 316 |  | 
Iron yoke Outer Diam. | mm | 614 |  | 
Max fringe field, 20 mm out of the cryostat (Modulus, 100% ID + 100% OD) | mT | 29 |  | 
Number of conductors (1st quadrant) | - | 139 |  | 187
* Higher field necessary to compensate the longer coil end at the outer dipole.

## Slide 11: Coil ends
260 mm long (50 mm less at Inner Dipole)
Some additional end spacers to ease manufacturing: de-keystoning, dimension accuracy...

## Slide 12: Integrated field quality at IN, both dipoles powered simultaneously
Field quality achieved, except for the sextupole variation caused by iron saturation.
Results below corresponding to IN on both dipoles, iron & cryostat included.
Same cross section and coil ends in both magnets.
Inner Dipole (ID) & Outer Dipole (OD) parameters | Units | MCBXFB (Short Magnet) | MCBXFA (Long Magnet)
Inner dipole current | A | 1600 | 1525
Integrated field B1 (ID) | T | 2.49 | 4.5
Integrated b3 | units | 17.37 | -16.65
Integrated b5 | units | 2.49 | -0.35
Integrated b7 | units | 0.62 | 0.98
Integrated b9 | units | -0.75 | 0.07
Integrated b11 | units | 3.6 | 4.3
Outer dipole current | A | 1470 | 1395
Integrated field A1 (OD) | T | 2.52 | 4.54
Integrated a3 | units | -10.33 | 20.12
Integrated a5 | units | -3.6 | -3.04
Integrated a7 | units | -3.26 | -3.98
Integrated a9 | units | -0.58 | -0.62
Integrated a11 | units | 0.12 | 0.02
MCBXFB
MCBXFA

## Slide 13
It is not possible to centre the sextupole variation simultaneously on both magnets with the same cross section and coil ends.
Shifting a MCBXFB sextupole moves that sextupole in the same direction for MCBXFA.
Integrated sextupole variation with the current

## Slide 14
Detailed mechanical design & assembly tests

## Slide 15
Wedges
Iron
Ti tube
Cooling channel
Outer collar
Coil blocks
Inner collar

## Slide 16
Rivets
Handling supports
Outer Keys
Press supports
Torque locking
Torque locking
Inner keys
Titanium tube
Inner collar outer diameter = 230 mm (Thickness = 27 mm)
Outer collar outer diameter = 316 mm (Thickness = 33 mm)
Self-supporting collars
1
2
Interference
3
4

## Slide 17
Results (108 % IN)
Looking at the difference between maximum and minimum radial deformation at the coils:
Inner dipole: 0,3 mm -> 0,36% of the diameter
Outer dipole: 0,49 mm -> 0,42% of the diameter
Inner
dipole
Outer
dipole
Successful torque locking
1
2

## Slide 18
Frictionless contact
between coil and collar nose
(worst possible scenario)
Inner titanium tube
(low contraction factor):
Decrease radial inward movement of the coil.
Prevention of sudden slipping movements that could trigger a quench.
Still under discussion if it is necessary for the final assembly.
With Tube VS Without tube
Results (108 % IN): Radial inward forces at inner dipole
4

## Slide 19
Things to be checked:
Stress concentration at filet radii.
Maximum stress over the coils depending on press support location.
Feasibility of the assembly looking at clearances and tolerances needed.
Assembly tests

## Slide 20: Inner dipole collaring (Collars)
Max (Von-misses) Stress= 300 Mpa
Probably due to numeric error
First calculations suggests that inner dipole collaring process will require:
MCBXFB -> 450 ton
MCBXFA -> 800 ton.

## Slide 21: Inner dipole collaring (Coils)
For 0,12 mm play
Max azimuthal Stress= 160 Mpa

## Slide 22: Inner dipole spring back (Collars)
Fillet radius [mm] = Ø4 Ø3
Max (Von-misses) Stress [MPa] = 400 MPa 460 Mpa

## Slide 23: Inner dipole spring back (Coils)
Max azimuthal Stress= 112 Mpa

## Slide 24: Outer dipole collaring (Collars)
Fillet radius [mm] = Ø4 Ø3
Max (Von-misses) Stress [MPa] = 353 MPa 400 Mpa

## Slide 25: Outer dipole collaring (Coils)
For 0,1 mm play
Max azimuthal Stress= 158 Mpa

## Slide 26: Outer dipole spring back (Collars)
Fillet radius [mm] = Ø4 Ø3
Max (Von-misses) Stress [MPa] = 440 MPa 500 Mpa

## Slide 27: Outer dipole spring back (Collars)
Plastic behaviour was simulated for this case (with subsequent cooling and powering) without major changes in the assembly deformations.
Equivalent plastic strain (mm/mm)
Ø3
Ø4

## Slide 28: Cooldown (Collars)
Max (Von-misses) Stress= 384 Mpa

## Slide 29: Powering to 108% IN (Collars)
Max (Von-misses) Stress= 758 Mpa
Only 110 MPa of azimuthal compression at coils

## Slide 30: Azimuthal pressure at coil edges (Inner Dipole)
Interference at coil/collar nose interface keep
the coils stuck to the collars in both dipoles at every scenario
3

## Slide 31: Azimuthal pressure at coil edges (Outer Dipole)
Interference at coil/collar nose interface keep
the coils stuck to the collars in both dipoles at every scenario
3

## Slide 32: Assembly gaps evolution
A
B
C
D
E
F
G
H
I
J
Inner collars play = 0,12 mm
Outer collars play = 0,1 mm
All values in mm
Gap | Original gap | ID Press | ID Spring Back | Before OD Press | OD Press | OD Spring back | Cool- down | 108% Power.
A | 0,2 | - | - | opens | 0,13 | opens | opens | 0,08
B | 0,1 | - | - | opens | 0,08 | 0,08 | 0,085 | contact
C | 0,5 | - | - | opens | 0,47 | opens | opens | 0,4
D | 0,55 | 0,42 | opens | opens | opens | opens | opens | opens
E | 0,3 | 0,18 | opens | opens | opens | opens | opens | opens
F | 0,03 | ≅0,03 | contact | contact | contact | contact | contact | contact
G | 0,7 | - | - | opens | 0,55 | opens | opens | opens
H | 0,6 | - | - | opens | 0,45 | opens | opens | opens
I | 0,03 | - | - | contact | contact | contact | contact | contact
J | 0,5 | - | - | 0,43 | 0,47 | 0,46 | 0,465 | opens

## Slide 33: Torque at the coil ends
Collars extended till the last sector of the central post (first end spacer).
Additional support could be necessary.

## Slide 34
Conclusions & planning

## Slide 35: Conclusions
Main design challenges:
  Large aperture.
  Magnetic field quality under different coil powering schemes.
  Hard-radiation resistant torque clamping.
Final conceptual design:
  Double layer cosine-theta magnet.
  Sextupole variation with current is unavoidable: under study by beam dynamics group.
  Mechanical clamping by means of self-supported collars. Possibly additional support will be needed at coil ends.
  No quench heaters required.
Detailed design:
  Mechanical analysis of the collars to assure assembly feasibility and admissible stresses at all stages.
  Magnetic analysis: real thickness of the cable, connection side coil ends.
  Quench simulations with improved cable model.

## Slide 36: Planning
Design | Detailed mechanical calculations | Jul-15
 | Short mechanical model | Oct-15
 | Fabrication drawings | Dec-15
Fabrication | Cable MCBXB H+V delivered (4+4 unit lengths) | Jun-15
 | First winding test | Oct-15
 | Cured coils | Nov-16
Test | Magnet prototype in vertical cryostat | Dec-16

## Slide 37: Thanks for your attention

## Slide 38
Annexes

## Slide 39: Single layer & Double layer designs VS old MCBX (same central field comparison)
Inner coil (ID) & Outer Coil (OD) parameters | Units | Single layer design | Double Layer design (Small Collars) | Double Layer design (Large Collars) | Old MCBX (Series Model, both coils powered )
Nominal field 100% (ID) | T | 2.13 | 2.13 | 2.13 | 2.13
Nominal field 10% (ID) | T | 0.214 | 0.214 | 0.218 | 0.2156
Non-linearity (ID) [B100%-10∙B10%]/10∙B10%∙100] | % | -0.47% | -0.61% | -2.29% | -1.2%
Nominal field 100% (OD) | T | 2.11 | 2.12 | 2.12 | 2.12
Nominal field 10% (OD) | T | 0.212 | 0.2154 | 0.219 | 0.2156
Non-linearity () [B100%-10∙B10%]/10∙B10%∙100] | % | -0.47% | -1.58% | -3.2% | -1.67%
Nominal current (ID) | A | 2450 | 1250 | 1560 | 362.5x8=2900
Nominal current (OD) | A | 2150 | 1036 | 1340 | 331.25x8=2650
Coil peak field | T | 4.27 | 3.95 | 3.93 | 3.817
Working point | % | 60% | 44.7% | 48.1% | 39.54%
Torque using Roxie Forces | 105 Nm/m | 0.92 | 0.98 | 1.19 | -0.455
Torque using Analytical Equation | 105 Nm/m | 0.93 | 1.03 | 1.13 | 0.45
Difference Roxie vs Analytical Eq. | % | +1.68% | +4.13% | -4.72% | -1.1%
Conductors height (h) | mm | 4.37 | 2x4.37 | 2x4.37 | 13.2 (8)
Mean radius (ID) | m | 0.0775 | 0.08 | 0.0825 | 0.0518
Mean stress at the coil and collar nose interface | MPa | 135 | 70 | 82 | 38
Aperture (ID) | mm | Ø150 | Ø150 | Ø156,2 | Ø90
Aperture (OD) | mm | Ø180 | Ø200 | Ø218 | Ø116.8
Iron yoke Inner Diam. | mm | Ø230 | Ø250 | Ø300 | Ø180
Iron yoke Outer Diam. | mm | Ø540 | Ø540 | Ø610 | Ø330
Number of conductors used (1st quad) | - | 162 | 357 | 324 | 800

## Slide 40: Considerations on a MCBXFB design based on a canted cosine-theta coil configuration
Comparing the main challenges in the case of MCBXFB design for both designs:
  The torque between nested dipoles:
    It will be the same for both designs.
  The separation of the pole turn from the collar nose due to the Lorentz forces:
    It does not happen in the CCT dipole (azimuthal forces support).
    In the pure cosine-theta it can be overcome with a small interference between the collar nose and the pole turn of the coil.
  The elliptical deformation of the support structure under Lorentz forces:
    In a CCT dipole the outer formers should hold the outwards radial forces coming from the inner layers, which complicates significantly the assembly and fabrication.
    The assembly of two nested collared coils is not easy, but seems more affordable.
The CCT configuration has not been broadly used up to now, so other open questions are:
  The handling of the axial repulsive forces between layers.
  The influence of the cable positioning accuracy on the field quality.
  The training of a large and high field superconducting dipole.
  The protection of the magnet in case of quench.
  Formers materials to be used (insulation, stiffness and easily machining required).
  Coils impregnation.

## Slide 41: Mechanical design: Challenges to face
As a combined dipole that requires a square range of operation in X and Y axis, a large torque arises when both coils are powered.
Due to the expected radiation dose a solution based on mechanical clamping is required to mechanically fix the coils and guarantee the magnet performance.
Other major challenges:
Mechanical model
  Powered with 108% of nominal current for sizing purposes.
  Material properties used:
 | Material | E [Gpa] | u [-] | CTE [K-1]
Coils & spacers (Impregnated) | NbTi+Cu | 40 | 0,0032 | 1.1*10-5
Collars | StainlessSteel | 193293K/2104.3K | 0,0028 | 0.983*10-5
Inner tube | Ti | 130 | 0,0017 | 0.603*10-5
Radial inward forces at the inner dipole | Inner titanium tube
Large azimuthal displacements of the coils | Azimuthal interference at collar noses
Large radial deformations of the assembly | Large self-supporting collars
Challenge | Solution proposed

## Slide 42: Some useful expressions to understand where mechanical stresses come from
dl
R
θ
d=2Rcosθ
IIC
-IIC
BOC
J[A/m]=J0cosθ
T
R
R
h
F
F
*
* Linear Iron

## Slide 43
Model settings and convergence challenges
2D Ansys Workbench model.
  0.5-mm-thick shell elements at the collars.
  1-mm-thick shell elements for the rest of the assembly.
Load steps.
  t=0-1: Contact offset (pre-stress).
  t=1-2: Assembly cooldown.
  t=2-3: EM forces (exported from Maxwell, 108% Nominal current).
Convergence/stability challenges
  No symmetry boundary conditions can be used. DOF more difficult to constrain.
  Many parts involved and linked by contact. Frictional contacts showed better performance that frictionless ones.
  Techniques used to achieve convergence:
    Adding extra boundary conditions.
    Tuning up contact settings at problematic zones (Stabilization dumping factor, Normal stiffness, ramped effects...).

## Slide 44: Materials
Cable, wedges and inter-layer insulation: glass fibre sleeve impregnated with binder treatment as hardener (PVA to be studied).
Wedges: machined from ETP copper.
End spacers: 3D printed in stainless steel.
Ground insulation: Polyimide sheets
Vacuum impregnated coils, radiation hard resin (cyanate-ester blend).
Collars: Machined by EDM in stainless steel.
Iron: To be evaluated.
Connection plate: Hard radiation resistant composite, like Ultem.
End plates: Stainless steel.
Inner pipe: Titanium grade 2 if grade 5 is not available.

## Slide 45: Winding
Customized winding machine lent by CERN
  New beam: 2.5 m long.
  Electromagnetic brake.
  Horizontal spool axis.
Winding process
  Stainless steel mandrel protected with a polyimide sheet.
  Binder impregnation and curation.
  Outer layer will be wound on top of the inner one with an intermediate glassfiber sheet for extra protection.
  Vacuum impregnation with hard radiation resin.

## Slide 46: Assembly
Collars placed around the coils with a vertical press (custom tooling required).
Layer of protection between both dipoles, likely a glass fibre sheet
Innermost turn of the coils will be protected by a stainless steel sheet from the collar nose sliding.
Iron laminations around the coil assembly.

## Slide 47
Protection

## Slide 48: CIEMAT in-house developed code based on finite difference method : Optimistic assumptions of the model
Rutherford cable is modeled as a monolithic wire with the same metallic area, discarding the voids or internal volumes filled with resin.
The wedges are not modeled.
Quench origin is placed at the innermost turn, although it is not where the peak field is placed when both coils are powered.
A uniform magnetic field is assumed in the wires, equal to the peak field.

## Slide 49: MCBXFB: No damping resistance included
Preliminary

## Slide 50: MCBXFB: Damping resistance = 0.3 Ω (0.1 s delay)
Preliminary
No quench heaters seem to be necessary

## Slide 51: MCBXFA: No damping resistance included
Preliminary

## Slide 52: MCBXFA: Damping resistance = 0.3 Ω (0.1 s delay)
Preliminary