## Slide 2: Overview of Quench Protection Systems in the LHC
B. Auchmann, L. Bortot , thanks to F. Rodriguez-Mateos, HL-LHC WP3 Meeting, 27.5.2015

## Slide 3: Overview
What we protect
Protection elements (pictures)
Detection
Protection strategies
Recurrent problems

## Slide 4: What we protect
Magnets (minimize peak temperature and voltage)
Busbars (cold and warm) (minimize peak temperature)
Current leads (prevent quenches, abort in HTS’s current-sharing regime)
Power converters (e.g., water-cooling fault)

## Slide 5: What we protect against
Magnet quenches
  Training
  Beam-induced
  Thermal propagation
  Due to internal short
Busbar quenches
  Thermal propagation from magnet quench
  Thermal coupling (Line-N)
  Bad splices
  Wrong He levels in busbar lines/DFBs
  He-bubble in SC link
Current-sharing in HTS leads
  Defective temperature sensors, bad regulation
PC failures

## Slide 6: Magnets and current levels
Mains: 12 kA
MB, MQ
ITs (Inner triplets): 7/12 kA
MQXA/B
IPDs (Individually powered dipoles, separation dipoles): 4-7 kA
MBX, MBRC, MBRS, MBRB
IPQs (Individually powered quads): 4-6 kA
MQM, MQY
600-A circuits
MCD, MCS, MO, MQT, MS, MCBX, MQSX
80-120 A circuits
MCO, MCBC, MCBY, triplet correctors
60-A circuits
MCB
Notes: Cu/Sc ratios
SYMQ protection?

## Slide 7: Means of protection 60/120 A
http://te-epc-lpc.web.cern.ch/te-epc-lpc/general.stm
Busbar voltage is monitored by PC, abort at 150 mV.

## Slide 8: Means of protection 600 A

## Slide 9: Means of protection Mains 1/4
from: Mishra, J. K. "Basics of SM18 Operation, An Introductory Guide (Graybook).”, CERN, Geneva, Switzerland, Bhabha Atomic Research Centre, Mumbai, India, 2005.
Diodes absorbe several thousand MIITs during fast power-abort.
Sensitive in closing direction  100 mΩ parallel resistor.

## Slide 10: Means of protection Mains 2/4
http://cern.ch/te-mpe-cp V. Anushat, et al., Modeling and computer simulation of the pulsed powering of mechanical D.C. Circuit breakers for the CERN/LHC superconducting magnet energy extraction system, Proc. of ICAP 2000, Darmstadt, Germany, Sep 2000.
LHC RQ switch
breaker unit
LHC RB switch

## Slide 11: Means of protection Mains 3/4
http://cern.ch/te-mpe-cp K. Dahlerup-Petersson, Energy extraction resistors for the main dipole and quadrupole circuits of the LHC, Proc. of EPAC 2000, Vienna, Austria, 2000.

## Slide 12: Means of protection Mains 4/4
Notes: Do they have crowbars? What’s their value?

## Slide 13: A word on heater redundancy
MBs: Unused low-field heaters as spares
MQs, ITs, IPQs, IPDs (except D3?): two heater circuits, each covering every coil/pole in the magnet. Up to 8 heater circuits per IPQ circuit.
Source: A. Erokhin

## Slide 14
Detection RB circuit
J. Steckert, QPS electronics, CERN PH-ESE electronics seminar, Nov 2011
iQPS: Uth = 0.1 V, tval = 10 ms nQPS busbar protection Uth = 500 µV, tval = 10 s inductive compensation by DSP
nQPS symmetric quench protection Uth = 0.5/0.9 V, tval = 20 ms adaptive thresholds, ‘sunglasses’
Notes: Jens: more on detection types
Adaptive thresholds
Sunglass duration 500 ms?

## Slide 15: Detection quadrupole circuits
MQs
  Compare voltage between pairs of poles.
  Have symmetric quench protection.
IPQs
  Compare voltage between same aperture of adjacent magnets (compensating for different magnetic lengths).
IPDs except D1
  compare voltages between apertures.
  No extra symmetric detection.
D1 compares upper and lower coil.
  Risk of beam-induced symmetric quench rather high.
Source: A. Erokhin

## Slide 16: Detection 600-A circuits
600-A circuits, U_RES is calculated by FPGA

## Slide 17: Protection strategies
Magnet protection
RB, RQ
heaters and diodes
IPQs, IPDs, ITs
Heaters fired in all elements
adjacent magnets act as EE.
600 A
EE where possible
Rpar if necessary
None for triplet correctors
60 A/80-120 A
None
Busbar/leads/PC protection
RB/RQ
EE
IPQs, IPDs, ITs
Heaters
600 A
EE
Rpar acts as EE in case of magnet quench.
PC off, crowbar
60 A/80-120 A
PC off/crowbar

## Slide 18: Details 600-A
EE was used to protect magnets and busbars.
Rpar was added if necessary – designed to absorb circuit energy.
Recent simulations show that Rpar protects a quenching magnet efficiently, even without EE.
Triplet correctors have no EE (larger cu/sc ratio in magnet and busbar).
F. Sonnemann, Resistive Transition and Protection of LHC Superconducting Cables and Magnets. PhD thesis, 2001.
D. Egede Rasmussen, Upper Limits for QPS Thresholds of the 600A Circuits in the LHC, EDMS 1432493
Status 2001!

## Slide 19: Protection recipe?
It is difficult to extract a single rule.
Example:
MCBC orbit correctors have energy density per coil copper volume equivalent to that of MB magnets.
Yet they have no QPS.

## Slide 20: Protection elements in numbers
Type | #circuit | #magnet | #EE | #heaters* | #Rpar
RB | 8 | 1232 | 16 | 9856 | -
RQ | 16 | 392 | 16 | 6272 | -
IT | 16 | 64 | - | 256 | -
IPQ | 76 | 220 | - | 2080 | -
IPD | 16 | 18 | - | 56 | -
600 A | 394 | 5337 | 202 | - | 3733
60-120 A | 1052 | 2268 | - | - | -
* .. active heater strips (MB LF heaters not counted)
Caveat: Quick calculation, not fully validated numbers.

## Slide 21: Recurrent problems 1/3
QPS trips
EM compatibility
Grid instabilities/Thunderstorms
Transfer-line effects
  Unbalanced apertures
  Phase-difference between adjacent magnets
0-V crossing
Imperfect inductive compensation
Single-event upsets
Remote power resets (operator errors)
Detector drift (undulator)
Adjust thresholds
Adjust ramp rate
Improved detection electronics

## Slide 22: Recurrent problems 2/3
Shorts to ground
  Spiders
  Lyras vs. MCS corrector
  Warm busbars
Lack of instrumentation wires!
  Single voltage/current measurement for circuits of > 100 magnets in series!
Lack of long. and transv. quench-propagation measurements
  at various current levels for model validation
  Ideally with spot heater for controlled quench origin

## Slide 23: Recurrent problems 3/3
Broken heater strips or reduced HV resistance (9 on MBs, 1 on IPDs, 1 on ITs, 2 on IPQs)
1 broken Rpar on an undulator
600-A EE switches are being replaced.
Diode lead resistances
Broken bypasses (copper foils, copper stabilizer)
Bad connection between busbar and copper-foil bypass in DFBAI P2.

## Slide 25
Extra slides on 600-A busbar protection.

## Slide 26: Quench in Helium-Tight Plug
Plug close to joint = quench stopper

## Slide 27: Quench Due to Joint Resistances Line-N
Dashed line: no quench propagation.
Equilibrium below 300 K.

## Slide 28: Resistive Joints in Spoolpiece Busbars
Spoolpiece busbars: Cu/Sc = 4, No EE

## Slide 29: Overview of Relevant Scenarios
Once joint resistances are known, there is only one busbar scenario and one magnet scenario left.