## Slide 1: Nb3Sn QPS strategies
How to protect

## Slide 2: Signals
Simple protection schemes (direct comparison) are preferred
Sufficient amount of voltage taps need to be provided
Proper instrumentation should provide good common mode rejection (reject 50Hz…) (avoid pick-up loops)
As cleaner the signal as faster detection

## Slide 3: Examples
Asymmetric quenches:
Comparison of two halves of a single magnet: Ures = U1M1 + U2M1
Symmetric quenches:
Comparison of two magnets (or more):
U1M1
U2M1
U1M2
U2M2
M1
M2
M3
M4
Solution with middle taps in magnet coil
Solution without middle taps in magnet coil
UM3
UM4
UM1
UM2
i
Asymmetric quenches:
Comparison two magnets: Ures = UM3 + UM4
Symmetric quenches:
Comparison of four magnets
With middle taps:
Without middle taps:

## Slide 4: How to cope with flux jumps
Flux jumps are short ~10..20ms
They tend to appear at lower currents
At lower currents time budget for detection (aka “evaluation time”) is bigger
Chart: Imagnet (kA)
| 12 | 10 | 8 | 6 | 4 | 2
Vth= 100 mV | 18.6333 | 24.4 | 34.675 | 58.3333 | 93.5
Vth= 200 mV | 17.2333 | 22.6 | 30.875 | 37.3333 | 1.5
Vth= 300 mV | 16.6333 | 20.4 | 23.475 | 13.3333
Vth= 400 mV | 15.6333 | 17.4 | 16.075 | -7.6667
 Couple evaluation time with circuit current (“ignore” signals above threshold for teval )
Plot by S. Izquierdo Bermudez

## Slide 5: Reaction time
After detection, counter measures should be triggered as fast as possible
Electromechanical components introduce delays of ~5ms
Solid state components (PhotoMOS) are a factor 10 faster
Quench detector
Current source
Quench Heater discharge supply
Classical solution: relay in quench detector and discharge power supply
(delay 2x ~5ms)
Fast solution: replace relays by semiconductors
(delay: 2x ~500us)

## Slide 6: Summary
Sufficient amount of instrumentation wires allow for simple (robust !) protection
Flux jumps can supressed by time discrimination filter with current-dependent time settings
System reaction time can be minimized by use of semiconductors in the actuator path