Fermilab CMS Upgrade Workshop
November 19-20, 2008
Calorimeter (off-detector) DAQ electronics
Eric Hazen, Boston University
On behalf of my ECAL and HCAL colleagues

---
Outline
Calo TriDAS upgrade goals and constraints
Review of HCAL and ECAL off-detector electronics
Hardware Upgrade Options	Covered well by J. Mans' talk
  - Summary of Options
  - Upgrade ”Scenario I”
Selective Readout
  - Review current ECAL scheme
  - Possible combined schemes
DAQ Path Issues
Staging options, compatibility with existing system
Summary

---
Calo TriDAS Upgrade Goals
Necessary:
  - HCAL front-end changes
    - Channel count, TDC data, etc
  - ECAL+HCAL: DAQ hardware changes, Lumi increase... more BW
  - ECAL+HCAL: Trigger – RCT opto inputs, architecture changes?
Desirable:
  - DAQ: common local/global readout path
  - Combine ECAL and HCAL in common hardware ($$$ savings?)
  - Provide for combined selective readout of ECAL and HCAL
  - Data compression in DAQ path
  - Provide more FPGA resources for calo trigger near detector
  - Comply with enforced or de-facto CMS standards
  - … others?

---
Calo TriDAS Upgrade Constraints
Common
  - 100kHz L1A limit stays
  - L1 latency also same
  - DAQ B/W likely will increase, but not necessarily by 2013
      - Must compress data if payload increases
ECAL
  - No changes in EB front-ends or links (EE not likely either)
      - L1 trigger towers stay the same in EB
      - EE could use partial sums in some clever way
HCAL
  - Use same data fibers, so speed limited to ~ 6Mb/s (guess!)
  - Replace back-end, so ~ complete design freedom
    (limited by cost/schedule)

---
ECAL/HCAL processing
(Current system)
HCAL
HTR
L1 Path (TPG)
SLB
RCT
Raw FE Data
@ 40Mhz
DAQ
Global
DCC
SLink
L2 Path
DR
DAQ
Local
VME
x32
x200
L1A
ECAL
On Detector
TCC
SLB
RCT
T-Sum
L1 Path (TPG)
Raw FE Data
@ 40Mhz
SRP
x90
DR
DCC
L2 Path
DAQ
Global
SLink
L1A
x54

---
Upgrade Options
ECAL Alone
  - New DCC
  - New TCC or optical SLB
  - Modify SRP algorithms
HCAL Alone
  - New HTR+DCC system with SR capability
ECAL+HCAL together (my ”Scenario I”)
  - New ”CTR” (Calo Trigger Readout) card
      - Receive ECAL trigger, data and HCAL data
      - Generate TPs, possibly perform some RCT processing
      - Perform selective readout processing on board
  - New ”DTC” (Daq / Timing Card)
      - Distribute timing/control signals to CTRs
      - Harvest DAQ data using SR flags

---
Selective Readout
Review of existing ECAL SR
Implementation options

---
ECAL Selective Readout Processor

---
Upgrade Scenario I
TPs
to
Trigger
CTR
Modules
DTC
Module
to
DAQ
HCAL Data
TT Flags
TTC
or equiv
ECAL Data
(staged)
SR Mask
ECAL Trig
Selective Readout
Flags to neighbors
DAQ Data
L1A, Clk, Ctrl
CCS
or
Similar
ECAL Control

---
Upgrade Scenario I
CTR Module Details
HCAL FE Data
 3 TT per fiber
(6-12 FE channels)
Opt Rx
~4Gb
L1 Path (TPG)
Tx
CT
TT Flags
(threshold results)
to DTC
Selective
Readout
Thresholds
Barrel: 1 fiber/TP
Endcap: 5 fiber/TP
ECAL FE
L1A
Readout mask
from DTC
Opt Rx
800M
T-Sum
L2 Path
DR
Opt Rx
800M
DR
Tx
DAQ
L1A
DTC

---
Cable/Fiber Counting
for CTR boards
Barrel -- 25 crystals = 1 TT
HCAL	1 fiber for 3 TT
EB	6 fibers for 3 TT
TP Out	1 fiber
Total	8 fibers / 3 TT
2448 TTs total	Boards	Crates
uTCA board(1) - 12 TTs	~200	~16
uTCA board(2) – 24-30	80-100	8-10
ATCA/VME -	16-25 TTs	100-150	10-14
Endcap -- 25 crystals = 1 RU
HCAL	1 fiber
EE	18 fibers
TP Out	1 fiber
Total	20 fibers
624 RUs total	Boards	Crates
uTCA board(1) - 1 RU	624	52
uTCA board(2) – 3-4 RU	150-200	14-16
ATCA/VME - 6-10 RUs	60-100	5-10
uTCA
(double)
ATCA
or VME
64-80
Fibers
128-200
Fibers
uTCA
 (single)
32
Fibers

---
DAQ Path
Currently 512 FEDs possible (in theory)
Each receives 100kHz * 2kB = 200MB/sec
Upgrade plans (no details yet)
  - Same 100kHz max L1A rate
  - ”Significant” additional bandwidth capability
  - Use commercial standards for networking
  - Common readout path for global and local DAQ
  - If possible embed TTC/TTS/control path in same links
To accommodate 10x more bandwidth, we would need 2GB/sec per FED:
  - Two 10GbE links in parallel per FED?
  - Single 40GbE or other link per FED?

---
DAQ Path Upgrades
Hard to plan without more DAQ group input, but here is a start:
  - ~ 10x current throughput internally
  - Build in support for full calo selective readout
  - Provisions for local / global DAQ via same link
  - Commercial standard (i.e. 10GbE), perhaps on daughterboard
  - Adapter to support current S-Link
  - Provisions for TTC-like control on network link as well as current TTC

---
DTC (DAQ/Timing Card)
TTC
(new?)
Crate
Management
(Control Interface)
   Currently VME
   Will evolve to Ethernet / PCI-x
Clock
Control
Fanout
Clock
Fast Control
L1A
Event readout via control/management
interface surely needed for commissioning
SR Readout
Mask @ L1A
Selective
Readout
Processor
Neighbor
Board/Crate
Communication
Combined on single link?
SR Flags
@40MHz
Should
be combined
in final
configuration
Global DAQ
Event
Builder
DAQ Data
@L1A
Local DAQ
Legacy DAQ
(SLink)
RAM

---
DAQ Bandwidth Estimate
Per TT/RU: ~ 50 bytes per timesample
  - HCAL:	4 depth segments @ 16 bits each
  - ECAL:	25 crystals @ 8 bits each
  - Both: TP's and overhead, say 50%
  - 50 * 100kHz * 10 timesamples = 50MB/sec per TT
Total ECAL+HCAL = 68 FEDs @ 2k bytes * 100kHz
  - ~ 14 Gbytes/sec total / ~ 4100 TT = 3.3MB/sec per TT
  - So, we can send only about 3.3/50 = 7% of the data
  - For Jeremy's example 34 TT FPGA,
    this is ~ 120MB/sec per FPGA average,
    but must handle peak rate of 50*34 = 1700 MB/sec to RAM

---
DAQ/Timing Card
Design details depend heavily on packaging standard
  - ...which should rightly be driven by other system issues
Current system uses cables / fibers for all inter-module links
(except VME)
  - This can and should change- ATCA and uTCA both support sufficient backplane bandwidth for SR / DAQ purposes
Must realistically support existing infrastructure (SLink, TTC)
  - Easy for larger formats (ATCA, 9U VME)
  - More challenging for uTCA
  - For DAQ output, fiber with SLink adapter may be best bet

---
Summary
Integration of many functions on DAQ card makes sense:
  - ECAL/HCAL DCC
  - ECAL SRP
  - ECAL/HCAL TTC fanout system
Prototyping can be done with existing or planned hardware
(at least in uTCA)
  - UMN ”mini-CTR” board for CTR
  - Matrix card for larger scale tests
  - UW TTC/Slink-64 card for DTC
Packaging choice should not be driven by DAQ path
  - ...and design cannot proceed very far until this is settled
Common hardware for ECAL / HCAL CTR and even DTC is not excluded