## Slide 1: Beam induced RF heating… …including TDI
Special thanks to our collaborators at INFN Frascati, la Sapienza, DESY, TU Darmstadt and IHEP Beijing!
O. Aberle, M. Albert, R. Alemany, F. Antoniou, M. Barnes, P. Baudrenghien, O. Berrig, N. Biancacci, J. Boyd, F. Carra, F. Caspers, E. Chapochnikova, P. Chiggiato, A. Danisi, H. Day, M. Deile, M. Ferro-Luzzi, S. Gilardoni, S. Jakobsen, J. Kuczerowski, M. Lamont, A. Lechner, I. Llamas Garcia, R. Losito, A. Masi, E. Metral, J.E. Mueller, N. Minafra, A. Nosych, A. Perillo Marcone, S. Redaelli, F. Roncarolo, G. Rumolo, B. Salvant, A. Tauro, J. Uythoven, A. Valimaa, J. Varela, C. Vollinger, N. Wang, M. Wendt, J. Wenninger, C. Zannini.

## Slide 2: Main questions for this talk
Is beam induced RF heating expected to be a limitation in 2016?
What about injection protection collimator TDI8 that was still a significant limitation in 2015?
Will we need to implement bunch length control in 2016?
Note: heating due to electron cloud is not addressed here. See the previous talk from Gianni.

## Slide 3: Agenda
Recap on beam induced RF heating
Reminder of issues before LS1
Situation in 2015
Outlook for 2016
Proposed actions

## Slide 4: Beam induced RF heating?
When the LHC beam traverses a device which
  is not smooth
  or is not a perfect conductor,
  it will produce wakefields that will perturb the following particles
   resistive or geometric wakefields (in time domain) and impedance (in frequency domain).
3D simulation of electromagnetic perturbation caused by an obstacle or a dispersive beam pipe:
In a round beam pipe
In a round beam pipe with sharp obstacle  resonant RF mode
 energy left behind by the bunch
 eventually dissipates in the surrounding walls
 Energy lost by the bunch heats up the surrounding walls
In a round beam pipe made of dispersive material  fields penetrate inside the material
 dissipation of energy inside the surrounding walls

## Slide 5: Beam induced RF heating?
Power spectrum for 25 ns beam (cos2 distribution and 9.75 cm) and measured 2015 TDIs impedance vs frequency
Normalized Power spectrum λ2
Can be computed from the impedance and the longitudinal beam spectrum
Power lost by a beam of intensity Ibeam and normalized power spectrum λ2 in a device of longitudinal impedance Zlong
TDI2: Ploss ~ 2 kW
For 2248 bunches with 1.15 p/b, we would compute:

## Slide 6: Beam induced RF heating?
Can be computed from the impedance and the longitudinal beam spectrum
Power lost by a beam of intensity Ibeam and normalized power spectrum λ2 in a device of longitudinal impedance Zlong
TDI8: Ploss ~ 3 kW
TDI2: Ploss ~ 2 kW
For 2248 bunches with 1.15 p/b, we would compute:
Power spectrum for 25 ns beam (cos2 distribution and 9.75 cm) and measured 2015 TDIs impedance vs frequency
Normalized Power spectrum λ2
Depending on available cooling at the location of the dissipated power, could lead to problems or not
(e.g. outgassing, structural issues)

## Slide 7: Agenda
Recap on beam induced RF heating
Reminder of issues before LS1
Situation in 2015
Outlook for 2016
Proposed actions

## Slide 8: Reminder: heating issues in LHC before LS1
Damaged vacuum modules
 Design not robust
Damaged injection collimators
 Design not robust
One injection kicker delays injection
 Non conformity
Damaged synchrotron light monitor  Design not robust
2 collimators reached temperature interlock dump levels
Cooling non conformity
Spurious temperature readings
ATLAS-ALFA detector almost reached damage level
 Design not robust
One single cryogenic module (Q6R5) has no margin for cooling, likely linked to TOTEM outgassing.
 TOTEM ferrite not baked

## Slide 9: Summary table of heating issues in LHC before LS1
equipment | Problem | 2011 | 2012 | 2015 | 2016
Vacuum module VMTSA | Damage |  | removed |  | 
TDI | Damage |  |  | Beam screen reinforced, copper coating on the jaw | New design should solve problems
MKI | Delay |  |  | Beam screen upgrade and non conformity solved | 
Collimators | Few dumps |  | 2 TCTVB removed | Non conformity solved. TCTVB removed | 
TOTEM/Q6R5 Beam screen | Regulation at the limit |  |  | Valve upgrade + new TOTEM design | 
ATLAS-ALFA | Risk of damage |  |  | New design + cooling | 
BSRT | Damage |  |  | New design + cooling | 
BGI | vacuum increase |  |  | To be followed up | To be followed up
Damaged
Limited operation
Worry that can limit operation
Was fine fine
Beam induced heating: major LHC limitation before LS1.
A lot of effort invested by equipment groups before and during LS1 to mitigate these issues

## Slide 10: Agenda
Recap on beam induced RF heating
Reminder of issues before LS1
Situation in 2015
  The good news
  The TDI
  Heating monitoring
  Bunch length
Outlook for 2016
Proposed actions

## Slide 11: Summary table
equipment | Problem | 2011 | 2012 | 2015 | 2016
VMTSA | Damage |  |  | removed | removed
TDI | Damage |  |  | Beam screen reinforced, copper coating on the jaw | New design should solve problems
MKI | Delay |  |  | Beam screen upgrade and non conformity solved | 
Collimators | Few dumps |  |  | Non conformity solved. TCTVB removed. | 
Beam screen | Regulation at the limit | Q6R5 and TOTEM | Q6R5 and TOTEM | Upgrade of the valves + ferrites baked out. | 
ATLAS-ALFA | Risk of damage |  |  | New design + cooling | 
BSRT | Deformation suspected |  |  | New design | 
BGI | vacuum increase |  |  | To be followed up | To be followed up
Damage
Limits operation
Worry that can limit operation
Should be fine
All the efforts paid off: 2015 went much better!
Non conformity
with TDI8, most likely the hBN jaw and its coating

## Slide 12: Agenda
Recap on beam induced RF heating
Reminder of issues before LS1
Situation in 2015
  The good news
  The TDI
  Heating monitoring
  Bunch length
Outlook for 2016
Proposed actions

## Slide 13: Situation of beam induced heating in 2015
Great success and big relief that new designs have worked so far!
  Shielded and cylindrical Roman pots (both ATLAS-ALFA and TOTEM)
   a lot of margin gained in 2015 for ALFA
   no vacuum problems with Q6R5 for TOTEM

## Slide 14: 2012 vs 2015: ATLAS-ALFA Roman pots
ATLAS-ALFA temperatures in October 2012
ATLAS-ALFA temperatures in October 2015
 Clear gain with new shielded design
Beam intensity
Beam intensity

## Slide 15: Situation of beam induced heating in 2015
Great success and big relief that new designs have worked so far!
  Shielded and cylindrical Roman pots (both ATLAS-ALFA and TOTEM)
   a lot of margin gained in 2015 for ALFA
   no vacuum problems with Q6R5 for TOTEM
  New design for synchrotron light telescope (BSRT) followed up with BI-TB
   barely any temperature increase (compared to more than 300C in 2012)
  New collimator design with ferrite (TCTP), followed up with collimation WG
   no significant difference observed so far with respect to the design without ferrite
  Full shielding of ceramic tube for injection kickers (MKI) – 24 instead of 15 screen conductors. followed up with MKI strategy meetings
  (see talk of Lee at Evian 2015)

## Slide 16: 2012 vs 2015: injection kicker MKI
Significant reduction of the temperature slope, but temperature has reached 50C after series of long fills.
Injection interlock kept low by TE-ABT (55C), but threshold can be incrementally increased once kicker behaviour is checked using softstarts.
MKI2 temperatures in October 2012
MKI2 temperatures in October 2015
Beam intensity
Beam intensity
MKIs are not expected to be a hard limitation for Run2 parameters.
In case it becomes too hot, it is then advised to keep the bunch length above 1 ns.
  We should be ready to control bunch length by bunch flattening

## Slide 17: Agenda
Recap on beam induced RF heating
Reminder of issues before LS1
Situation in 2015
  The good news
  The TDI
  Heating monitoring
  Bunch length
Outlook for 2016
Proposed actions

## Slide 18: TDI issues
Technical issues with implementing our recommendation to apply copper coating to reduce TDI impedance.
Abnormal vacuum behavior on TDI8 serious limitations during scrubbing and injection
Abnormal impedance observables (both longitudinal and transverse) observed during the run.
TDI8
TDI2
 x2 more power lost in TDI8
 Observations point towards a coating issue for TDI8 (LMC237 in Sept 2015).
TDI2
TDI8
 TDI8 has 4x more transverse impedance

## Slide 19: TDI issues
TDIs were taken out of the machine in December.
Indeed the coating on TDI8 is heavily compromised.
TDI2
TDI8
Blisters in Cu coating

## Slide 20: TDI issues
TDI2
TDI8
Something somewhere went terribly wrong.
More damage analysis (electromagnetic, chemical, structural) are planned to understand the origin of this non conformity.
Last week, bench impedance measurements confirmed the measurements with beam: the main suspect is the jaw material and its coating.
see N. Biancacci et al at LMC247.

## Slide 21: TDIs: what about 2016?
N. Biancacci et al, LMC247
2015
2016
2015
2016
 The 2016 TDIs are better in terms of impedance and more robust in case of coating issues

## Slide 22: Agenda
Recap on beam induced RF heating
Reminder of issues before LS1
Situation in 2015
  The good news
  The TDI
  Heating monitoring
  Bunch length
Outlook for 2016
Proposed actions

## Slide 23: Heating monitoring in 2015
Action from Chamonix 2014
 put surveillance tools in place for Run 2
Available tools during 2015:
  Temperature fixed displays (many thanks to our BE-CO colleagues!)
  Systematic fill analyzer
  Collimator webpage
  Synchronous phase error with observation box (for TDI)
  BigSISter can send prewarning text messages (no dump threshold).
  Beam spectrum fixed display, but unfortunately there is a serious issue with the scopes and they crash very often

## Slide 24: Heating monitoring in 2015
Cooling connection non conformity on one secondary collimator:
   Minor issue that was identified early and solved before it could lead to limitation.
Intervention to swap cooling pipes by EN-STI
Heating monitoring working well but technical issues remain to be solved:
  Several temperature probes of some collimators seem strongly perturbed by beam presence (especially TDI and TCLIA probes)
   Measured ΔT of 10C to 100 C in 10 s when beam is dumped  not physical
   Problem not addressed for the new TDIs and should still be there in 2016.
   studies ongoing to understand and mitigate these issues

## Slide 25: Agenda
Recap on beam induced RF heating
Reminder of issues before LS1
Situation in 2015
  The good news
  The TDI
  Heating monitoring
  Bunch length
Outlook for 2016
Proposed actions

## Slide 26: Impact of bunch length reduction during the fill:
  Power spectrum extends to higher frequency  more beam induced heating  not a showstopper so far as intensity also decreases.
  More luminosity  not a showstopper either (!): expected gain with 2016 parameters ~2 % (from Fanouria’s model).
  Reducing luminous region (input from Jamie)
   request of LHCb/ALICE to keep the luminous region more constant.
   ATLAS and CMS do not mind too much as long as there is a gain in luminosity.
  Longitudinal instabilities at very low bunch length
   not an apparent issue in 2015 from bunch by bunch luminosity
Beam intensity
Bunch length
 It would be useful to be ready to control bunch length by bunch flattening
start of stable beams:
Bunch length =1.35 ns
~22h later
Bunch length = 0.82 ns

## Slide 27: No adverse effect of bunch length reduction?
 Case of ATLAS-ALFA in September 2015.
Temperature does not reach equilibrium
This observation did not come back after the target bunch length was increased
Mild increase in any case
 We should be ready to control bunch length by bunch flattening

## Slide 28: Agenda
Recap on beam induced RF heating
Reminder of issues before LS1
Situation in 2015
Outlook for 2016
Proposed actions

## Slide 29: Heating issues in LHC before LS1
equipment | Problem | 2011 | 2012 | 2015 | 2016
VMTSA | Damage |  |  | removed | removed
TDI | Damage |  |  | Beam screen reinforced, copper coating on the jaw | New design should solve problems
MKI | Delay |  |  | Beam screen upgrade and non conformity solved | 
Collimators | Few dumps |  |  | Non conformity solved. TCTVB removed. | 
Beam screen | Regulation at the limit | Q6R5 and TOTEM | Q6R5 and TOTEM | Upgrade of the valves +TOTEM ferrites baked out. | ~12 W/half cell predicted
ATLAS-ALFA | Risk of damage |  |  | New design + cooling | 
BSRT | Deformation suspected |  |  | New design | 
BGI | vacuum increase |  |  | To be followed up | Temperature monitoring will be added
Damage
Limits operation
Worry that can limit operation
Should be fine
2016 looks “cool”, but beware of non conformities!

## Slide 30: Main questions for this talk
Is beam induced RF heating expected to be a limitation in 2016?
 no (with what we know).
What about TDI8 (injection protection collimator) that was a significant limitation in 2015?
 the new TDIs are expected and were measured to have a lower impedance than both 2015 TDIs.
 the new solution should be more robust in case of coating issues
 There is hope that TDIs will not be a limitation in 2016
Will we need to implement bunch length control in 2016?
It is very likely and bunch flattening should be tested early in commissioning

## Slide 31: Agenda
Recap on beam induced RF heating
Reminder of issues before LS1
Situation in 2015
Outlook for 2016
Proposed actions

## Slide 32: Recommendations for 2016
Test and validate impedance of the new TDIs during commissioning (4h).
Keep monitoring temperature, vacuum and beam spectra to identify issues in close collaboration with MPP and equipment groups.
Find a mitigation for the spurious temperature readings.
In view of HL-LHC, monitor in particular power lost in MKIs, TDIs, beam screen and ALICE beam pipe to assess the need for further modifications.
Test and validate bunch flattening during intensity ramp up in case bunch length levelling at ~1 ns or ~1.1 ns would be required by either heating or experiments.

## Slide 33
Thank you for your attention!

## Slide 34: Beam screen heat load from impedance (LHC and HL-LHC)
Beam screen | Radius (mm) | 2012 4TeV 1374b 1.7e11 1.25 ns | 2015 6.5 TeV 2248b 1.2e11 1.25 ns | 2016 6.5 TeV 2748b 1.2e11 1.25 ns | Nominal 7TeV 2808b 1.15e11 1 ns | HL-LHC 7TeV 2748b 2.2e11 1.08 ns
Arc(*) | 18.4 | 187 | 176 | 216 | 290 | 927
Current Q1(*) | 24 | 143 | 135 | 165 | 222 | 710
Current Q2-Q3(*) | 18.95 | 181 | 171 | 209 | 282 | 900
(*) Assumes 1 weld (2mm wide) on the side of the beam screen
Power dissipated by the beam in the beam screen in mW/m (for 2 beams)

## Slide 35: Beam screen heat load from impedance (LHC and HL-LHC)
Beam screen | Radius (mm) | 2012 4TeV 1374b 1.7e11 1.25 ns | 2015 6.5 TeV 2248b 1.2e11 1.25 ns | 2016 6.5 TeV 2748b 1.2e11 1.25 ns | Nominal 7TeV 2808b 1.15e11 1 ns | HL-LHC 7TeV 2748b 2.2e11 1.08 ns
Arc(*) | 18.4 | 10 W | 9 W | 11.5 W | 15.5 W | 49 W
(*) Assumes 1 weld (2mm wide) on the side of the beam screen
Power dissipated by the beam in the beam screen in W/half cell (for 2 beams)

## Slide 36: References
Beam induced heating at Chamonix (Elias, 2012), (Benoit, 2014)
Evian talk by Lee (2015)

## Slide 37: ATLAS instantaneous luminosity with longitudinal instabilities
Jamie Boyd
 Even looking at bunch by bunch individually, no striking change of slope visible on the curve.
 However, should be quantified if one needs % level.

## Slide 38: Effect of bunch length levelling on integrated luminosity
From Fanouria Antoniou’s model (for fills of 20h)
2015
2016
Keeping bunch length constant at 1.3 ns would have led to 3.1% to 3.6 % loss in integrated luminosity compared to leaving the bunch length decrease freely
Keeping bunch length constant at 1.2 ns would lead to 1.6 to 2% loss in integrated luminosity compared to leaving the length decrease freely
3.1%: full model IBS+SR+Burnoff
3.6%: bunch length follows model but transverse emittance evolves slowly

## Slide 39: Effect of bunch length levelling on integrated luminosity
From Fanouria Antoniou’s model (for fills of 20h)
Starting from 1.3 ns and levelling at 1.1 ns or 1 ns would lead to resp. 0.1% to 0.6 % loss in integrated luminosity compared to leaving the bunch length decrease freely.
Starting from 1.3 ns and levelling at 1.1 ns or 1 ns would lead to 0.3 to 1% loss in integrated luminosity compared to leaving the length decrease freely
(bunch length follows model but transverse emittance evolves slowly)
2015
2016

## Slide 44: Impact of bunch length on beam induced heating
Bunch length decreases but intensity also decreases
 Power loss leveling (here for TOTEM pot)
True for most devices, but…