## Slide 1: Experiment Control System
&
Electronics Upgrade

## Slide 2: ECS & Upgrade Electronics
ECS Design doesn’t change (in principle)
  Same tools:
    Communications: DIM
    Supervision: WinCC-OA
    Sequencing and Automation (FSM): SMI++
  Same philosophy:
    Generic tools to describe the hardware (FwHw)
      Board Types -> “chips” -> registers => Boards
    Operation tools to Configure/Monitor boards
      “Recipes” for different configuration modes
      Stored in Configuration DB
  New electronics will be interfaced like before

## Slide 3: Electronics Interfaces
Two types of boards to control:
  Back-End boards (Readout Boards, etc.)
    Physically only one board type (PCIe40):
    But logically different types TELL40, S-ODIN, SOL40
    (Past equivalent: fwCcpc)
  Front-End Boards
    Sub-detector Specific
    Several protocols available (via GBT-SCA)
    (Past equivalent: fwSpecs)

## Slide 4: BE Board Interface
Physically only one board type (PCIe40) for: TELL40, S-ODIN, SOL40, etc.
  But logically different types ( different firmware -> different “registers”)
Tools will be provided centrally:
  Low-level libraries and command-line tools:
    Allow accessing the different registers (PCIexpress)
  A DIM server:
    Will implement higher-level commands to configure and monitor the board components
  A WinCC-OA component
    Providing the high-level description and access of all electronics components

## Slide 5: ECS BE Dataflow
Control PC
Test UI
HW Description UI
Operation UI
FPGA
Firmware
DIMServer
PCIe40
PCIe driver P
PCIe Library P
GbtServ
PCIe
Host PC
WinCC-OA

## Slide 6: FE Board Interface
Interface to FE Electronics
  Two Architectures envisaged:
    FE electronics in one single FE board
    FE electronics accessed via a “Service” board (masterGBT <-> SCA via “long” Elink)

## Slide 7: FE Board Protocols
Interface to the FE Chips
  The GBT-SCA provides the following protocols:
    16 x I2C master controllers
    1 x JTAG master controller
    32 x ADC channels (multiplexed)
    1 x Memory bus (32 bits) controller
    4 x PIA (Parallel Interface Adapter) controllers
    1 x SPI (Serial Peripheral Interface) bus
    4 x DAC channels
  Recommended protocols (for bulk transfers) are:
    I2C
    SPI using independent chip selects (daisy chained SPI not allowed)

## Slide 8: FE Addressing
FE Chip Register Address:
<SOL-ip><GBT-i><SCA-j><ProtoCode><I2C-k><I2C-add>[<I2C-s.add>]
  fixed variable
Control PC

## Slide 9: ECS FE Dataflow
Control PC
Test UI
HW Description UI
Operation UI
GBT Link
SOL40
FPGA
Firmware
DIMServer
SOL40
PCIe driver P
PCIe Library P
GbtServ
PCIe
Host PC
WinCC-OA

## Slide 10: FE ECS Software/firmware
Will be centrally provided:
  The FPGA firmware for the SOL40 board
    Will prepare, send and receive the GBT-SCA frames for the various user protocols
      Should take load away from CPU as much as possible
  Low-level libraries and command-line tools:
    Will allow accessing the different FE chips
  A DIM server:
    Will implement higher-level commands to configure and monitor the FE chips
  A WinCC-OA component
    Providing the high-level description and access of all electronics components

## Slide 11: WinCC-OA: Test UI
For both BE and FE boards

## Slide 12: WinCC-OA: HW tool
Control PC
HW Description UI
GBT Link
SOL40
FPGA
Firmware
DIMServer
SOL40
PCIe driver P
PCIe Library P
GbtServ
PCIe
Host PC
WinCC-OA
XML Description

## Slide 13: WinCC-OA: HW tool

## Slide 14: WinCC-OA: Configuration
Control PC
HW Description UI
Operation UI
WinCC-OA
Conf.DB
Configuration Tools
  Use “Recipes”: Groups of settings for many registers
GBT Link
SOL40
FPGA
Firmware
DIMServer
SOL40
PCIe driver P
PCIe Library P
GbtServ
PCIe
Host PC

## Slide 15: Current Status
MiniDAQ Based
  BE boards:
    DIM Server adapted
    FwCcpc/FwHw adapted accepts XML input
    Started building Tell40 panels
  FE Boards:
    SOL40 Firmware 1st version exists
    Building low-level libraries (GBT-SCA protocols)
    Extending the XML description
  In general:
    FwCcpc / Ccserv (tell1)
    FwSpecs / SpecsServer
FwGbt / GbtServer
15
FPGA
CCPC
Firmware
DIMServer
Mini DAQ
PCIe driver P
PCIe Library P
Ccserv
PCIe

## Slide 16: Scalability & Efficiency
Configuration and Monitoring speed
  Is not just data size / bandwidth
  Depends on:
    How the data is distributed, for ex.:
      A few large registers or many small ones
    Are blocking operations needed, for ex.:
      A register needs to be set and read-back before configuring the next one
      or read-modify-write operations that need to be done by the back-end
    Which user protocol is used and how it is used, for ex.:
      Some I2C devices needed an extra I2C operation to write a sub-address before the block of data could be written
      Some did not implement auto-increment so block transfer could not be used
  Try to influence design early enough…