## Slide 1: Tapering options in the future low emittance high energy collider FCC-ee
Andreas Doblhammer (CERN, Geneva) for the FCC-ee lattice design team

## Slide 2
Sawtooth-Effect
Energy loss through synchrotron radiation and energy gain in RF cavities leads to characteristic “Sawtooth-Effect”
Notes: Sawtooth-Effect wird größer, weil wir ein gemeinsames Layout mit den Protonen haben. So number of RF sections will be reduced which makes the sawtooth larger and there are large offsets of the beam through. As we share a layout with FCC-hh, they want to reduce the number of RF sections as far as possible. With that, the orbit becomes really large (mm-Range)

## Slide 3
Energy Dependent Bending Angle

## Slide 4
Energy Dependent Bending Angle
Normally the sawtooth-effect would just be accepted, but in FCC-ee, the sawtooth orbit is in the mm-range  feeddown-effect of sextupoles and quadrupoles creates additional magnetic fields that distort the optics

## Slide 5
What is Tapering?
Tapering: Adjusting the strength of each magnet so that the beam with local energy of E0+∆E is on the design orbit
Of course tapering every magnet in the ring is both expensive and difficult to maintain  just dipole tapering and remachting the optics using dispersion suppressors and matching sections
Notes: Rematch the quads in the dispersion and matching sections to get rid of the optics distortions, reasonable beta beat

## Slide 6
Analytical Tapering

## Slide 7
Numerical Tapering
Kicker don’t just compensate the energy dependent dipole bending angles, but the orbit is optimized numerically
Kicker strength αKicker calculated using orbit correction in MAD-X
BPM

## Slide 8
The Lattices
FCC-ee 12-fold
Circumference: 100 km
Energy: 175 GeV
Energy Loss/Turn ≈ 8046 MeV
12 RF Sections (L= 1.8 km)
12 Arcs (L= 6.8 km)

## Slide 9
The Lattices
FCC-ee Racetrack
Circumference: 100 km
Energy: 175 GeV
Energy Loss/Turn ≈ 7870 MeV
4 Short Arcs (L= 4,4 km)
4 Long Arcs (L= 16,4 km)
6 Short RF Sections (L= 1,4 km)
2 RF Section (L= 4,2 km)

## Slide 10
The Lattices
FODO-design
Cell Length: 50 m
εx ≈ 1 nm*rad

## Slide 11
Racetrack Lattice, 8 RF Sections

## Slide 12
Racetrack Lattice, 8 RF Sections
analytical Tapering
sextupoles off
no IPs
kicker length: 0.0 m
βx-Beat: 1%
βy-Beat: 1,5%
Dx-Beat: 4%

## Slide 13
Racetrack Lattice, 8 RF Sections
numerical Tapering
sextupoles off
no IPs
kicker length: 0.0 m
βx-Beat: 2%
βy-Beat: 2%
Dx-Beat: 5%

## Slide 14
Racetrack Lattice, 8 RF Sections
analytical Tapering
numerical Tapering
numerical Tapering
sextupoles on
2 IPs
kicker length: 0.2 m
βx-Beat: 6%
βy-Beat: 12%
Dx-Beat: 5%

## Slide 15
Racetrack Lattice, 8 RF Sections
 tapered orbit ≈ factor 70 smaller

## Slide 16
Racetrack Lattice, 2 RF Sections

## Slide 17
Racetrack Lattice, 2 RF Sections
analytical Tapering
sextupoles off
no IPs
kicker length: 0.0 m
βx-Beat: 3%
βy-Beat: 5%
Dx-Beat: 5%

## Slide 18
Racetrack Lattice, 2 RF Sections
numerical Tapering
sextupoles off
no IPs
kicker length: 0.0 m
βx-Beat: 5%
βy-Beat: 6%
Dx-Beat: 6%

## Slide 19
Racetrack Lattice, 2 RF Sections
numerical Tapering
sextupoles on
2 IPs
kicker length: 0.2 m
βx-Beat: 9%
βy-Beat: 14%
Dx-Beat: 2%

## Slide 20
Racetrack Lattice, 2 RF Sections

## Slide 21
8 vs. 2 RF sections
 tapered orbit with 2 RF sections still ≈ factor 40 smaller than untapered orbit with 8 RF sections

## Slide 22
Kicker Strengths & Emittances
Magnet: | B*l (Tm):
Arc Dipole | 5.56*10-1
Kicker (175 GeV, 8RFs) | 7.82*10-4
Kicker (175 GeV, 2RFs) | 6.42*10-3
e.g.: for a kicker length of 0.2m, Bkick ≈ 0.07*Bdipole for 8 RFs 
Bkick ≈ 0.57*Bdipole for 2 RFs 
Lattice: | εx before tapering (nm*rad): | εx after tapering (nm*rad):
8 RFs | 0.9263 | 0.9512
2 RFs | 0.9269 | 0.9728
U0, Kick ≈ 400 keV
U0, Kick ≈ 26 MeV

## Slide 23
Correction Kickers in MAD-X
fitted curve
Are correction kickers suited for tapering studies in MAD-X?
in agreement with calculations:

## Slide 24
Correction Kickers in MAD-X
Are correction kickers suited for tapering studies in MAD-X?
fitted curve
?

## Slide 25
Summary & Conclusions
Several Tapering Methods possible
Orbit improvement through dipole tapering with kickers: ≈ Factor 50-80 (depending on method, lattice, number of RFs,...)
Integrated strengths of the tapering kickers are ≤ 1% of the integrated strengths of the arc dipoles
Emittances are nearly unaffected by the tapering process
Next Steps: Checking the effects of the kicker magnets on orbit tolerances, using orbit correction kickers (already in the ring) for tapering

## Slide 26
Thank you for your attention!