## Slide 2: Circuit-protection aspects of different preliminary magnet-design options
M. Prioli, B. Auchmann, A. Verweij with input from H. Thiesen
20.11.2015, Orsay, France

## Slide 3: Outline
Overview relevant parameters.
Magnet parameters from last coordination meeting (9 Oct.).
Parametric study.
Conclusions.

## Slide 4: Layout
From R. Schmidt, FCC week Washington, March 2015.

## Slide 5: Circuit
From R. Schmidt, FCC week Washington, March 2015.

## Slide 6: Magnet Design Parameters
Inom, Iultim.
Ld@inj, Ld@ultim
Stored energy E@ultim
Vgnd: max. voltage to ground during fast power abort without quench or earth fault.
Derived quantity:
  test voltage to ground, e.g., Vtest = 2*Vgnd + Vquench where Vquench includes a heater failure (LHC RB circuit).
EE unit with central grounding point.
11-T dipole 20% vairation of Ld.

## Slide 7: FPA time, EE parameters.
Max. MIITs for diode (heat-sink), busbar and joint (stabilizer), and DFB leads.
Derived quantity:
  Fast power-abort (FPA) time constant tFPA.
  e.g., tFPA = 100 s (LHC RB).
EE design consideration:
  cool-down time (LHC ~2 hours),
  semi-conductor, electro-mechanical, or superconducting.
Courtesy of Knud Dahlerup-Petersen, Gert-Jan Coelingh, Alexandr Erokhin
RB EE resistor
RB switch
Electro- mechanical switch
IGBTs on heat sink

## Slide 8: PC Parameters
PC max. voltage
  Negotiable. 2 kV may be reasonable.
PC max. current
  30 kA upper limit.
PC max. power
  60 MW?
  Total FCC power consumption during ramp should be minimized.
LHC RB power converter.

## Slide 9: Other Parameters
Operations/Availability
  Ramp rate dI/dt ~ Inom/tramp.
  e.g., tramp = 1800 s (here 30 min, LHC 20 min, faster?).
Cryogenics
  Max. heating from warm-cold transitions.
Cost
  Cost per PC ~ 1-2 MCHF*
  Cost per EE ~ 300 kCHF* (electro-mechanical)
  Cost for caverns?
Free parameters
  Nsec number of powering sectors, min. 8.
  NEE number of EE units per powering sector.
*… roughest of estimates!

## Slide 10: Magnet Variants Cos-Theta
Data from EuroCirCol WP5 coordination meeting on 9 Oct. 2015.

## Slide 11: Magnet Variants Block Coils
Data from EuroCirCol WP5 coordination meeting on 9 Oct. 2015.

## Slide 12: LHC Circuit Configuration
Nsec = 8, NEE = 2
lowest Ld
highest Ld

## Slide 13: Parametric Study
Ncir per octant number of powering sectors per octant, Nsec = Ncir per octant * 8.
Lowest inductance, lowest Nsec and NEE.
Highest inductance and Vgnd =1 kV : Nsec = 64, NEE = 8.

## Slide 14: Conclusion
Circuit protection does not put hard constraints on magnet design.
Low-inductance magnets are intrinsically advantageous:
  Reduced number of circuits and EE units.
  Reduced voltage in magnet during quench.
  Lower power consumption.
Voltage-to-ground has large impact on Nsec and NEE.
  Need ambitious design goal and risk analysis for test voltage.
Cost of PC/EE critical only for very large Nsec and NEE:
  Extreme example: 64 powering sectors, 8 EE units each: 128 MCHF + 154 MCHF + cavern cost.
Availability considerations need to be studied.
  Mean-time to failure in PC, etc.
  For training, shorter powering sectors are advantageous.

## Slide 15: Areas to work on
Fast transient analysis
Diode/busbar design
EE conceptual studies