## Slide 1: Update on CLICpix2
Pierpaolo Valerio
Edinei Santin

## Slide 2: CLICpix
65 nm CMOS r/o ASIC targeted to the CLIC vertex detector
Submitted in Nov./2012, tests started in Jan./2013
Based on Medipix chip family
64 x 64 pixel matrix, 1.6 x 1.6 mm2 active area
25 μm x 25 μm pixel pitch
Simultaneous time (4-bit ToA, 10 ns) and energy (4-bit ToT) measurements
Selectable on-chip data compression (pixel, super pixel, column-based)
Power pulsing enabled (Pavg < 50 mW/cm2)
Recent results using both capacitively coupled HV-CMOS and bump-bonded Si sensors show good uniformity and detection efficiency
CLIC Work in Progress
Column
Row
#hits
CLIC Work in Progress
Column
Row
1.85 mm
3 mm
#hits

## Slide 3: Why a redesign?
A crosstalk coupling to the input pad limits the minimum threshold (a fixed pattern noise is visible in the measurements)
A small readout bug limits the performance of the data compression
The I/Os work as intended, but the chip the interface is not very user-friendly or convenient
Limited counters length, despite meeting the CLIC specifications, makes data taking relatively slow and some measurements difficult

## Slide 4: CLICpix2
CLICpix2 is a redesign of CLICpix (referred to as “CLICpix1”), using the same CMOS technology
CLICpix1 was already successful as a proof-of-concept for the general architecture of the chip. Many blocks are reused with little changes
The new chip features bug fixes and “quality of life” improvements, along with a large number of minor upgrades to most blocks (too many to present them all!)
Main features:
  Longer counters for ToT and ToA to make testing more efficient
  Implement a smarter I/O protocol to allow an easier system design and a faster readout
  Bigger pixel matrix (128 by 128 pixels)
  Better noise isolation
  Integrated testing DACs
  Integrated bandgap
3.3 mm
4 mm

## Slide 5: Frontend block diagram
Composed of three building blocks: charge-sensitive amplifier, comparator, and calibration DAC
Conceptually the same as CLICpix1, but many blocks were improved to have better noise immunity and make their footprint smaller!

## Slide 6: Noise Isolation
All the analog structures have now a deep n-well isolation structure, to physically separate their substrate from the noisy digital blocks
The analog pixel has a mirrored layout, making the connections to their corresponding logic shorter
More care has been put in shielding critical nodes
Power supply distribution has been optimized to reduce “bouncing”

## Slide 7: Crosstalk at the input of the comparators (xRC)
1
2
4
3
5
~41mV
Extensive simulations were performed to address potential crosstalk
Maximum error due to crosstalk is ~0.5 mV (15e-) which is ~5x lower than the noise spec (70e-)

## Slide 8: Power distribution
Power is distributed along the columns with vertical lines
  This limits the chip area! TSVs would help
Simulations were used to optimize the placements of power pads to achieve a better uniformity and to reduce drops over the matrix

## Slide 9: DAC linearity
The periphery DAC were adjusted to achieve a better linearity
At the lower end the linearity is limited by the output buffer, and at the higher end it is limited by the combination of the buffer and the current mirror

## Slide 10: Pixel Layout
The matrix layout is similar to CLICpix1, as pixels are still organized in 2x8 “super-pixels”
The analog parts are now perfectly symmetrical, which should eliminate the fixed pattern noise seen in the first prototype
The pads are larger and designed to be compatible with both bump bonding and C3PD
Analog Part
Digital Part
Analog Part

## Slide 11: Performance summary
Parameter (Cdet = 20 fF) | Value
Power dissipation | 6.6 µW
CSA gain | 33 mV/ke-
CSA phase margin | 67°
ToT dynamic range | 270 ke- (holes) / 150 ke- (electrons)
ToA accuracy | < 10 ns (w/ offline calibration)
Input-referred noise | 67 e-
Input-referred mismatch error | 28 e-
Minimum threshold | 438 e- (w/ 6-sigma margin)

## Slide 12: Additional Analog Blocks
Some blocks in the periphery which were missing in the previous chip were added, including:
  A Bandgap reference, which makes the chip more robust to temperature changes
  Temperature sensor
  Power supply test-point
  An electrical connection for the grounding of sensor guard-rings

## Slide 13: Additional Digital Features
In the pixels:
  5 bits ToT (up from 4)
  8 bits ToA (up from 4)
  Optional 13 bits ToA instead of ToT (it can be used as event counter too)
Easier to decode and more robust data format
Faster readout with more standard protocol
Automatic test pulse generator
I/O link testing routine
Some debug features

## Slide 14: Readout algorithm
In order to use clock recovery from data stream, which simplifies the readout system, we set a target bandwidth of 640 Mbit/s over a single (differential) serial link
In CLICpix1 one column at a time is read: this solution doesn’t scale with clock speed
A more general solution is to read out data from multiple columns at the same time using a slower clock and then serialize data at the output
At the same time, the clock is divided by the same ratio to match the output bandwidth
The system is entirely configurable: we can read 1/2/4/8 columns at a time and the clock divider can be configured independently

## Slide 15: Parallel Readout
If the chip is configured to read more than one column at a time, the matrix is divided in equal parts (by column), reading one column from each part
The data is then serialized with the readout clock
8/10 bit encoding is added at the output to recover the clock from the data stream

## Slide 16: Readout Time
Occupancy
Readout time (ms)
# columns
Occupancy
Readout time (ms)
# columns
Readout time with a 640 Mb/s serializer
Readout time with a 2 Gb/s serializer
The readout time is well within the CLIC specifications (800 µs) even with 2 parallel columns

## Slide 17: Ethernet packet encapsulation
The data stream is now properly divided into packets, each containing data from one or more double columns
The data packets follow the Ethernet physical specification
Headers dividing the packets contain relevant chip settings to allow for data reconstruction without any additional information
These modifications make the data format much more easily readable

## Slide 18: Alignment marks for easier flip-chip assembly
marks on C3PD
(for illustration only)
3234.75µm
3175.00µm
3261.14µm
3230.50µm
CLICpix2

## Slide 19: Design status
The design is complete and the final simulations are ongoing
Mixed-mode simulations have validated the accuracy of the data acquisition blocks
A more comprehensive set of digital verifications are being developed to be sure to test every feature and corner case
As soon as the last verification are done, the chip can be submitted (MPW runs every two weeks with very fast turnaround time)

## Slide 20: Conclusions
CLICpix was a successful demonstrator for the CLIC vertex detector, leading to many interesting results within the CLICdp collaboration
Some bugs in the design warranted the development of an improved version, which could be used in a wider range of use cases
The design is complete and the last verification steps are ongoing

## Slide 21: Thanks for your attention