## Slide 1: Tolerance studies and coupling for extreme low emittance in the Future Circular Collider FCC-ee (TLEP)
Sandra Aumon CERN
On behalf of the FCC-ee Lattice Design team

## Slide 2: FCC-ee lattice: 1m/2mm beta*
Circumference: 100km
12 folds lattice
12 arcs (~6.8 km)
12 RF sections
4 and 2 IPs lattices with 0.5/1mm, 1m/2mm beta*
L*=2m
Priority on 2IP lattices, 1m/2mm 120 and 175GeV
RF
RF
RF
RF
RF
RF
RF
RF
RF
RF
RF
RF
IR
IR
IR
IR

## Slide 3: FCC-ee lattice
120 GeV
1m/2mm beta*, 2 Ips
Tool: MADX
Qx=419.08/ Qy=333.14
DQx = -573.6506369
DQy = -852.4978106
FODO cell
Interaction Region
Any errors are amplified
3km
Notes: Ideal lattice for electron
racetrack

## Slide 4: Method for tolerances and correction up to 120 GeV
Errors in lattice (up to 0.150mm for misalignments, 0.1mrad for rolls)
Orbit correction -> Correct the orbit and H.&V dispersions
Chromaticity correction with sextupoles of the arcs (large strength)
Tune corrections
Re-matching of the optics due to beta-beating
Coupling correction & V. dispersion correction
Switch the synchrotron radiation in MADX: - compute equilibrium emittances, final orbit with sawtooth effect
„Sawtooth Effect“ at LEP
BPM Number
Work in progress

## Slide 5: Sawtooth Effect in TLEP (120GeV)
Correction of the linear lattice before switching the radiation. (only Sawtooth effect remains)

## Slide 6: 120GeV-1m/2mm-2IPs
Emittance before coupling correction
Misaligned Quadrupoles
Beta-beating introduced by sextupoles
2pm
The coupling comes from off center orbit in the sextupoles for the chromaticity correction (first order)

## Slide 7: Preliminary results for coupling correction
Correct non-diagonal element of the transport Rmatrix Re13 at the BPMs (given by MADX) – the others (Re23 etc..) are going down automatically.
Building a Response matrix 3990x(2x3990)
Computation of the response matrix parallelized+inversion (20 hours CPU)
J1
J3990
Jn
…
…
bpmn
bpm1
bpm2x3990
.
.
.
.
.
.
M =
To correct
To be inverted
Javier Alabau Gonzalo for CLIC damping ring

## Slide 8: Preliminary results for coupling correction
120 GeV -1m/2mm beta*
15% beta-beating
Displacement (microm)
0.060 mm tolerance for quadrupole tolerance
Above 0.060mm, coupling correction counter-productive

## Slide 9: 120GeV-1m/2mm-2IPs
Horizontal Emittance

## Slide 10: Preliminary results for coupling correction
Very likely explanation: optics mismatch, vertical dispersion mismatch, skews combination/optimization

## Slide 11: SVD decomposition Eigen values
Work in progress
Optimization of the number of eigenvalues & skews & places

## Slide 12: Resonance Driving Term method from ESRF
Courtesy S. Liuzzio
Linear!

## Slide 13: Rolls angle in quadrupoles
120 GeV – 1m/2mm beta*
Before coupling correction
More relax situation than quadrupole misalignments

## Slide 14: Matching of FCC-ee optics
Use Dispersion suppressor/matching sections to rematch in straight sections and arcs. (ARC- Dispersion Suppressor – Matching section -SS – FF – IP)
Do not touch the quads of the arcs (4000 quads in the machine)
Work in progress
Straight Section
Arc
Arc
Matched
Arc
Mismatched Arc

## Slide 15: Racetrack lattice 120GeV – no tapering
Non linear beta_beat
120GeV -2 Ips – 2mm beta* - 2RF sections
Strong beta beat sur sawtooth – need to be tapered

## Slide 16: Conclusions – Next steps
Challenging machine in terms of tolerances toward linear collider requirements for tolerances
Beta-beating and vertical dispersion spoil the vert. emittance during the coupling correction - Re-matching of the machine (Resp. matrix based on ideal machine)
- Improve SVD decomposition for response matrix (exclude certain eigenvalues)
- skews in Dispersion Suppressor section less efficient.
Comparison with RDT method (A. Franchi et al., PRSTAB 14.0034002) – Able to measure
Tolerance for a Racetrack lattice - local chromaticity correction at the IPs (Katsunobu Oide) – Tunnel fitting with the FCC-hh machine

## Slide 17: Thank you for your attention!

## Slide 20
Courtesy Katsunobu Oide

## Slide 21: Optics at the IR
Optics for 120GeV (H) and 175GeV (ttb)
From Bastian Haerer’s presentation, tuning of the cell length and phase advance to get the correct emittances.
2 lattices with 2 scheme of chromaticity correction (in the arc or around the IPs)
Chromaticity correction in the arcs (stronger sextupoles) Bastian’s lattice
Beta*=1mm
Betaymax= 5km

## Slide 22: Only Coupling

## Slide 23: Influence quadrupoles of IPs

## Slide 24: Main challenges: parameter list
 | Z | W | H | tt
Beam energy [GeV] | 45.5 | 80 | 120 | 175
Beam current [mA] | 1450 | 152 | 30 | 6.6
Bunches / beam | 16700 | 4490 | 1330 | 160
Bunch population [1011] | 1.8 | 0.7 | 0.46 | 0.83
Transverse emittance ε Horizontal [nm] Vertical [nm] | 29.2 0.06 | 3.3 0.007 | 0.94 0.0019 | 2 0.002
Momentum comp. [10-5] | 18 | 2 | 0.5 | 0.5
Betatron function at IP β* Horizontal [mm] Vertical [mm] | 500 1 | 500 1 | 500/1000 1/2 | 1000 1/2
Energy loss / turn [GeV] | 0.03 | 0.33 | 1.67 | 7.55
Total RF voltage [GV] | 2.5 | 4 | 5.5 | 11
Lattice design & optimization for 4 different energies
Lattices with 2 and 4 IPs
Coupling ratio V.emit/H.emit ~0.2 & 0.1%
Challenging chromaticity correction scheme (chromaticity carried 90% by IR, 10% Arc) – B. Haerer and A. Bogomyakov
Average synchrotron radiation power per turn
Notes: 8 gev /turn/beam

## Slide 25: Emittance tuning in electron storage rings
L.C. Teng “Minimizing the Emittance in Designing the lattice of an Electron Storage Ring”, 1984.
L: cell length
lB: dipole length
: phase advance/cell
To match the baseline parameters, Bastian Haerer tuned cell length- phase advance per cell (90/60 degrees)
Energy (GeV) | Cell length (m)
45 | 300
80 | 100
120 | 50
175 | 

## Slide 26: Emittance tuning in electron storage rings
Alignment errors, rolls angle and coupling spoil the vertical emittance and compromise the coupling of 1/1000 (2/1000) -> Coupling and Dy should be under control.