## Slide 1
FCC status
F. Zimmermann on behalf of the FCC Collaboration
LHeC Coordination Group
2 October 2015
many thanks to
M. Benedikt and J. Gutleber

## Slide 2
International FCC collaboration (CERN as host lab) to study:
pp-collider (FCC-hh)  main emphasis, defining infrastructure requirements
80-100 km infrastructure in Geneva area
e+e- collider (FCC-ee) as potential intermediate step
p-e (FCC-he) option
HE-LHC with FCC-hh technology
~16 T  100 TeV pp in 100 km
Future Circular Collider Study
GOAL: CDR and cost review for the next ESU (2018)

## Slide 3
Hadron collider parameters
Parameter | FCC-hh |  | SPPC | LHC | HL LHC | 
collision energy cms [TeV] | 100 |  | 71.2 | 14 |  | 
dipole field [T] | 16 |  | 20 | 8.3 |  | 
# IP | 2 main & 2 |  | 2 | 2 main & 2 |  | 
bunch intensity [1011] | 1 | 1 (0.2) | 2 | 1.1 |  | 2.2
bunch spacing [ns] | 25 | 25 (5) | 25 | 25 |  | 25
luminosity/Ip [1034 cm-2s-1] | 5 | 25 | 12 | 1 |  | 5
events/bx | 170 | 850 (170) | 400 | 27 |  | 135
stored energy/beam [GJ] | 8.4 |  | 6.6 | 0.36 |  | 0.7
synchr. rad. [W/m/apert.] | 30 |  | 58 | 0.2 |  | 0.35

## Slide 4
Two parameter sets for two operation phases:
  Phase 1 (baseline): 5 x 1034 cm-2s-1 (peak), 250 fb-1/year (averaged)
    2500 fb-1 within 10 years (~HL LHC total luminosity)
  Phase 2 (ultimate): ~2.5 x 1035 cm-2s-1 (peak), 1000 fb-1/year (averaged)
   15,000 fb-1 within 15 years
  Yielding total luminosity O(20,000) fb-1 over ~25 years of operation
FCC-hh luminosity goals & phases

## Slide 5
20 ab-1 OK for physics

## Slide 6
phase 1: b*=1.1 m, DQtot=0.01, tta=5 h
phase 2: b*=0.3 m, DQtot=0.03, tta=4 h
  for both phases:
  beam current 0.5 A unchanged!
  total synchrotron radiation power ~5 MW.
radiation damping: t~1 h
Luminosity evolution

## Slide 7
High-Energy LHC
FCC study continues effort on high-field collider in LHC tunnel
2010 EuCARD Workshop Malta;
Yellow Report CERN-2011-1
based on 16-T dipoles developed for FCC-hh
extrapolation of other parts from the present (HL-)LHC
and from FCC developments
EuCARD-AccNet-EuroLumi Workshop: The High-Energy Large Hadron Collider - HE-LHC10,
E. Todesco and F. Zimmermann (eds.), EuCARD-CON-2011-001; arXiv:1111.7188; CERN-2011-003 (2011)

## Slide 8
circumference 27 km
in operation from 1989 to 2000
maximum c.m. energy 209 GeV
maximum synchrotron radiation power 23 MW
LEP – highest energy e+e- collider so far

## Slide 9
Lepton collider key parameters
parameter | FCC-ee |  |  | CEPC | LEP2
energy/beam [GeV] | 45 | 120 | 175 | 120 | 105
bunches/beam | 13000- 60000 | 500- 1400 | 51- 98 | 50 | 4
beam current [mA] | 1450 | 30 | 6.6 | 16.6 | 3
luminosity/IP x 1034 cm-2s-1 | 21 - 280 | 5 - 11 | 1.5 - 2.6 | 2.0 | 0.0012
energy loss/turn [GeV] | 0.03 | 1.67 | 7.55 | 3.1 | 3.34
synchrotron power [MW] | 100 |  |  | 103 | 22
RF voltage [GV] | 0.2-2.5 | 3.6-5.5 | 11 | 6.9 | 3.5
FCC-ee: 2 separate rings CEPC baseline: single beam pipe like LEP
Dependency FCC-ee: crab-waist vs. baseline optics and 2 vs. 4 IPs

## Slide 10
e+e- luminosity vs. c.m. energy
Z
WW
HZ
H?
aQED
?
CEPC
FCC ee

## Slide 11
90 – 100 km fits geological situation well
LHC suitable as potential injector
Site investigations

## Slide 12
∼12 m
30 mrad
9 m
“Middle straight”
∼1570 m
FCC-hh
Common
RF
Common
RF
“90/270 straight”
∼4.7 km
IP
IP
FCC layout
compatible layouts
for hh and ee
0.8 m
As the separation of 3(4) rings is within 15 m,
one wide tunnel may be possible around the IR.
K. Oide

## Slide 13
zoomed view
around the IP
K. Oide

## Slide 14
Chart: B in T
10 % margin FCC | 0 | 0.952
10% margin HL-LHC | 0 | 0.6831
16 T | 0 | 1.5
~10% margin
FCC ultimate
3150 mm2
~1.7 times less SC
~10% margin
HL-LHC
5400 mm2
16 T
Critical surface FCC
HL-LHC
Nb3Sn T = 4.5 K
LHC at 1.9 K
Nb-Ti
Not possible
Different technology
Superconductor performance

## Slide 15
Main Milestones of the FCC Magnets Technologies |  |  |  |  |  |  |  |  |  |  |  |  | 
Milestone | Description | 15 | 2016 |  | 2017 |  | 2018 |  | 2019 |  | 2020 |  | 21
M0 | High Jc wire development with industry |  |  |  |  |  |  |  |  |  |  |  | 
M1 | Supporting wound conductor test program |  |  |  |  |  |  |  |  |  |  |  | 
M2 | Design & manufacture 16T ERMC with existing wire |  |  |  |  |  |  |  |  |  |  |  | 
M3 | Design & manufacture 16 T RMM with existing wire |  |  |  |  |  |  |  |  |  |  |  | 
M4 | Procurement of 35 km enhanced wire |  |  |  |  |  |  |  |  |  |  |  | 
M5 | Design & manufacture 16T demonstrator magnet |  |  |  |  |  |  |  |  |  |  |  | 
M6 | Procurement 70 km of enhanced high Jc wire |  |  |  |  |  |  |  |  |  |  |  | 
M7 | EuroCirCol design 16T accelerator quality model |  |  |  |  |  |  |  |  |  |  |  | 
 | Manufacture and test of the 16 T EuroCirCol model |  |  |  |  |  |  |  |  |  |  |  | 
FCC magnet technology program
ERMC (16 T mid-plane field) RMM (16 T in 50 mm cavity) Demonstrator (16 T, 50 mm gap)

## Slide 16
SC RF R&D towards FCC
Many pertinent R&D and construction efforts at CERN:
R&D and production of Nb/Cu sputtered 401- MHz LHC cavities, and of HL-LHC 401-MHz crab cavities (with US-LARP and U. Lancaster),
fabrication of 802 MHz cavities & CM’s for HL-LHC (with JLAB & CEA)
testing 704-MHz Nb cavities, complete string and CM assembly (w ESS)
continue R&D on “high-” technologies such as “N2 doping” or Nb3Sn coating (with Cornell and FNAL)
contributions to int’l projects like ILC & PIP-II
optimized cool-down schemes
new fabrication techniques (3D-print, rapid forming, seamless cavities…)
new materials (Nb(Ti)N, V3Si, TBBCO…)
RF power sources energy conversion efficiency
more efficient cryogenics (optimum ?); improved cryomodule design
I. Syratchev

## Slide 17
Core aspects of hadron collider design: arc & IR optics design, 16 T magnet program, cryogenic beam vacuum system
Recognition of FCC Study by European Commission.
EC contributes with funding to FCC-hh study
EuroCirCol EU Horizon 2020 Grant

## Slide 18: Collaboration Status
62 institutes
23 countries + EC
Status: 28 September 2015
FCC International Collaboration

## Slide 19
62 collaboration members & CERN as host institute, 28 September 2015
ALBA/CELLS, Spain
Ankara U., Turkey
U Belgrade, Serbia
U Bern, Switzerland
BINP, Russia
CASE (SUNY/BNL), USA
CBPF, Brazil
CEA Grenoble, France
CEA Saclay, France
CIEMAT, Spain
CNRS, France
Cockcroft Institute, UK
U Colima, Mexico
CSIC/IFIC, Spain
TU Darmstadt, Germany
TU Delft, Netherlands
DESY, Germany
TU Dresden, Germany
Duke U, USA
EPFL, Switzerland
GWNU, Korea
U Geneva, Switzerland
Goethe U Frankfurt, Germany
GSI, Germany
U. Guanajuato, Mexico
Hellenic Open U, Greece
HEPHY, Austria
U Houston, USA
IIT Kanpur, India
IFJ PAN Krakow, Poland
INFN, Italy
INP Minsk, Belarus
U Iowa, USA
IPM, Iran
UC Irvine, USA
Istanbul Aydin U., Turkey
JAI/Oxford, UK
JINR Dubna, Russia
FZ Jülich, Germany
KAIST, Korea
KEK, Japan
KIAS, Korea
King’s College London, UK
KIT Karlsruhe, Germany
Korea U Sejong, Korea
MEPhI, Russia
MIT, USA
NBI, Denmark
Northern Illinois U., USA
NC PHEP Minsk, Belarus
U. Liverpool, UK
U Oxford, UK
PSI, Switzerland
U. Rostock, Germany
Sapienza/Roma, Italy
UC Santa Barbara, USA
U Silesia, Poland
TU Tampere, Finland
TOBB, Turkey
U Twente, Netherlands
TU Vienna, Austria
Wroclaw UT, Poland
FCC Collaboration Status

## Slide 20
FCC Week 2016
Rome, 11-15 April 2016