HARPO:
Measurement of
polarised gamma rays (1.7 to 74MeV)
with the HARPO TPC
Philippe Gros
for the HARPO collaboration

---
- The HARPO project
- Setup at the NewSUBARU photon beam
- Trigger design and efficiency
- Challenges for a balloon/space mission
- Conclusion and perspectives

---
HARPO Demonstrator
- Purpose
  - Assess challenges
  - Demonstrate performance in test
    beam
- Realisation
  - 30cm cubic TPC
  - Ar/iC4H10 95/5 up to 5bar
  - micromegas+2GEM amplification
  - 2x288 strips readout (x&y), 1mm pitch
  - AFTER readout electronics,
    511 time bins, up to 100MHz (33 used)
  - trigger: 6 scintillators+mesh signal + laser pulse

---
HARPO Demonstrator
scintillators
micromegas +GEM
readout strips
field cage

---
Event Geometry

---
NewSUBARU
photon beam
- Polarised gamma ray beam
  - Inverse Compton Scattering
  - electron beam 0.6, 1., 1.2 or 1.5 GeV
  - laser Nd (1ω or 2ω), Er or CO2
    => polarised photons 1.71 to 74MeV
- Pulsed mode
  - Nd: 20kHz, Er:200kHz, CO2: continuous
- Operated by LASTI, U. of Hyôgô, Japan

---
Conversion events

---
Trigger in beam
- Several kHz events in TPC
- DAQ max acquisition rate <600Hz
- Dominated by background
  - beam interaction in upstream material
  - >20x larger than signal
- Efficient BG suppression needed
- Signal rate important, not efficiency

---
Trigger building
Active volume
Channel
e-
e+
#ADC
0
3
6
9
12
Time (µs)
Drift velocity (~3cm/µs)
0
300
distance (mm)
Laser
Scintillator
Signal on mesh
Main trigger line (gamma)
Laser

---
Preliminary event selection
Estimate the vertex position as first signal in beam direction
The vertexes are located on a region corresponding to the 4mm circular beam collimator
Beam interaction in gas

---
Signal/BG selection
different trigger lines
No mesh veto: dominated by BG

---
Event rates
- 5 trigger lines for efficiency studies
- Rates for signal and BG
  - from vertex position selection
Main trigger

---
Trigger efficiency
- We can estimate accurately the rate of events corresponding to
  - Signal: conversion on beam in the gas
  - Background: mostly conversion in upstream material
- This allows to measure the trigger efficiency:
  - >99% BG rejection
  - >50% Signal selection efficiency
  Reconstruction efficiency not included

---
Reconstruction challenges
- Intrinsic challenges
  - matching X-Z and Y-Z tracks
  - multiple scattering
  - non directionality
  - delta electrons
- Extra challenges
  - electronics saturation
  - cross-talk

---
Sometimes it is easy

---
Matching X and Y
charge profiles
X	: track 1
Y	: track 1
X	: track 0
Y	: track 0

---
More difficults

---
Or very tricky

---
Challenges in space
- Readout electronics
  - low power => strips instead of pads
  - radiation hardness
- Adapted trigger
  - standalone TPC (minimize extra material)
  - high selection efficiency
  - self-triggered electronics

---
Challenges in space
- Gas stability
  - minimise outgassing
  - purification
- High pressure
  - optimise pressure: sensitivity, scattering, mechanical & HV constraints
  - small gap micromegas?

---
Conclusion and outlook
- Successful beam campaign with gamma rays
  - Good trigger performance
  - Challenging reconstruction
- Developments towards spatialisation
  - gas purification in sealed mode
    demonstrated
  - starting work on radiation hardening
    of AGET
  - trigger development (simulation)
  - ~1m3 balloon module design (4x4x4xHARPO)

---
Advertisement
Poster #2 on gas circulation and purification
attenuation
drift velocity
purification

---
Backup

---
1 m3 module trigger

---
Pressure scan
- One day dedicated to pressure scan
  - “Clean” gas at 1, 1.5, 2, 3 and 4 bar
  - Signal amplitude (dE/dx x gain) ~fixed
    (Adjusted on the fly)
  - At high pressure, cathode voltage was limited
- Good running condition at all pressures
- Increasing micromegas current spikes at high pressure
  - matching GEM over current => physics?

---
HARPO
- TPC for measurement of polarised gamma rays
  - e+e- conversion (MeV~GeV)
  - Various astrophysics applications (in space)
  - Low multiple scattering => high angular resolution
  - Sensitive to linear polarisation
  - High pressure gas for higher conversion probability

---
 beam

---
Beam campaign
- ~20 days of data taking
- 13 gamma energies, polarised or not
- 4 TPC orientation for angle systematics
- >60Mevents, >1TB of data
Angles
Egamma [MeV]
#events

---
NewSUBARU
Storage Ring
XFEL
Linac
NewSUBARU
Synchrotron