## Slide 1: Timing, Synchronization & Longitudinal Aspects I
H. Damerau
CERN
13 March 2017
CAS Course on
Beam Injection, Extraction and Transfer

## Slide 2
Introduction
General concepts
  Signals with noise, transmission of RF signals
  Phase detectors and dividers
Beam transfer
  Fundamental periodicity
  Transfer between circular lepton accelerators
Transfer between hadron accelerators
  Beam phase loop, bucket numbering
  Transfer process: Synchronization, transfer triggers
  Longitudinal matching
Summary
Outline

## Slide 3
Introduction

## Slide 4
Two or more people must be synchronized to meet
  Calendar item: date, time and location
  Typical uncertainty: some minutes
Slightly more precision required to have a meeting with a particle beam
  Typical uncertainty: some nanoseconds down to femtoseconds
Introduction
To be at the right time in the right place
Set conditions and generate timings and RF signals with a given time relation with respect to the beam
Make beam feel comfortable in its new accelerator

## Slide 5
Timescales
10 ns
1 ns
100 ps
10 ps
1 ps
100 fs
10 fs
Proton bunches in low energy synchrontrons
Hadron colliders
Electron storage rings
Pump-probe FELs
SASE FELs
Plasma wakefield experiments
Electronics
Low-level RF systems
Proton synchrotrons at medium energy
Geometrical size: few meters to some km

## Slide 6
How to get the beam trough the accelerator?
How to transfer beam from accelerator A to B?
Beam passes many elements on its way:
  RF structures  Must be in phase
  Septa, bumper and kicker magnet  Trigger
  Fast beam instrumentation  Trigger
  RF systems in source and target accelerator  Correct phase with respect to beam
Synchronization for beam transfer
Source
Exit
Accelerator A
Accelerator B

## Slide 7
Particle velocity depends on its type:
Old television set (30 kV): Electrons at 30% of c0
            Protons just at 0.7%
Small synchrotron (500 MeV): Electrons at 99.99995%
              Protons at 75.8%
Many electron accelerators at ‘fixed’ frequency
Particle velocity
p+
e-
p+
e-

## Slide 8
Synchronization needs for particle types
Lepton accelerators | Hadron accelerators
Velocity v  c in high energy accelerators Synchrotron radiation damping (mainly circular accelerators) Short bunches Storage rings: ~10…100 ps Linear free electron lasers: 50…200 fs | Slow, even velocity change relevant to the multi-GeV range Negligible or small damping from synchrotron radiation Long bunches Synchrotrons: 1...1000 ns (depends on RF frequency) Linear accelerators: typically few ns
Fixed frequencies High precision | Variable (sweeping) frequencies Moderate precision

## Slide 9
Bunch from sending accelerator into the bucket of receiving
Bunch-to-bucket transfer
Advantages:
Particles always subject to longitudinal focusing
No need for RF capture of de-bunched beam in receiving accelerator
No particles at unstable fixed point
Time structure of beam preserved during transfer to the next

## Slide 10
Noise on signals

## Slide 11
Degradation of signal quality due to noise
  Amplitude and/or phase jitter
What is the difference between a coherent signal and noise?
Amplitude of coherent, quasi monochromatic signal (at 200 MHz) is independent of observation bandwidth
Incoherent noise power (dominated by spectrum analyzer front-end amplifier/mixer) is proportional to bandwidth
Thermal noise power
Noisy signals
Noise
Noise

## Slide 12
Compare noise power with carrier power as reference
Analysis of phase noise
Ratio of carrier to noise: dBc
Df
Bandwidth Df = 1 Hz for normalization
Noise power density
Its integral is the phase jitter and using
the jitter in time becomes

## Slide 13
Measure phase noise of a synthesized lab generator
Typical phase noise plots
Frequency range | Dtrms [fs]
10…100 Hz | 12.4
100 Hz …1 kHz | 5.4
1…10 kHz | 5.4
10…100 kHz | 11.1
100 kHz…1 MHz | 13.0
Total | 31.0
Note: jitter values can be added as square root of quadratic sum
Convenient split to relevant ranges

## Slide 14
Signal transmission

## Slide 15
Thermal drift of long coaxial cables or optical fibres
Thermal coefficient of delay:
Transmission of reference signals
RG223 coaxial cable
Example: 2 km long RG223 cable with ~10 ms delay
DT of only 1° C (room temperature) changes delay by ~0.5 ns
1.8° at 10 MHz (CERN PS), but 73° at 400 MHz (LHC)
Optical fibres are typically 10…100 times more stable
What to do if this is still not sufficient?
Lutes/Diener, NASA TDA Progress Report 42-99

## Slide 16
Measured drift of optical fibres over long distance standard optical fibre
Drift by about 1 ns insufficient for requirements of setup
Active compensation of delay
Transmission of reference signals
Measured temperature and delay drift of ~6.3 km fiber
Time
Temperature [°C], Df at 200 MHz
1.67 ns

## Slide 17
Precise synchronization of proton beam from CERN SPS with plasma wake-field experiment AWAKE
Prototype hardware
Simplified diagram
Example: Active drift compensation
D. Barrientos, J. Molendijk
Expect picosecond precision over several kilometres

## Slide 18
Transmission of reference signals
Precision difficult to evaluate without 2nd ‘reference’ link
Arrival of two beams in AWAKE experiment stable to better ~100 ps over months
D. Barrientos, J. Molendijk
Total delay composed of coarse (steps of 10 ps) and fine ~30 ps range: t = tcoarse + tfine
1 ns

## Slide 19
Overview of transmission methods
Various approaches:
1) RF distribution
~
f ~ 100MHz …GHz
2) Carrier is optically
~
MZT
f ~ GHz
3) Carrier is optically + detection
f ~ 200 THz
standard
reflectometer
interferometer
~
MO
LO
4) Pulsed optical source
f ~ 5 THz
OXC
Mode locked
Laser
SLAC
FLASH
E-XFEL
SwissFEL
SLAC
FERMI
(LBNL)
SACLA
FERMI
FLASH
E-XFEL
SwissFEL
H. Schlarb
t
t f
=
f

## Slide 20
Phase detection

## Slide 21
Two signals at different frequencies w1 and w2
Phase difference, Df, between both signals changes linearly
Ambiguity to distinguish between Df = -p, p, -3p, 3p,...
Saw-tooth in phase means constant frequency difference
Equivalence of frequency and phase
Frequency and phase


## Slide 22
How to detect phase differences?
Example: analogue 4 quadrant multiplier and low pass filter
Signals:

## Slide 23
Example: analogue 4 quadrant multiplier and low pass filter
Signals:
How to detect phase differences?
Remove ripple  Low-pass filter

## Slide 24
Example: analogue 4 quadrant multiplier and low pass filter
Signals:
Phase discriminator in approximately +/-90° range
Remove ripple  Low-pass filter
Relative: arbitrary shift by 90°
How to detect phase differences?

## Slide 25
Multitude of different phase discriminators
Further phase detection techniques
Type | Range | Behavior
Analogue 4 quadrant multiplier | p | Sinusoidal: sout ~ cos f
Exclusive OR gate | p | Linear: sout ~ f - 3p/2, or sout ~ -f + p/2
Sample and hold | p | Sinusoidal: sout ~ sin f
Flip-flop phase detector | p | Linear: sout ~ f - p
Tri-state double flip-flop | 2p | Linear: sout ~ f
Balanced optical microwave phase detector (Sagnac loop) | <p | Sinusoidal: sout ~ sin f (clipped)
Full phase coverage of 2p range excludes ambiguity of ±p
Avoids locking of phase loop with unwanted offset
Measure phase at high frequencies for precision
R. Garoby

## Slide 26
Dividers

## Slide 27
Generate signals using frequency division from fRF
Works (well, on paper), so what is the problem?
Frequency dividers
n
1
fRF/n
n
1
fRF/n
fRF
n
1
fRF/n
m
1
fRF/m
fRF
Dividers are nothing but counters! Initial value?

## Slide 28
Generate signals using frequency division from fRF
How to fix?
Synchronizing multiple dividers
n
1
fRF/n
n
1
fRF/n
fRF
n = 2:
n = 5:
Re- set
Reset from master to slave divider(s) to force initial condition
Never more than one divider without reset!

## Slide 29
Counter with programmable offset value
Single counter/divider split in two output branches
Impossible to lose relative phase of outputs
More complicated set-up allows also fRF/m and fRF/n, etc.
Counter to n
Multiple divider with counting offset
fRF
Offset
+
x = 0?
x = 0?
fRF/n
fRF/n
Adder with Mod(x,n)

## Slide 30
Fundamental periodicity

## Slide 31
Storage ring circumference 240 m, fRF = 499.6 MHz
Circumference ratio of Booster and storage ring: 2/5
Example: BESSY II booster and storage ring
1/50
Everything repeats with periodicity of
  5 turns in booster
  2 turns in storage ring
Each gray point represents 4 RF buckets
1/25
1/10
240 m
96 m
Master: fRF = 500 MHz
3.125 MHz, frev booster
1.25 MHz, frev storage ring
0.625 MHz, periodicity
Sync. divider
1
16

## Slide 32
Storage ring circumference 288 m, fRF = 499.6 MHz
Circumference ratio of Booster and storage ring: 15/16
Example: SLS booster and storage ring
Fundamental periodicity (super-period)
  16 turns of booster corresponding to 15 turns in storage ring
500 MHz master
Booster frev
Booster super-period
Storage ring frev
Storage ring super-period
K. Babak, C. Gough

## Slide 33
Fundamental periodicity for transfer
Two accelerators with revolution periods Trev,1 and Trev,2
Beam transfer may take place at every period mTrev,1 or nTrev,2
This periodicity is, depending on the accelerator and laboratory, called super-period, common or fiducial period
In case of integer ratio of revolution frequencies, beam can be transferred once every turn of the larger accelerator
Sending | Receiving | Ratio | Remark
BESSY booster | BESSY SR | 2/5 | Fixed frequency
SLS booster | SLS SR | 15/16 | Fixed frequency
J-PARC RCS | J-PARC MR | 2/9 | Profit from ratio for bucket selection
PS booster | PS | 1/4 | 
PS | SPS | 1/11 | 
PS | AD | 3/1 | Particle type and energy change at transfer
SPS | LHC | 7/27 | fc as low 1.6 kHz

## Slide 34
How to generate beam synchronous triggers?
Chains of counters to re-synchronize timings
Synchronous triggers
Value
Clock
Start
Out
Value
Clock
Start
Out
Super-period marker
Booster frev marker
Value
Clock
Start
Out
fRF clocks
Each step re-synchronizes with respect counter clock
‘Start engine button’ synchronous to nothing
Complete system of two accelerators periodic with timing #1
Timing #2 marks, e.g., a delay in number of turns
Timing #3 counts fRF clocks to fine adjust, e.g., bucket number
#1
#2
#3

## Slide 35
Synchronous trigger trees
Value
Clock
Start
Out
Value
Clock
Start
Out
Super-period marker
Booster frev marker
#1
Value
Clock
Start
Out
Storage ring frev marker
#2
fRF clock counter
fRF clock counter
Booster ejection
Storage ring injection
#3
Timing counters may use different clocks, as long as the clocks are derived from the same source
Reproducible delay between clock #2 and #3
Tree structures of timings

## Slide 36
Simplification for most electron accelerators:
Leptons are practically at speed of light
Synchrotron radiation damping forces bunches into buckets
Beam synchronous timing triggers can be derived by counting RF master clock (or its sub-multiples)
Everything is predictable from the beginning
Circular electron/lepton accelerators
Each gray point represents 5 RF buckets
Kicker
magnet
Kicker
magnet
Diagnostics
Let’s get frequencies moving

## Slide 37
Transfer between hadron accelerators

## Slide 38
Circular hadron accelerators: master clock sweeps
Need again synchronous timings with respect to beam
  Kicker magnets
  Beam instrumentation
RF manipulations require bunches in certain buckets
  Beating pattern due to multiple RF harmonics
    Splits behaviour for different buckets
  Bucket numbering
Need to know longitudinal beam position for transfer
Where (in phase/in time) is the beam?
Do not measure!
Know!
Synchronous triggers and bucket counting

## Slide 39
fin, fin
Df
Phase-locked loop
Loop filter, H(w)
VCO
RF
Slow signal
Frequency re-generation and multiplication
Voltage controlled oscillator (VCO) locked in phase to input
fout, fout
fVCO
~fin - fVCO
1
n
Fixed phase relationship: fout/n – fin = const.
Optional divider: fout = n · fin

## Slide 40
Beam phase
Df
-
Loop corr.
Phase pick-up
RF cavity
Synchronous phase, fs
Cavity phase
Power amplifier
RF
Slow signal
Beam phase loop
+
DDS
Phase-locked loop with beam phase as reference for RF system
h · frev, from B
Digital synthesizer
fout = fin ± Df
h frev
Precision VFO
ferr ~Df
h
1
Beam synchro- nous frev
fRF

## Slide 41
Even large transients (injection, transition) can be controlled
Small longitudinal emittance blow-up
Rigid RF, no phase loop
With phase loop
Benefits of beam phase loop at transfer
Adapt RF phase to bunch phase before beam blows-up
Fast compared to timescale of synchrotron frequency, fs

## Slide 42
h
1
Beam synchro- nous frev
Start counting with injection
Start of divider/counter?
Get it right from injection
Use output from divider as reference for incoming beam
fRF

## Slide 43
h
1
Start counting with injection
Start of divider/counter?
Get it right from injection
Use output from divider as reference for incoming beam
Before injection:
  Distribute delayed revolution frequency to sending accelerator
  Bunches are injected synchronously with frev,delayed
  Shifted with respect to fRF and frev
fRF
Dt
Delay
frev
frev,delayed
To sending accelerator

## Slide 44
Start counting with injection
Start of divider/counter?
Get it right from injection
Use output from divider as reference for incoming beam
Before injection:
  Distribute delayed revolution frequency to sending accelerator
  Bunches are injected synchronously with frev,delayed
  Shifted with respect to fRF and frev
Counter to h
fRF
Offset
bucket #
+
x = 0?
x = 0?
frev
frev,delayed
To sending accelerator

## Slide 45
Beam phase loop without beam?
Just replace beam by a simple RF generator!
Df
DDS
VCO
RF cavity
Cavity phase
Power amplifier
RF
Slow signal
h · frev, from B
fout = fin ± Df
h frev
Precision VFO
ferr ~Df
h
1
Beam synchro- nous frev
fRF
Phase pick-up
Beam phase
Beam phase emulator

## Slide 46
Synchronization chain for bucket counting
Incoming beam
h
1
Synchro- nous frev
+
Offset
bucket #
Shifted frev to sending synchrotron
f const.
f const.
f const.
f const.
Incoming beam has reproducible phase with respect to RF bucket, synchronous frev and beam phase emulating generator
Straightforward switch to beam signals, already locked in phase
Beam phase emulator
f const.

## Slide 47
Synchronization chain for bucket counting
Incoming beam
h
1
Synchro- nous frev
+
Offset
bucket #
Shifted frev to sending synchrotron
f const.
f const.
f const.
f const.
Phase pick-up
f const.
Incoming beam has reproducible phase with respect to RF bucket, synchronous frev and beam phase emulating generator
Straightforward switch to beam signals, already locked in phase
Beam phase with respect to frev always known

## Slide 48
Bucket numbering

## Slide 49
3
4
2
1
3
4
2
1
1st injection
2nd injection
Must inject into the correct bucket numbers
Bucket numbering for RF manipulations
 | Triple splitting | Batch compression
Injection harmonic |  | 
Periodicity of RF manipulation | Every bucket | Only one beating along circumference
Injection bucket selection | 4 buckets difference between both injections | Both injections into independently defined buckets

## Slide 50
Bunches must be placed into the correct buckets numbers
Harmonic number change only for even number of bunches
Example: PS injection bucket selection
  Bucket number control during both transfers PSB  PS
  How to handle changing number of bunches?

## Slide 51
Intermediate summary
Basic techniques of signal synchronizations
  Beware of dividers
Beam transfer between circular lepton accelerators
  Constant frequency
  Predictable, independently from beam
  Fundamental periodicity
Beam transfer between circular hadron accelerators
  Beam is reference, keep track

## Slide 52: Timing, Synchronization & Longitudinal Aspects II
H. Damerau
CERN
13 March 2017
CAS Course on
Beam Injection, Extraction and Transfer

## Slide 53
Introduction
General concepts
  Signals with noise, transmission of RF signals
  Phase detectors and dividers
Beam transfer
  Fundamental periodicity
  Transfer between circular lepton accelerators
Transfer between hadron accelerators
  Beam phase loop, bucket numbering
  Transfer process: Synchronization, transfer triggers
  Longitudinal matching
Summary
Outline

## Slide 54
Synchronization and transfer

## Slide 55
Steps of beam transfer synchronization
1.
Set bending fields in both accelerators the to same magnetic rigidity
2.
Synchronize sending or receiving accelerator
 Ready for transfer
3.
Trigger bump and septum elements
4.
Start counting frev clock (sending/receiving accelerator)
5.
Start counting clock of fundamental periodicity
Start counting bucket clock
Fine delay
Ejection and injection kickers triggers
 Transfer

## Slide 56
Same magnetic rigidity rB of sending (1) and receiving (2) accelerators
No rule without exception: Particle type change at transfer
  Proton to anti-proton conversion, e.g., 120 GeV/c  8 GeV/c (Fermilab), 26 GeV/c  3.6 GeV/c (CERN),
  Charge state change at transfer, e.g. LHC ion injector chain Pb54+ in LEIR/PS  Pb82+ (in SPS)
Match bending field of both accelerator

## Slide 57
RF frequencies of both accelerators must have appropriate ratio assuming that the beam velocity is unchanged
Common choice of most circular electron accelerators fRF,1 = fRF,2
Harmonic number, h, proportional to circumference, 2pR
Again no rule without exception: Production of antiprotons in target in transfer line
Match RF frequencies

## Slide 58
Distance of bunches (bunch spacing, tbunch) from source accelerator must match distance of buckets
Example: tbunch = 2/fRF
Example: tbunch = 5/fRF
Common case: fRF,2 = n · fRF,1
  fRF,LHC = 2 · fRF,SPS and fRF,SPS = 5 · fRF,PS
Several exceptional cases:
  No bunch distance with single bunch  more flexibility
  Adjust bunch spacing using multiple RF systems
Distance between bunches

## Slide 59
2.
1.
2.
1.
1. Add h1 component such that bunches approach to 245 ns (small spacing) → big spacing becomes 327 ns
2. Synchronize on h1 to the PS
3. Trigger extraction kicker in-between the small spacing
4. Eject two bunches per ring at a distance of 327 ns
Exception: double-harmonic RF at transfer
Was used at CERN PSB-to-PS to transfer 2 bunches at once
Circumference ratio CPS/CPSB = 4
Ratio virtually moved to 2/7: use hRF = 2 + 1
Next bunch ejected
Short gap for ejection kicker
Christian Carli
Spacing larger than CPSB/2  hPS = 7, CPS/7

## Slide 60
1.
Set bending fields in both accelerators to the same magnetic rigidity
2.
Synchronize sending or receiving accelerator
Steps of beam transfer synchronization
 Ready for transfer
3.
Trigger bump and septum elements
4.
Start counting frev clock (sending/receiving accelerator)
5.
Start counting clock of fundamental periodicity
Start counting bucket clock
Fine delay
Ejection and injection kickers triggers
 Transfer

## Slide 61
Before synchronization
Even with magnetic rigidity matched: revolution frequencies not at theoretical ratio due to imperfections
Bunches and buckets slip in phase
Slippage of bunches and bucket
Rotation in source accelerator subtracted
But: important question left unanswered!

## Slide 62
Who is the boss?
• Transfer beam to a downstream machine: Bunch-to-bucket
Protons between synchrotrons → Synchronize accelerators
Move relative phase of RF together with beam between both machines to hit the empty buckets
?
Sending accelerator is, the boss?
Receiving accelerator is the boss?

## Slide 63
Choice of master for transfer synchronization
Sending accelerator is master of transfer
  Receiving accelerator adapts to incoming beam
  Common choice when receiving accelerator has no beam before transfer
  Interesting for only single beam transfer, e.g., protons from PS  AD for antiproton production
Receiving accelerator is master of transfer
  Sending accelerator adapts to incoming beam
  Common choice when receiving accelerator has already beam before transfer (multiple injections)
  Most common at CERN, e.g., proton injector chain PSB  PS  SPS  LHC

## Slide 64
Before synchronization
Source accelerator is master at transfer
Target accelerator is master at transfer
Simple test case of circumference ratio 2: C2 = 2C1

## Slide 65
Before synchronization
Source accelerator is master at transfer
Target accelerator is master at transfer
Simple test case of circumference ratio 2: C2 = 2C1
Synchronize both accelerator to force: frev,1 = 2frev,2

## Slide 66
Simple synchronization process
Bunch should be here
Locked!
Df
Beam azimuth
(from phase loop)
Beam phase (from master)
frev (h = 1)
Act on fRF of slave
Df
200 ms
Move beam to off-momentum (B const.):
  Well defined frequency difference between accelerators
Measure azimuth error, when beam at correct azimuth
  Close synchronization loop
  Moves beam to ref. momentum

## Slide 67
Example: Synchronization of SPS to LHC
SPS turns (10000 turns correspond to 231 ms
RF phase [°]
Arrival at flat-top +30 ms
Set frev,SPS = 27/7 frev,LHC
Measure Dt of azimuth SPS-LHC
Apply frequency bump
Re-measure Dt of azimuth
Apply frequency bump
Close fine re-phasing loop at fRF, LHC
Ready for transfer
LHC is master for beam transfer from SPS
Coarse and fine re-phasing to perfectly align bunches with respect to target buckets (400 MHz, 2.5 ns) in LHC
Complete synchronization process takes about 500 ms

## Slide 68
Example: Fast cogging of booster at FNAL
Rapid cycling synchrotron from 400 MeV to 8 GeV
Total cycle length is only 25 ms  How to synchronize fast?
Measure beam phase early in the cycle and predict azimuth at flat-top
Apply radial/frequency bumps already during acceleration
C. Drennan, R. Zwaska

## Slide 69
After synchronization
Source or target accelerator is master at transfer
Simple test case of circumference ratio 2: C2 = 2C1
Revolution frequencies coupled: frev,1 = 2frev,2
Transfer can be triggered every turn of the target accelerator

## Slide 70
Azimuthal position of 1st bunch ambiguous after RF manipulations
Number of buckets and bunches changes during acceleration
But: Synchronous frev,PS signal with reproducible phase to beam
‘Re-numbering’ of buckets by shifting reference from SPS
Shift of external reference frev,PS adjustable in SPS bucket units
Synchronize external and beam synchronous frev,PS
Ejection bucket selection
420
1
Reset
fRF,SPS
frev,SPS
Bucket number control
frev,PS (external)
frev,PS (internal)
fRF/h from beam-control
Synchronize
Example: Ejection bucket numbering in PS

## Slide 71
Example: Ejection synchronization chain
frev,SPS marker
Outgoing beam
frev,SPS, fRF,SPS for synchro.
Last turn before PS  SPS transfer
f const.
Outgoing
beam
f const.
Beam phase loop
frev,PS
internal
f const.
Synchroni- zation loop
frev,PS
reference
f const.
Ejection divider
Multiple ‘batches’ are transferred from PS to 11 times larger SPS
Beam phase with respect to frev always known

## Slide 72
Steps of beam transfer synchronization
1.
Set bending fields in both accelerators to the same magnetic rigidity
2.
Synchronize sending or receiving accelerator
 Ready for transfer
3.
Trigger bump and septum elements
4.
Start counting frev clock (sending/receiving accelerator)
5.
Start counting clock of fundamental periodicity
Start counting bucket clock
Fine delay
Ejection and injection kickers triggers
 Transfer

## Slide 73
Cascade of trigger counters for fast transfer elements
Very similar to transfer with lepton synchrotrons
Synchronous triggers
Value
Clock
Start
Out
Value
Clock
Start
Out
Common frequency marker, fc
frev,1 marker
Value
Clock
Start
Out
fRF,1 clock
Ejection elements
Value
Clock
Start
Out
Value
Clock
Start
Out
Common frequency marker, fc
Value
Clock
Start
Out
fRF,2 clock
Injection elements
frev,2 marker
Common

## Slide 74
1.
Set bending fields in both accelerators to the same magnetic rigidity
2.
Synchronize sending or receiving accelerator
Steps of beam transfer synchronization
 Ready for transfer
3.
Trigger bump and septum elements
4.
Start counting frev clock (sending/receiving accelerator)
5.
Start counting clock of fundamental periodicity
Start counting bucket clock
Fine delay
Ejection and injection kickers triggers
 Transfer

## Slide 75
Example: Turn count control at extraction
J-PARC rapid cycling synchrotron and main ring ratio: 4.5
Transfer possible once every two turns of main ring
Transfer of 4 times two bunches
Counter on frev of source (RCS) set normally
Counter on frev of source (RCS) delayed by one turn
Beam synchronous timing can also be used to control target azimuth (bucket number) of transferred beam

## Slide 76
Energy matching

## Slide 77
Energy matching of incoming beam
Ideal beam circulates with the expected revolution frequency (Df = 0) on the central orbit (DR = 0)  Dp = 0
Real beam behaviour is calculated using

## Slide 78
Energy matching of incoming beam
Ideal beam circulates with the expected revolution frequency (Df = 0) on the central orbit (DR = 0)  Dp = 0
Real beam behaviour is calculated using
Choice of two parameters from B, p, R, f directly constrains all others
o
o
o
Example: at fixed magnetic field (DB = 0), revolution frequency and radial position are directly linked

## Slide 79
Energy matching without RF
Observe de-bunching (no RF) with periodic trigger at n · frev
  Does the beam circulate with the expected frev?
  Does the beam circulate at the central orbit?
1.8 ms
1.8 ms
De-bunching with frev error
De-bunching expected frev
Changing B alone insufficient, since frev and R linked (const. p)
Change two parameters to fix the others, e.g., B and p or B and f
Badly matched,
DR  5.3 mm
Well matched,
DR  0 mm
All parameters are constrained
  Does the beam circulate
200 ns drift in 1.8 ms
Dfrev  50 Hz

## Slide 80
Longitudinal matching equations

## Slide 81
For a single harmonic RF system
with it becomes
using
The Hamiltonian simplifies to
Recap of longitudinal beam dynamics (1)

## Slide 82
In the centre of the bucket, particles move on elliptical trajectories in Df-DE phase space
Hamiltonian is constant on these trajectories
Aspect ratio of the elliptical trajectories must be identical in sending and receiving accelerator
Recap of longitudinal beam dynamics (2)
DE
Df
H = const.

## Slide 83
Compare two particles on the same trajectory
  No phase deviation 2. No energy deviation
Df depends on frequency  use physical duration Dt instead
Also replacing
Physical aspect ratio of bucket trajectories (1)
1.
2.

## Slide 84
Hamiltonian equal for both extreme particles, hence
which can be simplified to
This aspect ratio DE/Dt must remain unchanged at transfer
Physical aspect ratio of bucket trajectories (2)

## Slide 85
Equating for sending (1) and receiving (2) accelerator gives a general matching condition
For most cases (fixed energy and no particle type change)
It simplifies to the voltage ratio between RF systems:
Matched bunch-to-bucket transfer

## Slide 86
Phase space aspect ratio:
Simple matched transfer example
Transfer between to accelerators with fRF,2 = fRF,1/2
Source (1) bucket
Target (2) bucket

## Slide 87
Simple matched transfer example
Source (1) and target (2) buckets
Obvious case of matched bunch-to-bucket transfer
Phase space aspect ratio:
Transfer between to accelerators with fRF,2 = fRF,1/2

## Slide 88
Longitudinal matching

## Slide 89
Long. emittance is only preserved for correct RF voltage
Matched case
Longitudinal mismatch
Bunch is fine, longitudinal emittance remains constant
Dilution of bunch results in increase of long. emittance
Longitudinal matching at injection

## Slide 90
Longitudinal matching
Bunch is fine, longitudinal emittance remains constant
Dilution of bunch results in increase of long. emittance
Matched case
Longitudinal mismatch

## Slide 91
What is the difference?
Matching of phase and energy
-45° phase error at injection
Can be easily corrected by bucket phase
Equivalent energy error
Phase does not help: requires beam energy change

## Slide 92
Bunch length evolution
(Gaussian fit)
Mountain range
Intentional mismatch contributes to controlled longitudinal blow-up
Mismatch
Example: mismatch at injection to PS
Controlled blow-up
7.4 ms
Deliberate longitudinal mismatch at injection for blow-up

## Slide 93
No problem with electron accelerators
Synchrotron radiation damping matches bunches by itself
Phase and energy oscillations decay
f [2p rad]
Dp/p [%]
Septum blade
Proposed FCC-ee injection
R. Bailey, M. Aiba
LEP synchrotron injection
f
f
f
f
Circu- lating beam
Circulating beam
1st injection
2nd injection
1st turn
2nd turn
Mismatched injection can be a useful tool

## Slide 94
Summary
Basic techniques of signal synchronizations
  Beware of dividers
Beam transfer between circular lepton accelerators
  Constant frequency
Beam transfer between circular hadron accelerators
  Variable frequency
  Moving target
Follow the beam
  No need to measure  keep track
  Matching between accelerators

## Slide 95
A big Thank You
to all colleagues providing support, material and feedback
Masamitsu Aiba, Maria-Elena Angoletta, Kalantari Babak, Diego Barrientos, Philippe Baudrenghien, Chandra Bhat, Thomas Bohl, Craig Drennan, Roland Garoby, Christopher Gough, Steven Hancock, Stephan Hunziker, Andreas Jankowiak, Boris Keil, Karim Lihem, J. Molendijk, Holger Schlarb, Fumihiko Tamura, Frank Tecker, Daniel Valuch and many more…

## Slide 96
Thank you very much for your attention!

## Slide 97
References
R. Garoby, Timing Aspects of Bunch Transfer Between Circular Machines, State of the Art in the PS Complex, CERN PS/RF/Note 84-6, 1984, https://cds.cern.ch/record/2255149/files/Garoby_PS-RF-Note84-6.pdf
R. Garoby, Low level RF building blocks, CAS course, 1991, http://cds.cern.ch/record/225609
A. Gallo, Timing and Synchronization, CAS course, 2015, http://cas.web.cern.ch/cas/Poland2015/Lectures/Presentations/99Thursday08/Gallo.pdf
H. Schlarb, Timing and Synchronization, CAS course, 2013, https://cas.web.cern.ch/cas/Norway-2013/Lectures/Schlarb.pptx
F. Loehl, Timing and Synchronization, CAS course 2011, http://cas.web.cern.ch/cas/Greece-2011/Lectures/Loehl.pdf
C. Bovet et al., A selection of formulae and data useful for the design of A.G. synchrontrons, CERN-MPS-SI-INT-DL-70-4, 1970, http://cds.cern.ch/record/104153/files/cm-p00047617.pdf
S. Hancock et al., A Straightforward Procedure to achieve Energy Matching Between PSB and PS, CERN-AB-Note-2008-042, 2008, http://cds.cern.ch/record/1125475/files/AB-Note-2008-042%20MD.pdf
S.Hancock, Energy Matching Between LEIR and PS, CERN-ACC-NOTE-2015-0019, http://cds.cern.ch/record/2038693/files/CERN%20ACC%202015%20019.pdf

## Slide 98
For a single harmonic RF system
with it becomes
using
this simplifies to
Normalized Hamiltonian representation