## Slide 1: CREAM deployment Update on criteria for replacement of lcg-CE
Antonio Retico
Grid Deployment Board 11-Nov-09 - CERN

## Slide 2: Agenda
Status of the replacement criteria
CREAM in the production system
Plans for the next month
Good afternoon!

## Slide 3: The replacement criteria
List of criteria available at
  https://twiki.cern.ch/twiki/bin/view/LCG/LCGCEtoCREAMCETransition
Criteria for starting the full replacement of the LCG CE by the CREAM CE.
CREAM CE can (and should) be deployed into the production service

## Slide 4: Grouping the criteria
Technical features (B, C, G, Hi, Hii, I)
  Address new features and major change requests (tracking the due date)
  Set to ‘done’ when the functionality is delivered to production (wiki NOT used to track bugs)
Functional/Operational Requirements (A, Di, F, M, N, O)
  Validation mostly based on users’ and sites’ experience
  To be evaluated during ever increasing levels of deployment, VOs and use cases.
  Always open with “time-progress bar” (target date for replacement: December 2010)
Performance Requirements (Di, J, K)
  Address scaling beyond the scope of VO testing
  Need test rigs (later)

## Slide 5: Technical Features
Functional/Operational Requirements (A, C, Dii, E, F, G, L, M, O)
B: Condor-G developers now very active
  Plans and timelines set for CMS-related developments
  Good if ATLAS could test PanDA integration
  More in next talk
ID | Description | Status | Date | UPD
B | Submission via Condor-G | In progress (58%) | Jan 2010 ? | Y
C | ICE WMS in production | Done | Sep-2009 | N
G | Move away from using gJAF | Done | Mar-2009 | N
Hi | Integration with various LRMSs | In progress (80%) | Apr-2010 ? | N
Hii | new BLAH Parser available | Done | Oct-2009 | N
I | Process to integrate LRMs | Done | Jul-09 | N

## Slide 6: Functional/Operational Criteria
ID | Description | Status | UPD
A | Equivalent functionality wrt lcg-CE | In Progress (58%) | Y
Dii | ICE able to handle large peaks of jobs | In Progress (19%) | N
F | Monitoring infrastructure (SAM, metrics etc.) | In Progress (50%) | Y
M | Failures on CREAM due to reboot < 0.1% | In Progress (58%) | N
N | 1 month unattended running | In progress (58%) | N
O | Behaviour under heavy load | In Progress (58%) | N
A: Increasing VO activity
  Atlas starting tests in Milan ? ~35000 jobs submitted in 5 days
  CMS testing production workflows at T1s ? more in next talk
F: Monitoring (Alarms) and metrics (A/R) still to be enabled
F: SAM test reports late due to firewall issues on ICE
  Ports to be opened on the WMS/LB documented

## Slide 7: Performance Criteria
Functional/Operational Requirements (A, C, Dii, E, F, G, L, M, O)
Di: benchmark to be set-up again closer to the replacement date
ID | Description | Status | Date | UPD
Di | ICE  CREAM vs. WMS  lcg-CE | Frozen | May 2010 ? | N
J | 5000 simultaneous jobs per CE | Done | Jul-2009 | N
K | Multiple user/role combinations | Done | Jun-2009 | N

## Slide 8: Status of deployment
CREAM in the production system

## Slide 9: News and issues
WLCG MB requested the sites to publish CREAM as 'Production' instead of ‘Special’
  Request moved to the EGEE ROCs in SA1
  Now monitoring the change
Alarms and availability/reliability metrics not yet in use
  Services in Validation still unstable (issues with SAM as well)
  Algorithms to calculate site a/r still to be defined
CREAM for SL5 still missing  sites holding back
  Certified today 
SA1 set a timeline for the EGEE ROCs to have all the sites running CREAM by the end of March 2009

## Slide 10: Monitoring
SAM test in Validation available
  http://tinyurl.com/creamtests
Some GGUS tickets opened (and some closed)
  Still half sites failing though
SAM WMS malfunctioning
  Port 7010 needs to be opened at CERN
  Results possibly affected by delays in status update

## Slide 11: MB milestones for CREAM CE (From GDB 10th Jun)
  June 1st:
  All European T1 + TRIUMF and CERN; at least 1 CREAM CE each.
  5 T2s supporting ALICE with 1 CREAM CE each
  August 1st:
  At least 2 T2s for each experiment providing 1 CREAM CE each
  October 1st:
  50 sites providing CREAM CEs in addition to the ones above

## Slide 12: CREAM in production (data 11-Nov-09)
Scope | # Sites |  | T1 |  | T2 |  | # Nodes |  | T1 |  | T2 |  | Notes
All PROD | 34 | (+7) | 7 | (=) | 25 | (+7) | 42 | (+8) | 16 | (=) | 26 | (+10) | 
CMS | 14 |  | 5 |  | 9 |  | 19 |  | 9 |  | 10 |  | 
ALICE | 26 |  | 5 |  | 21 |  | 31 |  | 9 |  | 22 |  | 13 sites usable with VOBOX (=)
LHCb | 15 |  | 4 |  | 11 |  | 22 |  | 9 |  | 13 |  | 
ATLAS | 17 |  | 5 |  | 12 |  | 23 |  | 10 |  | 13 |  | 
OPS | 32 |  | 8 |  | 24 |  | 39 |  | 14 |  | 25 |  | 
(n): difference wrt to last sampling) |  |  |  |  |  |  |  |  |  |  |  |  | 
N: less then expected by MB |  |  |  |  |  |  |  |  |  |  |  |  | 
N: equals or more than expected by MB |  |  |  |  |  |  |  |  |  |  |  |  | 
GlueCEStateStatus |  |  |  |  |  |  |  |  |  |  |  |  | 
Production |  | 16 |  |  |  |  |  |  |  |  |  |  | 
Special |  | 22 |  |  |  |  |  |  |  |  |  |  | 
Other |  | 4 |  |  |  |  |  |  |  |  |  |  | 

## Slide 13: Plans
More CREAM service in the infrastructure
  With Status= “Production”
Deployment of alarms and a/r metrics
  Make the services in Validation work
  Propose site a/r algorithms to MB
Deploy CREAM on SL5
Follow-up CMS and Atlas testing issues

## Slide 14: Questions?
?