## Slide 1: The New CLIC Detector Simulation Model
Nikiforos Nikiforou
CERN/PH-LCD
on behalf of the CLICdp collaboration
LCWS2015:
International Workshop on Future Linear Colliders
Whistler BC Canada,
November 2nd 2015

## Slide 2: CLIC Physics Goals Detector Requirements
Momentum resolution
  e.g., Higgs coupling to muons
Jet energy resolution
  e.g. Separation of W/Z measurement in di-jet events
    for
Impact parameter resolution
  -tagging, Higgs branching ratios
Angular coverage
  Very forward electron tagging
    down to
Requirements due to CLIC beam structure and beam-induced backgrounds
e.g. W/Z
separation
e.g.

## Slide 3: Evolution of Detector Designs
Concept\Key param. | ILD (ILC) | CLIC_ILD | SiD (ILC) | CLIC_SiD | CLICdet_2015 (3 TeV) | CMS
Tracker | TPC/Silicon | TPC/Silicon | Silicon | Silicon | Silicon | Silicon
Solenoid Field [T] | 3.5 | 4 | 5 | 5 | 4 | 3.8
Solenoid Free Bore [m] | 3.3 | 3.4 | 2.6 | 2.7 | 3.4 | 3.0
Solenoid Length [m] | 8 | 8.3 | 6 | 6.5 | 8.3 | 13
VTX Inner Radius [mm] | 16 | 31* | 14 | 27* | 31* | 40
ECAL Inner Radius [m] | 1.8 | 1.8 | 1.3 | 1.3 | 1.5 | 1.3
ECAL ∆R [mm] | 172 | 172 | 135 | 135 | 159 | 500
HCAL Absorber B / E | Fe | W / Fe | Fe | W / Fe | Fe | Brass
HCAL λI | 5.5 | 7.5 | 4.8 | 7.5 | 7.55 | 5.8 Barrel/10 EC
Overall Height [m] | 14 | 14 | 12 | 14 | 12.8 | 14.6
Overall Length [m] | 13.2 | 12.8 | 11.2 | 12.8 | 11.4 | 21.6
For the CLIC CDR (2012): Two general-purpose CLIC detector concepts
Based on initial ILC concepts (ILD and SiD) but optimized and adapted to CLIC conditions
* For a variant with a VTX inner radius smaller by 6 mm is foreseen

## Slide 4: Simulation Model in Software
New detector model implemented and being refined in DD4hep with relative flexibility/scalability
  New package LCgeo holds model implementation
Developing simulation and reconstruction software based on DD4hep in collaboration with ILD
  Other relevant talks:
    Joint ILD/ SiD/CLICdp session on simulation tools and reconstruction algorithms: Tuesday afternoon
    Simulation/Performance/Reconstruction sessions: Tuesday morning
    Vertex/tracking joint session with Simulation/Performance/Reco: Thursday afternoon
See talk by M. Petric
(Thursday morning)

## Slide 5: Proposed Layout in New Detector Model
Return yoke (Fe) with detectors
for muon ID
Solenoid Magnet, ,
Main tracker, silicon-based (large pixels and/or strips)
Ultra low-mass
vertex detector
with 25 μm pixels
11.4 m
Forward region with LumiCal and BeamCal
Fine grained calorimetry used in Particle Flow (PFA), Depth: 1 + 7.5

## Slide 6: Magnet System Layout
To be added
B-field axial component with and without end coils as function of z
Use the end coils to compensate for thin endcaps
Quarter view of the magnet system with “thin” yoke Endcaps
Note 4 concentric ring end coils in blue
Tracker

## Slide 7: Forward Region Layout in the New Model
LumiCal
BeamCal
(incl. graphite)
ECAL plug
500 mm
1000 mm in old design!
HCal
(with cutout for LumiCal)
Wanted to extend HCal Endcap coverage closer to beampipe
Reoptimized for a working hypothesis of an QD0 outside detector region
  Simplified services, no need for an anti-solenoid
  No need for rigid support
  Smaller support outer radius: 250 mm (was 500 mm)

## Slide 8: Vertex Detector: Reminder
Flavor tagging was used as a gauge in various tests :
Effect of material (most significant effect on performance)
Vary inner radius (dictated by background rates B-field)
Effect of spiral geometry (only small impact)
Single vs. double layers (minor impact)
In the new detector model:
Double layers (benefits for support)
per (single) layer
Spiral geometry in the endcaps (better airflow)
Pixel size: 25
3single point resolution
See talks during CLICdp meeting with emphasis on Vertex/Tracking (Thursday morning)

## Slide 9: Silicon Tracker
We use an All-Silicon Tracker for our new model
  A TPC tracker would have very high occupancies (30%) for CLIC @ 3 TeV with 1x6 mm2 pads (without safety factors)
Fast Simulation (LicToy) studies varying geometry and layout (R, length, number of layers, etc) as well as material (supports, cabling, cooling)
  Use and resolution to gauge performance
Key parameters currently implemented:
  Material Budget: between and per layer
    Requires very thin materials/sensors
    Less critical than in Vertex Detector
  Single point resolution:
Full simulation studies ongoing with new Reconstruction Software
See talk by R. Simoniello
(Thursday afternoon)

## Slide 10: Silicon Tracker Radius/ B-field
B [T]
Can compensate a change in by rescaling by
B-Field and R also affect Particle Flow Performance
  Previous ILD studies by M. Thomson and J. S. Marshall [4,5]
A magnetic field strength of up to 4.5 T should be technically feasible
Converged to an outer tracking radius of 1.5 m and field strength of 4 T
Tracker length: at least like CLIC_ILD ( 4.6 m)
    Motivated by physics in the forward region (e.g. Higgs self-coupling)
    Reduce Endcap Yoke thickness by and use end coils
CLICdp Work In Progress
CLIC_SiD
CLICdet_2015

## Slide 11: Si Tracker Layout
5 “short” Barrel layers
  First layer at
7 “flat” Endcap disks (full )
  New First disk at
Arranged in an Inner and Outer Tracker
  Support tube for extraction with beampipe assembly
CLICdp Work In Progress
At least 8 hits (Vertex + Tracker) for θ> 8ο
Module arrangement and overlap still under investigation
Cell size should vary from layer to layer
  Motivated by occupancy (next slide)
4.6 m
2.9 m

## Slide 12: Tracker: Open Issues
Probably use gradually longer strips in layers
  Oriented along for barrel (endcap)
  Length ,
  Considering large pixels () for first endcap disk
Sensor Technology?
Power pulsing!
Air cooling not feasible in a large tracker volume
Use of liquid cooling restricts also options for module geometry/layout/overlap!
  Material budget for cooling and supports already implemented in model
Tracker hardware R&D recently started
See talk by A. Nurnberg (Thursday afternoon) and talks in the CLICdp meeting (Thursday morning)

## Slide 13: ECal Optimization
# Layers: Not very important for higher energy jets (PFA confusion dominates): Not much more improvement from 25 to 30 layers
  Keeping
Si vs Sc: No significant effect on JER
Cell size: JER degradation from 3% to ~3.5% when increasing cell size from 5x5 mm2 to 15x15 mm2
  Combinations of different granularities in layers considered
    No significant gain for the extra complexity
M. Thomson, J. S. Marshall [5,7]
In new simulation model:
Tungsten absorber, Silicon active material
25 Layers, 23 / 1
  17× 2.4 mm + 8 × 4.8 mm
Use 5.1x5.1 mm2 cells throughout
(Scintillator)
nLayers

## Slide 14: HCal Optimization
Example: HCal Barrel Absorber
  10 mm Tungsten (W)
  19 mm Steel (Fe)
Full Geant4 detector simulation + PandoraPFA + FastJet
JER Performance shown to be similar for tungsten and steel
  Steel is cheaper and easier to process
Keep same
Depth at
Use Steel as an absorber for the entire HCal
  60 layers
  20 mm Steel (1 mm in cassette)
  3 mm Scintillator
  30x30 mm2 Cell size
E.g. study overlap of and measurement in and events
Chart: 
| 250 | 500 | 1000 | 2000
19Fe_60L | 20.5465 | 16.0542 | 13.182 | 18.2938
10W_70L | 19.4088 | 16.8406 | 12.7232 | 17.7179
19Fe_60L + 60 BX Ov | 25.8017 | 20.5313 | 20.2829 | 24.7724
10W_70L + 60 BX Ov | 25.377 | 21.2794 | 19.7713 | 25.373
Chart: 
| 250 | 500 | 1000 | 2000
19Fe_60L | 20.5465 | 16.0542 | 13.182 | 18.2938
10W_70L | 19.4088 | 16.8406 | 12.7232 | 17.7179
19Fe_60L + 60 BX Ov | 25.8017 | 20.5313 | 20.2829 | 24.7724
10W_70L + 60 BX Ov | 25.377 | 21.2794 | 19.7713 | 25.373
Adding background
CLICdp Work In Progress
The shaded area gives one of the points on the plot below. Repeat for both models, all energies. Do also with background.
[GeV]
Entries/1 GeV
19 mm Fe
No Overlay
Z
W

## Slide 15: More Calorimetry
CLICdp Work In Progress
The ECal and HCal combined present at least down to
  Does not include BeamCal/LumiCal
HCal Endcap now extended down to
  With some cutout for LumiCal
We found that is a good compromise between letting in more background and increased acceptance
  Studied in events with overlay for various HCal Endcap inner radii
12-fold inner and outer symmetry for ECal/HCal/Yoke
CLICdp Work In Progress

## Slide 16: Summary
New simulation model for a detector at CLIC evolving from previous CDR models based on modified ILC designs
  Longer All Silicon Tracker, , , thinner endcap yoke with end coils
  25 layer W+Si ECal, 60 layer Fe HCal, 12-fold symmetry
Optimization result of a big effort from many people and still ongoing
  Important R&D efforts also ongoing (not covered in this talk)
Model implementation in DD4hep up to date
  Reconstruction software developed in parallel
Full simulation physics studies with the new software chain will start soon

## Slide 17: Backup Material

## Slide 18: References
L. Linssen et al., Physics and Detectors at CLIC : CLIC Conceptual Design Report, CERN-2012-003
N.Alipour Tehrani and P. Roloff, Optimisation Studies for the CLIC Vertex-Detector Geometry, CLICdp-Note-2014-002
D. Dannheim et al., Slides at https://indico.cern.ch/event/309925/contribution/2/material/slides/0.pdf
M. Thomson, Nucl.Instrum.Meth. A611 (2009)
J. Marshall, Slides at http://indico.cern.ch/event/309926/contribution/1/material/slides/0.pdf
B. Cure, Slides at https://indico.cern.ch/event/314325/contribution/1/material/slides/1.pdf
M. Thomson, Slides at http://indico.cern.ch/event/309926/contribution/1/material/slides/0.pdf
M. Valentan et al, LiC Detector Toy Fast Simulation
R. Simoniello, Slides at https://indico.cern.ch/event/376800/session/3/contribution/5/material/slides/0.pdf
A. Nurnberg, Slides at https://indico.cern.ch/event/376800/session/2/contribution/28/material/slides/0.pdf
M. Killenberg, LCD-Note-2011-029
J. S. Marshall, Slides at https://indico.cern.ch/event/336335/session/6/contribution/5/material/slides/0.pdf
F. Gaede, Slides at https://indico.cern.ch/event/376800/session/0/contribution/12/material/slides/0.pdf
M. Petric, Slides at https://indico.cern.ch/event/376800/session/0/contribution/11/material/slides/0.pdf
D. Dannheim, A. Sailer, Beam-Induced Backgrounds in the CLIC detectors, LCD-Note-2011-021
E. van Der Kraaij, Detector challenges at CLIC, contrasted with the LHC case, slides at http://indico.cern.ch/event/210720/

## Slide 19: CLIC and Detector Documentation
CERN-2012-007
CERN-2012-003
CERN-2012-005
arXiv:1307.5288
2012: CLIC Conceptual Design Report published
2012: CLIC detector and physics collaboration (CLICdp) was set up
2012/2013: CLIC input to the European strategy and the Snowmass Process in the US

## Slide 20: The CLIC Experimental Environment
Drive timing requirements for the CLIC detector
 | CLIC at 3 TeV
Luminosity | 5.9×1034 cm-2s-1
Bunch separation | 0.5 ns
#Bunches per train | 312
Train duration | 156 ns
Train repetition rate | 50 Hz
Particles per bunch | 3.72 ×109
Crossing angle | 20 mrad
σx / σy [nm] | ≈ 45 / 1
σz [μm] | 44
- not to scale -
CLIC bunch structure
1 train = 312 bunches, 0.5 ns apart
20 ms
156 ns
Very small beam profile at the interaction point
Very high E-fields
Beam-beam background
Low duty cycle
  Triggerless readout
  Power pulsing (turning power off when not needed)

## Slide 21: Beam-Induced Backgrounds
Beamstrahlung:
  Pair-background
    Coherent e+e- pairs
      Very forward
    Incoherent e+e- pairs
      Rather forward
      High occupancies influence detector design
  γγ to hadrons (3.2 events/BX @ 3 TeV)
    Energy deposits (19 TeV/train @ 3 TeV)
    Main background in calorimeters and trackers
tracker

## Slide 22: More on Beam-Beam Effects
Beamstrahlung can cause important energy losses
right at the interaction point
E.g. full luminosity at 3 TeV:
5.9 × 1034 cm-2s-1
Of which in the 1% most energetic part:
2.0 × 1034 cm-2s-1
Most physics processes are studied well above production threshold => profit from full luminosity
energy spectrum at

## Slide 23: CLIC power and energy consumption

## Slide 24: CLIC_ILD and CLIC_SiD
CLIC_ILD
CLIC_SiD
7 m
For the CLIC CDR (2012):
Two general-purpose CLIC detector concepts
Based on initial ILC concepts (ILD and SiD)
Optimized and adapted to CLIC conditions

## Slide 25: Vertex Detector: double layers
Estimate changes in performance due to layout by studying the flavor-tagging performance (N. Alipour Tehrani, P. Roloff [2])
-quark misidentification as a function of -quark Identification efficiency with a background rich in -quarks (Top lines) or Light-Flavored quarks (bottom lines). Similar study performed for -tagging
Lower panel shows ratio of double-layer over the single-layer geometries
  Almost the same as single-layer layout
per double-layer in simulation
Spiral Geometry (better airflow)
Barrel: 5 single-layers3 double-layers
Endcap: 4 single-layers3 double-layers
Dijet events at

## Slide 26: Vertex Detector Optimization
Use flavor tagging as a gauge in various tests:
Effect of material (most significant effect on performance)
Test single vs. double layers
Vary inner radius (for 4 T or 5 T B-field)
Spiral Geometry (better airflow)
In the new detector model: Use double layers with spirals and modules with per (single) layer,
Effect of extra material:
Ratio > 1 means worse performance for more material
(N.Alipour Tehrani, P. Roloff [2])

## Slide 27: Vertex Detector : Effect of Inner Radius /Material
Double-layer modules were simulated with twice as much material
Extra material leads to undesirable increase of fake rate
(N.Alipour Tehrani, P. Roloff [2])
In the new detector model: Use double layers with spirals and modules with per (single) layer
Inner Radius from 27 mm to 31 mm
Compensates for increase in the rate of Incoherent e-pair background if B-field is reduced
Small effect in flavor-tagging performance
Dijet events at

## Slide 29: More Tracker Optimization (R. Simoniello[9])
Fast Simulation (LicToy) Study varying geometry and layout (R, length, number of layers, etc) as well as material (supports, cabling, cooling)
  Use and resolution to gauge performance
Full simulation studies also ongoing with new Reconstruction Software

## Slide 30: Silicon Tracker
A TPC tracker would have very high occupancies (30%) for CLIC @ 3 TeV with 1x6 mm2 pads (without safety factors)
  We use an All-Silicon Tracker for our new model
Fast Simulation studies (LicToy) to determine optimal parameters
Material Budget per layer
  Requires very thin materials/sensors
  Less critical than in Vertex Detector
Single point resolution:
  Critical for high-momentum tracks
See CDR and [11]
Fast simulation studies (LicToy) with CLIC_SID_CDR geometry (D. Dannheim et al. [3])

## Slide 31: TPC Occupancy in CLIC_ILD
From CDR. See also LCD-Note-2011-029 [11]

## Slide 32: Occupancy in the Main Tracker
High occupancies in certain regions
Full Mokka-based (Geant4) simulation using a modified CLIC_ILD detector driver (TPC replaced with Si Layers) – DDSim-based study ongoing
Assume strips, avg. cluster size 2.6 , safety factors 5 (pairs) and 2 ()
  Need for large pixels and/or short-strips
  Maximal strip length to be below 3% limit depends on layer (2 – 50 mm in barrel)
(Recent study by A. Nurnberg[10]. See also LCD-Note-2011-021[15])

## Slide 33: Silicon Tracker Radius/ B-field
Fast simulation studies (LicToy) with CLIC_SID_CDR geometry (D. Dannheim et al. [3])
Tracking performance depends on tracker radius and magnetic field
Can compensate reduction of in new detector by rescaling by
Increase from 1.3 m (CLIC_SID) but not much gain by going to 1.8 m (CLIC_ILD) -> Converged to 1.5 m for new model
Stronger dependence on

## Slide 34: Extended Tracker: Momentum Resolution Vs B-Field

## Slide 35: Tracking in an All Si-Tracker
Based on DD4hep/DDRec
Track Fitting Strategy:
  Fit inside-out starting with vertex pixel hits
    1D hits in main tracker (strips) provide no constraint inso cannot be used to initialize tracks
  Finally smooth back to third hit and fit inside from there
Current pattern recognition being developed from ILD Celloular Automaton-based Vertex patt. Rec.
F. Gaede [13]
R. Simoniello [9]
The (>19000) tracking surfaces in the CLIC model

## Slide 36: Calorimeters
Fit to a sum of two Landau Distributions
Fit to a single Landau Distribution
Simulated 10 GeV , uniform in
<detector name=“Solenoid" type=“Solenoid_o1_v01"
<detector name="HCalBarrel" type="HCalBarrel_o1_v01" readout="HCalBarrelHits">
<detector name="ECalBarrel" type="ECalBarrel_o1_v01" readout="ECalBarrelHits">
<detector name="HCalEncap" type="HCalEndcap_o1_v01" readout="HCalEndcapHits">
<detector name="ECalEncap" type="ECalEndcap_o1_v01" readout="ECalEndcapHits">
Fairly scalable drivers
Radii, Layer/module composition in compact xml
<detector ...>
...
<dimensions numsides=“HCal_symmetry" rmin="HCal_inner_R" z="HCal_half_L*2“ />
<layer repeat="(int) HCal_layers" >
<slice material="Steel235" thickness="0.5*mm“/>
<slice material="Steel235" thickness=“19*mm“/>
<slice material=“Polysterene" thickness=“3*mm“ sensitive=“yes“/>
<slice material=“PCB" thickness=“0.7*mm“/>
<slice material=“Steel235" thickness=“0.5*mm“/>
<slice material=“Air" thickness=“2.7*mm“/>
</layer>
</detector>
Second MIP from secondaries
Simulation and reconstruction under validation

## Slide 37: Background Suppression
Identify of physics event offline
  Correct for shower development and TOF, define reconstruction window around
  Pass all calorimeter hits and tracks within window to reconstruction
  Obtain physics objects with precise and cluster time information
Then apply cluster-based timing cuts
  Cuts depend on particle type, and detector region
  Protects high- physics objects
Also: use hadron collider-type jet algorithms (FastJet)
tCluster
Triggerless readout of entire train:
t0 of physics event

## Slide 38: General Requirements on Detector Technologies
CLIC conditions impact on detector technologies:
  High tracker occupancies need small cell sizes (beyond what is needed for resolution)
    Small vertex pixels
    Large pixels / short strips in the tracker
  Background suppression
    Need high-granularity calorimetry
    accuracy for calorimeter hits
    hit time-stamping in tracking
  Low duty cycle
    Triggerless readout
    Allows for power pulsing
      less mass and high precision in tracking
      high density for calorimetry

## Slide 39: Calorimeter Optimization
High granularity imaging calorimeters to use with Pandora Particle Flow Algorithms
Variations on Number and Layout of Layers, Cell size, absorber material and thickness, active material and thickness, total depth, …
Optimization performed also in collaboration with ILD
  Used mainly ILD-based Mokka drivers and ILD software chain
Need to recalibrate detector response with each variation
  Developed a quasi-automatic calibration procedure
Gauge model performance using:
  Single particle response
  Jet Energy Resolution (, )

## Slide 40: ECal Optimization (J.S. Marshall [12])

## Slide 41: ECal Optimization: Active Material, Number of Layers, Granularity
Scintillator instead of silicon may give a slightly better resolution
  Depends on active element thickness
  Also considered Si/Sc combinations
Stronger dependence on number of layers ()
ILD-based baseline model: SiW ECal with 29 layers (23 / 1 ):
    Tungsten absorber: 20x2.1 mm + 9x 4.2 mm
    Silicon Active material, 500 μm thickness, 5x5 mm2 cells
10 GeV photons
(ILD)
M. Thomson, J. S. Marshall [5,7]
(2 mm)
(0.5 mm)

## Slide 42: Extending the HCal coverage:
The peak is resolved better with smaller HCal inner radius
However, at 120 mm probably the increased background spoils the efficiency
  Investigated more the peak below
ZZ @ = 1 TeV ->
CLICdp Work In Progress