Update on the RTML
for an introduction to the RTML please see last years talks
	Overview
	Update on
▪ General layout and parameters
▪ Beam dynamics simulations
▪ Bunch compression system
▪ Booster linac
▪ Long transfer line
▪ Magnetic stray fields in the long transfer line
▪ Turn around loop
▪ Misalignment studies
▪ Phase stabilization
	Other Work in Progress

---
Overview / Functional Layout
BC2 RF and Chicane
IP
Spin Rotator
Main Linac
Long Transfer Line
Vertical Transfer
9GeV loop
Turn Around Loop
Booster Linac
BC1 RF and Chicane
Damping Rings
not shown: Diagnostics, Collimation, Dispersion Correction, Coupling Correction, Spectrometers and Dumps

---
General Layout / Parameters
	The general layout is unchanged.
	But in view of the CDR some open points have been decided:
▪ The spin rotator will be behind the turn around loop.
▪ The vertical transfer will not be included in the horizontal 9 GeV loop.
▪ The lattices should be suitable for CLIC3TeV and CLIC500 parameters (e.g. double charge).
	Nominal parameters have been slightly updated:
Property	Symbol	Value	Unit
Particle energy	E0	2.86	GeV
Bunch charge	Q0	0.65	nC
RMS bunch length	ss	1400	µm
RMS energy spread	sE / E0	0.1	%
Normalized emittance	en,x	500	nm rad
	en,y	5	nm rad
Property	Symbol	Value	Unit
Particle energy	E0	8 (9?)	GeV
Bunch charge	Q0	> 0.6	nC
RMS bunch length	ss	44	µm
RMS energy spread	sE / E0	< 1.5	%
Normalized emittance	en,x	< 600	nm rad
	en,y	< 10	nm rad
@ exit of damping rings
@ entrance of main linac
Tolerances (static and dynamic) need further discussions.

---
Beam Dynamics Simulations
	Lattice files have been created for the codes ELEGANT and PLACET.
	The sub-systems have been connected by simplified optics matching sections.
	Simulations of the full RTML, i.e. BC1, booster linac, long transfer line, turn around loop and BC2,
including incoherent synchrotron radiation (ISR) and short range cavity wake fields have
been performed. Later some CSR simulations were done (ELEGANT only).
	The agreement in the longitudinal plane is very good. In the horizontal plane
the emittance growth is Den,x=44 nm rad for ELEGANT and Den,x=57 nm rad for PLACET.
This difference seems to be due to differences in the application of wake fields.
Elegant
Placet

---
Beam Dynamics Simulations
	First simulations showed that CSR along RTML and wake fields in BC2 RF are too strong.
	To improve, the compression has been reduced in BC1 from 175µm to 300µm and
the BC2 chicane has been split in two parts.
	The emittance growth induced by ISR, CSR and wakes is reduce by a factor of two
and is now Den,x<100 nm rad.
CSR induced emittance growth Den,x along RTML:
no energy correction in lattice
with energy correction in lattice

---
Bunch Compressor 1
4 GHz, 170 MV (no wakes)
(172 MV to compensate wakes)
E0	2.86	GeV
ss	1400	µm
sE,unc /E0	0.1	%
1/E0 dE/ds	0	1/m
sE,tot /E0	0.1	%
E0	2.86	GeV
ss	1400	µm
sE,unc /E0	0.1	%
1/E0 dE/ds	-4.95	1/m
sE,tot /E0	0.7	%
E0	2.86	GeV
ss	300	µm
sE,unc /E0	0.47	%
1/E0 dE/ds	-17.4	1/m
sE,tot /E0	0.7	%
To improve performance of BC1:
	less bunch compression (reduces CSR in all beam lines up to BC2)
	larger than necessary energy chirp (under-compression), i.e. less R56 => less CSR
(the induced chirp would allow a compression to 200 µm)
1.5 m
11.5 m
1 m
30 m
∢4.65 deg
R56=-16.6 cm

---
Bunch Compressor 2
12 GHz, 1084 MV (no wakes)
(1200 MV to compensate wakes)
E0	8	GeV
ss	300	µm
sE,unc /E0	0.17	%
1/E0 dE/ds	-6.22	1/m
sE,tot /E0	0.25	%
E0	8	GeV
ss	300	µm
sE,unc /E0	0.17	%
1/E0 dE/ds	-37.5	1/m
sE,tot /E0	1.14	%
E0	8	GeV
ss	100	µm
sE,unc /E0	0.5	%
1/E0 dE/ds	-102	1/m
sE,tot /E0	1.14	%
E0	8	GeV
ss	44	µm
sE,unc /E0	1.14	%
1/E0 dE/ds	0	1/m
sE,tot /E0	1.14	%
To improve performance of BC2:
	utilize double chicane
	reduce bend angles where bunches are shortest, i.e. less CSR
	gain a lot flexibility to adapt to different parameter sets
	due to longer initial bunches less RF required, i.e. less wake fields
1.5 m
11.5 m
1 m
30 m
∢1.0 deg
R56=0.75 cm
1.5 m
11.5 m
1 m
30 m
∢1.49 deg
R56=-1.7 cm

---
Booster Linac
by D. Wang (IHEP, Beijing)
	Optimized lattice with respect to single-bunch wake fields and misalignment tolerances.
	Compared different lattices (FODO and Triplet focusing) using different number of cavities per cell.
	3-4 cavities of 3 m length per quadrupole in a FODO lattice seems to be a good compromise,
Den,y=2 nm rad after orbit correction (dispersion free or wakefield free steering),
sensitivity on misalignment of quadrupoles and cavities and BPM errors is rather relaxed.
	Multi-bunch wakes have been analytically estimated. They might become a challenge.
FODO 1
FODO 2
FODO 3
FODO 4
FODO 5
FODO 6
FODO 7
FODO 8
FODO 9
FODO 12
before orbit correction
after orbit correction
(Plots taken from EUROTeV-Report-2008-092)

---
Long Transfer Line
by B. Jeanneret (CERN)
	“Just” a simple FODO lattice. But due to its length (21 km) it has its own challenges.
	k1 < 0.01 m-2 to reduce chromatic dilutions, huge average beta function > 600 m.
	Resistive wall wake fields and fast beam ion instability have to be taken into account.
	To mitigate resistive wall wake fields a large beam pipe of 10 cm diameter is being used.
	To mitigate fast beam ion instability the vacuum must be better than 0.1 nTorr (G. Rumolo).
	Emittace dilution and beam mis-steering due to magnetic stray fields are a huge issue.

---
Magnetic Stray Fields
by J. Snuverink (CERN)
	Time varying, periodic stray fields are expected to be a major challenge.
	Purely random stray field should be a lot less important.
	Resonant behavior is expected at the wave length of the betatron oszillation.
	First simulations show exactly this behavior
but also some more complex structure which at least agrees with analytical estimations.
	There is a quite strong dependence on simulation setup,
i.e. periodic or random fields in vertical plane only or in both planes.
	We will have to continue and simulate many different cases,
i.e. periodic, random, periodic only over a certain length, in vertical plane only,
in horizontal plane only, both planes, different strengths,...

---
Magnetic Stray Fields
by J. Snuverink (CERN)
The peak corresponds to
an offset of the order of
millimeters.
Due to coupling also the
emittance grows when
horizontal and vertical
fields are simulated.
Tomorrow C. Jach will present an engineers view on this topic: “Magnetic Background Issues above 1Hz for CLIC beams”

---
Turn Around Loop
	Performance was already not really good and got worse with new parameters and
in start-to-end simulations.
	Revised lattice to improve performance, to meet CLIC500 specifications
and to lower quadrupole and sextupole gradients.
	Unfortunately, length increased to almost 1700 m.
	ISR emittance growth remained unchanged, ~30 nm rad @ 8 GeV, ~60 nm rad @ 9 GeV.
	It seems this lattice is good as a proof of principle, but not really optimum.
Sextupole
Dipole
QF Quad
QD Quad
z [m]
x [m]

---
Misalignment Studies
by S. Molloy (RHUL)
	Simulations done with the code LUCRETIA.
Lattice translated partly manually and partly automatic from ELEGANT lattice.
	Random quadrupole misalignment in all 6 dimensions by 10 µm or 10 µrad rms.
	BPMs with perfect resolution and perfect alignment to quadrupole center.
	Steered beam to zero the BPM readings (matrix inversion).
	Main challenge is the turn around loop.
	Very preliminary and BPMs too idealized!

---
Misalignment Studies
by S. Molloy (RHUL)
Horizontal
Vertical

---
Phase Stabilization
	In the current RTML layout R56,BC2 = 2.5 cm. Requiring a phase stability in front
of the main linac of Dj < 0.1 deg (= Dl < 7 µm) means the energy stability after the
booster linac must be DE/E0 < Dl / R56,BC2 = 3 × 10-4 in case there is no phase feed-forward.
	To mitigate this very tight requirement we can build in a feed-forward system.
	Or can we prevent energy jitter from converting	into phase jitter,
e.g. by clever beam line design?
	Such a beam line would require R56 = 0 but still has to compress the bunches.

---
Phase Stabilization
	For the second stage of the drive beam feedforward we foresee a scheme
with R56 = 0 but no compression of the bunches.
Final Re-compression,
Phase Correction
PETS
DBA 2
Final compression,
Phase Correction
First Re-compression,
Phase and Energy
Measurement
Uncompression
CR
DBA 1
Gun
First Compression,
Phase and Energy
Measurement

---
Phase Stabilization
left( stack{s_f # {%DELTA p_f} over p_0} right) = M left( stack{s_i # {%DELTA p_i} over p_0} right) phantom aaaaa M= left( matrix{R_{55} # R_{56} ## R_{65} # R_{66}} right)
In general:
matrix{%sigma_{sf}=sqrt{%sigma_{si}^2 R_{55}^2 + {%sigma_{pi}^2} over p_0^2 R_{56}^2} # {}#{}#alignl {}<s_f>{}=R_{55} {}<s_i>{} + R_{56} {}<{alignc {%DELTA p_i} over p_0>{}} ## {} # {} # {} # {} ## %sigma_{pf} over p_0=sqrt{%sigma_{si}^2 R_{65}^2 + {%sigma_{pi}^2} over p_0^2 R_{66}^2} # {}#{}#alignl {}<{alignc {%DELTA p_f} over p_0}>{}=R_{65} {}<s_i>{} + R_{66} {}<{alignc {%DELTA p_i} over p_0>{}}}

---
Longitudinal Transfer Matrix
To mimic part of the RTML we need four matrices:
BC2 chicane (M4), BC2 RF (M3), Turn Around Loop (M2),
some RF to add a variable momentum chirp to the incoming beam (M1)
M_4 = left( matrix{1 # -R_{56,2} ## 0 # 1} right) phantom aaa M_3 = left( matrix{1 # 0 ## u_2 # 1} right) phantom aaa M_2 = left( matrix{1 # -R_{56,1} ## 0 # 1} right) phantom aaa M_1 = left( matrix{1 # 0 ## u_1 # 1} right) newline newline alignl M=M_4 M_3 M_2 M_1
M = left( matrix{1-u_1 R_{56,1}-u_2 R_{56,2} - u_1 R_{56,2} + u_1 u_2 R_{56,1} R_{56,2} # {} # -R_{56,1}-R_{56,2}+u_2 R_{56,1} R_{56,2} ## {} # {} # {} ## u_1+u_2-u_1 u_2 R_{56,1} # {} # 1-u_2 R_{56,1} } right)
u= 1 over p_0 {dp} over {ds}
u1 = momentum chirp behind the booster linac
u2 = additional momentum chirp induced in the BC2 RF
R56,1 = momentum-compaction factor of the turn around loop
R56,2 = momentum-compaction factor of the BC2 chicane
in general :

---
Decouple Momentum and Phase
We assume a correct phase at the entrance, i.e. <si> = 0.
We request <sf> = 0 for any initial momentum offset:
alignl {}<s_f>{}={alignc R_{55} {}<s_i>{} + R_{56} {}<{alignc {%DELTA p_i} over p_0>{}} = 0 phantom aaa forall {}<{%DELTA p_i} over p_0>{} in setR} newline newline alignl {}drarrow{} R_{56}=0 newline newline alignl {}drarrow{} -R_{56,1}-R_{56,2}+u_2 R_{56,1} R_{56,2} = 0 newline newline alignl {}dlrarrow{} R_{56,1}={alignc R_{56,2} over {u_2 R_{56,2}-1}} newline newline alignl {}drarrow{} M= left( {alignc matrix{1-u_2 R_{56,2} # 0 ## u_2 + {alignc u_1 over {1-u_2 R_{56,2}}} # {alignc 1 over {1-u_2 R_{56,2}}}}} right) newline newline alignl {}drarrow{} %sigma_{sf} = %sigma_{si} (1-u_2 R_{56,2}) phantom aaaa u_2 = {alignc {%sigma_{si} - %sigma_{sf}} over {%sigma_{si} R_{56,2}}} phantom aaaa R_{56,1} = -R_{56,2} {alignc %sigma_{si} over %sigma_{sf}}

---
Full Compression
We assume that the initial momentum spread is purely uncorrelated.
We request that the final momentum spread is purely uncorrelated:
alignl {alignc %sigma_{pf} over p_0 = sqrt{u_f^2 %sigma_{sf}^2 + %sigma_{pfu}^2 over p_0^2} {}={}%sigma_{pfu} over p_0} newline newline alignl {}drarrow{} u_f=0
Since longitudinal emittance must be preserved:
alignl %sigma_{pf} %sigma_{sf} = %sigma_{pi} %sigma_{si} newline newline alignl {}dlrarrow{} {alignc %sigma_{pf}^2 over p_0^2 %sigma_{sf}^2 " "=" " %sigma_{pi}^2 over p_0^2 %sigma_{si}^2} newline newline alignl {}dlrarrow{} {alignc left( %sigma_{si}^2 R_{65}^2 + %sigma_{pi}^2 over p_0^2 R_{66}^2 right) %sigma_{si}^2 R_{55}^2 " "=" " %sigma_{pi}^2 over p_0^2 %sigma_{si}^2} newline newline alignl {}dlrarrow{} {alignc %sigma_{pi}^2 over p_0^2 %sigma_{si}^2 left( 1-R_{66}^2 R_{55}^2 right) " "=" " %sigma_{si}^4 R_{55}^2 R_{65}^2} newline newline alignl {}dlrarrow{} R_{65} = 0
R_{55}= 1 over R_{65}
Note that (see previous slide)!

---
Full Compression
alignl R_{65}=0 newline newline alignl {}dlrarrow{} 0 = u_1+u_2-u_1 u_2 R_{56,1} newline newline alignl {}dlrarrow{} 0 = {alignc {%sigma_{si} %sigma_{sf} - %sigma_{sf}^2 + u_1 %sigma_{si}^2 R_{56,2}} over {%sigma_{si} %sigma_{sf} R_{56,2}}} newline newline alignl {}dlrarrow{} 0 = {alignc {%sigma_{si} %sigma_{sf} - %sigma_{sf}^2 + u_1 %sigma_{si}^2 R_{56,2}}} newline newline alignl {}dlrarrow{} R_{56,2} = {alignc {%sigma_{sf}^2 - %sigma_{si} %sigma_{sf}} over {u_1 %sigma_{si}^2}} newline newline alignl {}drarrow{} R_{56,1} = {alignc {%sigma_{si} - %sigma_{sf}} over {u_1 %sigma_{si}}} = - {alignc %sigma_{si} over %sigma_{sf}} R_{56,2} newline newline alignl {}drarrow{} u_2 = -{alignc {u_1 %sigma_{si}} over %sigma_{sf}} newline newline alignl {}drarrow{} M = {alignc left( matrix{ %sigma_{sf} over %sigma_{si} # 0 ## 0 # %sigma_{si} over %sigma_{sf} } right) }
taken from original M
plugged in what we know already
\rbrace
Since bunch lengths are given by specifications
only a single free parameter is left over, here it is u1!
not strictly isochronous since isochronicity requires R55 = 1 and R56 = 0
(see K. Brown: R51 = R52 = R56 = 0 and implicitly R55 = 1).
But often R55 is forgotten and only R51 = R52 = R56 = 0 is asked for...

---
Phase Stabilization
	The calculations have show that to first order one can decouple incoming
energy jitter and outgoing phase while still achieving full bunch compression.
	The second stage of the drive beam feed-forward is a
special case with no compression.
	Beam lines and bunch parameters have to fulfill strict requirements.
	There must exist a momentum chirp u1 in front of the turn around loop.
It has to have the opposite sign of R56,2 of BC2.
	R56,1 of the turn around loop must have the opposite sign of R56,2.
	The additional momentum chirp u2 induced in the BC2 RF must have the
opposite sign of u1.
	One solution would be:
u1 = 4.0 m-1, u2 = -27.3 m-1, R56,1 = 21.3 cm, R56,2 = -3.13 cm
These values could be achieved with proper lattice design. To get a	positive u1
either BC1 has to over-compress or the booster linac has to run off-crest.
	Simulations using the code ELEGANT show that non-linearities, i.e. RF curvature
and higher-order transfer matrix elements, limit the applicability to 10-3 relative
energy stability behind the booster linac.

---
Phase Stabilization
	Only the phase jitter is mitigated.
	Incoming (i.e. after booster linac) phase jitter will be reduced by a factor ssf / ssi.
	Incoming (i.e. after booster linac) energy jitter will be amplified by a factor ssi / ssf.
This could become a limiting factor.
	Only requirements on accelerating cavities upstream are relieved.
The BC2 RF still has to fulfill tight tolerances (DfBC2RF < 0.05 deg).
	The setup is inflexible. Whenever one parameter changes
all others have to be adjusted.
	BC1 is not discussed at all. Since it has a huge R56,BC1 = 23 cm
we require DE/E0 < Dl / R56,BC1 = 3 × 10-5 after BC1 RF. If we consider
the factor ssf / ssi = 44/300 = 1/7 still DE/E0 < 2 × 10-4 ( = 600 keV) is required!
	For the energy stability behind the damping rings Yannis says this is o.k.
	But what about stability of BC1 RF?
	Fortunately, BC1 RF is weak (170 MeV) and we run at zero-crossing,
i.e. 0.2 deg @ 4 GHz required.

---
Other Work in Progress
	Vertical transfer:
Main concern are ISR and CSR since the vertical emittance is so small.
For the CDR a civil engineering concept must be found how to layout
vertical transfer and 9GeV loop.
	9GeV loop (K. Zengin, Ankara University):
For civil engineering reasons this might become a real loop not just an arc.
It should be similar to the turn around loop due to similar requirements
(or will the turn around loop become similar to this loop?).
	Diagnostics:
Positions and specifications are existing but might need some revisions.
Some of the systems should be studied in detail, e.g. emittance measurement
	Spin rotator (hopefully N. Solyak, Fermilab):
Nothing has been done in the past. We hope that Fermilab collaborates. If not
and we don't find another collaborator we will not have it for the CDR.
	More work we have to do:
Collimation, Feedback and Feedforward, Field error tolerances, ...