## Slide 1: Large Momentum Acceptance Superconducting and Permanent Magnet Non-Scaling FFAG Gantries
Dr. Dejan Trbojevic
Brookhaven National Laboratory

## Slide 2
OUTLINE:
- Requests and Challenges
- Introduction: NS-FFAG?
- Carbon Gantries
- Proposal to the DOE
- Summary: smaller, less weight, simpler, large dp/p
- Proton Gantries
- Permanent Magnet Gantry

## Slide 3: INTRODUCTION
Future gantries for the ion cancer therapy need to have large momentum acceptance - longitudinal scanning - conclusions from the ion cancer workshop organized in January 2013, by NIH (US National Institute of Health), NCI (US-National Cancer Institute), DOE. Efforts should be put on: reducing the gantry cost, size, and complexity of operation.
Work on markers to be used for in city during the real time of treatment to provide information on ion-tumor interaction but also on the very low intensity beam measurements: precise dose, beam position, profile, and energy. There are some simple ideas at BNL of using the vacuum windows for determining the beam position, beam transverse profile and even the intensity (dose). For the reduction of size in both carbon or proton gantries the superconducting magnets are clearly needed. The larger the field the smaller the size.
S.A.D (Virtual–Source–to patient distance) without large magnets (Except the second scanner magnet still large 20 (30) cm aperture.

## Slide 4
What is the OBJECTIVE?
- Reduce the size of the gantry
- Improve its performance
- Reduce the cost
- Allow large energy range
The NEW carbon ion gantry replaces the 135 ton magnets of the Heidelberg gantry with smaller BNL superconducting magnets.

## Slide 5: Range of momentum = range kinetic energy
ΔEk carbon=400-195.4 MeV/u [27.3-8.2 cm]
ΔEk carbon=195.4-91.5 MeV/u [8.2–2.2 cm]
ΔEk proton=250-118.81 MeV [37.8-10.4 cm]
ΔEk proton=118.81-54.6 MeV [10.4-2.6 cm]
Permanent proton gantry
Superconducting
carbon/proton gantry

## Slide 6
?
MAKE IT SMALLER YET HIGHLY EFFECTIVE!
Two properties were annoying:
VERY LARGE MAGNET SIZE
30% OPPOSITE BEND - INNEFICIENT
Dx = Dx  dp/p

## Slide 7: EMMA the first Non-Scaling FFAG (Electron Model for Many Applications) Daresbury Laboratory
LEARNING FROM PREVIOUS EXPERIENCE FROM WORKING NON-SCALING FFAG “EMMA”
(Being aware that EMMA is a much more difficult application of FFAG than eRHIC in many ways)
ELECTRON ENERGY RANGE IN EMMA WAS BUILT TO SIMULATE MUON ACCELERATION 10 – 20 GeV

## Slide 8
The Principle of NS-FFAG-Used here for Hadron Therapy Gantry
has been selected for the Future Electron-Ion Collider
eRHIC at BNL
N
A new Energy Recovery Linac with the Non-Scaling Fixed Field Alternating Gradient arcs and straight sections is to be built at Cornell University Physics Department an eRHIC prototype

## Slide 9: eRHIC FFAG Rings in Perspective
Orbits exaggerated transversely 5000x, shape of hexagonal RHIC is evident
© Stephen Brooks

## Slide 10: Detector Bypass Scheme: a Flexible FFAG
-Dq
Dq
Dq
Curvature
Bypass straight
Normal straight
Dq
-2Dq
Angle
Displacement
3.08m
76 cells
3
9
9
17
9
9
3
17
90.3m

## Slide 11: Merging FFAG arcs to the straight section in eRHIC
7.75 mm

## Slide 12
3.2 m
3.2 m
The state of the art proton gantry at PSI

## Slide 13: The state of the art proton gantry at PSI

## Slide 14: SAD – SOURCE-TO-AXIS-DISTANCE VIRTUAL Source to Patient Distance Scanning system: patented by BNL
The maximum dose to the patient surface relative to the dose in the SOBP
increases as the effective source-to-axis distance (SAD) decreases. For a fixed,
horizontal beam, large SAD's are easy to achieve; but not for gantry beam lines. A smaller gantry with a physical outer diameter of less than 2 meters may have important cost implications. Such a gantry would require magnetic optics to ensure that the effective source-to-axis distance is large enough to provide adequate skin sparing.
S
Axis
S
Axis
S
Axis
S
Axis

## Slide 15: Permanent Halbach Magnet NS-FFAG Proton Gantry 35-250 MeV

## Slide 16: Halbach Permanent Magnet Gantry
3.8 m
63.4o
The Basic Cell
Magnified Orbit Offset for
35 MeV – 250 MeV protons

## Slide 17: Permanent Halbach Magnet NS-FFAG Proton Gantry
250 MeV
35 MeV

## Slide 18: Orbits in 3D in half of the Superconducting Gantry

## Slide 19: Gantry Halbach Magnet Design (Nick Tsoupas –BNL)
G=100 T/m

## Slide 20: Gantry Halbach Magnet Design (Nick Tsoupas-BNL)
GD=-90 T/m
BD=1.63 T
30mm

## Slide 21: Gantry New Halbach type Magnet Design (Stephen Brooks)
Routside=13.7 cm
Rinside =1.17 cm
Bdipole =1.6 T
GD = 90 T/m

## Slide 22: Built Models of Defocusing Modified Halbach Magnet

## Slide 23: Modified Halbach magnets for BNL eRHIC

## Slide 24: State of the art C-gantry at Heidelberg
Weight of the transport components – 135 tons
Total weight = 630 tons - 19 m long. WEIGHT and SIZE

## Slide 25: Carbon Ek=400 MeV/u  Br = 6.35 Tm ( q= Bl/Br ) Warm iron magnets: B=1.6 T then r ~ 4.0 m Superconducting magnets B=3.2 T then r ~ 2.0 m
4.1 m
8.6 m
20.8
DIMENSIONS of the CARBON GANTRY
4.09 m

## Slide 26: Very strong focusing Basic Cell
62 cm
QD/2
QD/2
B
QF
B
LBD=27/2 cm
LQF=27 cm
400 MeV/u
10.1 mm
-4.6 mm
LBD=27/2 cm
4 cm
4 cm
5.9 mm
9.4 mm
dp/p=-18%
210 MeV/u
dp/p=18%

## Slide 27: Reducing the size and weight from: 135 tons  to 3 tons
72o
4.09 m
2.9603 m
2.6 m
Magnified 10 cm
0.4
0.3
0.3
2.3 m
0.41
1.49 m
7.52 m
2.9603 m
h
a.
b.
c.
d.

## Slide 28: 72o Achromatic part of the Superconducting Gantry Brett Parker - BNL
62 cm

## Slide 29: Tools and quadrupole windings (Brett Parker – BNL)

## Slide 30: Achromatic Part of the Superconducting Gantry (Brett Parker – BNL)

## Slide 31: Brett Parker -BNL

## Slide 32: Dipole winding (close-up) (Brett Parker – BNL)

## Slide 33: Magnetic field of the Superconducting Gantry (Brett Parker – BNL)
Total volume of iron
V1=0.2611 m3
r=7870 kg/m3
Weight~2.055 tons
+ ~1 ton for cryostat

## Slide 35: CARBON GANTRY h=4.091m without magnification
216 MeV/u
292 MeV/u
400 MeV/u

## Slide 36
3.0503 m
6.84166 m
0.5 m
3.7913 m
2.7607 m
Magnified x10 =±10cm

## Slide 38: CRYO-COOLERS: reliable, maintenance free, easy to operate

## Slide 39: SUMMARY

## Slide 40: SUMMARY:
NS-FFAG gantries provide transfer of carbon ions with large momentum range: dp/p=± 20% (200-400 MeV–or-100-200 MeV) allowing longitudinal scanning as fast as the front accelerator can change the energy of the beam because the magnetic field is fixed for the required energy range
Weight is reduced for one or two orders of magnitude
Size of NS-FFAG the carbon gantry is of PSI proton one
Operation is simplified as the magnetic field is fixed
Scanning system is with SAD=∞
Beam size is adjustable with the triplet magnets
Triplet magnets do not need to be superconducting