## Slide 1: New MPGD Connector
Hans Muller CERN

## Slide 2: Motivation for new connector
Pansonic 130 pin connectors not produced any more
Panasonic 130 pin only available in large Qty
Pansonic 130 pin has only 2 GND pins
HRS 140 pin very similar, in production
HRS 140 pin available in single Qty
HRS 140 pin has GND pins every 10 position
HRS 140 pin allows for new functionality: 12 spare pins

## Slide 3: Lateral dimensions FX10A-140S
Fits on 50 mm wide hybrids

## Slide 4: Height dimensions

## Slide 5: HRS Manufacturer Specs http://www.hirose-connectors.com
FX10 series 0.5mm pitch
ICR Insertion Loss Ratio meets IEEE 802.3ap for 15+ Gbps

## Slide 6: New Hirose connector as from VMM-128 v3
Rui will start new connector on MPGD’s when adapters for transition period become available
Altium design A.Rusu

## Slide 7: Adapters for transition time
Flex PCBs to be designed ( A.Rusu) for both versions

## Slide 8: New Hybrid with HRS plugged on detector with old Panasonic connector

## Slide 9: Old Hybrid with Panasonic plugged on detector with new Hirose connector

## Slide 10: New functionalities a.) geographic address position
+2V5
FPGA
Detector Frame
Position coding by GND / No GND
Example Position = 10 0001
6
Readout via
slow controls SRS
6 code pins on right side viewed from top
TOP
Detector side
10k pullups
VMM hybrid
Will allow to read the geographical
position of a hybrid along a detector frame

## Slide 11: New functionalities b.) optional I2C devices on detector
Detector Frame
6 x I2C support pins on left side, viewed from top
TOP
Detector side
+2V5
FPGA
I2C device control and readout
via
slow controls SRS
VMM hybrid
gnd
Vcc
scl
sda
S-in
S-out
I2C device
6pin connector plugin
Will allow to place and
use intelligent sensors on the detector

## Slide 12: Examples I2C chips for potential use on detectors
ROHM color sensor BH1745NUC
Sensirion SHT25 Humidity and Temperature sensor
Analog Devices ADT7301ARTZ-500RL7 temperature sensor
Vishay Proximity and ambient light detector VCNL4010
Texas Instruments LED driver (up to 11 in series) with ambient sensing LM3530
MAX ambient light sensor 0.025 Lux to 104,448 Lux MAX44007