## Slide 1: SHIP Test Beam Oct-Nov 2015 G.Bencivenni LNF-INFN, Italy
LABORATORI NAZIONALI DI FRASCATI
www.lnf.infn.it

## Slide 2
Beam Test Setup
µ-RWELL detector
GEM detector
Emulsion
bending plane
No-bending plane
trigger scintillators and GEM trackers outside Goliath
setup was foreseen two kind of electronic detectors, both independently coupled with emulsion set-up:
a large drift gap XY GEM
two 1-D µ-RWELL coupled at 90° to supply XY info
beam set-up displaced wrt the beam axis of 10 cm in order to reduce the irradiation of the emulsion units
tracking with linear fit
track residual w/COG
analysis code by INFN - Ferrara
not delivered
GOAL: study of the matching between emulsion and electronic tracker

## Slide 3
Emulsion Target Units
The Emulsion Cloud Chamber (ECC)
The Compact Emulsion Spectrometer (CES)
The Emulsion Doublet (CS – Changeable Sheet)

## Slide 4
Emulsion Films
Film dimensions
      Surface: 125 mm x 100 mm
      Total thickness: 290 μm
New emulsion gel developed in Nagoya University
      Grain density: 50 grains/100 μm (higher than OPERA films)
Emulsion production
    Emulsion poured in middle August 2015 and cut by hand
    Shipped to CERN by plane
    Total amount of emulsion films produced: 120
    Emulsion films used in the Emu+GEM test beam: 30
Emulsion films produced in Nagoya University
60 μm
60 μm
170 μm

## Slide 5
CS exposure
Aim: study of the GEM space resolution with external track point (coming from the two CS) reconstructed with precision at level of few µm
θ
x
B=1T
7.5°
15°
30°
45°
0°
θ
.
B=1T
7.5°
15°
30°
45°
0°
Target: 2 x CS
Magnetic Field: + 1T
Target: 2 x CS
Magnetic Field: - 1T
Exposure 1
Exposure 2
Experimental setup: #2 CS attached on GEM upstream and downstream surfaces
      Low density: 50 tracks/cm2/angle
      5 exposure angles

## Slide 6
CES exposure
Target: 1 CES + 1 CS (Emulsion doublet)
      Low density: 100 tracks/cm2/angle
      6 exposure angles
      No magnetic field
θ
7.5°
15°
30°
45°
0°
Aim: track matching between GEM and CES (Emulsions interleaved with Rohacell)
-30°

## Slide 7
ECC exposure
Target: 1 ECC + 2 CS (Emulsion doublet)
      Low density: 100 tracks/cm2/angle
      6 exposure angles
      No magnetic field
θ
7.5°
15°
30°
45°
0°
Aim: track matching between GEM and ECC (Emulsions interleaved with Lead)
-30°

## Slide 8
COG method:
XY(elect) position from electronic detector is compared/matched with the XY(emu) by the emulsion unit.
It works only with small angle & low B field.
t1
t2
t3
Micro-TPC mode:
direct comparison/matching between the track_segment (elect) reconstructed by the electronic detector and the track_segment (emu) finely reconstructed by the emulsion unit.
It works well also at large angle & high B field
Electronic tracker & Emulsion matching
The electronic tracker should provide the time stamp to the event reconstructed by the emulsion unit

## Slide 9
Electronic Detectors layout
Triple-GEM detector:
6/2/2/2 gap geometry
µ-RWELL detector:
4 mm drift gap & resistivity 1M/
USE ONLY AS SW-TRIGGER TO CLEAN THE EVENT SAMPLE
6
2
2
2
4
X-Y r/o (650 µm strip pitch)
1 D r/o (400 µm strip pitch)
GEM operated in Ar/CO2=70/30
µ-RWELL operated in Ar/ISO=90/10
 =115 µm
 =152 µm
No-Bending-plane
Bending-plane
 =165 µm
Bending-plane
Center of Gravity (COG)
method

## Slide 10
Calibration RUN (upstream – downstream trigger):
Scan in drift field with orthogonal tracks & B=0 T (7 runs)
Scan in HV with orthogonal tracks & B=0, -1 T (18 runs)
Scan in angle (0,7.5,15,30,45) & B= 0, ± 1 T & 2 GEM Gain (30 runs)
Run with emulsion setup (trigger w/forward scintillators + SW trigger based on forward trackers + µ-RWELL):
Scan with CS emulsion: angle (0,7.5,15,30,45) & B= 0, ± 1T
(10 runs)
Scan with CES & ECC emulsion: tilt angle (0,7.5,15,30,45) & B= 0 T (10 runs)
We present preliminary results based on (COG) method for the Calibration runs
NO micro-TPC MODE ANALYSIS (the code is under development by INFN-FE)
NO COMBINED RESULTS BETWEEN GEM & EMULSIONS SETUP
RUN conditions

## Slide 11
Efficiency vs HV
with orthogonal tracks
GEM detector
µ-RWELL detector
Gain 2000
Gain 7000
The efficiency decrease with B

## Slide 12
Efficiency vs tilt angle
w & w/out magnetic field
GEM detector - Gain 4000
µ-RWELL detector - Gain 8000
Larger the incidence angle
Larger the spread of the charge over the readout strips
Smaller the charge collected by the strips
Smaller the efficiency
The effect is larger w/B

## Slide 13
beam
L
x
B
E
electron drift
FE
FB
Track residual vs magnetic field
for different tilt angle
GEM detector
µRWELL detector
The track reconstruction based on COG methode make sense only at small incidence angle and low B field.

## Slide 14
-TCP mode (I)
orthogonal tracks & B = 1T
Event with 3 hits
Charge distribution fitted with a Fermi-Dirac:
p1 is the time at half-maximum of the charge distribution
work in progress

## Slide 15
-TCP mode (II)
orthogonal tracks & B = 1T
The Fermi-Dirac’s parameter p1 for all events
ΔT = 102.3 +- 0.1 ns
Drift Gap = 4 mm
Drift Velocity = (3.9 +- 0.1) cm/s
Drift Velocity (Garfield) = (3.5+-0.1) cm/ s
T0 = 1.81 APV Sample 
( 45.323 +- 0.003) ns
Tmax = 5.91 APV Sample  (147.657 +- 0.004) ns
Double Fermi-Dirac Fit
work in progress

## Slide 16: Summary
The analysis of the SHIP TB data is still at an early stage:
the study of the GEM space resolution vs angle and B requires for more sophisticated analysis than usual COG (at least for α > 15°)
the code for micro-TPC mode (by Ferrara group) is under development
combined analysis between GEM and emulsion target units (CS, CES, ECC) still to be started (delay on the emulsion chemical development)
At the moment it’s difficult to foresee for other TB with emulsions in 2016

## Slide 17: 2016 Beam Time request
In the framework of µ-RWELL R&D we are collaborating with the CMS – phase2 upgrade group for the design & construction of a first prototype of large area µ-RWELL with the so called LR resistive scheme (see Morello presentation of today).
The goal is to have a dedicated TB of such a proto by the end of the 2016 (last H4 TB time slot).
In parallel we also aim to test some small (10x10 cm2) µ-RWELL protos with other features (such as HR resistive scheme and thicker WELL amplification stage – 125µm )

## Slide 18: SPARES

## Slide 19
The µ-RWELL architecture
The µ-RWELL(*) PCB is realized by coupling:
a “suitable patterned GEM foil” for the “amplification stage”
a “resistive stage” for the discharge suppression & current evacuation
  “Low particle rate” (LR) << 100kHz/cm2: single resistive layer  surface resistivity (∼100 M/)
  “High particle rate” (HR**) >> 100kHz/cm2: more sophisticated resistive scheme must be implemented (performed by MPDG_NEXT- LNF financed by GR5-INFN)
a simple readout PCB board  OK
The simplest scheme of µ-RWELL detector
1
2
3
(**) the final goal being O(1 MHz/cm2)
(*) the first prototype of such a type of detector (at that time called Blind-GEM detector) has been proposed in the 2009 by the author.
Copper top layer
Resistive layers
(by DLC)
Vias (conductive )
Vias (conductive)
Readout electrode

## Slide 20
Track residual vs HV
with orthogonal tracks
Bending-plane
No Bending-plane
GEM detector
WELL detector

## Slide 21
Track residual vs tilt angle
w & w/out magnetic field
GEM detector
µ-RWELL detector
beam
L
x
B
E
electron drift
FE
FB