## Slide 1
Predrag Buncic
CERN
ALICE Status Report
LHCC Referee Meeting
01/12/2015

## Slide 2: Grid usage
70%
16%
8%
6%

## Slide 3: Data processing in 2015
MC – 96 cycles – usual number of productions
  1,952,334,979 events
  p-p, p-Pb, Pb-p, some Pb-Pb, some G4
RAW – reprocessed Run1 data

## Slide 4: Run 2 progress
Registered data volume in 2015 – equal to the sum of 2010-2013
5.2 PB RAW

## Slide 5
pp √s = 13 TeV
At highest interaction rates, events with pileup comparable to Pb+Pb collisions
TPC tracking code was modified to be able to correct for large distortions caused by the space charge build-up

## Slide 6
New calibration step required to take these (time dependent) distortions
Comparing standard reconstruction with reconstruction using new correction:
  ITS Matching rate for triggered BC increases by ~60%
  N TPC clusters per track also increases
Note: ITS-matching was affected not only by the TPC track loss due to the distortions but also by wrong extrapolation from TPC to ITS
Test on 400 KHz interaction rate

## Slide 7
Pb-Pb at √sNN = 5 TeV
Initial track seeding in the presence of distortions required to open the cuts in track search leading to increased memory usage
  => Request for temporary large memory queues on T1 sites

## Slide 8
Memory consumption
Tests on the worst LHC11h data chunk
Now we are here
Last results obtained with modified code
  We remain under 2 GB/job limit for reconstruction

## Slide 9
CPU performance
Tests on the same LHC11h data chunk
Gain of ~20% as by-product of memory optimization and optimization of TPC code
Unfortunately this gains were quickly lost due to increased complexity of events in Run 2

## Slide 10: Status of Pb-Pb processing
Data taking
  Smooth operation
  40% of the data is
  replicated to T1s
Processing
  Fast cycle for Muon analysis and calorimeter calibration
  Full offline calibration cycle for global processing
  Special selection of runs for first physics
700 TB of RAW in one week

## Slide 11: Expected disk space evolution (T0+T1s+T2s+O2)
Chart: 
| 2015.0 | 2016.0 | 2017.0 | 2018.0 | 2019.0 | 2020.0 | 2021.0 | 2022.0 | 2023.0 | 2024.0 | 2025.0 | 2026.0 | 2027.0
 | 54.55 | 63.45 | 75.55 | 84.52 | 95.284 | 169.7358 | 182.9727 | 198.0339 | 215.1851 | 234.7312 | 257.0227 | 282.462 | 311.5116
CRSG
Scrutinized
request
PB
To be discussed
with CSRG
+02
+ 15% / year (T0,T1)
+5%/ year (T2)
Follow-up to O2 TDR
6-Oct: Meeting convened by the DRC with the 4 experiments to understand the global requirements
16-Oct: Meeting of ALICE (with IT and the WLCG
Conclusions
  Clarified projected evolution of resources at CERN
  O2 architecture compatible with the WLCG.
  Bandwidth need from P2 to the Tier 0 will need to be increased.
    precise costing is being established.
  Bandwidth needs to the Grid will also increase and the requests to the Tier 1’s will be done in the near future.

## Slide 12: First O2 milestones

## Slide 13: Dynamical Deployment System (DSS)
Current stable release - DDS v1.0 (2015-11-20, http://dds.gsi.de/download.html)
Home site: http://dds.gsi.de
User’s Manual: http://dds.gsi.de/documentation.html
DDS now provides pluggable mechanism for external schedulers

## Slide 14
Agile lifecycle: from code to published builds quickly, with automated tests
Philosophy: automatize as much as possible, trivialize human intervention
Objective for O²: refreshing aging infrastructure and paradigm
  Setup the infrastructure for running builds and tests: done
  Basic tools to build+publish current software and O²: done
  Visualization interface for the tests: In progress
  Automatic test and flagging of Pull Requests for O²: In progress
Basic infrastructure is ready way ahead of time: as of Sep 9, old system retired and already using it in production for current software
Develop
Build and test
Deploy and publish
Git-based
Integration builds
CVMFS, RPM, Ubuntu
source code
tarballs test results
Software Lifecycle

## Slide 15
Software Tools and Procedures
Common license agreed: GPL v3 for ALICE O2 and LGPL v3 for ALFA

## Slide 16: Summary
Data processing in 2015 follows usual pattern
  All requests have been fulfilled
  Number of tasks in the pipeline is manageable
  MC is, as usual, the main resources user (70%), followed by user tasks (22%) and RAW (8%)
Resources and infrastructure is able to cope with the production load
  Computing resources are stable and growing
Unexpectedly large distortions in TPC at high interaction rate required an extra calibration step and additional software development
  Now under control including memory per job
Work on O2 has started following the plan presented in the TDR