## Slide 1: Proposal for change of the reference emittance for the estimate of apertures, DA, etc.
G. Arduini with input from: C. Bracco, R. Bruce, H. Burkhardt, R. De Maria, M. Giovannozzi, J. Jowett, Y. Papaphilippou, S. Redaelli, R. Tomas, F. Velotti
62nd WP2 Meeting – 04/03/2016

## Slide 2: Status
Normalized emittance of 3.5 mm used for:
  Aperture calculations for protons and ions
  DA estimates without beam-beam
Proton nominal emittance of 2.5 mm used for:
  DA aperture in the presence of beam-beam
  Normalized beam-beam separation

## Slide 3: Proposal
Move to a single unit for all the simulations to avoid confusion
Appropriate scaling of the parameters in sigma so to keep the same “apertures” in mm (defined by the collimation system) is needed
It is a change of unit like moving from the imperial system to the metric system or the other way round
Use the sigma corresponding to the nominal normalized r.m.s. transverse emittance of 2.5 mm as unit.

## Slide 4: Implications
Minimum Physical Aperture (after subtraction of tolerances):
  See note: CERN-ACC-2014-0044 for tolerances used in collision.
  Note under preparation for injection summarizing based on presentations at WP2/5/14 joint meetings and presented at HL-LHC annual meeting:
    47th HiLumi WP2 (5/8/14) Task Leader Meeting, Friday, 17 April 2015 (R. Bruce and F. Velotti)
    F. Velotti, Aperture and protection tolerance for the injection into LHC, 5th Joint HiLumi LHC-LARP Annual Meeting 2015, CERN, 26-30 October 2015
    (*) When protected by nearby TCT
 | Old (en=3.5 mm) | New (en=2.5 mm)
Injection | 9 | 10.6
Collision | 12(*)/17 | 14.2 (*)/20.1

## Slide 5: Implications
Collimator settings at injection:
 | Old (en=3.5 mm) | New (en=2.5 mm)
TCP (LSS7) | 5.7 | 6.7
TCSG (LSS7) | 6.7 | 7.9
TCSTCDQ (LSS6) | 7.5 | 8.9
TCDQ (LSS6) | 8.0 | 9.5
TCLD (LSS7) | 13.0 (tbc) | 15.4 (tbc)
TCLA (LSS7) | 10.0 | 11.8
TCT (LSS1/5) | 13.0 | 15.4
TCP (LSS3) | 8.0 | 9.5
TCSG (LSS3) | 9.3 | 11.0
TCLA (LSS3) | 10.0 | 11.8
TCT (LSS2/8) | 13.0 | 15.4
TDI (LSS2/8) | 6.8 | 8.0
TCLI (LSS2/8) | 6.8 | 8.0

## Slide 6: Implications
Collimator settings in collision:
 | Old (en=3.5 mm) | New (en=2.5 mm)
TCP (LSS7) | 5.7 | 6.7
TCSG (LSS7) | 7.7 | 9.1
TCSTCDQ (LSS6) | 8.5 | 10.1
TCDQ (LSS6) | 9 | 10.6
TCLD (LSS7) | 10 | 11.8
TCLA (LSS7) | 10 | 11.8
TCT (LSS1/5) | 10.5 | 12.4
TCL (LSS1/5) | 12 | 14.2
TCP (LSS3) | 15 | 17.7
TCSG (LSS3) | 18 | 21.3
TCLA (LSS3) | 20 | 23.7
TCT (LSS2/8) | 30 | 35.5

## Slide 7: Implications
Minimum Dynamic Aperture (no beam-beam):
Minimum Dynamic Aperture* (with beam-beam):
 | Old (en=3.5 mm) | New (en=2.5 mm)
Injection | 10 | 11.8
Collision | 10 | 11.8
 | Old (en=2.5 mm) | New (en=2.5 mm)
Collision | 6 | 6
No Change
    (*) At injection and in the other phases before collision we assume that beam-beam is negligible. Should we quantify better this request?

## Slide 8: Long range beam-beam separation
Minimum normalized long range beam-beam separation
 | Old (en=2.5 mm) | New (en=2.5 mm)
Collision | 12.5 | 12.5
No Change

## Slide 9: To note
The above parameters are acceptable also for:
  Scrubbing at injection when larger emittances are expected (en=3.75 mm)
  Ion operation (en=1.5 mm) having the same physical emittance of a proton beam with en=3.75 mm for equivalent magnetic field in the magnets.

## Slide 10: Questions / Comments
Question form Yannis: Is our target of 6 sigma dynamic aperture (minimum value achieved at minimum b*) consistent with our TCP opening of 6.7 s?
Comment from Stefano: We should round the numbers for the target values (granularity of 0.5 s?)