## Slide 1: Radiation Resistant Lighting
Ben Fiedler 22.04.2016 Supervisor: J. Devine

## Slide 2: Context
LHC generates radiation when running
Maintenance and upgrades are performed by humans in between runs  need for proper heating, cooling, ventilation and lighting
Goal: Develop a radiation resistant lighting system for the LHC
My project: emergency lighting for safe egress

## Slide 3: Emergency lighting
Radiation resistant light system is installed already (“test zones”)
Open question: How long will these luminaires last?
System level test (“the whole thing”):
  100 kGy: Loss of approx. 40% of light output
  Functional validation
My project: Component level test for LEDs and PMMA plastic
  Gain better understanding of behavior of components
  Estimate lifetime of components  System lifetime

## Slide 4: Test system design
Design, solder and program a test box
Measure the light output of a LED over an extended period of time
Components:
  LED to be tested
  Light sensor
  Arduino
  Temperature sensor
  USB device for logging data
  Light tight box
  Source code (See it on GitHub)

## Slide 5: How it works
The system is connected to a logging device
The system calibrates itself
  Initial conditions (LED off) are determined
  The LED is switched on
  LED achieves operating temperature

## Slide 6: LED operation
src: http://image.slidesharecdn.com/ledlifetimeedndigikeylfi2010-12740463825976-phpapp02/95/led-lifetime-edn-digikey-at-lfi-2010-6-638.jpg?cb=1422627563

## Slide 7: LED temperature vs relative light output
http://www.ledrite.com/images/data_cree_jtchart.jpg

## Slide 8: How it works
The system is connected to a logging device
The system calibrates itself
  Initial conditions (LED off) are determined
  The LED is switched on
  LED achieves operating temperature
Actual data is recorded
  Once a minute
  Both light output and temperature

## Slide 9: The Test Box
Plastic box with all components installed inside
Cables to provide power and take data:
  Ingoing: The LED and its power supply
  Outgoing: USB cable to connect to logging device
External program controls interior

## Slide 10: Data capturing
Three Variables in testing:
  Radiation  This is the important one
  Time
  LED temperature
Elimination of variable temperature by waiting for calibration
Long sampling time accounts for time variable
Radiation left as only parameter

## Slide 11: Example Data (one sample)

## Slide 12: Example Data (avg. long run)

## Slide 13: Conclusion
Test Box is minimal working product built in two weeks
Minor errors still included:
  Too large heat sink  Use an isolator
Future work includes:
  PCB design for “mass-production”
  Enhancing box features, more program features (automated plotting, …)
  Design the same system for PMMA plastic / glass  color output

## Slide 14: Evaluation
Work was combination of hardware and software work
Mostly independent work, encouragement to work by myself and implement my own solutions
I enjoyed it a lot and learned much about electrical engineering, microcontrollers and hardware-software interfaces
Only criticism: Delivery time of the system’s components, therefore I idled some time

## Slide 15: Thank you for your attention
Any questions left?