## Slide 1: Beam Instrumentation
T. Lefevre (BE-BI)
M. Barros Marin, C. Boccard, A. Boccardi, B. Dehning, J. Emery,
M. Gasior, R. Jones, T. Levens, J. Olexa, E. Piselli, J. Storey

## Slide 2: Outline
Beam position monitor
  Resolution of the current BPM orbit/trajectory mode
  Need for extra BPMs around the cavity ?
Head-tail monitor
  Tool for measuring crabbing
  Status and plans
Emittance monitoring
  Wire scanner
  BGI
  No sync. Light if operation foreseen below 350GeV
Beam loss monitoring
  Any need for add. BLM for cavity protection system ?

## Slide 3: BPM in SPS – new MOPOS
New MOPOS electronic being developed
  Based on LogAmp and rad-hard digital FE (GEFE)
  Resolution over ±15mm aperture, for large intensity beams (>2.1010 p):
    Orbit mode: 0.1 mm
    Trajectory mode: 0.4 mm
    Batch by batch measurements possible
  Will also include a DOROS acquisition channel
Installation foreseen for LS2 but the fiber infrastructure is installed already in BA6

## Slide 4: New BPMs around the crab cavities ?
Possible pick-ups
SPS BPM design: conical flange
  BPCN - Ø80mm, 180mm long strip-line, possibly spares, Zt=6ohms
LHC BPM design : CF and helicoflex so no bake-out above 180C.
  BPMWI, Ø80mm, enlarged Button 40mm, Zt=1.1ohm, body and button existing
  BPMSX, 81mm, 120mm strip-lne, Zt=4ohms, body and feedthrough but no electrode
SLAC collimator: Conical flange, Ø80mm, enlarged buttons, helicoflex so no bake-out above 180C
….. Decision as soon as possible since in most cases it involves manufacturing

## Slide 5: SPS Head-tail monitor
Acquisition of BPM sum/delta signals with fast Digitizer (10GSPS)
“Features”
Limited resolution – 100um
Long acquisition length possible
(1.6 second)
Slow readout speed
Large file size

## Slide 6: SPS Head-tail monitor
Potential for crabbing measurements
Phase advance being looked at by ABP
  Hope the pick-up is located at position with an adequate phase advance..
Current HT needs to be adapted to match the input voltage (to cope with lower intensity bunches) with switchable attenuators
Foreseen upgrade and on-going developments
Required beam tests in 2016
  Measure more precisely the resolution of the system (using bumps or K-modulation)
Software upgrades already planned for 2016
  New FESA3 class optimised for instability measurements
  Post-processing (data reduction) done on window machine controlling the digitizers

## Slide 7: SPS Head-tail monitor
On-going developments (LHC or HL-LHC driven)
Higher sensitivities with a Multi-band instability Monitor
  Looks at different frequency components of BPM signal using RF filter bank.
  From the relative power in the bands can determine mode number.
  Diode detectors & 24-bit ADCs
  Sensitive but not bunch-by-bunch

## Slide 8: SPS Head-tail monitor
On-going developments (LHC or HL-LHC driven)
Faster time response with EO-BPM
  A fibre-coupled design with laser and detectors housed 160 m away from accelerator tunnel.
  Incoming light is collimated by a lens and polarized before entering the crystal.
  The electric field of passing bunch at the crystal induces a rotation in the polarization, by the linear Pockels electro-optic effect.
  Light emerging from the crystal passes through an analyser and is then fibre-coupled to the distant photodetector.
EO-BPM
BPCL.421

## Slide 9: Comparisons of different SPS wire scanners
Emittance measurement repeatability estimated by error bars, horizontal plane
  Relative error few % with a 1 um beam
  Vertical plane smaller errors
Linear scanner accuracy established be comparison of two linear scanners (optical ruler)
Measurements over several hours
Intensity 3E10 protons (TOTEM beam, one bunch)
Low dispersion scanners compared
Emittance smaller < 1 um at 26 GeV
Thesis: F. Roncarolo

## Slide 10: Wire scanner intensity limits and measurements errors
Scanners | Linear | Rotational | New rotational 517 vertical
Intensity limit max: E=26 GeV, emittance= 1um | 3.60E+12 | 2.40E+13 | 1.50E+14
Intensity limit max: E=270 GeV, emittance= 1um | 1.10E+12 | 7.30E+12 | 4.50E+13
Statistical error (single scan, beam size) | 40 to 100 um | 40 to 100 um | similar to linear
Repeatability (single scan, beam size) | 14 um | 70 um | similar to linear
Maximum number of scans per year | 40000 | 10000 | more as all others

## Slide 11: BGI

## Slide 12: BGI
Assumptions:
  Emittance = 1um
  Point Spread P = 400um +/- 100um (based on measurements in 2013)
Expected performance
Re-commissioning of the BGI foreseen in 2016
  Reliable operation of BGI
  MCP gain calibration (weighting factors)
  Understand PSF and resolution
Energy (GeV) | Beam width (mm) | Relative error (%)
26 | 1.8 | 1
270 | 0.55 | 13

## Slide 13: Conclusions
BPM
  Possibly new MOPOS (including DOROS) for few selected BPMs in BA6
  New BPMs around the crab – To be decided as soon as possible
HT
  Would work without major modifications if phase advance OK
  New EO-Pick-up and MIM under-development – possibly available by 2018
WS would work as baseline instrument for emittance measurements
BGI needs to be re-commissioned but would ultimately be the device for continuous emittance monitoring
Do we need extra BLMs around the crab-cavity ?