## Slide 1: SPS Transverse Damper with Crab Cavities
G. Kotzian, W. Hofle
BE-RF-FB, 11. January 2016 Crab Cavity SPS Tests Day I
https://indico.cern.ch/event/463435/

## Slide 2: Recap: Transverse Feedback Systems
Kicker
The transverse dampers [SPS Damper, Wideband FB] are feedback systems: they measure transverse oscillations [SPS Damper: bunch-by-bunch, Wideband FB: slice-by-slice] and damp them by fast electrostatic kickers.
Analog
Front
End
SUM
Signal
Processing
BPM
Power Amp
ADC
DAC
5ns Bunches
Active closed loop feedback
transverse
position
pre-processed
sampled
position
calculated
correction data
correction
signal
drive signal
BBQ

## Slide 3: Outline
Objective:
Illustrate operational modes of the SPS Transverse Damper, estimate the co-existence of damper and crab cavities (CC), address MD studies and potential diagnostics.
Structure:
SPS Damper Operating Modes
CC-Damper Interaction Scenarios  Proposal for MD studies
Beam Diagnostics Potential

## Slide 4: SPS Damper Operating Modes
Damping of injection errors a.k.a. Injection Damping
  handles large injection errors of the order of several mm
  Fully independent systems in the horizontal and vertical plane
Cure of resistive wall impedance driven coupled bunch instability
  threshold ~5x1012 protons total intensity
  between lowest betatron frequency and 20 MHz to damp all possible coupled bunch modes at 25 ns bunch spacing
  individual bunch damping (sampling synchronous with bunches)
  Boundary condition:
Counteract transverse emittance blow-up
  preventing non-linearities from shredding bunches into filaments
  Injection damping: feedback action must be sufficiently fast (kick strength)
  Low instability detection threshold, to work immediately against arising instabilities at the very onset (position sensitivity/detection resolution)
QUESTION: How much impact of CC to be expected?
… challenging to benchmark  see studies by R. Calaga [1]
[1] H.Bartosik et.al., “SPS CC TEST: ANALYSIS OF PAST MEASUREMENTS AND OUTLOOK TO FUTURE CAMPAIGNS INCLUDING THE REQUIRED INSTRUMENTATION”, at 4th Joint HiLumi LHC-LARP Annual Meeting 2014, Nov. 17-21, 2014.

## Slide 5: Examples: Damper Performance
Logbook: [Monday 27-Oct-2014, 23:15]
VERTICAL
1 ms
approx. 0.7 ms
1st batch
2st batch
3rd batch
4th batch
activity in the last injected batch
(+1st order roll-off
of damper gain)
HORIZONTAL
[10-Dec-2014, 10:45]
How much impact of CC to be expected?
Injection damping  better than 1ms
Counteract coupled bunch instabilities,  up to highest mode at 25 ns spacing

## Slide 6: Damper-CC Interaction Scenarios (1)
(1) Damper in Passive Mode:
  Open loop, no active excitation from TFB
  Use damper for passive diagnostics and monitoring (see following slides)
  Survey visibility of CC activity, to evaluate
    Effect of CC during Injection Transients (several mm injection errors)?
    Impact of CC on coupled bunch instabilities?
  Results valuable for benchmarking CC-TFB interaction
Damper diagnostics potential and monitoring tools: (this list is not exhaustive)
Sensitivity of transverse damper to intra-bunch motion (resolve bunch motion >> 20 MHz)
Transverse Observation Box (bunch-by-bunch, turn-by-turn data)
Wideband Transverse Feedback (RF synchronous sampling)
Transverse BQM (GUI and logging application readily available)
NB: Define an adequate metric to quantify impact of CC.
RMS transverse activity
Damping time
Emittance growth
…
assess beam effects in the presence of crab cavities only

## Slide 7: Damper-CC Interaction Scenarios (2)
(2) Active Mode: Driven Excitation
  Open loop, active excitation with TFB
  Use damper to actively perturb the beam with known patterns (single transverse deflection, sinusoidal excitation)
  generate a test pattern similar to what is expected with active crabbing:
  New Wideband kickers in BA3 (BW up to 700 MHz)
  Driven transverse excitation  CW 400.79 MHz (bunch synchronous)
  Allows for reproducible tests e.g. to calibrate diagnostics or exploration of parameters
(3) Active Mode: Active Feedback
  Closed loop transverse feedback
  Examine impact of co-existence: CC + TFB
  Once CCs installed and available in 2018
Complementary test bench, could be made available well before installation and testing with Crab Cavities in 2018

## Slide 8: Beam Diagnostics Potential (1)
Sensitivity of transverse damper to intra-bunch motion
  Separation in even/odd modes, turn-by-turn data
movement of
centre-of-charges
normalized position as implemented
in the Damper HW
Simulation Results: Symmetric Excitation
alternate processing scheme to detect and indicate anti-sym. oscillations:
cases shown:
LHC ADT
Simulation Results: Anti-Symmetric Excitation
400 MHz
400 MHz
Centre-of-charges oscillations
detectable by damper  feedback
G. Kotzian, W. Hofle, D. Valuch, “ADT SENSITIVITY TO INTRA-BUNCH MOTION”, at HSC meeting, Jan. 22, 2014.
Measure this quantitatively in 2016

## Slide 9: Beam Diagnostics Potential (2)
Observation Box
  Bunch-by-bunch, turn-by-turn data
  Prototype readily in place in BA2
  Some development work to be done (FESA, logging, fixed display)
cases shown:
LHC ADT
Frac. Tune
“Instantaneous” tune
Amplitude
Inclination of can be interpreted as “damping time”
(assuming the decay is exponential)
G. Kotzian, D. Valuch, “SPS AND LHC TRANSVERSE FEEDBACK PARAMETER EXTRACTION”, at LBOC 2014, Dec. 08, 2015.
Work in progress

## Slide 10: Beam Diagnostics Potential (3)
Visualization of bunch motion:
Rapid identification of
  quiet bunches
  bunches with transverse center of mass motion
  bunches with head tail motion
  bunches with combination of center of mass and headtail motion with correlation
   To be implemented
case shown:
LHC ADT
W. Hofle, “PERFORMANCE OF UPGRADED SPS DAMPER IN VIEW OF CRAB CAVITY TESTS COMPLEMENTARY TO HIGH BANDWIDTH TRANSVERSE FEEDBACK”, at 4th Joint HiLumi LHC-LARP Annual Meeting 2014, Nov. 17-21, 2014.
Work in progress

## Slide 11: Beam Diagnostics Potential (4)
Transverse BQM: Description
  10 bit resolution, 8 GSPS sampling rate
  Uses exponentially tapered stripline
  approx. 32 MSamples usable memory == max. 4k turns
  GUI and logging application in operation (UI developed by F. Foulin, FESA support by G. Papotti)
Courtesy T. Mastoridis
T. Mastoridis, “BEAM DIAGNOSTICS TOOLS FOR CRAB-CAVITY TESTS IN THE SPS”, at 4th Joint HiLumi LHC-LARP Annual Meeting 2014, Nov. 17-21, 2014.
In Operation

## Slide 12: Beam Diagnostics Potential (5)
Wideband Transverse Feedback: Present Status
  This systems primary purpose is active feedback, currently demonstrated for single bunch operation.
  8 bit resolution, 4 GSPS sampling rate (uses exponentially tapered stripline BPW), could allow for data compression/reduction at the source (e.g. by suppressing useless zero samples)
  Synchronized to RF clock
  Data processing and analysis software ready
Supported by LIU & US-LARP for 2016, but decision for full implementation not taken before Sept. 2016
J.D. Fox, “WIDEBAND FEEDBACK SYSTEMS CM23 PROGRESS AND PLANS”, at 4th Joint HiLumi LHC-LARP Annual Meeting 2014, Nov. 17-21, 2014.
Courtesy J. Fox
Data Processing and Analysis Software ready

## Slide 13: Brainstorming for MDs – before CC Installation (1)
Can we generate a test pattern similar to what is expected with active crabbing?
  Driven transverse excitation, CW 400.79 MHz (bunch synchronous)
  Use  wideband kickers in BA3 (BW up to 700 MHz)
  Implement remote control interface
    enable/disable excitation (timing)
    adjust drive level and RF phasing
    drive modulation (AM, PM)
Two new stripline kickers installed and available now (2016):
 | Units | Value
Stripline length, per kicker | cm | 10
Total length (2x) | cm | 20
Bandwidth | MHz | 700
Max. Drive Signal (solid state) | W | 2 x 250
Total Transverse Voltage |  | 2.8
Total Kick strength @ 26 GeV | nrad | 100
 | Units | Value
Stripline length, per kicker | cm | 10
Total length (2x) | cm | 20
Bandwidth | MHz | 700
Max. Drive Signal (solid state) | W | 2 x 250
Total Transverse Voltage |  | 2.8
Total Kick strength @ 26 GeV | nrad | 
Two striplines at 55 GeV: 51 nrad, sufficient to do head-tail with +/- 51 nrad,
measure this quantitatively in 2016
NB: no advantage for crab cavity tests (400 MHz) of slotline

## Slide 14: Brainstorming for MDs – before CC Installation (2)
Can we detect & resolve this excitation with our current instruments?
  SPS Damper [even & odd modes]  quantify Damper sensitivity to intra-bunch motion
  Prepare Transverse BQM, Transverse Wideband Feedback for diagnostics
  Use Head Tail Monitor from BI group
  Test Multiband Instability Monitor (MIM)
  etc.
Enable CW 400 MHz excitation during injection + damping
  Wideband kickers in BA3
  Single bunch, multiple bunches
  Evaluate impact on injection damping (if any …)  develop adequate metric.
Enable CW 400 MHz excitation during flat bottom + damping
  High intensity beams up to 4x72 trains
  Modulated CW drive (AM, PM) and
  Evaluate impact on coupled bunch instabilities (if any …)  metric?
Mid-Term plan (2017)

## Slide 15: Brainstorming for MDs – with CCs in Place (2018)
Assess overall behavior of damper - CC interaction:
CC and TFB during injection  compare results against vs. CC and with driven excitation
CC and TFB throughout the cycle  compare results against vs. CC and with driven excitation
Furthermore / optionally:
Examine CC behavior at the presence of external transvers perturbation signals  inject test patterns (CW, modulated AM/PM)
… in 2018

## Slide 16: THANK YOU
Questions?