## Slide 1
A virtual private network based on software defined network architecture for high energy physics data exchange
Zhihui Sun, Fazhi Qi, Tao Cui
Hepix Spring 2016
Computing Center, Institute of High Energy Physics, CAS

## Slide 2: outline
Background
Key Technologies
Current Status
Future work

## Slide 3: Background
Data Exchange Challenges
  HEP Experiments are data intensive science
  IHEP is hosting and participating in several HEP Experiments
  BESIII、DayaBay、Atlas、CMS、CSNS、JUNO、LHASSO …

## Slide 4: IHEP Current Network Status
IPv4
  Good connection for international cooperation
  Poor bandwidth for the domestic communication
    Universities…
IPv6
  Available bandwidth is good
  Always too busy in daytime,
  only good at night

## Slide 5: What shall we do?
Build a simple, flexible, robust, high performance and central－controlled network environment for HEP cooperation members in China
SDN is one of the Choices…

## Slide 6: The Key Technologies
IHEP
CCNU
SDU
SJTU
Network topology
  SJTU (Shanghai Jiao Tong University), SDU (Shandong University), CCNU (Central China Normal University), IHEP
  IPv4 & IPv6

## Slide 7: The Key Technologies
Overlay
  IPv4OverIPv6
  VPN：GRE tunnel,
  Efficiency: >95%
SDN Controller
  Based on OpenDaylight
  North-API: RESTAPI
  South-API: OpenFlow, SNMP
SDN Boundary Switch
  OpenFlow 1.3
  VPN function
  Link performance probing

## Slide 8: The Key Technologies
Link Quality Detection
  Packet loss
  Latency
  Available bandwidth: Active measurement
  (by iperf)
path | Packet loss | latency | Available bandwidth
Site A->site B(ipv4) |  |  | 
Site A->site B(ipv6) |  |  | 
Site A->site C->site B (ipv4) |  |  | 
Site A->site C->site B (ipv6) |  |  | 
Site A->(ipv4)site C-> (ipv6)site B |  |  | 
Site A->(ipv6)site C-> (ipv4)site B |  |  | 
Site
A
Site
B
Ipv4 GRE tunnel
Ipv6 GRE tunnel
wan
Site
C

## Slide 9: The Key Technologies
Routing Switching algorithm
Step:
  Rank the packet loss, latency, available bandwidth respectively
  : the score of packet loss rank result
  : the score of latency rank result
  : the score of available bandwidth rank result
  Routing weights(site A->site B) =
  Best path has max routing weight

## Slide 10: The Key Technologies
IHEP
SJTU
Ipv4 GRE tunnel
Ipv6 GRE tunnel
wan
SDU
path | Packet loss | Latency (ms) | Available bandwidth (Mbps)
IHEP->SJTU (ipv4) | 0 | 179.3 | 49.6
IHEP->SJTU (ipv6) | 0.2% | 66.75 | 337
IHEP->SDU->SJTU(ipv4) | 0.5% | 30.1 | 4.6
IHEP->SDU->SJTU(ipv6) | 3% | 110.6 | 1.05
IHEP->(ipv4)SDU-> (ipv6)SJTU | 1% | 32.13 | 4.57
IHEP->(ipv6)SDU-> (ipv4)SJTU | 4% | 116.132 | 1.43
path | Packet loss (score) | Latency (score) | Available Bandwidth (score) | Routing weights (score)
IHEP->SJTU (ipv4) | 6 | 1 | 5 | 4.9
IHEP->SJTU (ipv6) | 5 | 4 | 6 | 5.5
IHEP->SDU->SJTU(ipv4) | 4 | 6 | 4 | 4.2
IHEP->SDU->SJTU(ipv6) | 2 | 3 | 2 | 2.1
IHEP->(ipv4)SDU-> (ipv6)SJTU | 3 | 5 | 3 | 3.2
IHEP->(ipv6)SDU-> (ipv4)SJTU | 1 | 2 | 1 | 1.1
Test data
The best path is the path IHEP-> SJTU(ipv6)

## Slide 11: Scenarios
Site
A
Site
B
Site
C
Host A
Host B
Host C
✗

## Slide 12: Routing Switching
Site
A
Site
B
Site
C
Host A
Host B
Host C

## Slide 13: Routing Switching
Site
A
Site
B
Site
C
Host A
Host B
Host C

## Slide 14: Test Result
Path | Traditional method （Mbps） | SDN method （Mbps） | Best path | Traditional method （Mbps） | SDN method （Mbps）
IHEP->SJTU | 29.7 | 337 | IHEP->(IPv6)SJTU | 179.3 | 66.75
SJTU->IHEP | 23.1 | 43.5 | SJTU->(IPv6)IHEP | 180.1 | 66.79
IHEP->SDU | 4.76 | 28.8 | IHEP->(IPv6)SJTU->(IPv6)SDU | 9.14 | 87.33
SDU->IHEP | 4.46 | 27.3 | SDU->(IPv6)SJTU->(IPv6) IHEP | 10.3 | 87.29
SDU->SJTU | 4.84 | 28.40 | SDU->(IPv6)SJTU | 21.3 | 20.54
SJTU->SDU | 4.89 | 29.23 | SJTU->(IPv6)SDU | 20.5 | 20.53
Transfer performance test
latency test
Transfer performance has been improved a lot
Latency varies uncertainly, but it has little effect

## Slide 15: Current Progress
Phase I
  Aug. 2014
  SJTU,SDU,IHEP
  Only IPv6 link
  Manual path selection
  Problems
    VPN efficiency：70%
    IPv6 link performance was unstable
Phase II
  Oct.2015
  SJTU,SDU,IHEP,CCNU
  IPv6 & IPv4
  Automatic path selection
  Performance improvement
    testing

## Slide 16: Controller dashboard
SDN Switch
info
Flow table
info

## Slide 17: Controller dashboard – network & devices status
Ipv4 link
Ipv6 link
Control link

## Slide 18: Controller dashboard – link performance statistics
Available
bandwidth
(ipv4)
Available
bandwidth
(ipv6)
latency
(ipv6)

## Slide 19: Controller dashboard- Path selection
parameter
setting
path
Selection
result

## Slide 20: Future work
Optimization
  Available bandwidth probing
  Path selection algorithm
Add more HEP experiment sites
Couple with data transfer application

## Slide 21
Thanks for your attention !
Any questions？