## Slide 1: ARC CE overview and key concepts
Jon Kerr Nilsen,
ARC Release Manager

## Slide 2: ARC Overview and key concepts

## Slide 3: High-level overview
NorduGrid ARC is a set of products
  ARC, ARC-docs, ARC-Nagios-plugins, CANL-C++, GangliARC
Broad platform support
  Runs on RHEL/SL/CentOS/Fedora, Debian/Ubuntu, MacOSX
Developed in SVN
  Base language C++, parts written in Python, Perl and BASH

## Slide 4: Main components
Front-end to computing resources: the ARC Compute Element (CE)
  CE is a set of services and modules
    Authorisation and access control
    Job handling
    Job files handling (input/output data)
    Information handling
    Accounting
The Resource indexing server (EGIIS)
  A lightweight LDAP-based server
The client tools
  Built upon libraries, some shared with the CE

## Slide 5: ARC CE and interactions

## Slide 6: ARC CE key concept: optimized for data-intensive jobs

## Slide 7: ARC CE components on a cluster
Interfaced to a number of batch systems
  SLURM, SGE, PBS, LSF, LL, Condor
ARC CE is a uniform interface: batch system specifics are not exposed
No ARC component is installed on worker nodes
  No need, because the CE handles transfers

## Slide 8: ARC CE components with SSH backend
Job files are copied into cluster with sshfs
Jobs are submitted with ssh

## Slide 9: ARC Components and functionalities

## Slide 10: Registration
Information Registration Process periodically sends pre-configured information to one or more pre-configured information registries
  Service type (cluster in this case)
  Service contact details (contact string, port etc)
Currently all such data are communicated via LDAP
  Other technologies are possible, as primary data are stored internally as regular files

## Slide 11: Information publishing
A-REX periodically launches information providers which:
  Collect all details defined by relevant information schemas, such as
    Hardware details
    LRMS details
    Available application software (RTE)
    Authorised users (DNs)
    etc
  Create formatted output ready to be served on request
Populate ARIS databases
ARIS serves information when queried via LDAP
Same information can be obtained by a WS query to A-REX
  Not by default configuration yet

## Slide 12: Job submission
Client tool must:
  Query information
  Match it to the job description document
  Select the best site
  Convert to a server document (deterministic)
  Upload all the files
A-REX discovers uploaded job files and launches job processing
Currently, information and upload use different protocols
  WS is needed for better consistency
All steps require authorisation

## Slide 13: Handling file transfers
Jobs won’t start before all input files are present
Input files provided by the user are uploaded by the client tool
  normally, cached
External files are downloaded by DTR when triggered by A-REX
  also cached by default
All inputs are copied or linked to the session directory
Output files are uploaded by DTR to external storage if requested

## Slide 14: Job submission to the batch queue
Key component: batch “back-ends”
  Encapsulate specific properties of different batch systems and map them to generic functionalities
A-REX handles the job life cycle
  Sends them to the batch queue via back-ends
  Monitors status
  Triggers data movement
  Authorisation

## Slide 15: Non-shared File System
If the batch system supports it, a shared file system is not required

## Slide 16: Accounting
JURA harvests job information and submits it to an external accounting service
  For completed jobs only

## Slide 17: Computational jobs and environments

## Slide 18: Client interprets job description
37 attributes to find best matching resource
Job description language: xRSL, JSDL or JDL, but internally is ADL-like
* Interpretation of “slot” depends on batch system!

## Slide 19: Runtime Environment (RTE) concept
Application environment is formalised as “Runtime Environment” (similar concepts exist in other CEs)
Runtime Environment can encapsulate not just application software, but also:
  Batch system peculiarities
  Hardware aspects
  Can even emulate gLite WN
It is just a shell script
  Created manually by sysadmins
  Advertised via infosys
  For many RTEs, namespaces are handy

## Slide 20: RTE example: how to make jobs to use 4 cores per node (for PBS)
Good way: RTE script
Add line to job description file: (runtimeenvironment= "RESERVE_4_CORES")
As many RTE scripts as needed
Bad way: special queue
Add line to job description file: (queue=mpi_jobs)
And so on, introduce a new queue for every imaginable configuration

## Slide 21: RTE pros & cons
In practice is the only way to make parallel/multi-core applications work in heterogeneous clusters
No need to transfer executable, loader or libraries
Possibility to build clusters which allow execution of specified applications only
Better application performance with architecture specific optimizations
Initialization of environment variables and paths, i.e. providing standard environment for executables submitted by user
Version management
Logistical problem:
Who/how keeps track of all RTEs?
Currently, just a Web page
In ATLAS, RTEs are generally replaced now by CVMFS

## Slide 22: ARC CE in more details

## Slide 23: Job handling by A-REX

## Slide 24: The Control Directory
A-REX stores all information about jobs in files under the control directory
Important files:
  job.#.errors: logs from data staging and batch submission
  job.#.description: original job description
  job.#.input/output: input and output files
  job.#.proxy: delegated proxy certificate
  job.#.xml: accounting information

## Slide 25: Batch system interface
Scripts are called by A-REX to manage jobs, 3 per LRMS
  submit-condor-job
    creates the job submission script which is passed to LRMS
  scan-condor-job
    checks status of jobs and notifies A-REX if any have completed
  cancel-condor-job
    cancel a running job

## Slide 26: Installation and configuration

## Slide 27: Installation
From EPEL (Red Hat-like platforms: CentOS, SL etc)
  yum install nordugrid-arc-ca-utils nordugrid-arc-gridmap-utils nordugrid-arc nordugrid-arc-arex nordugrid-arc-client nordugrid-arc-gridftpd nordugrid-arc-hed nordugrid-arc-ldap-infosys nordugrid-arc-plugins-globus nordugrid-arc-plugins-needed
Host certificate
CA Certificates
  https://wiki.egi.eu/wiki/EGI_IGTF_Release

## Slide 28: Configuration
A single file, /etc/arc.conf
Full reference
  /usr/share/arc/examples/arc.conf.reference
Manual with full explanation
  http://www.nordugrid.org/documents/arc-ce-sysadm-guide.pdf
Good to start from an existing configuration from another site
  E.g., https://www.gridpp.ac.uk/wiki/Example_Build_of_an_ARC/Condor_Cluster

## Slide 29: Administration
Starting, stopping services
  /etc/init.d/a-rex start
  /etc/init.d/gridftpd start
  /etc/init.d/nordugrid-arc-ldap-infosys start
  /etc/init.d/nordugrid-arc-inforeg start
Log files
  By default all are in /var/log/arc and are rotated each day
/usr/libexec/arc/gm-jobs
  Utility for giving a summary of job under A-REX’s control
  Can also be used for manual operations, e.g. killing all jobs of a certain user

## Slide 30: NorduGrid Monitor
http://www.nordugrid.org/monitor/

## Slide 31: User mapping
Several options of varying complexity exist to map Grid DNs to local user ids
Most fundamental concept is gridmap file – a plain text file with lines “DN username”
  Static gridmap file
  Dynamic gridmap file produced by nordugridmap tool
    Options of using VOMS servers, combining static mapfiles, etc.
Local user/group mapping can also be done in many different and complex ways
  See system administration guide

## Slide 32: Testing an installation
Install nordugrid-arc-clients
arcls gsiftp://localhost/
arcsub -c localhost -e '&(executable=/bin/hostname)(stdout=stdout)' -d DEBUG
arcstat <job id>
arcget <job id>
ARC tools manual
  http://www.nordugrid.org/documents/arc-ui.pdf
Check if local infosys is working
  ldapsearch -h localhost -p 2135 -x -b 'mds-vo-name=local,o=grid'

## Slide 33: References
Server installation instructions
  http://www.nordugrid.org/documents/arc-server-install.html
ARC CE Sys admin manual
  http://www.nordugrid.org/documents/arc-ce-sysadm-guide.pdf
arc.conf.reference
  Installed at /usr/share/arc/examples/arc.conf.reference
Email list for ARC-related discussions: nordugrid-discuss@nordugrid.org
  Archive: http://mail.nordugrid.org/mailman/listinfo/nordugrid-discuss
Subversion repository
  http://svn.nordugrid.org/trac/nordugrid/browser/arc1/trunk
Bugzilla
  http://bugzilla.nordugrid.org