## Slide 1
The digital TPC:
the ultimate resolution
P. Colas
GridPix: integrated Timepix chips with a Micromegas mesh

## Slide 2
We now have a realistic (though unofficial) estimate of the ILC schedule (S. Komamiya, Lepton-photon 2015) :
Start
2016? 2018?
2033 ?
ILD Tracking:
Vertex detector
TPC
Silicon →
Magnet

## Slide 3
t0 = Ground Breaking
2033?
The yoke and the solenoid have to be assembled on surface site very early (start Y3)
The remaining of the tracker is for end of Y8
After Y. Sugimoto

## Slide 4: Detectors using TimePix chip
+
-
+
-
+
-
Medipix2/TimePix chip
TimePix chip
X-ray source
Ionizing
particle
Single pixel
readout cell
Flip-chip
bump bonding
connections
Semiconductor
sensor
Gas volume
Amplification System (MPGD)
Drift grid
Solid-state detector
Gaseous detector
x, y, F(x, y)  2D
x, y, z(t), E(x,y)  3D

## Slide 5: InGrid: Integrated Micromegas Grid
Integrate Micromegas detector directly on a CMOS chip by post-processing
Resistive layer for protection
NIKHEF (MESA+, Univ. Twente)
IMT Neuchatel
~ 80 kV/cm
avalanche
Micromegas is a Micro Pattern Gas Detector formed by
a metallic micromesh
sustained by 50μm pillars above the anode
Multiplication between anode and mesh

## Slide 6: InGrid: energy resolution
Energy resolution depends on the
grid geometry
Grids can be very flat
  best resolution:
  13.6 % FWHM with 55Fe source in P10
  removal of Kβ 6.5 keV line:
  11.7 % @ 5.9 keV in P10
Hole pitch down to 14 μm
with various diameters
Different gaps (35-75 μm)
Until now: grid is 1 μm of thin Al
but can also be increased to 5 μm by electrolysis to be more robust
Escape peak Kα
Escape peak Kβ
13.6 % FWHM
Kβ-filtered spectrum with Cr foil
11.7% FWHM
Gap: 50 μm; Hole picth: 32 μm,Ø: 14 μm

## Slide 7: The TimePix chip
Starting from the Medipix2 chip, modify to replace photon counting by time counting (clock on each pixel)
(PC, H. van der Graaf, J Timmermans, J. Vischers)
Technology : IBM 0.25 µm
Charactéristics:
  surface : 1.4 x 1.6 cm2
  256 x 256 pixel maxtrix
  Pixels : 55 x 55 µm2
Each pixel features:
  Preamplifier + shaper
  Threshold discriminator
  Configuration register
  synchronization logic (TSL)
  counter 14-bit
  Threshold ~ 700 e-
  (M. Campbell, X. Llopart)
55 mm
55 mm
pixel
Préamplificateur
Discriminateur
Registre de configuration
Interface
Compteur
Logique de
synchronisation

## Slide 8: TimePix Synchronization Logic Control
Medipix Mode
TOT Mode
Timepix Mode
DACs values |  |  | 
Mask | P1 | P0 | Mode
0 | 0 | 0 | Masked
0 | 0 | 1 | Masked
0 | 1 | 0 | Masked
0 | 1 | 1 | Masked
1 | 0 | 0 | Medipix
1 | 0 | 1 | TOT
1 | 1 | 0 | Timepix-1hit
1 | 1 | 1 | Timepix
100 MHz
Analog Signal
Internal Shutter
Shutter
Internal Clock
Digital Signal
not detected
detected
Each pixel can be configured independently in 5 different modes
Internal clock up to 100 MHz
Summed charge
10 ns

## Slide 9: Single electron efficiency
threshold
G/<G>
Single electron efficiency is limited by gain fluctuations
Close to 100% efficiencies are obtained.
(M. Lupberger’s diploma thesis, 2010)

## Slide 10: Micro-TPC using TimePix/Micromegas
Field cage
Cover
Micromegas
mesh
TimePix chip
Windows for
X-ray sources
Windows for
β sources
Gas mixture at atmospheric pressure
6 cm
Micro-TPC with a 6 cm heigh field cage
Size : 4 cm × 5 cm × 8 cm

## Slide 11: Micro-TPC TimePix/Micromegas
TimePix chip
+ SiProt 20 μm
+ Micromegas
55Fe source
Ar/Iso (95:5)
Time mode
z = 25 mm
Vmesh = -340 V
tshutter = 283 μs

## Slide 12: Measurements of primary statistics in gases
Diffusion σt should be big enough to separate electrons: cluster size per e- ~ 1
Study of primary electrons and Fano factor F using RMS
Spectrum of number of electrons for 2000 events:
Sensitive to Kα & Kβ lines
FWHM = 9,5 %
5.9 keV line at ~ 226 e-
TimePix+Ingrid+ 15 μm SiProt
Argon + 5% Isobutane
    F: Fano factor
    √b: single e- gain distribution rms (%)
    ε: detection efficiency
    N: number of primary e-

## Slide 13: GridPix progress
Wafer-based post-processing to add a protection layer and a mesh on pillars on top of the chips (107 chips at a time)
March 2015, there was a successful test with 3 modules (96 chip each) partially equipped : 160 chips!
This shows that this technique is applicable to large areas
This opens the way for ultimate dE/dx resolution

## Slide 14: Applications
e+e- collider TPC (with time)
basic studies of gases (avalanche fluctuation, ionization mechanisms, gas electron properties
Solar axion search (with a X-ray telescope)
Double beta decay
Dark matter directional search
Future work: INNOPIX EU project and LAAS RTB