## Slide 1: CERN Xboxes
N. Catalan Lasheras
X-band FEL meeting. 10.12.2015
Xbox
x

## Slide 2: Outline
Xboxes 1,2 & 3 presentation
  Location and layout, Differences, Capabilities
Associated systems
  LLRF, signal acquisition, Cooling, Controls
Operation
Diagnostics
Schedules
  Construction schedule
  Testing schedule

## Slide 3: Xbox1 operating since 2012
CTF3 klystron gallery
CTF2
Dog-Leg (beam loading) working since 2014
430 kV modulator
50 MW klystron
RF pulse compressor
LLRF

## Slide 4: Xbox2 in operation since 2014
430 kV modulator
50 MW Klystron
RF Pulse compressor
LLRF
Vacuum controllers

## Slide 5: CPI2-2 Klystron in Xbox2
First diode tests (no RF) of CPI#2 tube showed that 0.7 GHz gun oscillations starts at about 240 kV and even generate RF power from the input cavity:
12 GHz pulse from the input cavity
Fortunately, going higher in voltage, the instability zone moves towards the rise/fall time, so the plat top can be used now.
Example of the pulse with ~ 5 MW RF peak power expected:

## Slide 6: What is different?
Similar multiplication factor (~2.7)
Xbox1 actively tuned,
  large impact of temperature variations
Xbox2/3 tuned once after assembly
  Can be tuned with temperature
  Very stable
Notes: **

## Slide 7: Xbox3 being installed

## Slide 8: Xbox3 integration drawings
Testing area inside bunker x4
Power generation 2+2

## Slide 9: Toshiba E37113
The full delivery of 4 units will be completed before July 2015.
Peak power: 6 MW
Beam Voltage: 150 kV
Beam current: 90 A
Average power: 12.4 kW
Efficiency: 47.5%
Factory tests results
Design:

## Slide 10: Xbox3 acceptance tests

## Slide 11: Achtung!! Flanges
Xbox1&2 Xbox3

## Slide 12: Xboxes comparison
 | Xbox1 | Xbox2 | Xbo3x
Modulator | Scandinova K2-3X (solid state 450kV, 350 A, 1.5us, 50 Hz) |  | Scandinova K1 (solid state, 170 kV, 100 A, 6us, 400 Hz
Klystron | SLAC-XL5/CPI 50 MW | CPI-2 50 MW | Toshiba E37113 6MW
RF amplifier | TWT 3kW | TWT 3kW | Solid state
Pulse compressor | SLED1 Gycom (x2.8) | SLED2 CERN (x3.5) | 
Flanges | SLAC |  | IUWR90
Number of testing slots | 1(CTF2/Dog-leg) | 1(+1) | 4 (2+2)

## Slide 13: Dog-Leg experiment
XBOX1
12 GHz RF
MKS02
3 GHz RF
MKS03
MKS05
MKS06
MKS07
Beam:
CTF3 Drive Beam modified
3GHz beam at ~1.2 A
Pulse length up to 250 ns
Energy ~125 MeV at structure
Up to 25 Hz pulse rep. rate
12 GHz RF:
90 MW RF power
Up to 50 Hz rep. rate
Gun
35 m low loss waveguide
CTF3 Injector
High Gradient Accelerating Structure

## Slide 14: Dog-leg experiment. RF network
Thanks A. Solodko
RF network:
~ 35 meters from PC to structure
61% of transmission
230 ns round trip delay
Notes: The RF is provided

## Slide 15: LLRF and acquisition system
Based on PXI system for timing signal generation, acquisition and interlocks
Frequency multiplication and down sampling in separate crates
Interlocks though FPGA card
Retrofitted to Xbox1
Extended to Xbox3

## Slide 16: Control (Xbox3)
Based on NI LabVIEW. Runs in stand alone computer
Saves and plots RF data, temperature and vacuum signals.
Saves breakdown data and previous pulse
B. Woolley, J. Tagg

## Slide 17: Cooling system
Independent demineralized water system for Xboxes
  DT=10, 8Pa
  Feeds modulator, loads
Special chillers with temperature stabilization for structures and pulse compressors
  2kW average power
  0.1 degrees stability
Notes: ra

## Slide 18: Operation: Conditioning
The final pulse length and power is defined for each case
Conditioning algorithm sets a target value for vacuum level (network conditioning) or BDR (structures)
Real conditioning speed follows a complicated algorithm and is a function of the state of the DUT.
  Faster for lower power, shorter pulses or conditioned structures
Pulse length
Power
Time
Conditioning Parameter
target

## Slide 19: Operation: Radiation and shielding
Chart: Gradient (MV/m)
Measurements done around Xbox1
Data used for simulations of Xbox2 bunker
80cm shielding blocks
J. Vollaire

## Slide 20: Operation: Availability
Xbox1 and dogleg availability
estimated 63%
Not yet well established yet for Xbox2
A. DeGiovanni, B. Woolley

## Slide 21: Diagnostics: Accelerometers
6 accelerometers installed with dynamic range +/- 500 g
Aim at breakdown location
Under tests in Xbox2 for crab-cavity. See A. Degiovanni presentation
Wilfrid Farabolini

## Slide 22: Diagnostics: Spectrometer
Maximum electron energy < 20MeV
Real energy spread (single slit) 10-25%
Full energy coverage through a magnetic field scan
System under commissioning. Interesting data at B. Woolley presentation
Marek Jacewicz and Uppsala accelerator group

## Slide 23: Diagnostics: Calorimetric power measurements
Average power comparison
Directional coupler ~ peak power*pulse width*repetition rate
Calorimeter ~ specific heat*flow-rate*temperature difference
Xiaowei Wu et al. “Calorimetric power measurements in X-band high power RF”. IPAC 2015
Measurements taken in Xbox1 during CPI-1 commissioning
Good measurement in steady conditions
~50 s thermalisation delay
Tested in Xbox1
Being installed in Xbox2
Less than 7%!

## Slide 24: Schedule installation xbox3
Still procuring network waveguides, LLRF components and cables, solid state drivers.
Pulse compressors under fabrication with some brazing problems
  Last delivery expected in March
Installation from January.
  Some mimimum disruption to Xbox2

## Slide 25: Test schedule until 2016
Xbox1:beam loading experiment after Xmas shutdown
Xbox2: SLAC halves structure and installation in the bunker
Xbox3: Waveguide installation, cabling etc. in January

## Slide 26
Thanks for your attention!!!
Xbox
x