AHCAL Detector Interface electronics
AIDA 2020 first annual meeting, WP 14.4
New DIF
Jiri Kvasnicka
DESY Hamburg
14.6.2016

---
AHCAL Interface electronics
- Controls and reads up to 3 SLABs
  with 6 HBU each
- Major redesign of DIF (originally NIU)
- Redesign of POWER4, CIB (Central
  Interface Board)
- New production of CALIB2
- Redesign driving forces:
  - We had to replace the old FPGA (Spartan3)
  - Better power pulsing

---
DIF2
- Major redesign
- Zynq 7020 FPGA
- DDR3 memory (not used yet)
- Mini-USB (moved from CIB)
- Boots from:
  - JTAG (volatile)
  - QSPI FLASH (non-volatile)
  - µSD-card (non-volatile) – works only
    when DDR3 memory is on
- Different voltages
  - produced from 3.6V input: 3.3V, 2x2.5V, 1.8V, 1.0V, OC: 1.2V, DDR3: 1.35V and 0.65V
  - 5V from POWER4 for USB.
- Current consumption (everything on): 1.3A (~5W).
  - Without DDR3: 1A (~3.6W)

---
DIF2 Firmware
- Only FPGA part of ZYNQ used
- Changed design tool flow (ISE 14.7 → Vivado 2015.4)
- FW based on previous DIF
- Different clock distribution (Spartan3 vs. Artix7 resources)
- New commands for voltage control (incompatible with old DIF)
- First version worked out of the box
  => we could test all the functionalities before larger DIF2 production
- Firmware not final!
  - Unconstrained timing => many timing violations
  - Too much asynchronous logic
  - Major code review and retiming needed

---
POWER4 board
- Takes +4V, +12V, SiPM-Bias
  - No +6V any more
- Power dissipation significantly reduced!
- Power pulsing improved due to bigger capacitors
- Independent switching of voltage groups (matches new DIF)
- Improved software controlled adjustment of SiPM bias voltages

---
Cooling scheme
Hot spots have a thermal contact
to a copper cooling plate on top

---
Commissioning results
- Beam test @ DESY
- 1 bug if firmware fixed
  - stable afterwards
- Test of power-pulsing (single HBU)
  - no visible degradation of SPS from “MIP”
- Check of the timing of DIF2 (using external time reference – BIF)
  - no difference from old DIF

---
Summary
- New interface electronics delivered
- DIF2 firmware adopted from old DIF to a new FPGA
  - Commissioning successful
- Roadmap:
  - Q3 2015: Delivery of 4 DIF2 boards and 14 CALIB boards
  - Q4 2015: POWER4 boards and CIB delivered
  - Q1 2016: firmware for DIF2 ready, start of commissioning
  - Q2 2016: beam test @ DESY
  - Q3 2016: expected new batch of DIF2, POWER4, CALIB and CIB boards