AHCAL Beam Interface (BIF)
AIDA 2020 first annual meeting, WP 5
- Hardware
- Timing explained
- results
Jiri Kvasnicka
DESY Hamburg
14.6.2016

---
Beam InterFace (BIF)
- Mini-TLU without any hardware modification (→ talk by David)
  - FMC mezzanine card, 4 lemo inputs, 2 HDMI + 1 RJ45 DUT ports, 1 clock port
- Modified firmware (svn rev. 245) for operation as a slave device:
  - Clock distribution modified, whole BIF internally runs on the external clock
  - Learned the AHCAL fast commands from HDMI
  - External shutter for gating of the trigger data storage (only data within AHCAL readout cycle saved)
- Special cable for connection to CCC
- Software: EUDAQ (→ talk by Adrian)
Trigger
Spill
CCC
…
Up to 8
LDAs
EUDAQ
PC
LDA
PC
beam
trigger
BIF
DIF
HDMI cable
Clock (diff)
gnd
3 pairs
in RJ45

---
Timing: Introduction to AHCAL
- Two modes of operation:
- “Testbeam (TB) mode”
  - 4 us bunch crossing clock
  - External trigger validation → to eliminate SiPM noise in long acquisition
- “ILC mode”
  - 200 ns bunch crossing clock
  - No validation

---
Timing: Introduction to AHCAL
- Two modes of operation:
- “Testbeam (TB) mode”
  - 4 us bunch crossing clock
  - External trigger validation → to eliminate SiPM noise in long acquisition
- “ILC mode”
  - 200 ns bunch crossing clock
  - No validation

---
Spiroc time masurement: TDC principle
- A global TDC ramp for all channel
  - 2 physical ramps are multiplexed → 2 different slopes (=different color)
  - Different TDC ramp for ILC mode (not shown)

---
Timing of AHCAL and BIF
- A global TDC ramp for all channel
  - 2 physical ramps are multiplexed → 2 different slopes (=different color)
  - Different TDC ramp for ILC mode (not shown)...
- Time information is stored in the analog memory cells by
  sampling and holding the global TDC ramp value
...

---
- BIF and AHCAL run the same 40 MHz clock => everything synchronous
- BIF “time”: Timestamp difference from the current BX start (= from the BX clock edge)
- Where the BXID 0 starts? The AHCAL offset has to be calibrated
...

---
Results and experience
- Used by AHCAL group in:
  - Testbeam Nov 2015 (Spiroc2D single HBU)
  - Testbeam May 2016 (Spiroc2B, more layers)
- Useful for SPIROC TDC calibration
- We see the DESY beam structure in the
  histogram of time between two triggers
- Time between 2 events: 1.8 ns jitter
  => Single timestamp jitter: 1.3 ns
  - Includes jitter from scintillator, PMT, discriminator and coincidence units
  - Mini-TLU itself should be better
- Observed: UDP packet loss
  - UHAL library throws 1s timeout
    exception, but can recover
  - 1 readout cycle is typically lost
  - SW issue, HW counts correctly
- Firmware bug: end of acquisition data
  sometimes lost
- Test on table: 100 kHz trigger in AHCAL acquisition cycle timing sustainable (100x more than actual particle rate)

---
Summary
- Successful use case of mini-TLU as a slave device
- Beam interface (BIF) firmware was developed
  - Connects either to CCC or LDA via HDMI cable
  - Receives the system clock from outside
  - Receives and records AHCAL fast commands
  - Can be now easily modified for different external shutter protocol
- BIF already used in 2 beam tests
  - Perfect insight into the SPIROC TDC in beam conditions
  - We see a timestamp jitter of 1.3 ns (includes external electronics jitter)
- BIF Integrated into EUDAQ (producer based on mini-TLU producer)

---
backup

---
Readout cycle timing
- Busy signal tells other layers (or detectors), that it cannot take data
- Restart as soon as possible (as soon as all layers/systems are ready)\
- No time to sleep in TB mode
- ILC mode: fixed timing

---
Mini-TLU / BIF on SP605 board

---
SPIROC ILC mode (fast BX clock)

---
Results: TDC vs. BIF without any cut
AHCAL has 2 physical TDC ramps → 2 slopes