CMS-ECAL barrel upgrades for HL-LHC
- Legacy system
  - Today
  - Expected performances at LS3
- Upgrade constraints
  - Bounding conditions
  - Aging mitigation
  - Trigger constraints
  - Spike rejection
  - New features
- Upgrade scenarios
- On-going R&D
  - VFE
  - LV
  - FE
- Planning
Marc Dejardin
Irfu/SPP CEA-Saclay

---
Legacy system
- Modularity
  - 25 channels = 1 Readout unit
- Features
  - Trigger primitive generation
    - Trigger tower = 5x5 crystals
  - Pipeline, Event buffer in FE
    - 5 us
    - Full readout at L1-accept
    - Max 100 kHz trigger rate
FE card
FENIX
ASICS in 0.25um tech
STRIP
ASIC
FENIX
FENIX
GOL
800Mbps
STRIP
ASIC
TCP
ASIC
HSSer.
FENIX
STRIP
ASIC
FENIX
FENIX
GOL
800Mbps
STRIP
ASIC
DAQ
ASIC
HSSer
VFE card (5x)
FENIX
APD1; G=50
STRIP
ASIC
3 gain MGPA
 (5x)
PWO crystal
4p.e. / MeV to APD pair
PD1
QuadADC (5x)
PreAmp
ADC
APD2; G=50
Trigger etc.
PD2
Dynamic range 40MeV – 1.5TeV, 40ns RC-CR
Low voltage regulator board – 10 linear rad tol regulators

---
By LS3
- Noise
  - Evolution assuming present VFE design
- Spike rejection @L1
  (direct energy deposition in APD)
  - Online rejection= O(95%)(2012)
  - Sensitive to PU & APD Ileak
    - Sustainable up to LS3
400 MeV
250 MeV
140 MeV
100 MeV
40 MeV
LS3

---
Upgrade requirements
- Installation completed during LS3
- Comply to new trigger requirements
  - 12.5 μs latency (5 μs today)
  - 750 kHz L1 rate (100 kHz today)
- Mitigate spikes signals
  - Expect ~1 spike /bunch crossing
- Mitigate APD radiation damage
  - APD leakage current up to 200uA
    - Parallel noise increase /Worsen the spike signal tagging
- Mitigate Pileup
  - Out-of-time
  - In-time
- Maintain/Improve system reliability
  - Failure mitigation scheme
- All in one :
  - Try to restore initial ECAL performances

---
Boundary conditions
- Use back-end complying to CMS standard
  - e.g.: x-TCA
- Keep the mechanical
  structure as-is
  - Cooling system
  - Mother boards
  - Signal paths
    and connectors
You have to read-out here !
You have to plug here !

---
Upgrade concepts
- Put all algorithmic in OD electronics
  - Trigger-less FE
- Single crystal information available at L1
  - Synchronous readout of all crystal information
    - Improve trigger efficiency
    - Correlation with tracker info
- Reduce ECAL working temperature
  - 8 oC instead of 18 oC
    - APD Leakage current /2
    - Light yield +30%
- Reduce signal shaping time
  - Decrease parallel noise contribution
    - Goes like √τ
  - Improve OOT pileup mitigation
Trigger primitive
with 5x5 Xtals
LHC
Trigger primitive with 1 Xtal
Tracks matched
HL-LHC

---
The way to go
- Don't reinvent the wheel
  - Use common developments as much as possible
    - DC-DC converters
    - Optical links (lpGBT)
    - Off detector electronics
      - Common development with HGCAL, HB ?
      - Efficient calorimeter trigger generation
- Concentrate efforts on ECAL specific features
  - Optimize APD signal reconstruction
    - Mitigate leakage current increase
    - Improve spike signal mitigation
    - Improve pileup mitigation → Add timing information

---
APD signal conditioning
- Reminder:
  - Shaping as short as possible
    - Decrease parallel noise (APD leakage current mitigation)
    - Mitigate OOT pileup
- Options:
  - CR-RC shaper MGPA-like
    - Reduced shaping time
      - e.g: τCR-RC ~ 20 ns (~40 ns in legacy system)
    - Trade-off with ballistic deficit
  - Trans-impedance amplifier (TIA)
    - Shaping defined by TIA bandwidth (<50 MHz)
    - Hopefully more information on signal at high frequency
  - Gated charge integrator (GQI)
    - Enhanced version of QIE
      - resolution/radiation hardness
legacy MGPA
upgraded MGPA
TIA

---
Example: TIA R&D
- Design of TIA asic in TSMC 130 nm technology
  - Specifications :
    - Cdet=200 pF, Ileak from 10 uA to 100 uA
    - Emax = 2 TeV, Emin=100 MeV, 2 outputs : G1 and G10
    - Bandwidth <50 MHz
- Intended target
- Prototype
(P. Baron Irfu/SEDI CEA-Saclay)
ASIC
Gain1: range 0 -2 TeV
Filter
x1
TIA
50 MHz
Idet
ZT
ZT
Gain10: range 0 -200 GeV
Vout
Filter
Transimpedance
ZT = Vout/Idet [Ω]
x10
50 MHz
VFE test board
ASIC
TIA
ADC
(VME)
x1
driver
Idet
ZT
Vout
ADC
(VME)
driver
x10
ADC 12 bits
120/160 MSPS
ADC 12 bits
120/160 MSPS
APD
Idark
Cdet
100 nF
Idet
Filter
50 MHz
Filter
50 MHz

---
TIA architecture and performances (sim.)
Regulated common gate
Low input impedance
5
4.5
4
3.5
3
2.5
2
1.5
1
0.5
0
100
101
102
103
104
105
106
107
108
109
Frequency [Hz]
Noise
Dynamics
0.9
270
Rconv = 120 Ω
@ 50 MHz BW
260
0.8
250
240
0.7
230
220
0.6
210
Spike
200
0.5
190
180
0.4
170
0.3
160
Scinti.
150
0.2
140
130
0.1
120
110
0
100
0
0.2
0.4
0.6
0.8
1.0
1.2
1.4
1.6
1.8
2.0
0
10
20
30
40
50
60
70
80
90
100
E [TeV]
Ileak [μA]
R1
Rconv
M1
M2
Vout
Vdd
Idet
RB
Slope: 263 µV/GeV
Vmax [V]
Zin [Ω]
Noise [MeV]

---
G1 and G10 outputs performances (sim.)
G1 linearity
G10 linearity
0.40
0.45
Gain 1: slope= 211 nV/MeV
INL: +/- 0.13 %
Gain 10: slope= 1,93 µV/MeV
INL: +/- 0.5 %
0.40
0.35
0.35
0.30
0.30
0.25
0.25
0.20
0.20
0.15
0.15
0.10
0.10
0.05
0.05
0
0
0
20
40
60
80
100
120
140
160
180
200
0
0.2
0.4
0.6
0.8
1.0
1.2
1.4
1.6
1.8
2.0
E [MeV]
E [TeV]
G1 noise
G10 noise
260
240
Gain 10
Gain 1
250
230
240
220
230
210
220
200
210
190
200
180
190
170
180
160
170
150
160
140
150
140
130
130
120
120
110
0
0
10
10
20
20
30
30
40
40
50
50
60
60
70
70
80
80
90
90
100
100
Ileak [μA]
Ileak [μA]
Noise [MeV]
Noise [MeV]
Vmax [V]
Vmax [V]

---
System performances (sim.)
- Connect TIA to ECAL barrel
  - Add connection strip lines (a.k.a. kaptons)
Kapton Line parameters:
R = 0,05 Ω/cm;
L = 3,75 nH/cm;
C = 2,4 pF/cm
Length: 20 – 30 cm
Deal with 75-100 nH connections
Scintillation signal
Raw shape (wo kapton)
Connected with Rcomp=5 Ω
Connected with Rcomp=25 Ω
Drawback:
Noise ↑ (Ileak = 0 µA); Bandwith ↓; Timing↓
But:
Noise ↓(Ileak > 10-20 µA) since Bandwith ↓
0
10
20
30
40
50
60
70
80
90
100
120
140
Time [ns]
APD
Cdet
100 nF
Kapton
Rcomp
ASIC

---
System performances
Worse conditions: End of HL-LHC (sim.)
Timing resolution
Spike/scint separation @ 2GeV
Half Width at Half Maximum; Ileak = 100 µA @ 2 GeV
1000
Spike
With kapton
100
Scinti.
Without kapton
30
20
10
4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 19 20 21 22 23 24 25
1
10
100
E [GeV]
FWHM [ns]
G1 noise
G10 noise
230
220
220
210
210
200
200
190
190
180
180
170
170
160
160
150
150
140
140
130
130
120
120
0
10
0
20
10
30
20
40
30
50
40
60
50
70
60
80
70
90
80
100
90
100
Ileak [μA]
Ileak [μA]
Resolution [ps]
Noise [MeV]
Noise [MeV]

---
APD signal digitization
- Prepare for best online and offline analysis
  - Provide enough information for
    - Online spike tagging
      - Shape analysis
    - Timing measurement
    - Offline energy reconstruction with Pileup
      - Multifit algorithm
  - Investigate signal over-sampling
    - Benefits/costs of 80/160 MHz sampling
      - System performances gain
      - ADC design/cost
      - Data rate/volume
HL-LHC
LHC

---
Ongoing work
- Investigating use of commercial ADC core
- Check DC/DC converters compatibility
  with ECAL and CMS
  - Magnetic field
  - Induced noise on legacy system
- Get experience with GBT links
  - Upgraded FE board for legacy system
- Prepare test beam campaign to
  check working hypothesis
  - Prototype VFE with op-amp TIA
    - Check APD noise model, Ultimate timing resolution

---
Forthcoming major milestones
- Summer 2016: First Comprehensive Review
  - Evaluate concepts of VFE upgrade
- Q3 2017: Technical Design Report (TDR)
  - Evaluate technical specifications and expected performances of VFE, LVR, FE
  - Evaluate feasibility of SM cooling
  - Evaluate trigger strategy and online/offline performances
- Q3 2019: Engineering Design Report (EDR)
  - Technical validation of VFE, LVR and FE prototypes
- Q1 2021: Electronic System Review (ESR)
  - Assess readiness for production

---
Conclusions
- CMS barrel calorimeter upgrades project well defined
- Ambitious upgrade program
  - Recover ECAL performances after 10 years of running
  - Prepare detector for a new decade of data taking
  - Read enough information from detector to be versatile
  - Export all algorithms to back-end electronics
    - Freedom to tune algorithm to follow detector aging
    - Adapt to unforeseen “features”
- Rely on development from third party
  - DC-DC converters
  - lpGBT

---
Backup

---
CMS ECAL Barrel Anomalous events:
Spikes
CMS ECAL Barrel Anomalous events:
Spikes
Hadrons interacting with the APD’s causing anomalous high E deposits
Hadrons come from primary interaction and backsplash
APD
Crystal
HCAL
(2)

---
Spike rates
Spike rates
L1 Spike rejection in 2012 O(95%)
  - Rate sustainable up to LS3 with somewhat raised channel threshold
- Legacy Spike Rejection Algorithm is sensitive to PU (see plot ->)
- Exploring improvements having access to full granularity of data in the trigger path
  - Single crystal readout
- Exploring pulse-shape variables to provide an additional efficiency/rejection safety margin
  - Analogue Signal Processing

---
Data rate
- Hypothesis :
  - Oversampling @ 160 MHz
- 12 bits + 2 gains = 13 bits/sample
  - 10.4 Gb/s per VFE board
    - Above GBT capabilities
- 11 bits + 2 gains = 12 bits/sample
  - 9.6 Gb/s per VFE board
    - At the edge of GBT capabilities
- 12 bits + 2 gains
  + digital compression (LUT)
  = 11 bits/sample
  - 8.8 Gb/s per VFE board
    - Fit in 1 GBT link

---
Timeline of High Level Milestones
Timeline of High Level Milestones
Q2 2016:
VFE.HL.2016.1: Draft initial VFE ASIC specifications
LVR.HL.2016.1: Demonstrate feasibility of EB electronics with DC/DC
convertors instead of LV regulators
VFE.HL.2016.2: Define final VFE ASIC specifications - commence design
FE.HL.2017.1: First FE demonstrator with 5 Gb/s links
REV.HL.2017.1: Technical Design Report
LVR.HL.2017.1: Test beam appraisal of LVR board - benchmark performance
VFE.HL.2018.1: First prototype of VFE board available with new ASICs
FE.HL.2019.1: First FE prototype with 10 Gb/s links
LVR.HL.2019.1: Final validation of LVR board - demonstrate performance
VFE.HL.2019.1: Validation of overall concept (VFE+FE+LVR)
REV.HL.2019.1: Engineering Design Report
VFE.HL.2020.1: Accelerated ageing and radiation exposure of all 3 boards
OD.HL.2020.1: Validation of OD readout design
VFE.HL.2020.2: Test-beam verification of all components in SM, at lower temperature.
REV.HL.2021.1: Electronics Systems Review (readiness for production)
Q4 2016:
Q1 2017:
Q3 2017:
Q1 2018:
Q1 2019:
Q3 2019:
Q2 2020:
Q4 2020:
Q1 2021: