## Slide 1: ETF for IPv6
Marian Babik
Andrea Sciabà

## Slide 2: Setup
Hostname: etf-ipv6-dev.cern.ch
OS: SLC6
Networking: dual stack
  Disabling IPv4 altogether makes very difficult to manage the machine
  Configured Apache to listen on IPv6
    Listen [::1]:5000
  Forcing IP resolution to go via IPv6 by adding (some) testbed nodes to /etc/hosts with only their IPv6 address
HTCondor
  Configured to use IPv6 only via /etc/condor/condor_config
    ENABLE_IPV6 = True
    ENABLE_IPV4 = False
    NETWORK_INTERFACE = <IPv6 address>
BDII
  Using the dual-stack BDII at IC (topbdii.grid.hep.ph.ic.ac.uk) (thanks Duncan)
Tests
  Running the CMS SAM tests with a CMS certificate
    CE: Condor-G submission + WN tests
    SE: lcg-utils
Hosts
Added as many hosts as possible from those listed in https://hepix-ipv6.web.cern.ch/testbed-nodes
URL: https://etf-ipv6-dev.cern.ch/etf/

## Slide 3: Issues
The BDII discovery in the Condor probe is buggy, it had to be manually fixed by hard-coding the BDII (thanks Marian)
The CMS SRM tests had to be hacked to hard-code the PFN-to-SFN translation rules (as the tested SEs are mostly non-production)

## Slide 4: Results by host: CEs
ce04.esc.qmul.ac.uk
  CREAM, dual stack, in /etc/hosts only IPv6
  All tests OK
  Condor uses IPv6 but gsiftp uses IPv4??
ce05.esc.qmul.ac.uk
  CREAM, IPv4-only
  All tests OK apart from DNS6 check: IPv4 not really disabled in Condor?
ceprod05.grid.hep.ph.ic.ac.uk
  CREAM, dual-stack but no public IPv6 address
  All tests OK apart from DNS6 check: IPv4 not really disabled in Condor?
cetest01.grid.hep.ph.ic.ac.uk, in /etc/hosts only IPv6
  ARC-CE, dual stack
  All tests OK
  Gsiftp seems to be using both IPv4 and IPv6??
dc2-grid-25.brunel.ac.uk, in /etc/hosts only IPv6
  ARC-CE, dual stack
  Not found in BDII since December 17th (it used to be OK), in maintenance

## Slide 5: Results by host: SEs
dc2-grid-64.brunel.ac.uk
  DPM, dual stack
  All tests OK
f11-101-102-e-v6.gridka.de
  dCache, IPv6-only
  All tests fail, authentication failed: CMS VO not configured?
gfe02.grid.hep.ph.ic.ac.uk
  dCache, dual stack
  All tests OK
golias100.farm.particle.cz
  DPM, dual stack
  All tests fail, authentication OK but no directory for CMS VO
se01.esc.qmul.ac.uk
  StoRM, dual stack
  All tests fail, due to “Error reading token data header: Connection closed”
srm-pps.pic.es, in /etc/hosts only IPv6
  dCache, dual stack
  All tests OK
t2dpm1-v6.physics.ox.ac.uk
  DPM, IPv6 only
  All tests fail, due to “Error reading token data header: Connection closed”

## Slide 6: Conclusions
ETF for IPv4 ran unattended for the duration of the Xmas break without any issue at all!
Tests run mostly OK
Verified that SE tests go via IPv6
Condor tests show some strange behaviour
  ENABLE_IPV4 = False does not prevent submission to IPv4-only nodes
  CREAM still uses IPv4 for Gsiftp traffic
  ARC-CE appears to use both IPv4 and IPv6 for Gsiftp traffic
  Edgar reported that something similar happens fot the GRAM GT5 CE
  HTCondor CEs behave as expected (no IPv4 used)
ETF already shows to be very useful as a tool to monitor the testbed

## Slide 7: Next steps
Continue investigating why IPv4 is still (partially) used
Add any new nodes to the configuration
Fix some issues with the existing nodes (mostly SEs)
Add the LHCb tests
  Added value is the HTTP/Webdav tests
  They should not depend on any LHCb software or service
Add the ATLAS tests
  Added value is that they use GFAL2
  Work needed to make the probes VO-agnostic