## Slide 1
Magnet Temperature Measurement LHC
Máté Patalenszki Electronics engineering students @ University of Debrecen
Balázs Nagy
NI Big Physics Summit @ CERN Conference 2016

## Slide 2: The Team
Angéla Váradiné Szarka Dr
Kornél Sarvajcz
László Kazup
Ádám Papp
Balázs Nagy
Máté Patalenszki
Undergraduate Electronics Engineering Students
PhD Students
Acc Professor at Dept. of Electrical and Electronic Engineering
Márta Bajkó
Maryline Charrondiere
Leader of SM18, CERN
Technician at SM18, CERN

## Slide 3: University of Debrecen
LabVIEW Academy Institution

## Slide 4: EuCARD-2
Enhanced European Coordination for Accelerator Research & Development
13 Work Packages
MagNET@CERN

## Slide 5: SM18 – Cryogenic Test Facility
Testing superconducting magnets & instrumentation
10 test benches in horizontal or vertical position
Test on 1.9°K using up to 20kA current
Serial and prototype testing

## Slide 6: Testing Superconducting Magnets
Temperature measurement from ambient down to 1.9K
LHC Superconducting Magnet
Signal Conditioner for Each Sensor
Outputs of Each Signal Conditioner
Up to 20 sensors to measure
0.5% accuracy in the whole measurement range
Notes: Let’s talk about testing superconducting magnets. Superconductors works at 1.9K, so it’s very important to keep them at this temperature because a little increase can cause quench that means the

## Slide 7
One Signal Conditioner of Each Type
Outputs of Each Signal Conditioner
Switching Level
Aim of the Project
Up to 20 sensors to measure
0.5% accuracy in the whole measurement range

## Slide 8
Challenges
Accuracy: 0.5% in the whole measurement range
3 different measurements on each sensors:
- CERN signal conditioners - NI DMM 4 wire measurement
- Direct resistance mesurement between each 2 wires
Compact & mobile instrument

## Slide 9
NI Hardware - Requirements
Voltage, 4 wire resistance measurement
Control of the switching level
Mobility
Data storage
Wireless communication

## Slide 10
NI Hardware - Configurations
PCIe
PC is included in the chassis
DAQ card
cDAQ
Controller
AI module
PXI
Controller
DMM card
DIO module
DMM (USB)
DAQ card
DMM card

## Slide 11
One Signal Conditioner of Each Type
Outputs of Each Signal Conditioner
Switching Level
Block Diagram of the Instrument
DMM
DAQ

## Slide 12: Hardware – The Switching Level
Connecting sensor wires to the appropriate signal conditioner
Providing direct measurement for verification
Not exceeding 0.2% relative measurement error

## Slide 13: Switching Level - Specifications
Because of circuit considerations we decided to use analog switches
Switch caused realitve error <= 80 ppm
Final circuit based on the same specifications as NI PXI Modules

## Slide 14: Switching Level - Realisation

## Slide 15: Instrument Integration

## Slide 16: Software

## Slide 17: Software
Producer/Consumer Design Pattern
User Interface Loop
Measurement Loop
Load/Save sensor data
Load/Save configuration
Show online the result
Control the switches
Make measurements
Make data conversion
Save data

## Slide 18: Software – User Interface
Sensor Data Upload
Channel Configuration
Measurement Monitoring

## Slide 19: Software - Measurement
Initialize
(Create report file)
Measure
Convert
Between
Save
Save data to the result file
Show online the results
Voltage
Resistance
Temperature
Configure switches
Select the proper analog input or the DMM
Take measurement

## Slide 20: Summary

## Slide 21
Acknowledgement
The research is part of the EuCARD-2 co-funded by the partners and the EC-Capacities-FP7 under Grant Agreement 312453.
Speakers would like to thank the cooperation possibility to CERN, and to express special thanks for contribution and help to Marta Bajko, Maryline Charrondiere, Maria de Fatima Gomez de la Cruz, Huber Raymond.
Also the team wishes to express their appreciation to NI Hungary for accepting and hosting this project in the Open Laboratory, and personal thanks to Botond Barabás who has been done his best to provide all the necessary hardware for research, development and tests.

## Slide 22: Thank you for your attention