## Slide 1: EUV ERLs for Semiconductor Integrated Circuits Lithography
Norio Nakamura
High Energy Accelerator Research Organization(KEK)
ERL17, 18-23 June 2017, CERN, Geneva, Switzerland

## Slide 2: EUV-ERL Design Group
(KEK) T. Furuya, K. Haga, I. Hanyu, K. Harada,
T. Honda, Y. Honda, E. Kako, Y. Kamiya, R. Kato,
H. Kawata, Y. Kobayashi, T. Konomi, T. Kubo,
S. Michizono, T. Miura, T. Miyajima, H. Nakai,
N. Nakamura, T. Obina, K. Oide, H. Sakai, M. Shimada,
R. Takai, Y. Tanimoto, K. Tsuchiya, K. Umemori,
S. Yamaguchi, M. Yamamoto
(QST) R. Hajima
(Tohoku Unv.) N. Nishimori
The design study has been done under collaboration with a Japanese company.

## Slide 3: Outline
Introduction
Design of EUV ERL Source
S2E Simulation
Activities and Considerations for Industrialization
Summary

## Slide 4: Outline
Introduction
Design of EUV ERL Source
S2E Simulation
Activities and Considerations for Industrialization
Summary

## Slide 5: EUV Lithography
EUV Lithography :
・ Next generation lithography using extreme ultraviolet light (13.5 nm)
・ Allows exposure of fine circuit pattern with a half-pitch below 20 nm
・ Laser-produced plasma(LPP) source is under development for ≥ 250 W
H. Mizoguchi et al., Komatsu Technical Report 59-166 (2013)
Concept of LPP EUV source
H. Mizoguchi et al., Proc. of SPIE 10143, 101431J (2017)
Schematic of EUV exposure tool
EUV ERLs (EUV FEL sources based on ERLs)
・ Meet future demand for 1 kW EUV power or more
・ Distribute 1-kW class power to multiple scanners  more economical
・ Produce no debris contaminating the EUV optics
・ Reduce dumped beam power and activation drastically

## Slide 6: Compact ERL(cERL)
Beam Energy: 20 MeV
RF Frequency: 1.3 GHz
in operation at KEK since 2013
cERL technologies and resources are available for EUV ERLs.
History of achieved beam current
plan of kW-class IR FEL

## Slide 7: Outline
Introduction
Design of EUV ERL Source
S2E Simulation
Activities and Considerations for Industrialization
Summary

## Slide 8: Image of EUV-ERL Source
Main SC Linac
Injector Linac
Beam Dump
Undulators(FEL)
1st Arc
2nd Arc
Chicane
~200 m
~20 m
Gun
Merger
Injector Diagnostic Line
Beam energy: 800 MeV
RF frequency: 1.3 GHz
©Rey.Hori/KEK
EUV Light
Parameter | Design value
Injection Energy | 10.5 MeV
Beam Energy | 800 MeV
Bunch Charge | 60 pC
Repetition Rate | 162.5 MHz
Ave. Current | ~10 mA
Acc. field | 12.5 MV/m
EUV Wavelength | 13.5 nm
EUV power | > 10 kW

## Slide 9: Injector & Merger
Merger section (top view)
recirculation loop
matching section
Injector section (side view)
electron beam
Einj~10.5 MeV
injection point
B : Bending magnets（θ=15°, ρ=1m）
Q : Quadrupole magnet
cERL Injector cryomodule
Cryomodule design
Vacuum Vessel
5K Panel
2K He Jacket
5K Support
80K Base-plate
80K Shield
2K Gas
Return Pipe
5K Panel
5K Duct
e-
Input Coupler
2-cell Cavity
HOM Coupler
2-cell SC cavity
Input coupler
cavity cells
HOM coupler
Cathode
(-500kV)
Anode
(0V)
Electron
beam
Segmented
ceramic duct
NEG pump
Ti chamber
Photocathode DC gun
Buncher cavity
Solenoid magnets

## Slide 10: Main Linac
Cryomodule(4 cavities)×２
Quadrupole
triplet
Quadrupole
triplet
Basic unit of main linac structure
 | cERL | EUV ERL |  | cERL | EUV ERL
Frequency | 1.3 GHz | 1.3 GHz | Iris diameter | 80 mm | 70 mm
Rsh/Q | 897 Ω | 1007 Ω | Qo×Rs | 289 Ω | 272 Ω
Ep/Eacc | 3.0 | 2.0 | Hp/Eacc | 42.5 Oe/(MV/m) | 42.0 Oe/(MV/m)
cERL cavity
EUV ERL cavity
Under design. A large-aperture pipe will be also applied to the left side.
Stable operation at 8.5 MV/m (cERL)  12.5 MV/m (EUV-ERL)
Main linac (9-cell cavities × 64 in 16 cryomodules)

## Slide 11: Arc Sections
r =2.2 m, q =p/6 rad,
LB=1.15 m, LQ1=LQ6=0.2 m
LQ2-Q5=0.3 m, LS=0.2 m
R56= 6r (q - sinq ) =0.3115 m
21.3 m
3 DBA cells
1st arc lattice
2 TBA cells
21.3 m
r =3 m, q =p/8 rad,
LB=1.178 m, LQ=0.4 m,
LS=0.2 m
R56: -0.25 m (tunable)
2nd arc lattice
t
p
e-
Bunch compression
(1st arc, R56 > 0）
t
p
t
p
t
p
Bunch decompression
(2nd arc, R56 < 0）
e-
Blue：Bending magnet
Red： Quadrupole magnet
Yellow：Sextupole magnet
Optics are optimized for bunch compression and decompression.

## Slide 12: Undulator System for FEL
Undulator System（including matching section）
….
Exit of 1st arc
e- beam
….
Matching Section
Undulator System（FEL）
Undulator segment
(K=1.652, lu=28 mm)
QMs for focusing
1.12m
4.9m
Circularly-polarizing undulator
developed at KEK
QMs for optics matching
Parameters of undulator system to be optimized
（１）Undulator period and K-value (magnetic gap)
（２）Segment length and gap between segments
（３）Magnetic strength of QMs for focusing
（４）Undulator tapering
Adjustment of Twiss parameters βx,y,αx,y@ FEL entrance
for maximizing FEL output power
18 units

## Slide 13: Outline
Introduction
Design of EUV ERL Source
S2E Simulation
Activities and Considerations for Industrialization
Summary

## Slide 14: Injector & Merger
Bunch charge: Qb=60 pC, Injection energy: Einj=10.5 MeV, Bunch length: st ~ 1 ps
Injection beam optimization by GPT and genetic algorithm
e-
-20
-10
0
10
20
x[mm]
-20
-10
0
10
y[mm]
20
-5.0
-2.5
2.5
t[ps]
5.0
18.0
19.0
21.0
22.0
20.0
23.0
p/mc
entrance of main linac
enx=0.65 mm mrad
eny=0.73 mm mrad
st=1.08 ps
sp/p=0.347 %

## Slide 15: Bunch Compression
e-
st=47.4 fs
sp/p=0.112 %
enx=2.02 mm mrad
eny=0.72 mm mrad
exit of 1st arc
5ps
Peak current Ip > 700 A
Slice enx/eny ≈ 1.2/0.7 mm mrad at I=Ip
Current&slice emittance
st=1.04 ps
sp/p=0.103 %
enx=0.66 mm mrad
eny=0.72 mm mrad
entrance of 1st arc
E=800 MeV
st=1.08 ps
sp/p=0.347 %
enx=0.65 mm mrad
eny=0.73 mm mrad
entrance of main linac
E=10.5 MeV
simulation by elegant

## Slide 16: FEL
e-
PFEL > 10 kW is achieved.
(PFEL=88.5 mJ x 162.5 MHz =14.4 kW, Iav=60pC x 162.5 MHz=9.75 mA)
FEL power without tapering: 12.9/25.8 kW @ 9.75/19.5 mA (162.5/325 MHz)
FEL power with 2% tapering: 14.4/28.8 kW @ 9.75/19.5 mA (162.5/325 MHz)
79.5 mJ
88.5mJ
bandwidth of
Mo/Si reflectivity
<gb>=1564.0
st=47.4 fs
sp/p=0.113 %
enx=2.00 mm·mrad
eny=0.72 mm·mrad
<gb>=1561.1
st=48.5 fs
sp/p=0.299 %
enx=1.98 mm·mrad
eny=0.71 mm·mrad
Energy spread is increased.
simulation by Genesis

## Slide 17: Bunch Decompression
Electron beam is transported without beam loss.
e-
st=48.5 fs, sp/p=0.299 %
exit of FEL
enx/eny=1.98/0.71 mm mrad
2cm
sx=3.10 mm
sy=0.034 mm
point of maximum beam size
pipe aperture of cERL arc
exit of main linac
st=2.51 ps
sp/p=1.55 %
5ps
enx=6.52 mm mrad
eny=0.70 mm mrad
E=10.5 MeV
st=2.35 ps
sp/p=0.295 %
exit of 2nd arc
enx=7.68mm mrad
eny=0.70 mm mrad
E=800 MeV
simulation by elegant

## Slide 18: Outline
Introduction
Design of EUV ERL Source
S2E Simulation
Activities and Considerations for Industrialization
Summary

## Slide 19: EUV-FEL Light Source Study Group for Industrialization
since 2015

## Slide 20: EUV-FEL Workshop
Date: 13 Dec 2016 10:00-17:00
Site: Akihabara UDX 4F NEXT-1
Participants : > 100
(Source group, tool and material venders, end users etc.)
URL: http://pfwww.kek.jp/PEARL/EUV-FEL_Workshop/

## Slide 21: Availability Issues
Electron gun
  Short photocathode lifetime ( one week for ~10 mA )
  Remote control of photocathode exchange
SC Cavity
  Reduction of trip rate
  Pulse processing time for suppression of field emission increase
Undulator
  Demagnetization of permanent magnets
Cryoplant
  High pressure gas safety law
  Safety inspection (once per year in Japan)
Required availability for industrialization: ≥ 98 %
( non-operation time ≤ ~ 1 week per year)

## Slide 22: Cathode Preparation System
Vacuum
Suitcase
(Option)
Cathode
Storage
Atomic H
Cathode Cleaning
NEA
Activation
Cathode-container
Loading
Cs & O2
Gun chamber
Cleaning
chamber
Activation
chamber
Storage
chamber
Heating
Activate & storage
6~9 cathodes per day.
Short dead time for
exchange cathode
during gun operation.
Gate
valve
Courtesy of M. Yamamoto
cathode preparation system at KEK

## Slide 23: Trip of SC Cavities
3rd run（5 weeks）
(2014/5/20-6/20)
4th run（9.5 weeks）
(2015/1/26-4/4)
5th run（5 weeks）
(2015/5/25-6/27)
6th run（7 weeks）
(2016/2/15-3/31)
LLRF change
High gain
 Medium gain
8.57MV×2
ML1:10MV, ML2: 7.16MV
8.57MV×2
Courtesy of H. Sakai
No trip
(2/9～3/23)
Number of trips
Date(year/month)
Trips of cERL Main Linac Cavities

## Slide 24: Redundant System
Redundant System for ensuring high availability
  Critical parts (Cryoplant, Injector, Main Linac, Undulator, … )
  Entire light source system

## Slide 25: Reduction of Source Size
Higher field gradient of Main SC cavities
  Increase of power consumption ∝ Eacc2/Q
  High-Q SC cavity (Nitrogen doping etc.)
Lower Beam Energy
  Shorter-period undulator with strong magnetic field
  Increase of current or energy conversion efficiency for the same FEL power
2-loop/2-turn ERL
  Optics design for CSR effect suppression
  Increase of current for the same FEL power

## Slide 26: Outline
Introduction
Design of EUV ERL Source
S2E Simulation
Activities and Considerations for Industrialization
Summary

## Slide 27: Summary
EUV ERLs are expected to be high-power EUV sources for lithography that meet future demand.
An EUV ERL source has been designed with available technologies and resources and its performance has been checked by S2E simulation.
  Generation of FEL power more than 10 kW at 10 mA in the designed EUV-ERL source
  Successful transportation of electron beams throughout the EUV-ERL source without any beam loss
We established the source group for industrialization and organized the EUV-FEL workshop. R&D efforts are required for industrialization to achieve high availability, size reduction and so on.

## Slide 28: Thank you for your attention!

## Slide 29: Backup Slides

## Slide 30: Suppression of CSR effects
DBA lattice can well suppress CSR effects on ERL beam.
Electron distribution after bunch compression
Initial parameters: Qb=60 pC, enx=eny= 0.7 mm mrad, sp/p=0.31 %, st,inj=1 ps (Gaussian beam)
Projected normalized horizontal emittance
DBA arc (R56=0.31 m, bx2=0.5 m, ax2=1.9)
TBA arc + chicane (R56=-0.15/-0.15 m)

## Slide 31: Optics of Recirculation Loop
Betatron function [m]
Dispersion function[m]
Main linac（deceleration）
2nd arc
M3
M4
(2) Bunch decompression (after FEL)
E=10.5 MeV
E=800 MeV
Main linac
1st arc
M1
Betatron function [m]
Dispersion function[m]
(1) Bunch compression (before FEL)
M2
E=800 MeV
E=10.5 MeV

## Slide 32
32
Operation of Gun & ML Cavities
Entering
acc. room
Gun voltage
( kV)
Gun
2 weeks
Main cavities
(ML-1, ML-2)
RF voltage
(MV)
2 weeks
Dispersion measurement
Entering
acc. room
in 2015
in 2015
Conditioning
Gun operation (2015/2/16-2015/3/2)
ML operation (2015/2/16-2015/3/2)
No trip
No trip