## Slide 1: Twin-Axis Elliptical Cavity
Frank Marhauser, Andrew Hutton Jefferson Laboratory (JLab), Newport News
Jean Delayen, HyeKyoung Park, Subashini De Silva, Laura Sweat Center for Accelerator Science (CAS), Old Dominium University, Norfolk
ERL Workshop, 18-23 June 2017, CERN

## Slide 2: Principle Idea
Twin-axis elliptical cavity can accelerate and decelerate beams in two separate beam pipes
Primary idea of proposal for twin-axis cavity was that the low energy (vulnerable) beam from the electron source has to be merged with high-energy (spent) beam
Usable for high-current, low energy electron beams for bunched beam cooling of high-energy protons or ions (JLEIC cooler ERL)
  Energy recovery feasible of physically separated beams traversing the same cavity
  Twin-axis cavity allows injecting the beam without requiring bends (no complex merger magnet) as beams are separated physically
  Allows maintaining small emittance from source (high brightness)
Second idea related to the ability to dump beam without an intervening bend thus containing beam size (otherwise large energy spread and emittance of decelerated beam)
  Improve feasibility of recovering energy of otherwise fully dumped beam  out-couple RF power, e.g. feed back to injector
  Ease dump design, i.e. energy can be lowered to minimize activation
Notes: Red Interior Page Design 1

## Slide 3: Funding Opportunity
Funding for this project provided by the US DoE Office of High Energy Physics as part of an Accelerator Stewardship Test Facility Pilot Program (“ASTFPP”) initiated in 2015
Work effort required beyond the one year period is based on no-cost extension
No follow-up phase was permitted through same stewardship program
Our proposal was award in August 2015 for a one-year duration
Pre-requisite of the stewardship program was partnering with a university (in our case ODU/CAS) and engaging a graduate student in the research
Mission of long-term accelerator R&D stewardship program is to
  Support fundamental accelerator science and technology R&D
  Disseminate accelerator knowledge and training
The new ASTFPP specifically endorses access to the Office of Science accelerator R&D infrastructure
Notes: Red Interior Page Design 1

## Slide 4: Objective
Design, optimize, and build a novel twin-beam axis superconductive RF cavity prototype (single-cell) for ERLs
Prototype is proof-of-principle of technical feasibility
To our knowledge this is the first twin-axis cavity built despite past, similar proposals and conceptual design studies
Operational mode conceived is a dipole HOM (TM110-like)
  Requires to symmetrize RF fields in beam tubes by design
  Minimization of higher order multipole components of operating mode needed that can cause residual kick to electrons even when beams traverse on ideal tube axis
Further design/practical goals:
  Target a rather large separation of the beam tubes
  Limit surface field enhancement ratios (Eacc/Epk, Bpk/Eacc) to acceptable values
  Achieve acceptable R/Q and R/Q·G (cryogenic losses)
  Gain fabrication experience while using conventional, readily applicable techniques, i.e. forming of Nb sheets into half cells, rolling of beam tubes and join all components by electron-beam welding (EBW)
  Assess (to some extent) potential multipacting barriers and structural integrity
  Frequency chosen is 1.5 GHz (JLab/CEBAF), but design scalable to any frequency
Notes: Red Interior Page Design 1

## Slide 5: Past Proposals
  Lower the beam energy in the injector
  Avoid a complex injection beam line and optics
  May allow to increase charge/current maintaining low beam emittance
  Deliver beam to ERL and FEL simultaneously
TM-110 mode is monopole mode (TM010-like)
TM-210 mode is operational mode (TM110-like)
Squeezing the center of twin-axis cavity provides better balance of RF fields around two beam axes (favors weakly coupled structure, but not simple to press)
Later conceptual design (ANL - ERL 2007) using two more interleaved cavities
Potential of multi-beam axis cavities for ERLs identified early (KEK - SRF 2003)
Notes: Red Interior Page Design 1

## Slide 6: Design Evolution
Notes: Red Interior Page Design 1

## Slide 7: Multipacting (MP) Studies
Impact energy of electrons surviving 50 RF cycles. MP barrier below Eacc = 4 MV/m
Electrons with resonant MP trajectories
at cell equator (impact energy in eV)
MP barrier below 4 MV/m vanished (MP barrier beyond 16 MV/m still possible)
3D ACE3P/Track3P resonant MP studies performed up to Eacc = 16 MV/m
  Electron impact energy range of 50-2000 eV considered
Eacc = 15 MV/m is an envisioned operating field
final design (increase equator axis)
Notes: Red Interior Page Design 1

## Slide 8: Final RF Design
RF magnetic field plots
Bpk
1.5 GHz design
136.44mm
 = 60 mm
RF electric field plots
Transverse field components of operating mode minimized at beam tube centers
Beam tubes slightly shifted off the peak electric field to cancel dipole effect
@ Eacc = 15 MV/m  Bpk = 78.9 mT
Notes: Red Interior Page Design 1

## Slide 9: Design Parameters - Comparison
Parameter |  | New JLab/ODU Design | KEK Design (2003) weak to strong coupling | JLab (KEK-type) Strong coupling | JLab (KEK-type) Weak coupling | Single-Tube Standard Cavity (C100 LL)
Operational mode |  | TM110 | TM110 | TM110 | TM110 | TM010
Epk/Eacc |  | 2.33 | 1.9-2.1 | 2.26 | 2.20 | 2.17
Bpk/Eacc | mT·(MV/m)-1 | 5.26 | 4.0-5.6 | 6.13 | 5.87 | 3.74
R/Q – US def. | Ohm | 61.8 | 57-63 | 62.9 | 62.5 | 103.71
G | Ohm | 313.8 | 210-250 | 266.5 | 270 | 282
R/Q·G | Ohm2 | 19377 | 11550-14931 | 16773 | 16875 | 29270
KEK design
JLab/ODU design
strong coupling
weak coupling
Notes: Red Interior Page Design 1

## Slide 10: Deep-Drawing of Half Cells
coining ring
hole punch die
male die
female die
blank holder
Deep-drawing study done with Al and Cu discs (1/8” = 3.175 mm thick material)
Cu
Al
blank shape for studies
final Nb blank shape (wire EDMed)
Notes: Red Interior Page Design 1

## Slide 11: Fabrication Flow Chart
after rolling
1st prototype twin-axis cavity
made from high RRR Nb (cavity #1)
Notes: Red Interior Page Design 1

## Slide 12: Mechanical Fabrication Completed
after rolling
We actually have built 2 prototype cavities concurrently
Cavity #1
Cavity #2
One concern was that electron beam welding (EBW) requires full penetration weld along a rather complex curvature with varying beam current
cavity in EBW chamber
outside machining on half cells for full penetration weld
equator weld prep
Notes: Red Interior Page Design 1

## Slide 13: EBW Experience – 1st Prototype
after rolling
Kyoto camera inspection
Outside machining of equator done based on ideal cavity contour
Does not take into account spring-back effect of cell material after forming
Equator thickness variations along perimeter was actually on the order of ~1 mm
Welder decided to weld, but faced issues:
  2) No full penetration weld achieved on narrow sides after 1st weld pass  2nd weld pass conducted all around perimeter for repair (twice the weld shrinkage)
  1) Few blow-thru holes  needed to be patched by local re-weld
Deep patches likely limit performance
  Attempt will be made to locally grind blemishes with grinding tool
Centrifugal barrel polishing is an option depending on outcome
Cell 1: 0.076-0.112” [1.93-2.82 mm]
Cell 2: 0.068-0.108” [1.73-2.74 mm]
Notes: Red Interior Page Design 1

## Slide 14: EBW Experience – 2nd Prototype
Lessons learned applied to 2nd prototype
Outer contour of half cells as pressed has been recorded with CMM
Inner contour machined with reference to actual outer profile to provide better uniformity of equator thickness around perimeter (0.07” ± ~0.01”)
outer cell contour as measured with CMM
Full penetration weld achieved on 1st pass, overall cleaner weld seam
However: still few holes blown thru, needed local patches
clean weld seam
Irregularity, varying e- (this is not a patch)
Endgroup equators machined at interior to achieve nearly
uniform thickness
endgroups after final
machining
2nd prototype cavity after equator welding
Notes: Red Interior Page Design 1

## Slide 15: Summary
Design and fabrication of new twin-axis single-cell cavity completed
  Few holes were blown thru and needed local re-welding
No major feasibility issues concerning production, but several lessons learned as part of prototyping:
Actually delivered 2 prototypes (extra cavity beyond scope, but within budget)
  Equatorial electron beam weld of curved perimeter is not standard, full penetration weld needed (riskier than outside/inside weld)
  Welding issues likely avoidable if more time would have been available for practicing welds
  Equatorial weld preparation improved for 2nd prototype by proper machining based on measured contour after forming  full penetration achieved without 2nd weld pass, overall improved quality of weld seam
First proof-of-principle, while using standard fabrication techniques
  Weld parameter/current changes, JLab welding machine is mature and programming did not allow to vary parameters smoothly, but stepwise
Notes: Red Interior Page Design 1

## Slide 16: Summary
So what’s next?
  Cavity #1 interior will be grinded, CBP considered
  But cavity #2 will proceed to vertical RF baseline test as-is in parallel
Chemical post-processing (bulk BCP) is panned for cavity #2
  High pressure rinse hardware under development
One design benefit:
Bpk
Bpk = 0
Vertical test coming soon (all still within budget)…
Notes: Red Interior Page Design 1

## Slide 17: In Memory of My Beloved Brother
Jost Marhauser
24. Aug. 1973 – 23. July 2016
Notes: Red Interior Page Design 1

## Slide 18: Back-Up Slides and Additions

## Slide 19: Target Frequency
Target frequency is 1497 MHz at 2K under vacuum, but exact frequency not important for vertical testing (large RF bandwidth)
For this reason we did not trim half cell equators based on frequency measurements (would need dedicated RF fixture), but aimed for nominal length (incl. weld shrinkage)
Unfortunately, all (4) endgroups were inadvertently trimmed considerably too short
Based on length shortage, the expected frequency (warm, air) is 1499.64 MHz
  Cavity #1 measured: 1506.03 MHz
  Cavity #2 measured: 1501.27 MHz
  Discrepancy is f = 4.73 MHz, double weld-shrinkage for cavity #2 only accounts for 1 MHz
  Rest are fabrication tolerances, note: spring-back effect can be large (several MHz)
TM110 trimming sensitivity for endgroup is 4.16 MHz/mm
Notes: Red Interior Page Design 1

## Slide 20: Mechanical Stiffening of Cavity
after rolling
Heat treatment for H2-degassing (typically at 800 °C) reduces Young’s modulus (YM) of high RRR Nb material (100 GPa to ~30 GPa)
  Need to consider worst case when YM ~ 30 GPa and yield strength ~ 30 MPa
G.R. Myneni et al., Proc. of SRF 2003
  SSR = Slow Strain Rate is 5.561e-5 s-1
  FSR = Fast Strain Rate is 2e-4 s-1 up to yield point and 1e-3 s-1 until break
Beam tubes deflect when cavity evacuated
no stiffener
1 ksi ~ 6.895 MPa
  Added minimal stiffening between tubes to stay within the elastic range
  Chemical vapor-deposition of Nb3Sn considered at later stage (T = 1200°C)
with stiffener
Stress linearization along thickness (Membrane stress) resulted in only 11.8 MPa
VTA setup with gravity and outside pressure of 0.133 MPa considered
Notes: Red Interior Page Design 1

## Slide 21: 2-Beam Excitation Scheme
Conventional TM010 cavity
2 beams counter-propagating (ERL mode)
acc. beam
dec. beam
e-
e-
Beam excitation can be resembled numerically with 2-beam excitation scheme to calculate broadband coupling impedance or loss factor
Twin-axis TM110 cavity
- 2 beams co-moving (ERL mode)
e-
e-
acc. beam
dec. beam
Drawback: In twin-axis cavity monopole modes may have dipole components to kick the beam away from tube axis and transverse HOMs can be excited on tube axis since long. field components may exist
How to quantify drawback without specific ERL design and optics?
  Accelerating and decelerating beam in cavity cell at the same time

## Slide 22: 2-Beam Loss Factor
Expect larger energy deposition in parasitic modes for twin-axis cavity compared to standard single-axis cavity
Machine and beam-pattern dependent BBU impedance instability threshold must be considered
HOM-damping necessary
Avoid beam spectral lines by design

## Slide 23: 2-Beam Coupling Impedance
Operating mode - zero beam loading
Bare cavity
TE11 cutoff
Unresolved (bare cavity) broadband coupling impedance on tube axes

## Slide 24: 2-Beam Coupling Impedance
TESLA-type coaxial couplers (scaled – no optimization)
Preliminary study – add HOM couplers (beyond scope funded project)
TE11 cutoff
TESLA-type coaxial couplers (scaled), no further optimization
Critical HOM impedance can be damped further with adequate coupler design – up to 4 beam tubes available

## Slide 25: Prospect for Multi-Cell
Single-die design built in consideration of fabrication of a multi-cell cavity
HOM-damping studies beyond scope of funded project
Notes: Red Interior Page Design 1

## Slide 26: Alternative
Two independent cavities, one resonant coupling cell for TM010 operational mode (only)
  Threshold current for instabilities increase by factor ~5 compared to symmetric cavities
Mitigate regenerative BBU with cavities of slightly different shape and decoupled HOMs