## Slide 1
Michael Abo-Bakr
Institute for Accelerator Physics
Helmholtz-Zentrum Berlin
Beam Dynamics and Optics Challenges of
the Berlin Energy Recovery Linac Project
ERL17: 59th ICFA Advanced Beam Dynamics Workshop on Energy Recovery Linacs – CERN, Geneva, 20.06.2017

## Slide 2
Outline
Introduction: bERLinPro
ERL Beam Dynamics & Beam Optics
  Goal Beam Parameter & Energy Recovery Issues
  Linear Beam Optics
  Nonlinear Beam Optics
  Collective Effects
    space charge effects
    CSR – coherent synchrotron radiation
    BBU – beam break up

## Slide 3
beam dump
6.5 MeV, 100 mA
 650 kW
linac module
3 x 7 cell srf cavities
44 MeV
modified Cornell booster
3 x 2 cell srf cavities
4.5 MeV
srf-gun
1.4 cell srf cavities
1.5-2.3 MeV, single solenoid,
Basic Parameter | value
maximum beam energy | 50 MeV
maximum current | 100 mA (77 pC/bunch)
normalized emittance | < 1 mm mrad
bunch length | 2 ps (~100 fs)
repetition rate | 1.3 GHz
relative losses per turn | < 10-5
bERLinPro – Berlin Energy Recovery Linac Project

## Slide 4
bERLinPro – building: technics and accelerator hall
From an artists view to …
A. Jankowiak:
“Status of bERLinPro”
Wed 08:55
J. Kühn:
“Semiconductor Photocathode development for the bERLinPro photo injector”, Mon 11:15
A. Neumann:
“The bERLinPro SRF Photoinjector system”
Wed 17:25
accelerator hall
GunLab

## Slide 5
bERLinPro Beam Dynamics: Goal Parameter & ERL Issues
Goal Beam Parameter:
  efficient “Energy Recovery”
    adjust recovery conditions: rf phase advance & path length
    minimize losses of high current beam:
      small transverse beam size, dispersive regions  small E-spread
      halo: avoid, remove, transport
      instabilities: maximize threshold currents
  maintain beam quality from source
    transport beam preserving the emittance
  bunch manipulation: compression
    increase longitudinal bunch density as far as energy spread and transverse emittance degradation allow  user experiment
many issues known from SRs and/or Linacs
Notes: RF power, machine damages

## Slide 6
Linear and Nonlinear Beam Optics
  energy recovery  phase advance tuning
  beam manipulation  short pulses in ERLs
  beam transport without emittance degradation & losses
  high power beam dump & MPS
  requirements for beam diagnostics & commissioning
  error studies  misalignments effects of magnets and cavities
  tolerance & acceptance studies  hardware specification
  halo & dark current  low losses
    McAteer: “Dark Current and Halo Tracking in ERLs”, Thu 8:55
Notes: RF power, machine damages

## Slide 7
Linear Beam Optics: recovery phase & path length
t
V
on crest
acc
recirculator passage time: LRec / (bc) = (n + ½) Trf (½ Trf = 180° rf phase advance)
path length may change: v = f(E), misalignments & field offsets  orbit oscillations, switch between acceleration & deceleration (n ↔ n+ ½, multi-turn ERLs)
 adjust RF frequency: frf , Trf 
 adjust recirculator length Lrec
(Linear) Beam Optics: recovery of energy by passing the linac @ dec. phase
on crest: jdec = jacc + 180°
of crest: jdec = 180° + jacc
jdec = 180° – jacc

of crest
acc
Arc 2
options: - extra chicane
- inside arc
- moveable arc
3
1
2
1
2a
3
1
2
2b
bERLinPro

## Slide 8
Linear Beam Optics: beam manipulation
choice of bunch length / compression?
  injector, merger: long  reduced SC effects, short  minimize rf curvature
  linac: long  reduced beam loading to HOMs, short  minimize rf curvature
  recirculator: long  reduce SC, CSR, wakes, short  experiment / project goal
bERLinPro: 6-8 ps (laser/cath.)  4-5 ps (merger/linac)  2 ps (~100 fs) (recirc.)
Before deceleration: decompress bunch to restore chirp & minimize sE  R56,Arc2 = -R56,Arc1
R56,Arc2 = R56,Arc1  inverted chirp  jdec = 180° – jacc with unbalanced beam loading
many techniques: bunch compression, emittance exchange, laser heater, …

## Slide 9
linac
injector: gun & booster
merger
recirculation
arc 1
beam dump & dump line
splitter
recirculation
arc 2
straight section
bERLinPro = one stage ERL:
Injector  Merger  Linac(acc)  Arc1  Straight Section 
Arc2  Linac(dec)  Splitter  Dumpline & Dump
Linear Beam Optics: bERLinPro
injectior / merger / splitter / dumpline:
  low energy beam transport
  merge / separate low & high energy beams
  first stage of bunch compression
linac section:
  merger / splitter chicanes
  matching to injection line, arcs and dump line
recirculator arcs & straight section:
  2 x 180° total bending angle
  final bunch compression
  sufficient space for user experiments in the straight section
section requirements:

## Slide 10
only one magnetic element: solenoid
beam dynamics dominated by SC
   emittance compensation
emittance: en,xy < 1 mm mrad
Linear Beam Optics: bERLinPro Injector
energy
rms beam size
Twiss parameter

## Slide 11
Linear Beam Optics: Merger / Splitter
Mergers for existing and proposed ERLs:
  (a) JLAB IR-demo, IR-upgrade,
  Cornell ERL, Daresbury ERLP
  (b) JAERI-ERL
  (c) BINP-ERL
  (d) BNL-ERL (proposed)
design considerations:
  length & hardware
  chromatic properties, R56 range
  SC sensitivity / e compensation
bERLinPro

## Slide 12
bERLinPro: merger
bERLinPro: merger
beam dynamics dominated by SC
  emittance compensation continued
  beam transport in dispersive section: e-growth (“space charge dispersion”)
first stage of compression
   rf curvature limits R56
jbend = 20°
R56 = 10 cm
Linear Beam Optics: Merger / Splitter
Qb = 77 pC
ex = 0.63 mm mrad
ey = 0.52 mm mrad
gun
booster
merger
linac

## Slide 13
Linear Beam Optics: Linac Section
rf focusing in the linac (with few/no quads)
two (or multi) energy beam optics: matching beam optics from merger (LE) & Arc2 (HE) and into Arc1 (HE) & Dumpline (LE)
adjust b-function in the linac cavities for maximum BBU threshold current
include merger and splitter chicanes for the HE beam
main linac
splitter
chicane
merger
chicane
matching quads
low energy: 1st turn
matching quads
low energy: 2nd turn
merger
splitter
beam

## Slide 14
Linear Beam Optics: Recirculator
arc optics: various option also known from SR’s
 DBA, TBA, MBA (achromatic closed FODO)
 Bates Arc
TBA
FSF: A. Matveenko, et al., ERL WS, 2013.
Bates Arc
design considerations:
  length & hardware
  flexibility / tunability
  chromatic properties, R56 range
  ISR / CSR properties
H.L. Owen et al., “Choice of Arc Design for the ERL Prototype at Daresbury Laboratory”, EPAC, Lucerne, Switzerland 2004.
bERLinPro:
4 (2 x double) bend achromat
MBA with antibend

## Slide 15
linac
(dec)
arc1
arc2
rec. straight
splitter chicane
merger chicane
Linear Beam Optics: Recirculator
Betatron phase advance:
  minimize CSR induced emittance growth
  maximize BBU limited current threshold (tune & chromaticity)
Variable R56:
  tunable ‑0.25 m < R56 < 0.25 m
  standard mode R56 = +/- 0.14 m
  recirculator in total isochronous
Lattice design: various demands  difficult to meet all simultaneously
High transmission:
  moderate b-functions around the recirculator
  matching to the linac section
  closed and small dispersion function in the arcs

## Slide 16
Nonlinear Beam Optics
  RF curvature: E(t)=E0 cos(wt + j0)
  aberrations: geometric & chromatic:
  counteracted by nonlinear fields  multipole magnets
Example: bunch compression E(si) = E0 cos(s 2p/l - j0)  di = d(si) : rel. energy dev. DLi = R56 di + T566 di2 + U5666 di3 + …
bERLinPro recirculator: bunch compression test with and without multipole (sextupole and octupole) magnets
ss,start = 0.5 mm
ss,start = 1.0 mm
ss,start = 1.5 mm
ss,start = 2.0 mm
with MP / without
ss,start = 2.0 mm
 ss,end = 73 mm
D
D
bERLinPro recirculator: bunch compression test with varying initial bunch length indicating the influence of the the rf curvature

## Slide 17
Nonlinear Beam Optics
bERLinPro: two modes of operation - both require multipole magnets for nonlinear corrections
 four sextupole magnets per arc (each individually powered)
Low Emittance Mode (LEM): high current, emittance ≤ 1 mm mrad, st = 2 ps
  sextupoles first arc  counteract chromatic effects causing emittance growth
  sextupoles second arc  restore longitudinal phase space before deceleration to minimize the downstream energy spread
Short Pulse Mode (SPM): st ≤ 100 fs @ reduced current & degraded emittance
  sextupoles in first arc  linearize long. phase space / optimize T566 for shortest bunches
  sextupoles in second arc  restore long. phase space (like in LEM)
optimization procedure:
numerical optimization (Elegant)  minimize goal function from tracked bunch:
  @ experiment (recirculator straight section): e, ss
  after deceleration: phase space optimized to dump the beam  low e, sE & no linear / nonlinear chirp

## Slide 18
ERL Beam Dynamics: Collective Effects
Collective Effects:
  Space Charge
  Coherent Synchrotron Radiation
  Beam Break Up
  Geometric & other wakes
  Ion Trapping

## Slide 19
Fields & Forces
SC: perveance K=f(I,g), a: (round) beam size
ext. focusing: k(s)
 SC: defocusing forces in the bunch
linear force
within bunch
nonlinear
force
distrib.:
Gaussian
uniform
Collective Effects: Space Charge
eqn. of motion:
least degradation due to SC:
  radial force as linear as possible  uniform radial charge density distribution
  no variation of K(s) along bunch  K = const  flat top, long. charge density distribution

## Slide 20
SC Effects in ERLs
(moderate) tune shift: minor issue in ERLs
emittance growth
  nonlinear SC forces  phase space nonlinearities (x-x’, y-y’, t-p)
  varying strength of SC effects along bunch
bunch: longitudinally sliced
each slice with individual
  charge & charge density
  transverse size & divergence  e
  energy & energy spread
 individual SC forces
z
x, y
x’, y’
effective (projected)
emittance
charge density
Collective Effects: Space Charge
emittance compensation:
realign slices to minimize projected emittance
r

## Slide 21
bERLinPro: simulations & optimization of SC dominated beam transport  ASTRA, OPAL
for 2D - emittance compensation: SCO*
space charge at current ramping = increase of bunch charges at 1.3 GHz bunch rep-rate
s / m
Collective Effects: Space Charge
SRF
Solenoid
Bends
Quads
2.3 MeV
6.5 MeV
50 MeV
QB = 77pC
*SCO: A. Bondarenko, A. Matveenko, “Emittance Compensation Scheme for the BERLinPro Injector”,IPAC 2011, San Sebastian
ex = 0.63 mm mrad
ey = 0.52 mm mrad

## Slide 22
coherent
incoherent emission of
Synchrotron Radiation
coherent emission of
Synchrotron Radiation
 CSR
g: form factor
incoherent
Collective Effects: Coherent Synchrotron Radiation
charge density
distribution
CSR steady
wake potential

## Slide 23
CSR: energy variation in dispersive sections  betatron oscillation  emittance growth
Collective Effects: Coherent Synchrotron Radiation
bERLinPro: LEM (ss = 2 ps, Q = 77 pC, N = 8, E = 50 MeV)  PCSR ~ 4.4 kW
SPM  CSR power (4.4 kW from LEM) limits bunch charge:
 QSPM ~ 10 pC @ 100 fs
Countermeasures:
Shielding: suppression of long wavelength CSR  reduced aperture & increased losses
Beam Optics: cancel out energy modulation by long. beam flipping s  -s:, requires crossing of full compression  more CSR & large R56, unbalanced beam loading 
Beam Optics: reduce emittance growth by adjusting phase advance in bending plane  cancel out excited betatron oscillations from previous CSR kick(s)
bERLinPro: 1D-simulations  CSR no major issue
limited tune adjustment range  optics not optimized with respect to CSR
linac
(dec)
arc1
arc2
rec. straight

## Slide 24
ERL Beam Dynamics: Beam Break Up
Beam Break Up: resonant interaction of short & long range cavity wake fields with the generating bunch or subsequent bunches
  if HOM excitation exceeds HOM damping  kick strength rapidly increases  instability & beam loss
various BBU variants: single bunch BBU, multi bunch BBU (cumulative / regenerative, transverse / longitudinal, single-/multi-cavity, single-/multiple-turn)
x
z

## Slide 25
ERL Beam Dynamics: Beam Break Up
regenerative transverse BBU
(single cavity, single turn, one mode):
Countermeasures:
cavity design:
  HOMs: small R/Q, varying wl at fixed w0  multi cavity BBU thresholds increase
  no HOM on a fundamental’s harmonics: wl ≠ n*wrf
  low Q for HOM  HOM dampers (ferrites, waveguides, …)
recirculator beam optics:
  for a=0 & uncoupled beam transport
   m* = m12 = (b1b2)1/2 sin(Djx) =0 for Dj = np
  adjust sin(wl Trec) = 0 for the worst HOM large path length change  inpractical 
  large chromaticity  similar to Landau damping
  strong sextupoles
PhD: Y. Petenev
BBU thesholds
@ bERlinPro
Vladimir N. Litvinenko, “Chromaticity of the lattice and beam stability in energy recovery linacs”, PRST-AB 15, 074401 (2012)

## Slide 26
ERL Beam Dynamics: Beam Break Up
regenerative transverse BBU
(single cavity, single turn, one mode):
Countermeasures:
recirculator beam optics (continued):
  coupled beam transport: switching of planes X↔Y: m12=0  horizontal HOM kick transforms to vertical offset  polarized HOM not further excited,
  two options: solenoid (low energy) or skew quadrupole based rotator
bERLinPro:
rotator concept
with 5 skew quads prepared

## Slide 27
Thanks …
… to the bERLinPro Optics & Theory group:
J. Knedel, B. Kuske, D. Malyutin, A. Matveenko, M. McAteer & C. Metzger-Krauss
… to the bERLinPro team
M. Abo-Bakr, W. Anders, A. Büchel, K. Bürkmann-Gehrlein, P. Echevarria, A. Frahm, H.-W. Glock, F. Glöckner, F. Göbel, B. Hall, S. Heling, H.-G. Hoberg, A. Jankowiak, C. Kalus, T. Kamps, G. Klemz, J. Knedel, J. Knobloch, J. Kolbe, G. Kourkafas, J. Kühn, B. Kuske, J. Kuszynski, D. Malyutin, A. Matveenko, M. McAteer, A. Meseck, C. Metzger-Kraus, R. Müller, A. Neumann, N. Ohm-Krafft, K. Ott, E. Panofski, F. Pflocksch, J. Rahn, M. Schmeißer, O. Schüler, M. Schuster, J. Ullrich, A. Ushakov, J. Völker
… to all supporting colleagues @ HZB and from other Accelerator-Laboratories
… for your attention!