## Slide 1
Avalanche Pixelated Detectors for Time Resolved Experiments
NICOLA TARTONI
Diamond Light Source

## Slide 2: Techniques requiring time resolving detectors
Crystallography
Powder diffraction
Small angle scattering
Spectroscopy
…

## Slide 3: Timepix3
Time stamp per pixel 1.56ns resolution
Data-driven Zero-suppressed Sparse readout
Pixel size 55 μm x 55 μm
Pixel matrix array 256 x 256

## Slide 4
Small molecule crystallography
Courtesy Mark Warren
10 Hz
Laser
10 kHz
Laser

## Slide 5: Hystogram of ToAs
Best achieved resolution:
8 ns (sigma)
Measurements taken in Hybrid and Low-Alpha modes

## Slide 6: Limitations
DEAD TIME: Time Over Threshold + 475ns
MAX GLOBAL COUNTING RATE: 80 Mhits/s/chip

## Slide 7: Avalanche Pixelated Sensors Hi-Res Silicon
Structures fabricated by Micron Semiconductor and
Glasgow University

## Slide 8: Issues to be addressed
Uniformity of gain

## Slide 9: Issues to be addressed
Dedicated front-end electronics

## Slide 10: Mini-Attract Project
Development of front-end electronics with 55 micron pitch dedicated to Avalanche Detectors
Development of Avalanche Pixelated Sensors suitable to build large area detectors

## Slide 11: Possible Attract Project
Full detector system development
  Avalanche sensor
  ASIC (4-side buttable with high performance digital section)
  Interconnections (board-level optical interconnections)
  DAQ

## Slide 12: Potential Impact
Enhancement of hybrid detector technology
Much more efficient Time Resolved Experiments
Effective operation in 1 keV – 4 keV range