## Slide 1: The ATLAS Tile Calorimeter hybrid demonstrator and test-beam activities at CERN
Chamunorwa Oscar Kureba
oscar.kureba@cern.ch | Chamunorwa.Kureba@wits.ac.za
University of the Witwatersrand
High Energy Particle Physics workshop, 10 February 2016
Oscar

## Slide 2: Introduction
In the Large Hadron Collider’s Phase II upgrade, there will be a complete re-design of the read-out electronics in the Tile Calorimeter of the ATLAS detector
The completed new read-out architecture is expected to have the front-end electronics transmit fully digitized information of the detector to the back-end electronics system
The back-end system will, thus, provide digital calibrated information with greater precision and granularity to the first level trigger, thereby resulting in improved trigger efficiencies
A hybrid demonstrator has been built and tested under beam conditions

## Slide 3: Large Hadron Collider
Oscar Kureba, Wits
Located at the France-Switzerland boarder
test-beam activities at CERN
Site for test-beam

## Slide 4: CERN accelerator complex
Oscar Kureba, Wits
test-beam activities at CERN
Site for test-beam

## Slide 5: ATLAS detector
Largest of all detectors at the LHC (25 m high, 44 m wide)
All purpose detector of pp collision products

## Slide 6: ATLAS Tile Calorimeter
TileCal measures energy and direction of hadrons, jets and tau leptons
Made of Absorber (steel) + Scintillator (plastic) materials
Super-drawers contain front-end electronics which process signals
Undergoing upgrade to meet HL-LHC conditions

## Slide 7: Tile Calorimeter upgrade for Phase II: Hybrid Demonstrator
Aim to cope with luminosity increase (5-7x) and reduce single point failures (improve reliability)
Fewer failure-prone connectors with the challenge of routing more fiber optic and LV cables
Smaller DAQ elements by introduction of mini-drawers
Increase the redundancy in the read-out path from the cell to the backend
Similar redundancy in the power distribution and introduction of Point-Of-Load regulators

## Slide 8: Tile upgrade for Phase II
Present electronics
Hybrid demonstrator with analog output for phase-II upgrade

## Slide 9: Front-end electronics: present and future
Present
Future
Off-detector
On-detector
Off-detector
On-detector
To ROD
TilePPr

## Slide 10: Mini-drawers

## Slide 11: Demonstrator calibration results
Integrator response for Extended Barrel Cell D-6 to a passing Caesium source
Low Gain response to a LASER pulse in the hundreds of GeVs, sampled at 40 MHz.
Average Low Gain response of a 3in1 card to an injected charge

## Slide 12: Test-beam activities
ATLAS TileCal electronics upgrade team got test-beam from 7-21 October 2015
Previous test beam was 10 years ago
Lots of work in run up to- and during test beam period
Members from Wits: Oscar Kureba, Roman Hartmann and Charles Sandrock
Oscar et al, testing hardware & firmware for the TilePPr
Roman, working on software
Charles, soldering

## Slide 13
Demonstrator, before insertion into hadronic module
Module on truck ready
for transport from
Meyrin to Prevesin

## Slide 14
Before test-beam , operation of the TilePPr emulator used to take place from an open table top
Prone to accidental bumping and a lot of uncontrollable shifting about the place
Hence the need to have the TilePPr system inside a casing/box
Very little or no physical interfearance with the PPR hardware during testbeam
Open system
Boxed system
Casing for TilePPr for test-beam

## Slide 15: Test-beam activities
Cable connection onto boxed TilePPr system
Routing of fibre optic cables

## Slide 16: Test-beam facility
Warehouse contains several beam lines
Beam could be:
  180 GeV proton
  180 GeV muon
  150 GeV electron
  100 GeV electron
  50 GeV electron
Modules placed on
top of automatically
movable table

## Slide 17: Test Bench
Two modules on test bench:
  Long barrel – legacy electronics
  Extended barrel – Demonstrator
Longer module is a standard legacy module, used to make
sure the system is working
Shorter module is extended barrel sitting on top, holds the demonstrator electronics

## Slide 18: Test-bench
Beam Path:
The module captures all of the energy of the beam and its interactions via scintillation tiles
Legacy/Demonstrator electronics processes the signals

## Slide 19: Daily operations
9 am meeting daily
  Description of progress and challenges
  Setting and allocation of the day’s priorities
  Many small teams working on different elements in parallel
Massive expertise and helpful mindset in all involved members ensures that work progresses quickly

## Slide 20: Control room
Houses back end electronics racks
  New and old electronics
Has enough floor space for the whole test beam crew to work in
Also houses computers for:
  Beam control
  Table control
  Shifters stations

## Slide 21: Shift activities
https://twiki.cern.ch/twiki/bin/viewauth/Atlas/TileCalDemonstratorTestBeamShifterInstructions
Shift: Two members work in 8 hour shifts around the clock to manage and assist in the data taking process
Shifters need to monitor the DCS for system faults (and fix them if able, call for help if not), manage data taking runs, check the data, update the data DB, make sure beam information is correct etc
If unoccupied, shifters continue with their previous work – or new work. There is always something to do

## Slide 22
Shifts taken by Witsies marked with

## Slide 23: Run summary from test-beam
Module 0 [Legacy electronics]
90°, muons, 180 GeV, all tiles
20°, electrons, 50-100-150 GeV, all cells
Module EB [Demonstrator electronics]
+/- 90°, muons, 180 GeV, all tiles
20°, electrons, 50-100-150 GeV, all cells
Projective, muons, 180 GeV, all cells
+/- 90°, electrons, 50 GeV, all tiles
90°, muons, 180 GeV, z-scan
20°, electrons, 50 GeV, z-scan
20°, hadrons, 50-100-150 GeV

## Slide 24: Pre-analysis
Cleaning/beam properties
Establish a set of cleaning cuts (reject multi particle events, empty events, off-axis particles, …)
Study of the beam composition : how to select electrons, muons, hadrons, estimate contamination
Extract beam energy and its uncertainty
Precise computation of the beam impact point using the survey measurements of TileCal table and beam chambers

## Slide 25: Group photo taken at the end of test-beam

## Slide 26: Summary and outlook
The goal of the October 2015 test-beam was to verify if the ATLAS TileCal Demonstrator electronics can take meaningful data in ATLAS-like environment and yes it can
The data was taken with the aim to uncover the EM scale (pC/GeV ratio) already set in the Demonstrator by the Cs scan
Priceless experience was gained in operating the new TileCal readout electronics in close to real operational conditions
Mainly muons (180GeV) and electrons (50-150GeV) were taken in different conditions. Both data types can independently lead to the EM scale measurement.
Some important data sets were also taken with the legacy electronics readout path
Data analysis is on-going

## Slide 27: Thank you!

## Slide 28: The backup plan

## Slide 30: Super-drawer
The Hybrid Demonstrator is fully compatible with the current electronics and acts as a
validation for the new read-out architecture
4 mini-drawers make up a
super-drawer

## Slide 31: Wits contributions to the Demonstrator
Wits is responsible for the conceptual design and manufacture of
the next generation front-end electronics test-bench
Portable ReadOut ModulE for TileCal ElectrOnics (PROMETEO)
Used for the certification of the new electronics design for Phase II upgrade
All custom-designed modules were manufactured in South Africa
PROMETEO

## Slide 32: ADC Board (For PROMETEO)
Project Aim: Develop, test and validate a new ADC board
  Manufactured in South Africa
Used to test adder cards on TileCal front end electronics
  16 analog signals digitised from the TileCal and Muon Triggers
7.68 Gb/s Data to FPGA
  Xilinx Virtex7 on VC707 Dev Board
  Two 8 channel, 12 bit, 50 MSample/s ADCs
Developing VHDL Firmware for Control and Readout
Integration with TilePPR Firmware

## Slide 33: TilePPr
Formerly known as the sROD, this 16 layer board is the most complex manufactured so far in South Africa
In production at Trax company, Cape Town
It is able to process a total throughput of 290 GB/s
Main functionality: Main data read out,
Trigger and Timing Control distribution, DCS commands
to front-end
TilePPr
1st ptototype

## Slide 34: ATCA Framework (Advanced Telecommunications Computing Architecture)
ATCA will replace current VME Crates ATLAS-wide
  Modern and High Data Throughput
Wits-developed framework allows easy integration into ATLAS Detector Control System
  Wits HTEL has an ATCA chassis for R&D and Validation

## Slide 35: Processing Unit (To be installed in ATCA Chassis)
Wits is developing a general purpose co-processing unit for offloading complex algorithms from TilePPr FPGA
  PCI-Express via ATCA for high data throughput using energy efficient and cost effective ARM System on Chips found in mobile devices
  Will make use of RDMA over PCIe with a shared memory space for easier application development and higher performance.
Potential for generic use for example in SKA

## Slide 36: GPU Research for Processing Unit (Low cost, high performance for ATLAS Trigger or SKA)
Cluster of 11 NVIDIA Tegra-K1 GPUs in Wits HTEL
Currently researching the feasibility of TileCal front end energy reconstruction algorithms on GPU
  Redistribute the massively parallel implementation of the TileCal front-end from FPGA to GPU
High Performance Computing with GPU and 64 bit X-Gene system

## Slide 37: General Purpose Processing Unit
GPU
Cox M, Reed R, Mellado B 2015 JINST 10 C01007
Re-purpose the co-PU for the TileCal into a general purpose PU
Notes: sROD is a key link between the detector front-end and back-end
Performs, amongst other things, online energy reconstruction and quality factor checks
Because it is FPGA-based it is difficult to implement high-level signal-processing algorithms
Solution: ARM-GPU based co-processing unit (PU)

## Slide 38: Ipbus protocol
An implementation of the IPbus protocol in
few kilobytes of code, available in
C++, Java and python
IP bus hub enables multiple clients to
connect to the same host with a low impact
on transaction speed
IP bus hub program logic

## Slide 39
Long term commitments: