## Slide 1
FCC-hh
Daniel Schulte
CERN, February 2016

## Slide 2: Basic Parameters
 | LHC | HL-LHC | FCC-hh Baseline Ultimate | 
Cms energy [TeV] | 14 | 14 | 100 | 100
Luminosity [1034cm-2s-1] | 1 | 5 | 5 | <30
Machine circumference | 27 | 27 | 100 | 100
Arc dipole field [T] | 8 | 8 | 16 | 16
Bunch distance [ns] | 25 | 25 | 25 | 25 (5)
Background events/bx | 27 | 135 | 170 | 1020 (204)
Bunch length [cm] | 7.5 | 7.5 | 8 | 8
Baseline 1250fb-2 per 5 year cycle (considering shutdowns, stops, MDs, … )
= 2fb-2 per day with no problems
Ultimate 5000fb-2 per 5 year cycle
= 8fb-2 per day
Total 17.5ab-2

## Slide 3: FCC-hh Layout
Two high-luminosity experiments (A and G)
Two other experiments (F and H)
Two collimation and extraction insertions
  Exact layout being developed
Two injection insertions
Insertion lengths (1.4km, 4.2km for J and D) will be reviewed as optics designs are optimised

## Slide 4: FCC Injection and Site Study
LHC can be used as injector
Small changes on LHC
The two tunnels would match nicely
Energy and beam quality are sufficient
Also consider SPS and FCC tunnel for injector
SPS located at the right place
Detailed site studies are ongoing
Geology
Surface buildings
…
100km ring fits well into the Geneva area
V. Mertens, tomorrow

## Slide 5: Arc Cell Layout
Longer cell
fewer and shorter quadrupoles
better dipole filling factor
Shorter cells
more stable beam
smaller beam
12 dipoles with L=14.3m
Lcell=214.755m
to be reviewed with update magnet design
Fill factor about 80%
Field (100km ring): (16-ε)T
B. Dalena, A. Chance, J. Payet

## Slide 6: Magnets
FCC goal is 16T operating field
Requires to use Nb3Sn technology
At lower field levels used for HL-LHC
Also potential for 20T is being explored
Requires use of HTS
Also field quality is important
at injection energy
At top energy
Important parameter is the required aperture of the coils
Larger is more expensive
L. Bottura, tomorrow

## Slide 7: Initial Beam Parameters
 | FCC-hh Baseline | FCC-hh Ultimate
Luminosity L [1034cm-2s-1] | 5 | 20
Background events/bx | 170 (34) | 680 (136)
Bunch distance Δt [ns] | 25 (5) | 
Bunch charge N [1011] | 1 (0.2) | 
Fract. of ring filled ηfill [%] | 80 | 
Norm. emitt. [mm] | 2.2(0.44) | 
Max ξ for 2 IPs | 0.01 (0.02) | 0.03
IP beta-function β [m] | 1.1 | 0.3
IP beam size σ [mm] | 6.8 (3) | 3.5 (1.6)
RMS bunch length σz [cm] | 8 | 
Crossing angle [s’] | 12 | Crab. Cav.
Turn-around time [h] | 5 | 4

## Slide 8: Synchrotron Radiation
At 100 TeV even protons radiate significantly
Total power of 5 MW
Needs to be cooled away
Equivalent to 30W/m /beam in the arcs
Protons loose energy
They are damped
Emittance improves with time
Typical damping time 1 hour

## Slide 9: Luminosity Run Example
Ultimate example, 25ns, no luminosity levelling
8fb-1/day
Turn-around time
Example with ultimate parameters shown
Burn beam quickly
But emittance shrinks
Can reach 8fb-1/day
    5000fb-1 per 5 year cycle
X. Buffat, D.S.

## Slide 10: Beam Screen Design
Impedance:
Aperture >26mm
Impedance:
0.3mm copper coating
Cooling:
O(5mm) outer diameter
Stress in quench:
1.25mm steel
Cold bore + space for helium 1.5mm+1.5mm
Space for support:
O(1mm)
Total magnet aperture 50mm
LHC screen

## Slide 11: Cooling
L. Tavian, C. König,
Ph. Lebrun
16K beamscreen would require 300MW for cooling
50K requires 100MW => current baseline
For 4K magnets would prefer T>100K
But more impedance
Cross section determines length that can be cooled

## Slide 12: Vacuum Quality
For 2K cold bore meet target after 1 day
twice better than LHC design
but need to work on connections
Cryo absorbers required for 4K cold bore
R. Kersevan

## Slide 13: FCC Beam Screen Mechanical Design
Beam screen remains relatively cool
Stress is acceptable from heat
Worry about sheer stress in quench
attachment copper steel
C. Garion

## Slide 14: Low Frequency Impedances
At injection multi-bunch instability is driven by resistivity of arc beam screen
Resistivity increases with temperature
2b=26mm
N. Mounet, G. Rumolo, O. Boine-Frankeheim, U. Niedermayer, F. Petrov, B. Salvant, X. Buffat, E. Metral, D.S.
Minimium radius is defined by strong dependence of impedance
Multi-bunch instability O(10) worse than in LHC
Assumes fast feedback

## Slide 15: High Frequency Impedance
X. Buffat, O. Boine-Frankeheim, U. Niedermayer, F. Petrov, B. Salvant, D.S.
In LHC pumping holes are important contribution to high frequency impedance at injection
Pumping holes in LHC-like design would lead to instability (TMCI) at 1.5x1011
Way to little margin for charge of 1x1011
        In FCC holes are shielded
        Removes impedance
        Other sources need to be studied (e.g. collimation system, …)

## Slide 16: Feedback
W. Höfle, J. D. Fox et al.
Analog
Front
End
Analog Back
End
Signal
Processing
BPM
Kicker
Power Amp
ADC
DAC
Beam
Active closed loop
Feedback
pre-processed
pre-distortion
drive signal
Higher bandwidth than in LHC (5ns bunch spacing)
Faster feedback allows to rise beam screen temperature
Even intra-bunch feedback is considered

## Slide 17: Electron Cloud Effects
Still a potential performance limitation for LHC
Heat load
Beam instability
Twice as many photons as in LHC
At 100 times the energy (4.3keV vs. 44eV)
Similar to B-factories
Surface properties important like photoelectron yield, secondary emission yield, reflectivity, …
Experimental input critical

## Slide 18: Electron Cloud Effects
Simulations for 5ns shown
Required:
Photoelectron yield <0.02
Secondary emission yield dm<1.2
Not much margin
25ns is better
Need mitigation methods
Need to measure surface properties
Photoelectron yield 0.02
L. Mether,
G. Rumolo, K. Ohmi
Photoelectron yield 0.1

## Slide 19: Mitigation Methods
a-C
LESS
Developments for LHC are critical
Carbon coating
Laser treatment of surface
Can also learn from B-factories
Cryo Beam Vacuum
Prototype and experiments in EuroCirCol WP 4
P. Costa Pinto et al.
Simulation of exact geometry is important, may help

## Slide 20: Alignment
Good alignment required for beam quality
good pre-alignment
good beam-based alignment
Alignment beam vs. slit is also important
M. Jones, N. Ibarrola Subiza
First system is based on wire and hydrostatic leveling

## Slide 21: Current FCC Detector Model
W. Riegler et al.

## Slide 22: Space for FCC Detector
35m
L*=45 m
Tracking
Ecal
HCAL
Magnets and cryostat
Muons
W. Riedler
Have iterated on L*
Modified from W. Riegler et al.

## Slide 23: High-luminosity Insertions
Squeezes the beam to few microns
Have designs for L*=36m and L*=61m to explore
Now will go for L*=45m
R. Martin, R. Tomas et al.
High-luminosity Insertions

## Slide 24: High-luminosity Insertions
Small beam in interaction point leads to large beam in triplets
For given triplet, aperture is limited due to required field gradient
R. Martin, R. Tomas et al.
Beam stay clear >15σ
Can reach enough beam stay clear for target beta-function

## Slide 25: Radiation from Beam-beam
Total power of background events 100-500kW per experiment
Car or truck engine
Already limit in LHC and HL-LHC
Magnet lifetime, heat load
Study of 3000fb-1 in older FCC-hh detector design
Goal: survive at least 5000fb-1
One 5-year run
Shield (TAS)
Magnets
Dose for
3000fb-1
30MGy=
Current limit
Shielding
5mm
10mm
15mm
20mm
M. I. Besana, F. Cerutti, et al.

## Slide 26: Countermeasures
Split magnets
Vary crossing scheme to distribute damage (S. Fartoukh)
Improvements in radiation hardness
M. I. Besana, F. Cerutti, et al.
Longer triplet with more aperture to better shield/spread radiation
R. Martin et al.
A. Langner et al.
Need to push hard to gain small factors

## Slide 27: Beam-beam Effects
Emittance growth
Beam loss

## Slide 28: Beam-beam Effects
X. Buffat

## Slide 29: Beam-beam Effects
X. Buffat

## Slide 30: Beam-beam Effects
X. Buffat

## Slide 31: Beam-beam Effects
X. Buffat

## Slide 32: Limit and Mitigation
Crossing scheme and angle determined by beam-beam
Effect is about OK for baseline
But would like to have margin and to push further
Wires
Mitigation technique examples:
Larger crossing angle (and crab crossing)
X. Buffat
Mitigation technique examples:
Larger crossing angle (and crab crossing)
Compensating wire (to be tested for HL-LHC)

## Slide 33: Extraction
(Enlarged quadrupole)
Triple chamber quadrupole?
MKBH
MKBV
Kicker
0.13mrad
Septum
1.7 mrad, 1.42 T
Normally fire kickers in the abort gap of the beam
But kicker can fire on its own
In LHC fire all and sweep beam out
  Does the extraction line survive?
Can we segment kicker such that we can leave beam circulating until abort gap?
  Is this safe?
Design based on LHC design
Alternatives studied
W. Bartmann, B. Goddard, F. Burkart, …

## Slide 34: Beam Dump Considerations
Hydrodynamic tunneling
Simulation show beam will penetrate ~ 300 m in Copper, assuming no dilution.
 Dilution required!
F. Burkart et al.
8GJ kinetic energy per beam
Airbus A380 at 720km/h
2000kg TNT
400kg of chocolate
  Run 25,000km to spent calories
O(20) times LHC

## Slide 35: Dilution System
1.4 km dump insertion
2.8 km collimation insertion
2.5 km dump line
Kicker
Septum
10 mrad bend
Dilution
Absorber
Horizontal and vertical kicker system as in the LHC
~ 300 m, ~150kickers, to be optimized
Large magnet apertures required towards dump
Different solutions studied
Require up to 80cm radius
F. Burkart et al.
Fluka studies of required pattern:
Bunch separation > 1.8 mm
Branch separation: 4 cm
Keeps T<1500°C
A. Lechner, P. Garcia
LHC pattern (same scale)
2m

## Slide 36: Collimation
To protect machine and experiments
At injection tightest part is arcs
At collision energy triplets at experiments
S. Redaelli et al.

## Slide 37: First Collimation Studies
M. Fiascari,
S. Redaelli
R. Tomas
First collimation system lattice designs exist
Based on LHC designs
Starting point for exploration
Fix issues from LHC design
LHC
Betatron collimation

## Slide 38: Collimation
First performance studies are ongoing
Collimation efficiency
Power losses
Many studies to be performed
Protection of machine from experiments
Background from one experiment to the next
…
Have to review FLUKA at FCC energies
A complex long-term optimisation

## Slide 39: Injection Insertion
Have to limit injected batch
With LHC limits can inject O(100) bunches
Very fast kicker (O(300ns)) for beam filling factor of 80%
W. Bartmann, B. Goddard, F. Burkart, …

## Slide 40: RF Design Considerations
RF integrated in injection insertion
Limited radiation
400.8 MHz seems a good baseline
16MV minimum with no margin
32MV seems fine
Higher voltage helps for other instabilities as well
To accelerate beam in 1000s require 16MV and 8MW
Assumed impedance (x2)
E. Shaposhnikova
Bunch length
32MV
24MV
16MV

## Slide 41: Turn-around Time
Integrated luminosity is strong affected by turn-around time
Higher luminosity would not help a lot
Turn-around time in LHC larger than theoretical limit
Need to understand in more detail
Ultimate example, 25ns, no luminosity levelling
8fb-1/day
Turn-around time
Ensure we are not too optimistic
Explore options to speed it up
Magnets need >640s (linear ramp)

## Slide 42: Injector Considerations
100 km intersecting
Current baseline injection energy is 3.3TeV
B. Goddard at al.
Many choices
SPS -> LHC -> FCC
SPS -> FCC
SPS -> FCC booster -> FCC

## Slide 43: Filling Time
Overhead to accelerate all p+ to 450 GeV
B. Goddard, L. Stoel, et al.
LHC-type Nb-Ti
Single layer Nb-Ti
LHC-type Nb-Ti
*
*
Single layer Nb-Ti
*
LHC-type Nb-Ti
LHC with 5x faster ramping
LHC high field
SPS -> FCC
SPS -> LHC -> FCC
SPS -> FCC booster -> FCC
Superferric
1 T
Higher fields lead to long ramp times
LHC would work as injector
Will study other options in more detail
Study effects of lower energy in collider ring

## Slide 44: LHC as Injector
Many studies to come
5ns bunch spacing
Injection into LHC
…
Develop the other options
The LHC is basically suited as injector
Some modifications required
Faster ramping of magnets is required
Need four fillings into FCC
In total roughly 1.5h ramping up and down
Realistic goal seems a factor 5 improvement
  Better ramp shape
  Upgrade of power converters
4TeV
0.46TeV
800s
B. Goddard, A. Milanese et al.

## Slide 45: Dynamic Aperture
Magnets have field errors
Random and systematic
Non-linear fields can lead to chaotic motion
particle loss over many turns
Need to also work at low field at injection
Critical limit for magnet design
Example table: Need to consider many errors
E. Todesco, S. I. Bermudez et al.

## Slide 46: Example Estimate
B. Dalena, A. Chance,
D. Boutin, J. Payet,
Collision energy
Design to have B3 mainly at full energy
Design to have B3 mainly at injection
Conclusion:
Dynamic aperture too small
Would need very strong correctors (10xLHC)
2) Dynamic aperture looks fine
Need to work on dynamic aperture at injection

## Slide 47: LHC Experiments
http://indico.cern.ch/event/469656/
B. Goddard et al.
Inject beam into LHC at 225GeV
Or decelerate injected beam to 225GeV
Many changes are required and need to be undone
Best at the end of a run
Field error depends on injection energy
Uncertain about reproducibility and stability at low fields
Experiment is important
D. Tommasini et al.
Important for FCC as well:
Faster ramping
Profit from LHC and HL-LHC MDs
Impedances
Beam-beam
…

## Slide 48: If You Want to Contribute
Work/meeting structures established based on INDICO, see:
FCC Study: https://indico.cern.ch/category/5153/
In particular:
FCC-hh Hadron Collider VIDYO meetings
  https://indico.cern.ch/category/5263/
  Contacts: daniel.schulte@cern.ch
FCC-hadron injector meetings
  https://indico.cern.ch/category/5262/
  Contacts: brennan.goddard@cern.ch

## Slide 49: Conclusion
FCC-hh developed as option for future flagship project at CERN
  Goal is to have CDR ready for European strategy update (2018)
  https://indico.cern.ch/category/5153/
  Workshop in Rome April 11-15, 2016
Work is progressing
More work to be done
  Exciting technological challenges
  Exciting beam physics
  Exciting physics
Your contributions are most welcome

## Slide 50: Many thanks to FCC Collaboration
Status: November, 2015
70 institutes
26 countries + EC

## Slide 51: And EuroCirCol
Japan
KEK
Finland
TUT
France
CEA, CNRS
Italy
INFN
Germany
KIT, TUD
Switzerland
EPFL, UNIGE
Netherlands
UT
Spain
ALBA, CIEMAT
CERN
United Kingdom
STFC, UNILIV, UOXF
CERN | IEIO
TUT | Finland
CEA | France
CNRS | France
KIT | Germany
TUD | Germany
INFN | Italy
UT | Netherlands
ALBA | Spain
CIEMAT | Spain
STFC | United Kingdom
UNILIV | United Kingdom
UOXF | United Kingdom
KEK | Japan
EPFL | Switzerland
UNIGE | Switzerland
NHFML-FSU | USA
BNL | USA
FNAL | USA
LBNL | USA
Arc Design
EIR Design
Cryo Beam Vacuum
High Field Magnet
EU co-funded design study for FCC-hh, focus on core activities
Accepted in 2015

## Slide 52: Reserve Slides

## Slide 53: Magnets
Combination of materials used to reduce cost
Different designs are being explored for FCC
A recent test AT CERN has achieved world record of 16.2T
But a short racetrack magnet
Older example designs (one quarter)
(L. Rossi, E. Todesdco, P. MacIntyre )

## Slide 54: Limits for the Field
This limits the achievable field
  In theory
  Even lower limit in practice (shown)
Can use different materials
  Nb-Ti is used for LHC
  Nb3Sn is used for high luminosity upgrade
The cable can quench (superconductivity breaks down)
if the current is too high
If the magnetic field is too high

## Slide 55: Cost Effective Magnet Design
Coil sketch of a 15 T magnet with grading, E. Todesco
Nb3Sn is much more costly than Nb-Ti
Use both materials

## Slide 56: Cost Effective Magnet Design II
Coil sketch of a 20 T magnet with grading, E. Todesco
HTS is even more expensive than Nb3Sn
Even more complex design

## Slide 57: Dump Insertion Alternatives
Asymmetric insertion optics
Avoid asynchronous dumps by accepting single kicker erratic
High segmentation of kicker system (200-300 modules)
Asymmetric optics
  to reduce oscillation from single kicker failure (small hor beta)
  to reduce kicker strength and dilute beam at absorbers (high betas at septum)
SSC like
  Septum is part of extraction bump
  Use field free channel of septum to extract
  Need strong, good field quality septum

## Slide 58: Beam Dump Dilution
Fixed dilution frequency:
f = 50.9 kHz
Maximum amplitude at the dump block: 80 cm
Bunch separation > 1.8 mm
Branch separation: 4 cm
Max deflection: 0.32 mrad
B.dl = 53 T.m
Alternative with frequency change:
f = 20.4 kHz – 42.9 kHz
Bunch separation = 1.9 mm constant
Branch separation = 4 cm
Max deflection = 0.24 mrad
Max amplitude = 0.59 m
Bdl = 39 Tm (2.5 km dump line)
Dilution pattern was evaluated as a function of dilution kicker magnet MKB parameters and energy deposition on the TDE.
Energy deposition studies by FLUKA (A.Lechner & P. Garcia)
Max. temperature below ~ 1500 °C.

## Slide 59: Injection from SPS Tunnel
NC / SF
SC Nb-Ti
SC Nb3-Sn
low
high
3.3 TeV
X
X
X
X
X
Exists
Interesting upgrades
Probably slow to ramp
B. Goddard at al.

## Slide 60: Injection from LHC Tunnel
NC / SF
SC Nb-Ti
SC Nb3-Sn
low
high
3.3 TeV
Maximum for existing LHC
Faster ramping of existing magnets
X
X
X
X
New magnets
B. Goddard at al.

## Slide 61: Injection from FCC Tunnel
NC / SF
SC Nb-Ti
SC Nb3-Sn
low
high
3.3 TeV
Superferric
X
X
NC magnets
B. Goddard at al.

## Slide 62: Thickness of Copper Coating
N. Mounet, G. Rumolo
DQ=0.5, can probably assume this upper limit on working point
Need maybe 300mm of copper coating
Difficult because of eddy currents in quench
Induces stress on beam pipe
LHC has 50mm
HTS coating? Lots of work
Impedance, coating technology, ecloud, …
Coating is very thin
Has hardly any effect
Coating is very thick
Material on the outside is hardly seen
Coating has some effect

## Slide 63: Example for Loss Mechanism
Beam-gas scattering goal
>100h beam lifetime
<O(1015m-3) H2 (σ≈100mb)
45kW proton losses
power for cooling
  @2K <30MW
  @4K <15MW
  some part is lost in collimation system
First studies indicate peak power density O(1mW/cm-3) and 3.5W/beam/dipole in cold
Seems very acceptable but need to define margin
Work in progress
F. Cerutti, I. Besana

## Slide 64: Estimates of Beamipe Impedance Effects
N. Mounet, G. Rumolo
Many more impedance studies required
Need feedback within 10 turns
Challenge for RF and instrumentation
Or increase the beam screen radius
Or decrease beam current
Multi-bunch effect at 50K and injection (worst case)
Only resistive wall (infinite copper layer assumed)
10 turns
50 turns
100 turns
Growth rate of multi-bunch instability
Noise growths every 20-30 turns by factor e

## Slide 65: Low Frequency Impedances
Impedance more critical than in LHC
* www.copper.org
50
FCC
LHC
At injection multi-bunch instability is driven by resistivity of arc beam screen
2b=26mm
N. Mounet, G: Rumolo, O. Boine-Frankeheim, U. Niedermayer, F. Petrov, B. Salvant, X. Buffat, D.S.
Strong dependence on radius
Defines minimum b
Multi-bunch instability O(10) worse than in LHC

## Slide 66: FCC-hh Layout
Two main experiments on opposite sides of the collider
All bunches collide in main experiments
  independent of filling pattern
  Highest luminosity
Each bunch collides with the same bunch in both experiments
  Compensation of beam-beam effects

## Slide 67: FCC-hh Layout
The injection insertion position is determined by LHC/SPS, if used as injector
Best place for RF

## Slide 68: FCC-hh Layout
Additional experiments close to one main experiment
Separation to suppress background from one to the next
Symmetric to injection (could be changed)
Short arcs should allow for enough tuning

## Slide 69: FCC-hh Layout
Foresee two collimation and extraction insertions
Insertions with largest risk
Scheme provides flexibility
Current baseline
betatron-collimation after extract to protect machine
Energy collimation