## Slide 1: Concepts for magnet circuit powering and protection M. Prioli with many inputs from A. Verweij, R. Schmidt and A. Siemko

## Slide 2: Outline
Subject
  Circuit layout of the FCC main bending magnets
Goal
  To outline possible directions
Motivation
  To understand if powering is feasible
  To discuss new ideas for powering
  To identify the necessary R&D
Method
  Protection point of view (fast power abort), limiting factor: voltage to ground
  Powering point of view (ramp-up), limiting factors: voltage (maximum di/dt) and peak power

## Slide 3: FCC magnet designs
Description | LHC MB | Cos-theta | Block Coil | Common Coil | Units
Number of turns per aperture | 80 | 230 | 306 | 394 | -
Nominal field | 8.33 | 16 | 16 | 16 | [T]
Current @ nominal field | 11.85 | 10.275 | 8.47 | 9.03 | [kA]
Inductance per aperture | 49 | 367 | 632 | 912 | [mH]
Stored energy per aperture | 3.5 | 19.4 | 22.7 | 37.1 | [MJ]
Description | LHC MB | Cos-theta | Block Coil | Common Coil | Units
Number of turns per aperture | 80 | 230 | 306 | 394 | -
Nominal field | 8.33 | 16 | 16 | 16 | [T]
Current @ nominal field | 11.85 | 10.275 | 8.47 | 9.03 | [kA]
Inductance per aperture | 49 | 367 | 632 | 912 | [mH]
Stored energy per aperture | 3.5 | 19.4 | 22.7 | 37.1 | [MJ]
A comparison among the designs is presented in (refer to Arjan presentation)
cos-theta 28b38
Block coil v26cmag
Common coil v1h intgrad

## Slide 4: The FCC layout
From R. Schmidt, FCC week Washington, March 2015
Half arc (L=8km)

## Slide 5: FCC vs LHC powering layout
In order to reduce the circuit inductance, the half arc of the FCC is subdivided in two powering sectors (PS)
The total number of power converters (PC) is doubled
PC 1
PC 2
PS 1
PS 2
HalfArc 1
8km
PC 1
PS 1
Sector 1
3km
LHC
FCC
Description | LHC PS | FCC PS | FCC MiniArc | Units
Powering sector (PS) length | 3000 | 4000 | 3200 | [m]
Number of PS in the accelerator | 8 | 16 | 4 | -
Filling factor | 74% | 77% | 77% | -
Number of dipole magnets per PS | 154 | 215 | 172 | -
Inductance per PS | 15 | 272 | 218 | [H]
Stored energy per PS | 1 | 10 | 8 | [GJ]

## Slide 6
B
PC 1
PS 1
EE1
EE2
Powering layout options
PC 1
PS 1
EE1
EE3
EE2
EE4
PC 1b
PS 1
EEb
PC 1a
EEa
EE2b
PC 1b
PS 1
EE1b
PC 1a
EE1a
EE2a
PS 1
PC 1a
EE1a
PC 1b
EE1b
PC 1c
EE1c
PC 1d
EE1d
PC 1e
EE1e
SC link
A
C
D
E

## Slide 7
Pros
Direct extrapolation of LHC layout
PC 1
PS 1
EE1
EE2
PC 1
PS 1
EE1
EE2
Option A: 1 circuit with 2 EE
 | Description | LHC MB | FCC Block |  | Units
Energy and inductance | Diff. inductance per circuit | 15.2 | 272 |  | [H]
 | Stored energy per circuit | 1.1 | 9.8 |  | [GJ]
FPA | Maximum voltage to ground | 450 | 1000 | 2000 | [V]
 | Discharge time constant (τdisc) | 100 | 576 | 288 | [s]
 | Resistance per energy extractor | 76 | 236 | 472 | [mΩ]
 | Integral of I^2(t)*dt (MIITs) | 7e3 | 21e3 | 10e3 | [MA^2 s]
 | Busbar size (adiabatic, ΔT=300K) | 220 | 370 | 260 | [mm^2]
Cons
High stored energy per circuit
EE2 position
High voltage to ground for a lower discharge time constant (τdisc)
LHC
FCC

## Slide 8
Pros
The stored energy per circuit is halved (cf.A)
All EE are close to an access point
Option B: 2 circuits with 1 EE
 | Description | LHC MB | FCC Block |  | Units
Energy and inductance | Diff. inductance per circuit | 15.2 | 136 |  | [H]
 | Stored energy per circuit | 1.1 | 4.9 |  | [GJ]
FPA | Maximum voltage to ground | 450 | 1000 | 2000 | [V]
 | Discharge time constant (τdisc) | 100 | 576 | 288 | [s]
 | Resistance per energy extractor | 76 | 236 | 472 | [mΩ]
 | Integral of I^2(t)*dt (MIITs) | 7e3 | 21e3 | 10e3 | [MA^2 s]
 | Busbar size (adiabatic, ΔT=300K) | 220 | 370 | 260 | [mm^2]
Cons
The number of circuits is doubled (cf. A), unless quadrupoles are powered in series
High voltage to ground for a lower τdisc
PC 1b
PS 1
EEb
PC 1a
EEa

## Slide 9
Pros
A lower τdisc is obtained for 1kV (cf.A)
Option C: 1 circuit with multiple EE
 | Description | LHC MB | FCC Block |  | Units
Energy and inductance | Diff. inductance per circuit | 15.2 | 272 |  | [H]
 | Stored energy per circuit | 1.1 | 9.8 |  | [GJ]
FPA | Maximum voltage to ground | 450 | 1000 | 2000 | [V]
 | Discharge time constant (τdisc) | 100 | 288 | 144 | [s]
 | Resistance per energy extractor | 76 | 236 | 472 | [mΩ]
 | Integral of I^2(t)*dt (MIITs) | 7e3 | 10e3 | 5e3 | [MA^2 s]
 | Busbar size (adiabatic, ΔT=300K) | 220 | 260 | 180 | [mm^2]
Cons
High stored energy per circuit
Position of EE2, EE3 and EE4
PC 1
PS 1
EE1
EE3
EE2
EE4

## Slide 10
Pros
The stored energy per circuit is halved (cf.A)
A lower τdisc is obtained for 1kV (cf.A)
Option D: 2 circuits with 2 EE
 | Description | LHC MB | FCC Block |  | Units
Energy and inductance | Diff. inductance per circuit | 15.2 | 136 |  | [H]
 | Stored energy per circuit | 1.1 | 4.9 |  | [GJ]
FPA | Maximum voltage to ground | 450 | 1000 | 2000 | [V]
 | Discharge time constant (τdisc) | 100 | 288 | 144 | [s]
 | Resistance per energy extractor | 76 | 236 | 472 | [mΩ]
 | Integral of I^2(t)*dt (MIITs) | 7e3 | 10e3 | 5e3 | [MA^2 s]
 | Busbar size (adiabatic, ΔT=300K) | 220 | 260 | 180 | [mm^2]
Cons
The number of circuits is doubled (cf. A), unless quadrupoles are powered in series
Position of EE2a and EE2b
EE2b
PC 1b
PS 1
EE1b
PC 1a
EE1a
EE2a

## Slide 11
Pros
Relatively small energy per circuit (cf.A)
All EE are close to an access point
A lower τdisc is obtained for 1kV (cf.A)
Option E: multiple circuits with 1 EE
 | Description | LHC MB | FCC Block |  | Units
Energy and inductance | Diff. inductance per circuit | 15.2 | 54 |  | [H]
 | Stored energy per circuit | 1.1 | 2 |  | [GJ]
FPA | Maximum voltage to ground | 450 | 1000 | 2000 | [V]
 | Discharge time constant (τdisc) | 100 | 230 | 115 | [s]
 | Resistance per energy extractor | 76 | 236 | 472 | [mΩ]
 | Integral of I^2(t)*dt (MIITs) | 7e3 | 8e3 | 4e3 | [MA^2 s]
 | Busbar size (adiabatic, ΔT=300K) | 220 | 230 | 160 | [mm^2]
Cons
Higher number of circuits (cf.A)
SC link
PS 1
PC 1a
EE1a
PC 1b
EE1b
PC 1c
EE1c
PC 1d
EE1d
PC 1e
EE1e
SC link

## Slide 12: Overview
Comparison between options A and B, and options C and D
  Same Vgnd, τdisc , MIITs
  But B and D lead to the half stored energy and to a simpler positioning of the EE systems at the price of a more complex circuit
Option E seems promising if the SC link technology will be developed
Option | # Circuits | E [GJ] | # EE per circuit | Vgnd [V] | τdisc [s] | MIITs [MA2 s] | Energy | EE position | Circuit complexity
LHC | 1 | 1.1 | 2 | 450 | 100 | 7e3 |  |  | 
A | 1 | 9.8 | 2 | 1000 | 576 | 21e3 |  |  | 
 |  |  |  | 2000 | 288 | 10e3 |  |  | 
B | 2 | 4.9 | 1 | 1000 | 576 | 21e3 |  |  | 
 |  |  |  | 2000 | 288 | 10e3 |  |  | 
C | 1 | 9.8 | Mult. (4) | 1000 | 288 | 10e3 |  |  | 
 |  |  |  | 2000 | 144 | 5e3 |  |  | 
D | 2 | 4.9 | 2 | 1000 | 288 | 10e3 |  |  | 
 |  |  |  | 2000 | 144 | 5e3 |  |  | 
E | Mult. (5) | 2 | 1 | 1000 | 230 | 8e3 |  |  | 
 |  |  |  | 2000 | 115 | 4e3 |  |  | 

## Slide 13: Comments
Directions for traditional layouts:
  1 circuit per PS (Options A and C), R&D on safe operation at high energies
  OR
  2 circuits per PS (Options B and D), R&D on series powering of quadrupoles
  Long time constant (Option A and B with 1kV to ground), R&D on feasibility
  OR
  High voltage to ground (Option A and B with 2kV to ground), R&D on feasibility
  OR
  Multiple (4) EE per PS (Option C and D with 1kV to ground), R&D on feasibility
Direction for a new layout
  SC link (Option E with 1kV to ground), R&D on the SC link technology

## Slide 14: FCC vs LHC ramp-up
Maximum power to ramp-up dipole magnets in the whole accelerator
  Independent of the circuit layout
  MiniArcs included
  Losses and inefficiency non included
For tramp=20 min, a factor 22 is obtained with respect to the LHC
310 MW
14 MW

## Slide 15: FCC vs LHC ramp-up
Constant voltage
Pmax
Constant power
Pmax=160 MW
For a single circuit (L=54 H)
For the whole accelerator
Constant voltage
Pmax
Pmax=310MW

## Slide 16: Distribution of power flows
Ramp-up of dipole magnets only, MiniArcs included, net power (no losses and inefficiency)
17 MW
17 MW
17 MW
17 MW
17 MW
17 MW
15 MW
15 MW
15 MW
15 MW

## Slide 17: Conclusions
Possible directions for the layout of dipole circuits have been identified for the FCC
  Powering is feasible but R&D is necessary to identify the best option
For the ramp-up, the choice of the ramp time is a trade off between
  Peak power
  Machine availability
  Decrease the power peak while preserving the same ramp-up time is possible

## Slide 18: Thank you for your attention
Questions, comments ?