## Slide 2: CERN Reliability Training
Andrea Apollonio, TE-MPE-PE
Acknowledgements: J. Gutleber, R. Schmidt

## Slide 3: Scope of the Training
Raise awareness on the importance of RAMS studies in the domain of particle accelerators
Provide basics for performing reliability analyses to CERN staff members
Train 120-150 people from CERN over 4 years
2 People from IMA Stuttgart
1 from RAMENTOR

## Slide 4: First Training - Test
Validate contents (quantity, complexity,...)
Tailor contents to the accelerator domain
Participants (total ~20):
CERN staff members WITH previous experience with reliability analyses
CERN staff members WITHOUT previous experience with reliability analyses
Students from IMA Stuttgart

## Slide 5: Contents
Days 1-3 (29th Feb – 2nd Mar):
Introduction
Mathematical Treatment of Reliability
Determination of System Reliability
Failure Mode and Effects Analysis
Fault Tree Analysis
Evaluation of Lifetime Tests and Failure Statistics
Availability
Modeling and Simulation of Availability
Day 4 (3rd Mar):
Hands-on training with ELMAS

## Slide 6: External and Internal Influences on Reliability
Greater
functionality
-
Greater complexity
-
Reduced
development costs
-
Shorter
development time
-
Increasing
product liability
+
Minimization of fault costs
+
Increased
customer demands
+
Reliability

## Slide 7: Power of Ten Rule: Relationship Between Fault Costs and Product Lifetime
Fault prevention Fault detection
Opportunity for action Necessary reaction
Field
Production
Development
Purchasing
and
manufacture
Field
use
Development
and
purchasing
Concept phase
Design,
product development
Planning,
purchasing
Production
Product utilization
Costs per fault
1.00
10.00
100.00
0.10
Influence on fault

## Slide 8: Reliability Methods in the Product Life Cycle
Planning
Layout
Design
Production
Field
Usage
Conception
Recycling
Reliability
Goal
Specifi-
cations
Fuzzy Data
Calculation
- Know-How
- ...
time
- ABC-Analysis
- Design Review
- FMEA
- FTA
- ....
- Weibull-Distr., exponential...
- Testplanning
- Boolean Theory
- Markov Model
- ....
Quality
Management
- Audits
- ....
- Statistical Process Planning
- ...
Field Data
Collection
Early
Warning
- ....
Field Data Analysis
- ......
- Recycling Potential
- ....
- Remaining Lifetime
- ....
Qualitative
Quantitative

## Slide 9: Accelerator Operation
Tradeoff: Availability Protection
[Source: CERN]
Result of equipment reliability, maintenance actions and protection requirements

## Slide 10: Survival Probability and Failure Probability
Failure time t
Density function f(t)
Survival probability R(t) as complement of failure probability F(t)

## Slide 11: Classification of Reliability Methods
Qualitative methods
Employ methodical, systematic procedures to determine possible faults/failures and their effects
Provide evaluation by way of estimation and classification (not by calculation)
Aim: (Qualitative) ranking of weak points
Methods:
FMEA (FMECA)
Fault tree analysis
Event tree analysis
Check lists / Design review
Quantitative methods
Make use of terms and processes from statistics and probability theory
Provide (quantitative) probability values for reliability by way of calculation
Methods:
Fault tree analysis
Boolean system theory
Markov's theory
Monte-Carlo method

## Slide 12: FMEA Form VDA 4.2
12
 |  | Failure mode and effect analysis (FMEA) System |  |  |  |  |  |  |  |  |  | FMEA-No.:
 |  |  |  |  |  |  |  |  |  |  |  | Page:
Type/Model/Fabrication/Load: |  |  |  |  |  | Item Code: State: |  | Responsible: Company: |  |  |  | Compartment: Date:
System-No./System Element: Function/Task: |  |  |  |  |  | Item Code: State: |  | Responsible: Company: |  |  |  | Compartment: Date:
Potential Effects | S | Potential Failure | C | Potential Causes |  | Preventive Actions | O | Detection Actions |  | D | RPN | Responsibility/Date
S = Assessment value for the severity |  |  |  |  | O = Assessment value for the occurrence |  |  |  | D = Assessment value for the detection |  |  | 
RPN = Risk priority number |  |  |  |  |  |  |  |  |  |  |  | 
University of Stuttgart
System element,
System structure
and functions
Risk
Analysis and assessment
Optimization

## Slide 13: Boolean System Theory
Example:
Serial structure
Parallel structure
Example:
System limit
System limit
≤1

## Slide 14: Top-down-method (deductive procedure)
DOWN
= basic event (causes)
system failure
failure of the partial system
failure of the assembly group
failure of the component
failure modes
component characteristic,
design flaw
TOP
= undesired result
overload
false calculations
incorrect operation
…
…
fretting
breakage
pittings
…
…
failure of the synchronization
failure of gear 1
failure of gear 2
…
…
transmission failure
failure of the bearing
output failure
failure of the housing
…
…
≥ 1
≥ 1
≥ 1
≥ 1
vehicle failure
≥ 1
…
…

## Slide 15: Exercise 5.4: Task
Create the system structure of the given simplified system for the top event “Safety Critical Fault”. Consider only the safety critical failure modes.
Add functions, malfunctions and failure modes.
Create a qualitative Fault Tree based on a)-b).
MPS
Accelerator (i.e. LHC)
Primary Fault to be detected
(rate 10^-4 / h)
Sensor
(e.g. voltage measurement)
Decision logics (electronics board)
Communication link 1
Communication link 2
Actuator (e.g. Beam Dumping System, …)
Functionality:
Measure a given quantity to detect possible failures
Transmit information to the rule-based process
Decide if an emergency action has to be undertaken
Transmit information to the actuator
Execute the requested emergency action

## Slide 16: Exercise 5.6: Task
Create a Fault Tree of the given redundant MPS system and evaluate its failure probability after one production year (t = 5000h).
LHC
String 1
String 2
Primary Fault to be detected
(rate 10^-4 / h)
Sensor
(e.g. voltage measurement)
Decision logics (electronics board)
Communication link 2
Actuator (e.g. Beam Dumping System, …)
Communication link 1

## Slide 17: Demonstrating Reliability: Test overview
Real Case: 113 PSU units (same ref) delivered @ CERN
  A PSU-LAB is in charge of the qualification / reception
  2 different tests were organized to check units reliability
        1st test: All units running during 24 hours (nominal conditions)
        2nd test: 5 units – only - running during 6 months.
Up to 10 units under test conditions
Test duration counters (1 per unit under test)

## Slide 18: Re-Testing reworked units, with clear goal!
The 0-failure test was successful (done on reworked units)
  Even if testing only 10 units makes the 1st failure heavier in the distribution test duration was long and exclusion of steep beta Cumulative Distribution Function becomes possible.
These distributions are still possible
Compare to 100 units running 340 hours ! (1 failure over 100 tested units would represent 1 %, but exclusion of high beta is very poor)
This point was reached without any failure (34 000 hours in total) (1 failure over 10 tested units = 7 %, using Benard’s approximation)
3 400
34 000 hours both in total

## Slide 19: Definition of availability (accelerator specific, adaption of availability definition from literature)
Availability for Physics (PA): “It is the probability that an accelerator provides beam to the experiments for measurements or to the next accelerators.” … Run Time (RT): scheduled operation time of the accelerator … Stable Beams (SB): effective time for beam delivery to experiments or other accelerators
Beam Availability (BA): “It is the probability that an accelerator can be operated with beam at time .” … Machine Cycle Time (MC): time needed to achieve nominal operating conditions of the accelerator, when no faults occur
Machine Availability (MA): “It is the probability that an accelerator can be operated at time , even without beam.” … Fault Time (FT): time needed to clear a system fault
NB: an extension of the availability definitions for the injectors is currently under discussion.
[Source: Diss. Apollonio & CERN]

## Slide 20: The role of injectors – simple sketch
[Source: CERN]
7 TeV
450 GeV (EP to LHC)
26 GeV (EP to SPS)
Beam to different destination
Beam to different destination
LHC
SPS
PS

## Slide 21
21
Row-wise
System of differential equations
Step 2: Construction of the transition matrix and of the system of differential equations
1
2
λ
µ
Transition probability:
  Product of status probability and transition rate
  Arrows towards a state: positive
  Arrows away from state: negative
Summary:
Based on the transition graph, possible state transitions and their related transition rates will be arranged in a transition matrix.
Hint

## Slide 22: ELMAS – Hands On Training

## Slide 23: Feedback

## Slide 24
Thanks a lot for your attention!