## Slide 2: Summer School and Workshop Energy Based Modelling, Simulation, and Control of Complex Physical Systems
Michał Maciejewski
Bernhard Auchmann
Lorenzo Bortot
Jonas Blomberg Ghini
TE-MPE-PE
20.04.2016

## Slide 3: Summer School
Goal: introduction to energy based modelling, simulation, and control of complex physical systems with particular emphasis on port-Hamiltonian systems.
Period: 4/04-6/04
Place: Technical University of Berlin
Lecturers: prof. Arjan van der Schaft, University of Groningen
Peter Breedveld, PhD, University of Twente

## Slide 4: Bond graph modelling
effort
flow
effort*flow = Power
domain | effort | flow
electromagnetic | voltage | current
mechanical | force | velocity
hydraulic | pressure | volume flow
thermal | temperature | entropy flow
R-type element
I-type element
C-type element
0-junction – common effort
1-junction – common flow
Se - source of effort
Sf – source of flow

## Slide 5: Port-Hamiltonian systems
Port-Hamiltonian system
with energy function
For presented example flow and effort variables are given as
resulting in a set of equations

## Slide 6: Workshop
Goal: The workshop fosters the opportunity that the young researchers participating in the summer school can learn about current research directions in the field of energy based modelling, simulation, and control.
Period: 7/04-8/04
Place: Technical University of Berlin

## Slide 7: Challenges
Electrodynamics
Inductive Couplings
Saturation
IFCC-ISCC
Thermal
IFCL-ISCL
Joule losses
Quench propagation
Fluid dynamics
Superfluid Helium
Phase transition
Mechanics
Lorentz forces
Thermal strain
Circuit
154 Magnets
~7 km length
~1e4 net components
Material properties
Extreme non-linearity within few Kelvin
Switch
Appropriate model
Numerical discontinuity
EM waves
Measurements
Coupling
Information exchange
Stability of solution
Performance
Components
Diodes
Thyristors
Properties as f(T, B)

## Slide 8
Status
Co-simulation field-network coupling
COMSOL for electro-thermal problem
PSPICE for electrical network analysis
Benefits
Full electro-thermal dynamic phenomena
Full electro-dynamic circuital analysis
Nodal structure suitable for parallelism

## Slide 9: Challenges
Consistent representation of various domains
Selection of a coupling scheme (coupling strength)
Convergence study for field-circuit coupling

## Slide 10: Order of talks
Michał Maciejewski – Port-Hamiltonian Modelling of Electro-Thermal Coupling in Superconducting Magnets
Jonas Blomberg-Ghini – Towards a Port–Hamiltonian Description of Superfluid Helium in LHC Magnets
Bernhard Auchmann – Port-Hamiltonian Representation of RLC Network Equations
Lorenzo Bortot – Port-Hamiltonian Formulation of Circuit-FEM Coupling for Superconducting Magnet Circuits
Fields of study
FEM modelling
Electrodynamics
Thermal
Mechanics
Fluid-Dynamics
Materials
COUPLING interface
Interface
Solvers Benchmark
Stability
Performance
NETWORK modelling
Transient Phenomena
Nonlinear components
Modularity
Coupling Strength
Scalability

## Slide 11: Port-Hamiltonian Modelling of Electro-Thermal Coupling in Superconducting Magnets
1
0
0
C::H(B)
C::H[u(s)]
DEM
DTh
Resistive field
-
DNetwork

## Slide 12: Towards a Port–Hamiltonian Description of Superfluid Helium in LHC Magnets

## Slide 13: Port-Hamiltonian Representation of RLC Network Equations PH Representation of the Combination of Loop-Current and Cut-Set-Voltage Method
For the example (right) the equations read in terms of fluxes and charges
We compare to the dissipative constrained port-Hamiltonian system
with and
I
II
III

## Slide 14: Port-Hamiltonian Formulation of Circuit-FEM Coupling for Superconducting Magnet Circuits
Coupling methods, magneto-quasi-static field to electrical network:
I: U-control on the boundary ( formulation) ,
II: I-controlled port (formulation),
III: Parameter coupling (Ld, Rq).
IV: Parameter coupling (Ld, Rq, uC ).
Which method is consistent and the most computationally efficient?
R
R
R
R
Ld
I
II
III
IV
Ld
+
-

## Slide 15: Co-simulation of superconducting magnets - Open questions
Coupling strength between physical domains
  Sensitivity bond graph?
  Dirac structure analysis?
Order of execution of simulations
  Computational causality.
Convergence of various co-simulation schemes
  Stability analysis based on Hamiltonian function as a Lyapunov function candidate for time-delay systems?

## Slide 17
Field-circuit coupling – Implementation (1)
I Voltage Source Coupling Interface
Circuit: Inductor as a voltage source
Field: Inductor driven by the current obtained from circuit
No Convergence
III Parameter Coupling Interface
Conceptually wrong: energy is not conserved, unless Ld = L
In the trivial scenario where Ld = L no coupling is needed
Not meaningful
uM(t)
Field
R
Circuit
i(t)
iR(t)
uR(t)
iM(t)
+ -
uM(t)
iM(t)
R
Ld
Circuit
i(t)
iR(t)
uR(t)
uL(t)
iL(t)
L
uM(t)
Field
?

## Slide 18
R
Ld
Circuit
i(t)
iR(t)
iL(t)
uR(t)
uL(t)
+ -
uC(t)
iL(t)
L
uM(t)
uC(t)=uM(t)-uL(t)
iL(t)
Field
iM(t)
L
uM(t)
Field
R
Circuit
i(t)
iR(t)
uR(t)
iM(t)
+ -
iM(t)
uR(t)
iM(t)
Field-circuit coupling – Implementation (2)
IV Parameter Coupling Interface
Circuit: Inductor as a differential inductance
Field: Differential inductance calculated from magnetic flux
The effect of the difference between the two differential inductances is represented as a voltage source uc.
II Current Source Coupling Interface
Circuit: Inductor as current source
Inductor is driven by a voltage source obtained from the circuit
+ -

## Slide 19
Parameter Coupling Interface
Source Coupling Interface
Linear inductor coupling - convergence