## Slide 2: Summary of Joint HiLumi/LARP Meeting at SLAC
Apollonio 9/06/2016
Selection of slides from L. Rossi, G. Arduini, P. Ferracin, R. Calaga, D. Perini and others
Link to indico event

## Slide 3: HiLumi/LARP - Agenda

## Slide 4
FP7-HiLumi classified as «success story» by EC

## Slide 5: Timeline & Goal: Commissioning 2026; 3 ab-1 by 2037 (250 fb-1/y)

## Slide 6: Reviews 2016
10 March: (internal) management review of CC plan for SPS
21-23 March: Conceptual Design Review of the HL-LHC Magnet Circuits
6-8 April: 11T dipole for DS Collimator HL-LHC
27 May : (Internal) Tech. Infr. C&S review
7-10 June: MQXF review
30June-1Jul: D1 review (KEK)
August/Sept. : Review of the need for Halo control via e-lens.
17-19 Oct: C&SR-II

## Slide 7: The boat is (near) full steam… Time for changes is narrowing plan must be frozen (LS4 becoming part of HL-LHC: CC and…)

## Slide 8: 200 MHz option
Drawbacks:
  Co-existence with 400 MHz crab-cavities, in particular, potential DA restrictions  no sign so far
  Longitudinal stability limits are lower
  Lower TMCI threshold but always well beyond the operational bunch parameters
Advantages:
  Potentially allowing to inject higher bunch populations with longer bunches  needs to be confirmed by LIU
  Minimization of electron cloud effects if scrubbing not sufficient to suppress electron cloud in the dipoles (SEY=1.4) , intra-beam scattering and heating
  Possibility of luminosity leveling with bunch length
G. Iadarola, K. Li

## Slide 9: 200 MHz
e-cloud quad.
e-cloud dip.
Impedance
Syn. radiation
256 fb-1/year
HL-LHC baseline (400 MHz)
243 fb-1/year (-5% w.r.t. 400 MHz)
200 MHz option, “natural” shortening
G. Iadarola
SEY=1.4

## Slide 10
J. Fox

## Slide 13
With axisymmetric electron distribution the beam core is unperturbed whereas the halo gets a smooth tuneable transverse kick. This device is a complement of the collimation system and will increase its efficiency.
G. Stancari, V. Previtali, A. Valishev, R. Bruce, S. Redaelli, A. Rossi, and B. Salvachua Ferrando “Conceptual design of hollow electron lenses for beam halo control in the Large Hadron Collider”.
Hollow e- lens

## Slide 14
Functional main requirements
Beam-to-beam distance 420 mm
Other devices around
We need a set of magnets to drive the electrons, an e-gun, a collector, instrumentation and all services and power supplies.
Robust and reasonably simple ( an often quenching 5 T solenoid is not a good idea).
Easy installation, maintenance, modifications.
Compact construction.

## Slide 15: Crab Cavities – Ongoing Activities
Notes: Design per SPS, lo stesso concetto da tenere per LHC. DQW: vertical kick

## Slide 16: Crab Cavities – Ongoing Activities
Update on the Cavity + CM production
SPS Test preparation
Cost & Schedule Review (New Baseline)
CM Review, Nov 2015 (Basic design choices approved)
SPS Test Day I
DQW
RFD
Notes: Design per SPS, lo stesso concetto da tenere per LHC. DQW: vertical kick

## Slide 17: Revised Planning
First Re-Baselining after C&S Review I
    US cavities delayed (+ unresolved “conformity standards”)
    CERN cavity production (DQW) for SPS is adopted as baseline
Impact on SPS is significant
SPS test prototype (2 CM)
preparation
Tests (DQW)
LHC pre-series (2 CM)
Fabrication & tests
Installation
LHC series production (8 Mod)
Run 2
2015
2016
2017
2018
2019
2020
2021
2022
2023
2024
2025
2026
LS2
LS3
EYETS
Run 3
Run 4
YETS
YETS
YETS – 8 weeks
EYETS – 14 weeks
Tests (RFD)

## Slide 18: Impedance (crab cavities)
Impressive progress in the impedance reduction of crab cavities!
Pick up antenna (5/2015)
modified to lower Qext of 1.75 GHz mode
Z. Li
Before
After
Remaining HOM mode at 920 MHz for DQW cavities to be damped
DQW cavity

## Slide 19: SPS-LSS6 Implantation
Cryo-module
Movable Table
QDA 61710
CC
TPSG 61773
Multiple Vacuum sectorization to accommodate bypass & module replacement
11.5m overall space, CM installed in a by-pass & motorized transfer table
RF & Cryo on movable table with liquid Helium

## Slide 20: HiLumi low-β quadrupole MQXF
Target: 132.6 T/m
  150 mm aperture, 11.4 T Bpeak
Q1/Q3 (by US-HiLumi Project)
  2 magnets MQXFA with 4.2 m
Q2a/Q2b (by CERN)
  1 magnet MQXFB with 7.15 m
Different lengths, same design

## Slide 21: MQXFS1 test Quench performance
Ultimate reached both at 1.9 K and 4.5 K
Reached 85% of current limits at 1.9 K and 93% at 4.5 K
  Significant margin confirmed by ramp-rate
Full memory
8 hours at ultimate without quenches
By G. Chlachidzei

## Slide 22: Powering requirements - ripple
Tight requirements on triplet powering from:
  Accuracy in the measurement of b* (low frequency regime – O(Hz))
  Dynamic aperture considerations (10 Hz – 1 kHz)
Class 1 power converter mandatory
Triplet powering scheme with 1 main power converter (recommended by Powering review) minimizes tune ripple but still marginal
  pending update on power converter performance WP6b (ongoing)
Higher frequency performance marginal for 300-600 Hz frequencies but pending:
  Evaluation of the transfer function B(I) (f) taking into account beam screen and cold bore  WP3
  Reduction of the noise at thee frequencies should be possible. Updated performance expectations  WP6b
  D1s, D2s, and Q4s ±1 ppm accuracy is adequate
  MDs to evaluate the possible impact of low frequency ripple/vibrations to be pursued
R. De Maria, M. Fitterer

## Slide 23
Thanks a lot for your attention!

## Slide 24
 | 2016 |  |  |  | 2017 |  |  |  |  |  | 2018
 | Qtr1 | Qtr2 | Qtr3 | Qtr4 | Qtr1 | Qtr2 |  | Qtr3 | Qtr4 |  | Jan
RF Power | 2 IOTs SM18 2 IOTs in BA6 (FPC Conditioning) |  |  |  |  |  |  |  |  |  | 
LLRF/Controls | SM18-Vertical Tests Setup |  |  | Deploy for VTA | BA6-SM18 Setup High Power & deployment |  |  |  |  |  | 
Dressed Cavities | Cavity 1 Fabrication (Treatment + Cleanroom tooling) |  |  |  | Cav 2 Fabrication + Cav 1 & 2 Treatment/Testing + Clean room assembly |  |  |  |  |  | 
FPCs | 2xFPCs in SM18 Cleanroom |  |  |  | FPC Conditioning (TB) |  |  |  |  |  | 
Cryomodule | Cryostat & Tooling Design/Procurement |  |  | Cryomodule/Tooling Preparation |  |  |  | CM Assembly |  | Cold Tests | SPS
Cryogenics | Cryogenic Distribution & Valve Box SM18/SPS |  |  |  |  |  |  |  |  | CM + VB | 
Movable Table | Design & Manufacturing |  |  |  |  |  |  | Tests at CERN |  |  | 
SPS Revised Planning

## Slide 25: Voltage Withstand Levels
Update of table peak temperature and voltages
Data used to define voltage level of electrical acceptance test (work in progress)
By F. Rodriguez-Mateos